## Slide 1: Automation of Geometric Accuracy Assessment Algorithm
Alana Semple1,2
Bin Tan1,2
Guoqing (Gary) Lin1
1. NASA Goddard Space Flight Center, Greenbelt, MD
2. Science Systems and Applications, Inc., Lanham, MD
Sponsorship: NASA Commercial Smallsat Data Acquisition (CSDA) Program
JACIE 2023 Workshop
USGS Headquarters, Reston, VA
03/29/2023

## Slide 2: Outline
Background
Geolocation Offsets Assessment Algorithm
Automatic Filtering Algorithm
Application of Algorithm
Summary

## Slide 3: Geolocation Offsets Between Satellite Images
Characterize geolocation accuracy of satellite data for NASA’s Commercial Smallsat Data Acquisition (CSDA) program.
Necessary step in time series analysis of satellite imagery such as flood mapping and remotely sensed season changes.
Inter-sensor and inter-resource analysis
[1] L. Eklundh & P. Jönsson, 2017 TIMESAT manual
[2] N. Levin & S. Phinn, 2022
Notes: Intro & motivation, ex: flood mapping, NDVI calculation

## Slide 4: Geolocation Accuracy Assessment Algorithm
Example Case 1: MAXAR's Worldview 2 (0.8 m) red band (.63 - .69 µm) vs Planet’s SuperDove (3 m) red band (0.65 - 0.68 µm) over Manta, Ecuador.​
Determine area of overlap between images based on UTM coordinates.
Split overlapped region into 350 m x 350 m image subsets (chips).
Resample chips to common resolution with bicubic interpolation.
False color image visually showing initial offset between images.
PS image
Taken: 2021/12/24
WV image
Taken: 2021/04/19
R: PS image
G: WV image
B: WV image
Notes: Image comparison and chips

## Slide 5: Calculate Chip Offsets
Impose offsets between chip pairs.
Calculate Pearson Cross Correlation Coefficient (PCC) at each offset.
Final chip offsets are those that give the best PCC between the images.
PCC
NS offset
EW offset
Ideal PCC map if offsets are 0 m in North-South (NS) and East-West (EW) directions
Chip pair with best PCC at offsets:
NS = -2.1 m
EW = -10.0 m
Notes: PCC

## Slide 6: Calculate Chip Match Quality
Correct chip offsets and calculate measurement uncertainty (MU) for quality check.
Find MU for all chips to preform the filtering step.
MUx =
1
)
(
1
c2
c1
1
2
D
NM
zpk
2
1
1
PkShx
PkShx : Peak sharpness
N and M : image dimensions
zpk : refined PCC
c1 & c2: normalized contrast of two images
D: normalized contrast difference at overlap region
[3] F. De Luccia et al. 2016
Notes: MU

## Slide 7: Apply Quality Filter: Previously Manually
Low quality can be caused by: Clouds water, building shadow, seasonality of dense vegetation cover, etc.
Low quality chips influence final image offsets and should be removed.
North-South offsets (m)
Chip Match Quality
Notes: 1/MU = gauss, previously manual

## Slide 8: Apply Quality Filter: Previously Manually
Low quality can be caused by: Clouds water, building shadow, seasonality of dense vegetation cover, etc.
Low quality chips influence final image offsets and should be removed.
Removal was previously manual and based on a threshold quality (red line in example data), this was reasonable when few sensors were being assessed.
North-South offsets (m)
MU is dependent on sensor properties, so each sensor will have a different ideal threshold value
North-South offsets (m)
Chip Match Quality
Notes: 1/MU = gauss, previously manual,

## Slide 9: Apply Quality Filter: Previously Manually
Low quality can be caused by: Clouds water, building shadow, seasonality of dense vegetation cover, etc.
Low quality chips influence final image offsets and should be removed.
Removal was previously manual and based on a threshold quality (red line in example data), this was reasonable when few sensors were being assessed.
Can the Gaussian-like shape be used to automate threshold determination?
North-South offsets (m)
Chip Match Quality
Notes: 1/MU = gauss, previously manual,

## Slide 10: Automatic Determination of Threshold value
[4] Tan et al., 2011 determines growing season start and end based on derivatives of the Enhanced Vegetation Index (EVI) time series.
[4] Tan et al, 2011
Notes: Timesat, 3rd derivative for auto cutoff

## Slide 11: Automatic Determination of Threshold value
[4] Tan et al., 2011 determines growing season start and end based on derivatives of the Enhanced Vegetation Index (EVI) time series.
Geolocation assessment automation uses a similar approach to find the threshold quality value.
[4] Tan et al, 2011
North-South offsets (m)
Chip Match Quality
Notes: Timesat, 3rd derivative for auto cutoff TIMESAT curve fitting

## Slide 12: Preprocess data for Gaussian Approximation
Remove initial outliers based on moving average of chip match quality.
In the example, gold box shows approximate window size, and red points are those removed by this filter.
Moving Window
North-South offsets (m)
Chip Match Quality
Notes: Step1, loose data filter

## Slide 13: Extract Profile for Gaussian Approximation
Select the top most point (green in example) within a narrow moving window to construct data for line fitting.
North-South offsets (m)
Chip Match Quality
Notes: Step 2, designate only outer pts

## Slide 14: Least Squares Inversion of 1-sided gaussian
Data split to left side and right side based on maximum value.
Gaussian parameters determined by Python library SciPy’s least_squares function with initial guesses:
x1 = position of data’s maximum quality
x2 & x4 = data’s standard deviation
x3 & x5 = 2
[1] L. Eklundh & P. Jönsson, 2017
Right
Left
North-South offsets (m)
Chip Match Quality
Notes: Step 3, approximate 2 1-sided gaussians, TIMESAT

## Slide 15: Threshold Value Calculated and Applied
Calculate solutions of the 3rd derivative.
Determine the threshold value by evaluating which solution returns a higher chip match quality.
Remove all matches of quality below the threshold (black points in figure).
Calculate mean offset between the images with the remaining filtered data (blue points in figure).
Before Filter
# Chips: 2047
Mean offset: -0.7 m
Std Dev: 9.3 m
RMSE: 9.3 m
CE90: 23.3 m
After Filter:
# Chips: 403
Mean offset: -2.4 m
Std Dev: 2.1 m
RMSE: 3.1 m
CE90: 12.8 m
North-South offsets (m)
Chip Match Quality
Notes: Step 4: find 3rd derivative and use as cutoff,

## Slide 16: Automated Geolocation Accuracy Assessment
Examples of full application of the automated geometric assessment algorithm.
Blue points are those that passed all filters, black points were removed by either preprocessing or quality threshold, red line indicates the automatically determined quality threshold
Case 1, Manta, Ecuador
North-South offsets (m)
East-West offsets (m)
Case 2, Boston, MA, USA
North-South offsets (m)
East-West offsets (m)
Chip Match Quality
Chip Match Quality
Notes: Effectiveness: mean and std

## Slide 17: Application to Large Scale Assessment
Table shows results for running this automated algorithm on PS SuperDove images compared to a single WV image at each location.
A City Within: | # of PS Images | # of Chips | X Mean (m) | Y Mean (m) | X StdDev (m) | Y StdDev (m) | X RMSE (m) | Y RMSE (m) | CE90 (m)
California | 11 | 2257 | -2.2 | .3 | 1.7 | 1.8 | 2.8 | 1.9 | 3.5
New Mexico | 20 | 6072 | -.4 | -.3 | 1.9 | 1.4 | 1.9 | 1.5 | 3.2
Canada | 6 | 517 | 1.4 | 2.0 | 2.0 | 3.2 | 2.4 | 3.7 | 6.0
Mexico | 5 | 4361 | 2.0 | 1.0 | 1.5 | 1.4 | 2.5 | 1.7 | 4.4
Ecuador | 6 | 3301 | -5.6 | -7.6 | 1.6 | 2.3 | 5.8 | 7.9 | 11.3
Brazil | 6 | 6848 | -.9 | 3.3 | .9 | 1.6 | 1.3 | 3.7 | 5.1
Chile | 5 | 1023 | -4.6 | 3.8 | 1.2 | 1.6 | 4.8 | 4.1 | 7.6
Argentina | 7 | 1851 | -2.5 | -5.4 | 1.7 | 1.5 | 3.0 | 5.6 | 7.8
England | 6 | 2727 | -3.7 | 12.8 | 1.9 | 2.8 | 4.1 | 13.1 | 16.6
Ireland | 5 | 2668 | -1.1 | 10.3 | 1.4 | 1.5 | 1.8 | 10.4 | 12.3
Sicily | 5 | 2182 | -5.8 | 10.4 | 4.3 | 5.1 | 7.2 | 11.6 | 15.7
Turkey | 9 | 2901 | -22.0 | 12.2 | 2.4 | 1.9 | 22.1 | 12.3 | 28.1
Morocco | 5 | 1182 | 4.3 | 2.0 | 5.0 | 4.2 | 6.6 | 4.6 | 7.0
Angola | 6 | 4292 | 3.8 | .4 | .8 | 1.5 | 3.8 | 1.6 | 5.0
Somalia | 5 | 5244 | -1.2 | 1.0 | 1.3 | 1.2 | 1.7 | 1.5 | 3.3
South Africa | 6 | 4597 | -6.2 | .1 | 1.6 | 1.2 | 6.4 | 1.2 | 8.2
Cairns | 6 | 2758 | 1.7 | -.3 | 3.0 | 3.7 | 3.4 | 3.7 | 6.0
Melbourne | 6 | 2485 | -10.1 | 9.8 | 1.0 | 1.6 | 10.1 | 10.0 | 15.2
Perth | 6 | 3387 | -7.6 | -7.5 | 1.8 | 1.6 | 7.8 | 7.6 | 13.2
Singapore | 6 | 1169 | -.5 | 2.8 | 3.8 | 2.9 | 3.8 | 4.1 | 7.1
Total Data: | 137 | 61822 |  |  |  |  |  |  | 
Notes: Conclusions

## Slide 18: Summary
Our geolocation accuracy assessment algorithm is now fully automated and can evaluate any imagery pair (WV, PS, NAIP, etc.) without manual intervention.​
Data filtering is needed for an appropriate image offset calculation.
Automation is needed for analysis involving a large number of individually built sensors.​
Effective automated data filtering is preformed based on the 3rd derivative of a Gaussian fit to determined offsets vs. chip match quality.
The automated assessment has been run on 2000+ image pairs since Dec 2022.
Notes: Conclusions

## Slide 19: References
[1] Eklundh, L., and P. Jönsson. "TIMESAT 3.3 with seasonal trend decomposition and parallel processing Software Manual." Sweden: Lund and Malmo University (2017).
[2] Levin, N., and S. Phinn. "Assessing the 2022 Flood Impacts in Queensland Combining Daytime and Nighttime Optical and Imaging Radar Data." Remote Sensing 14.19. doi:10.3390/rs14195009 (2022).
[3] De Luccia, F. J., Houchin, S., Porter, B. C., Graybill, J., Haas, E., Johnson, P. D., Isaacson, P. J., and Reth, A. D. “Image navigation and registration performance assessment tool set for the GOES-R Advanced Baseline Imager and Geostationary Lightning Mapper”, Proc. SPIE 9881, Earth Observing Missions and Sensors: Development, Implementation, and Characterization IV, 988119 (2 May 2016); doi: 10.1117/12.2229059 (2016).
[4] Tan, B., Morisette, J. T., Wolfe, R. E., Gao, F., Ederer, G. A., Nightingale, J., & Pedelty, J. A. "An Enhanced TIMESAT Algorithm for Estimating Vegetation Phenology Metrics From MODIS Data," in IEEE Journal of Selected Topics in Applied Earth Observations and Remote Sensing, vol. 4, no. 2, pp. 361-371, June 2011, doi: 10.1109/JSTARS.2010.2075916 (2011).

## Slide 20: Questions?
Notes: Conclusions