## Slide 1: Mobile Laucher 2 - NASA Pete Carrato Joe Cartledge Kevin MacLeod

## Slide 2
PDH Code
######

## Slide 3: Misson
Pete Carrato

## Slide 4: Misson
https://moon.nasa.gov/news/46/nasas-exploration-campaign-back-to-the-moon-and-on-to-mars/
Pete Carrato

## Slide 5: Misson
NASA Fact Sheet: NASA Space Launch System (usra.edu)
Pete Carrato
Artemis I-III (Block 1)
Artemis IV + (Block 2)

## Slide 6: Misson
Pete Carrato

## Slide 7: The Team
Pete Carrato
...and many more.

## Slide 8: The ML2 Structure - Nomenclature
Joe Cartledge
Bechtel’s Vision – Extraordinary Teams Building Inspiring Projects.
Base
Tower
  Chair
  MOD04-MOD10
  Umbilical
    Mandatory Inspection Points (MIPS)
ML1 compared to ML2
  X-Bracing vs Chevron Bracing
  Plate Girders vs Trusses
  Tower Chair Integration
  Extended Trusses
  Increased height, vehicle weight, and plume loads

## Slide 9: The ML2 Structure - Nomenclature
Joe Cartledge
Mount Mechanism
  Six (6) Mounting Mechanisms (MM): At Park Site, VAB and Launch Pad
  Four (4) Extensible Columns (XCS): At Launch Pad
  Four (4) Crawler Transporter (CT) pick up point

## Slide 10: The ML2 Structure - Nomenclature
Joe Cartledge
  Crawler: Lifts Mobile Launcher from the MMs and transports from the Vehicle Assembly Building (VAB) to the Launch Pad.
  One of the largest self-powered land vehicles in the world. Upgraded in 2014-2016 to increase lifting capacity to 18 million pounds.
    Critical design requirements is weight, based on capacity of crawler.

## Slide 11: Rollout Video
Artemis 1 on Launch Pad - 39B

## Slide 12: The ML2 Structure – Structural System
Joe Cartledge
Side 1
Side 3
Side 2
Side 4
Primary Base
  Deep Trusses
  Plate Girders
  Decks (0, A, B)
Secondary
  Commodity Supports
  Equipment Supports
    Stand-Offs
    Isolators
  Stairs
  Interior/Exterior Wall Panels
ML2 Base: Plate Girders Trusses
Deck B, Typical Floor Panel with Equipment Support Beams

## Slide 13: The ML2 Structure – Structural System
Joe Cartledge
Primary Tower
  Chair
  Modules
  API – Columns/Bracing
  Cast Connex
    104 Cast Connex Nodes
  Floor Framing
  Electrical Rooms
Secondary
  Elevator Shaft
  Umbilical Rails
    Adjustable Connections
  Commodity Chase
  Commodity Supports
  Equipment Supports
  Stairs
ML2 Tower: Columns, Bracing, Floor Framing, Elevator Shaft
Electrical Rooms

## Slide 14: Design Constraints – Weight
Joe Cartledge
Weight Status | Weight (lbs.)
Total Weight | 12,499,057
Required Weight | 12,867,700
Weight Limit | 12,967,700
NASA Weight Reserve | 100,000
Weight Savings Study Executed

## Slide 15: Design Constraints – Center of Gravity
Joe Cartledge
Center of Gravity
CT2
Crawler pick-up point spacing is fixed
Stiffen section and truss within a truss provides flexibility to adjust pickup locations
Analysis allows for adjustment of pickup points (Z direction) from assumed COG
CG

## Slide 16: Structural Design, Connection Design, & Detailing
Structural Design
  75 Calculations
  1000 IFC Drawings
Connection Design
  DOR
    Self-Performed Connections (Bechtel)
    Fabricator Performed Connections (CSD)
    Fabricator Performed Castings (Cast Connex)
  Bolting
    F3148 Grade 144, TNA
  Welding
    D 17.1 Requirements: Class A, B, C
      Class A (Critical) – 100% VI, 100% RT or UT, and 100% MT or PT
      Class B – 100% VI and 100% MT or PT
      Class C – 100 % VI
      Weld Map/Data
Detailing
  Dowco
  Clashes
Joe Cartledge
Cast Connex, K- Node
Cast Connex, X-Node
Complex Connection MM5, Bechtel

## Slide 17: Analysis Models
Global Model
  Establish Geometries
  Baseline Load Combinations
  Macro Loading
  Construction Sequence
  Design of Trusses, Pre-Buy of API Pipe
  Force and displacement input to local models
Local Models
  Start from Basic Global Model Load Cases
  Refined Geometry
  Add concentrated/peak component loading
Stiffness Checks
  Global Model Geometry
Kevin MacLeod
Notes: Build all possible geometry, BC, and load cases, then align and combine them

## Slide 18: Loads and Load Combinations
Kevin MacLeod
Independent Load Cases (ILC)
  1500
Dependent Load Cases (DLC)
  String of ILC: 1500
Load Combinations
  String of DLC: 6300
DLC: 'PLUME_1' FROM ILC 'PI_S_B' 1.0 'PI_TF_B' 1.0 'PI_IT_V' 1.0 'PI_FS_V' 1.0 'PI_VS_V' 1.0 'PI_EE_V' 1.0 'PI_VD_V' 1.0 'PI_CA_V' 1.0 'PI_CA_L' 1.0 'TSMPI_X' 1.0 'TSMPI_Y' 1.0 'PI_PGT1' 1.0
LOAD COMBINATION: 'PLUME_1' COMBINE 'DL_CON' 1.0 'DLA_PF6' 1.0 'IOP_WO' 1.0 'DLA_PI' 1.0 'PDB_1' 1.0 'PLUME_1' 1.0
DLC:
ILC(1):
ILC(2):

## Slide 19: Loads and Load Combinations
Kevin MacLeod
Operational Phases | Support Condition | Dead Load Adjustments | Vehicle Loads | Dynamic Loads | Wind Speed Spec | Additional Cases Considered 1
Rollout | CT | Arms Extended | No Vehicle/ Unfueled Vehicle | Transport | DSNE | Multiple C.G. Support Locations
On Pad Stay | MM | Arms Extended | No Vehicle/ Unfueled Vehicle |  | DSNE | Min DL/Uplift
On Pad Operations | MM (+XCS) | Arms Extended, Deluge Filled | Unfueled Vehicle/ Fueled Vehicle (+XCS) |  | DSNE | 
Liftoff | MM+XCS | Arms Retracting T-0 | Fueled Vehicle | Engine Shutdown | DSNE | 
Plume | MM+XCS | Arms Retracted | No Vehicle | Thermal/ Vibration | DSNE | Max Base Driven and Tower Driven Loading
Hurricane | MM | Arms Retracted | No Vehicle |  | ASCE | Min DL/Uplift
1. MM Spherical Bearings Fixed and Pinned
Notes: Live Load is local concern for member design, not impactful globally, high level of LLR.
Challenges: Controlling DL changes, aligning model weights to C.G. with SDL.
24 Lateral Cases aligning with ASCE 7 corner and eccentricity cases

## Slide 20: Dead Load and Vehicle Load
Deluge: 600 kip of Water
Max Vehicle Weight:
  Block 2 Empty: 4,100 kip
  Block 2 Fueled: 6,600 kip
Kevin MacLeod

## Slide 21: Dead Load and Vehicle Load
https://www.nasa.gov/image-article/birds-eye-view-of-sls-rocket-mobile-launcher/​
https://www.nasaspaceflight.com/2021/11/sls-ml-2-update/
Arms and Umbilicals: ~30kip each
  Extending 40’ off MLT
Kevin MacLeod

## Slide 22: Wind/Hurricane Loads
Kevin MacLeod
Operational Wind Consideration
Hurricane: ASCE 7, Risk Category I, Exposure D
Hurricane Nicole November 2022
Hurricane Ian September 2022
https://www.geekwire.com/2022/nasa-artemis-sls-moon-rocket-weather/
https://indianexpress.com/article/technology/science/nasa-artemis-sls-rocket-hurricane-8267262/
Notes: 5 DSNE wind speeds determined to achieve NASA’s desired probability of occurrence for the duration of the operation. Treated as service level winds.
Design level hurricane per ASCE 7, ultimate level wind speeds assuming no vehicle.
Each of 6 speeds has 24 lateral cases, applied to each dead load configuration.

## Slide 23: Launch Environment
Kevin MacLeod
Plume Impingement
Plume Load Development
Direct Pressures vs. Probabilistic Pressures
Base Driven vs. Tower Driven
  Time consistent Loading
Other Launch Environment Considerations
Vibration
Acoustic
Thermal
Notes: 5 GNC Data Sets, each with 2001 sims. Using Heavy Slow Measured Winds. Low Vehicle thrust to weight ratio statistically representative wind profiles. Simulates a magnitude and direction varying distribution of launch day winds which most closely represents the pad environment.

## Slide 24: Plume Vertical Loads
Kevin MacLeod
Direct Pressures Applied to Top of Tower and 0-Deck
Haunch Loads
Time Consistent Probabilistic Pressures
Model Application
Pressure Contour
Notes: 9 Cases to capture different drift directions
Haunches 120-150psi

## Slide 25: Plume Lateral Loads
Kevin MacLeod
Free Flowing Plume
Turned Flow

## Slide 26: Combinations
Kevin MacLeod
Global Model
6300 Load Combinations
4800 Tons of Steel
Local Models
Elevator
Stairs
Electrical Rooms
Umbilical Rails/Attachments
Platforms
Equipment/Piping
Commodity Grids
Commodity Chase
Cameras

## Slide 27: Local Loads
Kevin MacLeod
Equipment and Piping
23 Subsystems
Commodity Support Framing
  14,000 Pipe Supports
  50,000 LF of Piping
  25,000 LF Tubing
  650,000 LF Cables
Equipment Frames and Support
  1000 Pieces Framed/Skids
  1500 Minor Pieces/Censors

## Slide 28: Stiffness Requirements
Kevin MacLeod
Developed from NASA Coupled Analysis
ML to Vehicle Interface Limits
Tower requirements
Horizontal displacements Vehicle Stabilizer (VS) and Vehicle Damping System (VDS)
  Unit Loads
  Emergency Egress System (EES) Loads
Base requirements
Vehicle Support Post (VSP) Displacement
  Vertical Displacement under Vehicle Loads
  Planarity and Relative Stiffness
Top of Vehicle Displacement
  Stacking operations
  Transition between support conditions
  Relative to tower
Notes: Revolve around vehicle interface, VS/VDS/VSP
T/vehicle displacement after stack and BC transitions

## Slide 29: Stiffness Analysis
MLT Stiffness
Buttress Columns
Virtual Work to Optimize Critical Members
MLB Stiffness
Integrate chair and base trusses
Virtual Work to Optimize Critical Members for Stiffness
Kevin MacLeod
Notes: Block 2 uses ring mount around VSP’s to control load to vehicle through VSP

## Slide 30: Design Constraints – Installation Tolerances
Kevin MacLeod
Mandatory Inspection Points (MIPs)
  Critical umbilical to vehicle interface
Umbilical Self-Weight and Extension Front Load MLT Causing Tower to Lean
Design Shim Plates Installed Between MLT Modules to Counter Tower Lean
  Simulate shims in analysis with concentrated axial distortion
  Utilize real time construction metrology data to refine model
Tower Deflection due to Self -Weight (left)
Tower Deflection due to Shimming (right)

## Slide 31: Conclusions
Designing a Mobile Launch platform is a unique engineering challenge.
  Meet stringent stiffness and weight limit requirements.
  Deal with a moving structure that has different operation needs and changing support conditions.
  Unique loads and code requirements that are outside of industry standards and handle thousands of load combinations to assess every possible scenario.
  Incorporate construction sequence and modular design needs to support construction schedule.
  Analyze critical temporary conditions through construction to monitor displacements and design countering measures to minimize risk of stringent installation tolerances.
  Management of numerous interfaces among the design team, and supplier.
Close coordination among the analysis team, engineering disciplines, construction planners, steel fabricators, and NASA is required to ensure mission success.
Kevin MacLeod

## Slide 32: Launch
Kevin MacLeod

## Slide 33
CONTACT
PDH CODE ######
Speaker
Email address
Phone #