## Slide 1: Carbothermal Reduction Demonstration (CaRD)
overview
This project will integrate the key components of the solar-carbothermal process (solar concentrator, carbothermal reactor, gas analysis, avionics, software) and demonstrate operations in a relevant environment. In the solar-carbothermal reduction process, concentrated solar energy is delivered into a pressurized reactor. The thermal energy delivered to the reactor is used to melt lunar regolith simulant contained within the reactor. The molten regolith reacts with a source of carbon and oxygen is removed from silicate minerals in the form of carbon monoxide. The reaction products are quantified using a mass spectrometer to determine the performance of the process.
TX 7.1.3 Resource Processing for Production of Mission Consumables TRL: start 4 / current 5
Project Management Aaron Paz / 281-244-0163 / aaron.paz-1@nasa.gov
Leads Nilab Azim, Chris Bond, Tony Colozza, Jim Kania, Jeff Michel, Desmond O’Connor, Brant White
Primary Mirror
Composite Mirror Applications
Secondary Mirror
Composite Mirror Applications
Deployable Structure
Glenn Research Center
Avionics/Software
Kennedy Space Center
Optical Shutter
Johnson Space Center
Carbothermal Reactor
Sierra Space
Fluid System
Sierra Space
Azimuth/Altitude Mount
Glen Research Center
CaRD Integrated Solar-Carbothermal Prototype System
Lander Deck Mockup
Johnson Space Center
Not Shown:
Gas Analysis
Kennedy Space Center
Heliostat
Johnson Space Center
CaRD will generate CO, which can be combined with hydrogen to make methane and water like Mars ISRU