## Slide 1: Automated Space Link Connectivity (AutoCon) HP20 Payload & Mission Operations Division Gayleen Ijames (HP26), Ramon Pedoto (HP25), Jeff Lippincott (HP25), Andrew Cecil (HP27)
Automation Flow
TReK Planning interface will ingest contact schedule and create a timeline template for contact events including start and stop times.
TReK Telemetry & Commanding will process downlink data for data storage and retrieval.
TReK Automation software will be launched prior to the pass to begin automated pass. The following functions will be performed during the pass (at a minimum): receive, monitor and process telemetry, send e-mail/text for out of limit condition, send commands and log all activities performed during the pass.
TReK provides framing and SLE support and makes the SLE bind/connection to SLE Network using CCSDS.
Stored data will be accessed through the AEON Portal.
1
2
5
4
A ground system solution that automatically connects to ground stations and executes pre-defined commands and file operations based on a contact timeline.
6
Downlinked telemetry data will be made available in LUCA for Users to access.
3
Huntsville Operations Support Center
Lunar Utilization Control Area (LUCA)
AutoCon
Satellite/Spacecraft
Ground Station (SCaN)
User (Windows)
Telescience Resource Kit (TReK) Server
Browser
TReK Desktop
EPC
Ground Station Schedule
AEON Portal
AEON Front End Server
Files
Recorded
Files
5
6
TReK
Web Server
* Status & Control
* Messages
TReK Telemetry & Commanding
TReK SLE Proxy
3
4
Telemetry Status/Uplink Commands
TReK Planning
TReK Automation
2
DAX
1
Other Features
Remotely view significant messages from vehicle.
Remotely perform system administration tasks (for privileged users).
Manually command and create rich Telemetry displays using EPC/TReK Desktop.
Create timelines that align commanding and file operations with contact passes.