## Slide 1: Planetary Protection
Amy Baker1, J. Nick Benardini2, Erin Lalime2, Elaine Seasly2 and J. Andy Spry1
1SETI Institute; 2NASA Headquarters
April 25, 2024
MEPAG Hybrid Meeting #41
Washington DC

## Slide 2: Planetary Protection Objective
Protect current and future scientific investigations by limiting biological and relevant molecular contamination of other solar system bodies through exploration activities and protecting the Earth’s biosphere by avoiding harmful biological contamination carried on returning spacecraft, as described in the Outer Space Treaty.
Forward PP - Understand and control harmful contamination of other worlds by terrestrial organisms, organic materials, and volatiles from spacecraft
Backward PP - prevent harmful biological contamination of the Earth-Moon system by potential extraterrestrial life and bioactive molecules in returned samples

## Slide 3: International Planetary Protection Process
Committee on Space Research (COSPAR)
Panel on Planetary Protection forms international consensus guidelines
Defines PP Categories I – V based on target body and mission type
NASA
Supports the science-based international consensus process
Develops new guidelines and provides significant input to COSPAR
The Outer Space Treaty of 1967
International Responsibility
Planetary Protection
Article VI:
States Parties to the Treaty shall bear international responsibility for national activities in outer space, including the moon and other celestial bodies, whether such activities are carried on by governmental agencies or by non-governmental entities, and for assuring that national activities are carried out in conformity with the provisions set forth in the present Treaty
Article IX:
States Parties to the Treaty shall pursue studies of outer space, including the Moon and other celestial bodies, and conduct exploration of them so as to avoid their harmful contamination and also adverse changes in the environment of the Earth resulting from the introduction of extraterrestrial matter and, where necessary, shall adopt appropriate measures for this purpose
3
Support the science-based international consensus process
Develop new guidelines and provide significant input to COSPAR

## Slide 4: NASA’s Planetary Protection Policy & Guidance
NASA Policy Directives (NPDs)
Documents Agency policy statements
Describe what is required by NASA management to achieve NASA’s vision, mission, and external mandates
NPD 8700.1F
Replaced NPD 8020.7G
NASA Policy for Safety and Mission Success
Effective Date July 28, 2022
Expiration Date: July 28, 2028
NPR 8715.24
Replaced NPR 8020.12D/NID 8020.109A
Planetary Protection Provisions for Robotic Extraterrestrial Missions
Effective Date September 24, 2021
Expiration Date: September 24, 2026
NASA-HDBK-6022
Handbook for the Microbial Examination of Space Hardware
Expiration Date: N/A
Status: Revision planned. Last draft revision released Aug 17, 2010
NID 8715.129 (“Mars NID”)
Biological Planetary Protection for Human Missions to Mars
Effective Date: July 9, 2020
Expiration Date: Sept 30, 2025
NASA-STD-8719.27
Implementing Planetary Protection Requirements for Space Flight
Effective Date August 30,2022
All published documents found in NODIS: https://nodis3.gsfc.nasa.gov/ or
the OPP website: https://sma.nasa.gov/sma-disciplines/planetary-protection#PolicyGuidance
NASA Procedural Requirements (NPRs)
Provide detailed procedural requirements to implement policy
Guide how policy directives are implemented in the context of specific missions
NASA Standards
Provide technical requirements
Each NASA Technical Standard is assigned to a Technical Discipline
NASA Handbooks
Companion documents to NPRs and NASA Standards
Provide supporting material such as guidelines, lessons learned, procedures, and recommendations
NASA Interim Directives (NIDs)
Documents an immediate, short-term statement of the Agency’s policies, requirements, and identifies responsibilities for implementation
Temporarily modify policy directives or implementation requirements
= Document being updated
Link to NASA Planetary Protection policy and guidance documents at www.sma.nasa.gov

## Slide 5: NASA’s Planetary Protection Roles
Mission Directorates
Programs Projects
Office of Safety and
Mission Assurance
Program/Project-level
Technical Authority
Office of Planetary Protection
Administrator’s Office
Chief Scientist
implement
maintain NASA policy
oversee implementation (Technical Authority)
White House / OSTP
Inter-Agency
International Partners
National Academies
Review Panels
NPD 1000.3 §4.13.2 “OVERALL RESPONSIBILITIES. The Chief, Safety and Mission Assurance reports to the NASA Associate Administrator and advises senior leadership, including the Administrator, on matters related to risk, safety, and mission success. Serves as the lead Technical Authority for safety and mission assurance, providing independent oversight of programs and projects in support of safety and mission success. Serves as the designated Agency-level "official voice" for institutional safety and the associated requirements established by NASA policy, law, and other external mandate aimed at protecting the public..”

## Slide 6: NASA Policy Enabling Missions
Increased flexibility for gate products and reviews
  Enables missions to streamline PP reporting into the standard project life cycle reviews.
Risk-informed decision-making leveraged per NPR 8000.4.
  Enables missions in that they can propose a performance or prescriptive approach.
Adds the ability to leverage NASA, other government agency, and industry consensus standards.
  Enables missions by increasing the potential implementation trade space through adopting or adapting consensus standards of their choice.
Current scientific consensus used throughout the project life cycle
  Enables missions to propose alternative and analytical approaches that are both responsive to PP requirements and fit within a projects allocated resources.

## Slide 7: Planetary Protection Categorization – Outbound + Inbound
Planetary Target Priority | Mission Type | Planetary Protection Category | Example Target Bodies
Not of direct interest for understanding the process of chemical evolution or where exploration will not be jeopardized by terrestrial contamination. | Any (Flyby, Orbiter, Lander) | I | Undifferentiated, metamorphosed asteroids, Io
Of significant interest relative to the process of chemical evolution but only a remote chance that contamination by spacecraft could compromise future investigations. | Any (Flyby, Orbiter, Lander) | II | Earth’s Moon (Cat. IIa & IIb), Venus, Comets, Asteroids, Jupiter; Jovian Satellites (excluding Io, Ganymede and Europa), Saturn; Saturnian Satellites (excluding Titan and Enceladus), Uranus, Uranian Satellites, Neptune, Neptunian Satellites (excluding Triton), Kuiper-Belt Objects <1/2 the size of Pluto
 |  | II* | Jovian Satellites: Ganymede, Saturnian Satellites: Titan, Neptunian Satellites: Triton, Pluto/Charon
Of significant interest relative to the process of chemical evolution and/or the origin of life and for which scientific opinion provides a significant chance that contamination by spacecraft could compromise future investigations | Flyby, Orbiter | III | Mars, Europa, Enceladus, Others to be determined
 | Lander, Probe | IV | Mars (Cat. IVa, IVb & IVc), Europa, Enceladus, Others to be determined
Any Solar System Mission | All Earth Return | V(r): Restricted Earth Return | Restricted Earth Return: Mars Europa Enceladus Others to be determined
 |  | V(u): Unrestricted Earth Return | Unrestricted Earth Return: Earth’s Moon Venus Most asteroids and comets (e.g., Bennu, Ryugu) Others to be determined

## Slide 8: Exploration Planetary Protection Comparison: Moon vs Mars
Moon
COSPAR Assessment: “of significant interest relative to the process of chemical evolution and the origin of life, but where there is only a remote chance that contamination carried by a spacecraft could compromise future investigations.”
Categorization (Outbound): II/IIa/IIb
Implication: Documentation
Categorization (Return): V(unrestricted)
Implication: No further constraints
Mars
COSPAR Assessment: “a target body of chemical evolution and/or origin of life interest and for which scientific opinion provides a significant chance of contamination which could compromise future investigations.”
Categorization (Outbound): III/IVa/IVb/IVc
Implication: Documentation Avoidance of Impact and/or Cleanliness Requirements
Categorization (Return): V(restricted)
Implication: Documentation Rigorous containment of unsterilized material to protect Earth’s biosphere Quarantine of crew
EASY
NOT SO EASY
Notes: Comparison of Moon and Mars from a planetary protection perspective

## Slide 9: Control of Forward Contamination
Mission Design & Categorization
Spacecraft Assembly, Test, Transport, Launch, and Operations
Avoiding Contamination following Inadvertent Impact
Avoiding Contamination for Robotic Landed Missions
End of Mission Disposition
Information to be included in the PP Mission Categorization Proposal
Biological and organic contamination knowledge inventory materials
Controlled manufacturing environments and cleanrooms
Bioburden Control Approach
Analytical Approach
Documentation requirements and communication of data/analysis updates
Avoiding inadvertent impact of solar system bodies by spacecraft and launch elements during flyby, gravity assist, or orbital insertion
  Mars (Cat III-IV)
Secondary and auxiliary payloads
Prevent occurrence of a biological inoculation event into a potentially habitable environment during landing and surface operations
  Stationary and mobile activities
Mars IVa, IVb, IVc requirements
Bioburden Control Approach
Analytical Approach
Documentation of final disposition of hardware
Updates to organic, biological, and combustion product inventories
Information to be included in End of Mission PP Report

## Slide 10: Mars Forward PP Implementation Trade Space
Orbiter - Spacecraft reliability and mission design to maintain orbiter inadvertent impact so bioburden considerations are not necessary.
Orbiter - Burnup and Breakup as a primary means to meet planetary protection compliance for bioburden managed spacecraft.
Orbiter / Lander – Evaluation of manufacturing provenance for bioburden credits from cleanroom manufacturing environments and non-metallic material cure and electronic break-in times and temps.
  Note: This is also can balanced with commercial off-the-shelf usage for lower risk class missions. Can you reduce PP implementation with MIL Spec parts?
Orbiter / Lander – Heat microbial reduction of strategic sub-systems to reduce bioburden below required limits. Typically, these are large surface areas such as cabling and thermal systems.
Orbiter / Lander – Bioburden management, microbial reduction, bioburden verification with wipe and swab sampling – required PP laboratory
$
$$$
*Note that some combination of the above techniques may be required.
Spacecraft Implementation

## Slide 11: Backward Contamination – Restricted Earth Return
NASA/USG has obligations under the Outer Space Treaty to safeguard the Earth-Moon system.
  Article IX: States Parties to the Treaty shall pursue studies of outer space, including the Moon and other celestial bodies, and conduct exploration of them so as to avoid their harmful contamination and also adverse changes in the environment of the Earth resulting from the introduction of extraterrestrial matter.
Preventing harmful biological contamination of Earth’s biosphere is the highest priority.
Implementation Example
NASA-Standard 8719.27 §5
Key Tenants
NASA Procedural Requirements 8715.24 §3.4
Establish and implement a strategy and design concepts to break the chain of contact with the target body, isolate, and robustly contain restricted samples.
Approach to assure public safety and containment requires approval by relevant government entities.
Alternative approaches allowed with scientific and engineering consensus.

## Slide 12: Notional Forward PP Mars Exploration Trade Space
IMPLEMENTATION
REQUIREMENTS
Easier
Challenging
Prescriptive
Performance Based
Robotic - Mars Orbiter
PP Category III – Orbital Lifetime
Mars Odyssey
Robotic - Mars Lander / Rover
PP Category IVa
Mars Science Laboratory – Curiosity
NASA/JPL-Caltech
Credit: NASA/JPL-Caltech/MSSS
Robotic - Mars Lander / Rover
PP Category IVc – Mars Special Region
Phoenix Lander
Robotic - Mars Lander
PP Category IVb – Life Detection
Viking Lander
Robotic - Mars Orbiter
PP Category III – Bioburden
MAVEN mission
Crewed + Robotic - Special Region Exploration
Crewed – Habitat / Close EVA Study
Crewed Special Region/Sampling for life detection/In-situ life detection
Crewed – Habitat / Far (kilometers?) EVA Study
Key
Robotic
Robotic + Crewed
Crewed
Knowledge Gaps
Credit: NASA/JPL-Caltech
Credit: NASA
Credit: NASA
Credit: ESA
Credit: NASA
Credit: CoSTAR / NASA / CalTech
Credit: NASA
Credit: NASA
Credit: NASA
Credit: NASA
Credit: NASA
Credit: NASA

## Slide 13: Knowledge-Based Robotic to Crewed Transition
Assumptions
Landed missions ≠ closed systems
Crew will be exposed to Mars
Crew is a constant source of bioburden unlike robotic spacecraft.
Priority = crew safety
Priority = safeguard the Earth from potential biologicals
Assumption
Microbial assessment + control of human associated contamination = key to preserve astrobiological exploration (PP enabling science)
Driving question
How do we define contamination vs. harmful contamination?
Guidelines
Maintain intent of PP to avoid harmful contamination
Mars Special Regions apply
Backward PP will require containment/quarantine
Baseline understanding of site
Knowledge gaps need to be established and mitigated
Notes: To frame the discussions, and constrain the problem, this “evolved” set of assumptions provided boundaries so that we didn’t devolve into speculative conversations about terraforming, and the like.

## Slide 14: Roadmap and Identification of Knowledge Gaps
NASA Workshop at Ames
1st COSPAR Meeting at LPI
2nd COSPAR Meeting at LPI
COSPAR Working Meeting on Contamination Transport on Mars at LPI, May 2018
COSPAR Working Meetings on Spacecraft Systems (virtual) May 2020 and June 2022
COSPAR Working Meeting on Microbial Monitoring & Health at LPI, May 2019
Identification of Planetary Protection Knowledge Gaps for human missions to Mars
Refinement and prioritization of Planetary Protection Knowledge Gaps for human missions to Mars
Mission Opportunity identification for addressing Planetary Protection Knowledge Gaps for human missions to Mars
Measurements and Payload/Operation Concepts for addressing Planetary Protection Knowledge Gaps for human missions to Mars
2015
2016
2018
2018 & beyond





…to establish the right quantitative and implementable planetary protection requirements for safe
and sustainable exploration and utilization of Mars.
What Knowledge Gaps…
…in what order…
…using what missions…
…to make what measurements…

Key knowledge gaps: microbial and human health monitoring, spacecraft technology and operations, and natural transport of contamination at Mars
  Spry, J. A., et al. (2024). Planetary Protection Knowledge Gap Closure Enabling Crewed Missions to Mars. Astrobiology, 24(3), 230–274.
Notes: Just to emphasize how Workshop content, via COSPAR, feeds into Agency policy and implementation

## Slide 15: Planetary Protection Crewed Moon to Mars Knowledge Gaps
Key technology development areas for planetary protection include:
1) microbial and human health monitoring,
2) technology and operations needed for contamination control, and
3) natural transport of contamination Mars.
Credit: ESA, DLR, FU BERLIN (CC BY-SA 3.0 IGO)
Credit: JPL-CALTECH/NASA, MALIN SPACE SCIENCE SYSTEMS
Credit: NASA/JPL-Caltech
Credit: NASA
Microbial manifestations on the ISS:
Credit: NASA
  Spry, J. A., et al. (2024). Planetary Protection Knowledge Gap Closure Enabling Crewed Missions to Mars. Astrobiology, 24(3), 230–274.

## Slide 16: Enabling and Evolving Crew PP Policy
Objectives-Driven
Risk Informed
Case Assured
Objectives are substantiated, monitored, and independently evaluated throughout the lifecycle based on systematic argumentation, explicit assumptions, and objective evidence.
Risks are understood, documented, and consistent with the established risk posture.
Consider the potential benefits and strategic importance of the mission(s) and consequences of failure,
Comprehensive and logical claims made with sufficient argument(s) & objective evidence​.
Does planetary protection permit crewed exploration of Mars?
  Yes, if …Mars is explored so as to avoid harmful contamination there, and also adverse changes in the environment of the Earth resulting from the introduction of extraterrestrial (Martian) material.
How can this be achieved?
  Policy and implementation still being evolved, but are likely to include:
    Requirements to manage cleanliness of operations on the surface, based on best available scientific data.
    Requirements to quarantine (containment of) returning crew and contain Martian samples, respectively, until shown to be safe.
    Development of an assurance based, risk-informed decision-process

## Slide 17: Resources Available Through The OPP Website
Videos
Articles
Planetary Protection: An Introduction
Forward and Backward PP Overview
Just How Small is a Spore?
Behind the Spacecraft Perseverance
Mission Design and PP Categorization
Ocean Worlds
Probability of Impact
End of Mission Disposition
How to Build a Clean Spacecraft
What Are Spores?
Cleanroom Gowning or How to Dress in the Cleanroom
Ground Support Equipment
Protecting the Planet: Planetary Protection vs. Planetary Defense
OSIRIS REx Sample Return Doesn’t Pose a Risk to Earth’s Biosphere
Missions & Studies
Mission Reports
NASEM Study Reports
Organic Inventory Workshop
PP Crewed Knowledge Gaps
Bioburden Accounting Tool Release
https://sma.nasa.gov/sma-disciplines/planetary-protection

## Slide 18: Questions?
Feel free to reach out as well!
J. Nick Benardini – NASA Planetary Protection Officer – James.N.Benardini@nasa.gov
Erin Lalime – NASA Deputy Planetary Protection Officer (Acting) - Erin.Lalime@nasa.gov
https://sma.nasa.gov/sma-disciplines/planetary-protection