## Slide 1: TEMPO vs. STAQS GCAS
Most recent results for NO2
Laura Judd, NASA LaRC
Presented at the GEO-XO Meeting 2024

## Slide 2
Above shows maps of the geographical regions/dates sampled in June-August 2023 during STAQS.
Purpose: To integrate TEMPO satellite observations with traditional air quality monitoring to improve understanding of air quality science for increased societal benefit
The NASA DC8 for NOAA AEROMMA and GCAS on the Gulfstreams flew together all flight days except 2.
All STAQS data are publicly available!
GCAS was integrated on both the JSC G-V (before 16 Aug) and LaRC G-III (after 22 Aug)
Cloud filtered using a count rate threshold in the NO2 fitting window
More info: Judd et al. (2019) and Judd et al. (2020) with exception of the GEOS-CF profile input
Resolution: 250 x 560 m
Retrieval window: 425-460 nm
A priori: MCD43A1 BRDF kernels over land and 3% Lambertian + sun glint kernel over water and GEOS-CF atmosphere
AMFs are retrieved via the GEO-CAPE tool thanks to SAO (a VLIDORT package)
Notes: Red dates are those that coincide with TEMPO data.

## Slide 3
GCAS Validation with Pandora
Right plots show the median GCAS value within 750m of the Pandora site during the overpass. Vertical bars are the 25th-75th percentile within that 750m radius. The Pandora value is the nearest in time where the horizontal bars represent the max/min within 15 minutes of the GCAS overpass.
Bottom plot shows the absolute difference between the measurements.
r2=0.87
Slope=0.88
Intercept=1.7e15
N=135
GCAS is 1.1e15±1.9e15 higher than Pandora
Median % difference: 47%-Interquartile: 2-103%
r2=0.90
Slope=1.00
Intercept=1e15
N=120
GCAS is 1.0e15±1.5e15 higher than Pandora
Median % difference: 12%-Interquartile: 0-25%
PhiladelphiaPA
BristolPA
NewBrunswickNJ
ManhattanNY
BronxNY
QueensNY
OldFieldNY
WestportCT
NewHavenCT
MadisonCT
ChicagoIL
SWDetroitMI
DearbornMI
Windsor-West
TorontoScarborough
Downsview
WrightwoodCA
WhittierCA
Still waiting for direct-sun results from the California and Chicago domains
GCAS has a nearly 1:1 relationship with the PGN Pandora observations (well within 25%).
Comparisons indicate a slight high bias of ~1E15
Notes: If the tropospheric columns are in total column magnitude (adding the stratosphere)
The Median % difference and interquartiles become 20% and 2-36% (so about the same range as before)

## Slide 4
Satellite Validation: TROPOMI with STAQS GCAS NO2
Notes: This slide shows application of methods developed for TROPOMI validation in Judd et al. 2020 (https://doi.org/10.5194/amt-13-6113-2020) to STAQS data in four different cities and with TROPOMI’s updated NO2 product (v2.5).
Maps show an example overpass of coincident data. GCAS, as you can see, is more spatially refined.
The scatter plot represents the spatially degraded GCAS data to the TROPOMI pixel footprint.
TROPOMI and GCAS correlate extremely well. The only major offsets occur over very polluted scenes in NYC (previously seen as well). Higher scatter in Chicago may be attributed to increased cloud coverage during those flight days, but more investigation may be needed.

## Slide 5: Example day: August 12th, 2023
Comparison criteria
TEMPO has a qa=0 and effective cloud fractions less than 0.3
GCAS is subset +/- 30 minutes from TEMPO observations and includes only cloud free data
# Scans=5
# Pixels=1033
r2=0.45
Y=1.7x-2.3e15
Median bias:
7% (0.2e14)
Interquartile:
-37%:30%
(-1.1e15-1.0e15)
Conditions:
Cloud bank in the morning delayed flight
Small cumulus impacts in afternoon
Grey: all coincidences—Color: labeled scan
“Unofficial TEMPO Data: Not for Public Release”

## Slide 6: Example day: August 26th, 2023
Comparison criteria
TEMPO has a qa=0 and effective cloud fractions less than 0.3
GCAS is subset +/- 30 minutes from TEMPO observations and includes only cloud free data
# Scans=7
# Pixels=2035
r2=0.72
Y=2.56x-0.7e15
Median bias:
117% (3.1e15)
Interquartile:
58%-217%
(1.1e15-7.1e15)
Conditions: Cloud free (some marine stratus VERY early in the morning offshore)/sea-breeze midday
Grey: all coincidences—Color: labeled scan
“Unofficial TEMPO Data: Not for Public Release”

## Slide 7
Los Angeles: August 22nd & 25-26th
NYC: August 5th & 9th
Toronto: August 4th
Chicago: August 2nd & 12th & 15th
# Scans=24
# Pixels=6499
r2=0.66
Y=2.1x-0.6e15
Median bias:
84% (2.6e15)
Interquartile:
29%:167%
(0.8e15-6.5e15)
# Scans=14
# Pixels=2787
r2=0.53
Y=1.6x-2.2e15
Median bias:
0% (0.002e15)
Interquartile:
-33%:35%
(-1.2e15:1.5e15)
# Scans=9
# Pixels=1283
r2=0.25
Y=1.0x-1.1e15
Median bias:
-38% (-1.1e15)
Interquartile:
-5%:-61%
(-0.1e15:-2.0e15)
# Scans=14
# Pixels=3581
r2=0.44
Y=1.4x-1.4e14
Median bias:
-1% (-0.3e15)
Interquartile:
-35%:32%
(-1.3e15:1.1e15)
R2 for slant columns
R2 for slant columns
Chicago: 0.53 (weird that this one is the same but I double checked)
Toronto: 0.56
NYC: 0.69
LA: 0.83
“Unofficial TEMPO Data: Not for Public Release”

## Slide 8: Looking ahead
Continued NO2 Validation and updates with V3 and other versions
Analysis by time of day
Deep dive into Los Angeles to look for causes of bias
Deep dive into other cities to investigate pixel-to-pixel variance:
  Cloud free scenes only? Cloud impacts in known cloud free scenes? Surface reflectance/type?
Other ideas?
  Contributions to validation documentation/manuscript writing
HCHO validation with GCAS
HSRL2 tropospheric/near-surface ozone?
Lessons learned under GEMS from ASIA-AQ?
Continued data collection with SCOAPE2 (June 2024) and HAMAQ (Mexico City and other location with TBD date)
Thailand sunrise from ASIA-AQ in March 2024
Add acknowledgements

## Slide 9: Backup slides

## Slide 10
Los Angeles
Aug 26th
NYC: Aug 9th
Toronto: Aug 4th
Chicago: Aug 2nd
August 2nd coincides with first light. This day was pretty impacted by cirrus clouds (above the flight altitude of GCAS)
Not imaged in this presentation is August 15th
(mostly one raster mid afternoon due to clouds)
Not imaged in this presentation is August 5th which has two rasters before getting cirrus impacted
“Unofficial TEMPO Data: Not for Public Release”
Not imaged in this presentation is August 22nd and 25th. Results are similar between days
August 4th is the only day in Toronto. The day was impacts by low level clouds.
Notes: Overview of the other regions/flights