## Slide 1: Surge Pressure Testing of Flight-Like Components
Wanyi Ng
NASA Goddard Space Flight Center
Propulsion Engineer
May 21, 2024
PREP II Final Presentation

## Slide 2: Outline
Background and Motivation
Test Setup
Methodology & Results
  Burst Disk Testing
  Pressure Transducer Testing
  Thruster Valve Testing
Conclusions
Notes: Move to beginning

## Slide 3: Outline
Background and Motivation
Test Setup
Methodology & Results
  Burst Disk Testing
  Pressure Transducer Testing
  Thruster Valve Testing
Conslusions
Notes: Move to beginning

## Slide 4: Background – What is Surge Pressure?
A transient, high pressure event
Occurs during priming of propellant lines
Usually the highest pressure event during the entire life of the mission
Difficult to model analytically in complex systems
Valve opens, flow starts
Scroggins and Fiebig (2014). “Surge Pressure Mitigation in the Global Precipitation Measurement Mission Core Propulsion System”. 50th AIAA/ASME/SAE/ASEE Joint Propulsion Conference
Bombadieri, Traudt, and Manfletti (2014). “Experimental and Numerical Analysis of Water Hammer During the Filling Process of Pipelines”
Liquid hits dead end, pressure spike
Propellant Upstream He/Vacuum Downstream
Notes: https://www.ecosimpro.com/wp-content/uploads/2015/02/SP2014_2968541_Bombardieri.pdf
“top, middle, bottom”

## Slide 5: Motivation
Pressures can damage propulsion components
System design includes flow control orifices to reduce surge pressures
Flow orifices drive system performance
  High pressure drop during flow
  Reduced thruster performance
  Increases required tank pressure and/or volume
Extensive testing to optimize orifice size
Typically size orifices to keep surge pressure below component proof pressure
Is this over-conservative and limiting system performance?
  Evidence that pressure spikes do not affect components in the same manner as static pressures do
Example flight mission surge test setup
Notes: Verbally indicate that last bullet is true

## Slide 6: Objective
  Improve understanding of transient surge pressure events
  and their effects on flight components
  Are existing test requirements over-conservative?
  Compare the component failure point under transient surge pressures versus static pressures by:
  Impart transient surge pressure on flight-like component
  Determine pressure at which the component fails
  Compare that pressure to the rated proof pressure of the component

## Slide 7: Outline
Background and Motivation
Test Setup
Methodology & Results
  Burst Disk Testing
  Pressure Transducer Testing
  Thruster Valve Testing
Conclusions
Summary
Notes: Move to beginning

## Slide 8: Simplified Diagram of Test Setup
Design a simple, repeatable test configuration for generating pressure surges
Control surge magnitude by changing water tank pressure and venturi throat diameter
Measure pressures during surge event
P2
P1
Venturi
Latch Valve
Kistler Pressure Sensor
High Pressure Water Tank
Initialize High Pressure Upstream
Initialize Vacuum Downstream
Open Latch Valve to Create Surge Event
P3
(Test Article)
Notes: Putting different components here

## Slide 9: Simplified Diagram of Test Setup
Design a simple, repeatable test configuration for generating pressure surges
Control surge magnitude by changing water tank pressure and venturi throat diameter
Measure pressures during surge event
P2
P1
Venturi
Latch Valve
Kistler Pressure Sensor
High Pressure Water Tank
Initialize High Pressure Upstream
Initialize Vacuum Downstream
Open Latch Valve to Create Surge Event
P3
(Test Article)
Notes: Putting different components here

## Slide 10: Simplified Workflow
Flow water through system to fully wet upstream section
Close latch valve
Purge water out of downstream section using low pressure nitrogen
Vacuum downstream section using vacuum pump
Set upstream pressure
Enable data collection
Open latch valve to generate surge event
Close latch valve
Save data
Repeat steps 3 through 9
P
P
Venturi
Latch Valve
Kistler Pressure Sensor
High Pressure Water Tank
Test Article

## Slide 11: Sample Raw Data
Close Up
Peak Surge Pressure

## Slide 12: Full Schematic of Test Setup
Additional Electronics Not Shown

## Slide 13: Photographs of Test Setup
Pressurized Nitrogen
Pressure Control System
Water Tank
(not shown)
Latch Valve
Test Article
Valve Actuation Equipment
Data Acquisition Equipment

## Slide 14: Setup Calibration
Determine initial conditions (upstream pressure and venturi size) to achieve any desired surge pressure
Notes: Knobs you can turn are pressure at water tank and venturi throat diameter
Tested two different venturi sizes (one at a time) at different water tank pressures, measured surge pressures
For any target surge pressure (e.g. 1500, can initialize venturi and upstream pressure to achieve it)

## Slide 15: Setup Calibration
Verify that the location of P2 was appropriate the measure the pressures at the test article
(Test Article)
Notes: Make sure P2 and P3 read the same value because eventually P3 is replaced by test article – plot shows within 20% difference across all initial pressures

## Slide 16: Simplified Diagram of Test Setup
Place different components on the downstream end and determine failure pressure
  Burst Disc
  Pressure Transducer
  Thruster Valve
Notes: Putting different components here

## Slide 17: Outline
Background and Motivation
Test Setup
Methodology & Results
  Burst Disc Testing
  Pressure Transducer Testing
  Thruster Valve Testing
Conclusions
Notes: Move to beginning

## Slide 18: Burst Disc
Burst disc
Disc holder with pressure tap
Disc and holder installed in-line
Burst disc simulates flight-like component with similar geometry to pressure transducer
Readily available at achievable rupture pressures
Manufactured to a tight tolerance actuation pressure – good for comparing transient and static pressure failure
Inexpensive to test to failure compared to flight components

## Slide 19: Burst Disc Setup
BD
Burst Disc in Holder
Holder Includes Pressure Tap
Venturi
Latch Valve
Kistler Pressure Sensor
High Pressure Water Tank
P2
P1
P3
Notes: Same setup diagram as before, but with test article replaced with burst disc

## Slide 20: Test Video – No Disc Failure
Notes: Will hear click for LV opening, immediately followed by thud as water flows and hits the dead end, LV closing

## Slide 21: Test Video – Disc Failure
Two different broken burst discs
Notes: Explain what ppl will see

## Slide 22: Burst Disc Results
Observed rupture pressure due to transient pressure spike was significantly above rated rupture pressure
Disc 4 not tested to failure to allow for 3D imaging
Notes: Each column represents data for a separate disc that was tested

## Slide 23: Deformation Before Burst
Credit: Justin Jones, Charles He, NASA GSFC
Digital microscope imaging shows dome deformation
May lead to strain hardening or thinning of disc material
After Surge Event
Before Surge Event

## Slide 24: Deformation Before Burst
Credit: Justin Jones, Charles He, NASA GSFC
3D scan shows dome deformation
May lead to strain hardening or thinning of disc material
After Surge Event
Before Surge Event

## Slide 25: Burst Disc Conclusions
Aluminum responds differently to transient pressure spikes than static pressures
The short duration of transient spikes can cause static deformation without full rupture
Transient failure pressure is higher than static failure pressure
Existing branch practices of treating transient and static pressures equally may be overly conservative
Notes: Block out 7

## Slide 26: Outline
Background and Motivation
Test Setup
Methodology & Results
  Burst Disk Testing
  Pressure Transducer Testing
  Thruster Valve Testing
Conclusions
Notes: Move to beginning

## Slide 27: Pressure Transducer
Pressure transducers tested because they are commonly placed in locations that see high surge pressures
Flight spare selected for testing

## Slide 28: Pressure Transducer Setup
P2
P1
PT
Pressure Transducer
Venturi
Latch Valve
Kistler Pressure Sensor
High Pressure Water Tank
Notes: Take a little longer on this slide

## Slide 29: Pressure Transducer Diagnostics
Performed before testing and after each surge event:
  Calibration
Performed before testing and after failure:
  CT Scan
Paper includes details about each diagnostic test

## Slide 30: Pressure Transducer Calibration
Use pressure controller to apply pressure to pressure transducer
Measure transducer’s voltage output
Verify no change to calibration after each surge event
GN2 bottle
Pressure Panel
Pressure Transducer
Power
Supply
Digital Multimeter
Pressure Controller

## Slide 31: Pressure Transducer Calibration Results
Specified proof pressure: 488 psia
Specified burst pressure: 813 psia
Calibration showed no change up to 784 psi surge
Failure after 1135 psi surge
Would still be useable after re-calibration
3 identical units on a flight mission were unintentionally exposed to static pressure of 788 psi and similarly went out of calibration
Notes: “Didn’t see out of cal after 784 psi, but did see it under static pressure of 788”

## Slide 32: CT Scan
Before Testing
After Failure
Diaphragm top surface
Diaphragm bottom surface
Credit: Bruno Munoz, NASA GSFC
Diaphragm top surface
Diaphragm bottom surface
No visible change in cross section and diaphragm surface views
Cross section view not shown (proprietary)
Notes: Mention that you can see differences, but that’s more due to image quality

## Slide 33: Pressure Transducer Conclusions
Pressure transducer was fully functional and accurate after surge pressures well above specified proof pressure
Existing branch practices of requiring surge pressure to stay below proof pressure may be overly conservative
For this pressure transducer design, overpressure still results in a useable unit after recalibration

## Slide 34: Outline
Background and Motivation
Test Setup
Methodology & Results
  Burst Disk Testing
  Pressure Transducer Testing
  Thruster Valve Testing
Conclusions
Notes: Move to beginning

## Slide 35: Thruster Valve
Thrusters tested because they are commonly placed in locations that see high surge pressures
Flight spare selected for testing

## Slide 36: Thruster Valve Setup
Thruster Valve
Venturi
Latch Valve
Kistler Pressure Sensor
High Pressure Water Tank
P2
P1

## Slide 37: Thruster Valve Diagnostics
Performed before testing and after each surge event:
  Internal Leak Test
  Pull-In / Drop-Out Voltage Test
  Response Time Test
  Flow Impedance Test
Performed before testing and after failure:
  Filter Inspection Using Borescope
Paper includes details about each diagnostic test

## Slide 38: Internal Leak Test Procedure
Pressurize upstream of closed thruster valve
Open downstream valve seat
Use Norquist leak detector to measure internal leak rate
Verify no change to leak rate after each surge event
Norquist leak detector
P
P
Thruster Valve
Norquist Leak Detector
Venturi
Latch Valve
Kistler Pressure Sensor
High Pressure Water Tank

## Slide 39: Pull-In / Drop-Out Voltage Test Procedure
Pressurize upstream of closed thruster valve
Apply low voltage through pulse box to thruster valve
Slowly increase the voltage to determine minimum voltage for valve opening
While water is flowing, reduce the voltage to determine threshold voltage for valve closing
Verify no change to threshold voltage after each surge event
P
P
Venturi
Latch Valve
Kistler Pressure Sensor
High Pressure Water Tank
Thruster Valve
Power
Supply
Pulse Box
Notes: Current and voltage traces

## Slide 40: Response Time Test Procedure
Apply voltage through pulse box to actuate thruster valve
Use oscilloscope to measure current and voltage over time
Calculate response time
Verify no change to response time after each surge event
P
P
Venturi
Latch Valve
Kistler Pressure Sensor
High Pressure Water Tank
Thruster Valve
Power
Supply
Pulse Box
Oscilloscope
Current & Voltage Signal
Current Trace
Voltage Trace
Valve Opening
Valve Closing
Oscilloscope Output
Notes: Current and voltage traces

## Slide 41: Flow Impedance Test Procedure
Flow water through open thruster valve
Measure flow rate and pressure drop across valve
Verify no change to flow rate and pressure drop after each surge event
P
P
TV
Thruster Valve
Differential Pressure Transducer
Venturi
Latch Valve
Kistler Pressure Sensor
High Pressure Water Tank
dPT
FM
Flow Meter
Metering Valve

## Slide 42: Thruster Valve Diagnostics Results
Specified proof pressure: 525 psi
Specified burst pressure: 875 psi
Specified water hammer pressure: 1200 psi
Vendor has proof pressure tested units up to 1510 psi
No damage to component up to 2200 psi
  Higher surge pressures not possible due to test setup limitations
* Verified no leakage using helium sniffer. Concluded that this measurement was due to thermal expansion. Specification is 1 scch at 350 psi
 | Internal Leakage | Response Time |  | Pull-In / Drop-Out Voltage |  | Flow Impedance | 
 | Leak rate, GN2 400 psi (scch) | Opening time (ms) | Closing time (ms) | Pull-In (V) | Drop-Out (V) | Flowrate at 0 psid (GPM) | Flowrate at ~10 psid (GPM)
Baseline | 0 | 10.32 | 2.72 | 12.4 | 2.378 | 0 | 0.102
After 1100 psi surge | 0.24* | 10.4 | 2.16 | 12.52 | 2.031 | 0 | 0.107
After 1500 psi surge | 0.24* | 10.24 | 2.92 | 12.55 | 2.177 | 0 | 0.106
After 2200 psi surge | -0.06 | 10.12 | 2.32 | 12.17 | 2.32 | 0 | 0.102
 | No Change | No Change | No Change | No Change | No Change | No Change | No Change

## Slide 43: Thruster Valve Filter Borescope Inspection
Borescope used to image filter showed no damage
Borescope image of inlet filter

## Slide 44: Presence of Thruster Valve Reduces Surge Pressure
Replacing dead end tube with thruster valve appears to reduce surge pressure, despite all other conditions remaining identical
  Systematically eliminated other possible causes
25% decrease in surge pressure
Possibly due to inlet filter acting as additional flow control

## Slide 45: Thruster Valve Conclusions
Thruster valve was likely undamaged after surge pressures well above specified and tested proof pressure
  Existing branch practices of requiring surge pressure to stay below proof pressure may be overly conservative
This thruster valve design inherently reduces surge pressure compared to a Kistler used in branch surge testing
  Existing assumption that surge testing reflects flight conditions may be overly conservative

## Slide 46: Outline
Background and Motivation
Test Setup
Methodology & Results
  Burst Disk Testing
  Pressure Transducer Testing
  Thruster Valve Testing
Conclusions
Notes: Move to beginning

## Slide 47: Conclusions
Tangential findings:
  A thruster valves reduces surge pressure – surge test setups used to size flight orifices do not have a thruster valve in line, therefore are over-conservative
  Short-duration pressure spikes can cause deformation different from static failure
Using specified proof pressure as the limit when designing flow orifices is over-conservative
  Burst Disc did not rupture under transient surge pressure until > 20% above its static rupture point
  Pressure transducer remained fully functional and accurate after surge pressures 60% above its specified proof pressure
  Thruster valve showed no indications of damage after surge pressures 4x its specified proof pressure, 45% above its highest vendor-tested proof pressure
Adding separate vendor specification for surge pressures is warranted and would improve system performance
  Improves system performance by allowing higher surge pressures
  Verification test would add cost

## Slide 48: Acknowledgements
Thank you to:
Mentors (NASA GSFC)
  Alison Rao
  Eric Cardiff
Testing (NASA GSFC)
  Hal Baesch
  Justin Brumley
  Sean Fitzsimmons
  Jacob Stahl
Test Article Imaging (NASA GSFC)
  Bruno Munoz
  Charles He
  Justin Jones
Paper Review
  David Benson (NASA GSFC)
  Zac Regan (Continental Disc)
Continental Disc Corporation provided burst discs and custom holder at no cost and provided input on testing

## Slide 49: Thank You