## Slide 1
Tropospheric Emissions:
Monitoring of Pollution
A New Era of Air Quality Monitoring from Space over North America with TEMPO: Commissioning and Early Nominal Operation Results
Xiong Liu1, Kelly Chance1, Raid Suleiman1, John Houck1, John Davis1,
Kevin Daugherty2, David Flittner2, David Rosenbaum2, Crystal Fenn2,
Gonzalo Gonzalez Abad1, Caroline Nowlan1 , Huiqun Wang1, Heesung Chong1, Weizhen Hou1, Junsung Park1, Christopher Chan Miller1, Juseon Bak1, Jim Carr, James Szykman, Mike Newchurch, Aaron Naeger,Ronald Cohen,Zolal Ayazpour1,
Christopher Brown2, Zachary Fasnacht, Marcellin Feasson1, Jean Fitzmaurice1, Jeffrey Geddes, David Haffner, Jay Herman, Joanna Joiner, Laura Judd,
Emma Knowland, Xuming Lei, Nischal Mishra2, Robert Neece2, Ewan O'Sullivan1,
Brad Pierce, Wenhan Qin, Eric Roback2, Justin Strickland2, Robert Spurr,
Luke Valin, Alexander Vasilkov, Eun-Su Yang, Barron Henderson,
Katherine Travis, Prajjwal Rawat, and the TEMPO Team
1CfA | Harvard & Smithsonian
Int’l. Space Science Institute (ISSI) Workshop on
Geostationary Satellites & Atmospheric Chemistry
May 27, 2024

## Slide 2: TEMPO Commissioning and Early Nominal Operation
Launch
TEMPO
Power On
First Light
TEMPO Commissioning
S/C Activity (TEMPO Off)
Activation
Outgassing
Instrument Characterization and Analysis
PLAR
Nominal Operations
L+61 days (6/7/23)
L+115 days (7/31-8/2/23)
L+194 days
(10/19/23)
L+0 (4/7/23)
TEMPO commissioning: SAO + LaRC + Intelsat + Maxar + Ball + Carr Astronautics
  TEMPO power on 6/7, Dry out (6/9-7/9) and cool down (7/10-7/12)
  First light (7/31-8/2): working/reference diffuser solar & Earth imaging
  Instrument Characterization and Analysis (ICA) activities
  Coordinate with AGES+ campaigns in Aug. and Coastal Texas Air Quality Field Campaign in Sep. (no Earth imaging for only 6 days, special observations over LA and Texas)
Nominal operation: after the Post Launch Acceptance Review (PLAR) on 10/18-19/2023
  Weekly commanding, no special observations before L2/3 public release
  Optimize off-nominal twilight observations: city lights=>lighting types, Aurora, gas flaring, moonlight
  Overall very smooth operation except for some data dropouts
Successful TEMPO commissioning and early nominal operation!

## Slide 3: Baseline Line Mission & Data Products Public Release Timeline
Data Product | Description | Time beyond On-Orbit Checkout (OOC) to deliver initial data | Maximum data latency after first release for ≥ 80% of products
Level 0 | Reconstructed, Unprocessed Instrument Data | 2 months | Within 2 hours of receipt at SAO
Level 1b | Calibrated, Geolocated Radiances | 4 months | Within 3 hours of Level 0 and ancillary data receipt at SAO
Level 2 | Derived Geophysical Data Products | 6 months | Within 24 hours of production of Level 1 at SAO
Level 3 | Derived Gridded Geophysical Data Products | 6 months | 1 month after completion of data accumulation required for individual geophysical products
Baseline mission (Phase E, 20 months, 10/2023-6/2025), will be continued with NASA extension / senior review
Data products sent to ASDC for archival & distribution before nominal operation
Early access to TEMPO Science and Validation team members. Bi-weekly L2 Cal/Val meeting led by Jim Szykman & Brad Pierce
Mini release (Dec. 17-30, 8 days during Aug. commissioning) on Feb. 05, 2024
Beta Level 1 public release: Feb. 27,2024
Level 2/3 public release: May 20, 2024
We are nearly on track to release the data products to the public!

## Slide 4: TEMPO Instrument & First Light (8/1-2/2023)
Imaging spectrometer measuring solar irradiance and solar backscattered Earth radiance
First Light Earth 8/2/2023 @11:13-17:16 ET
RGB Images
First Light Solar
8/1/2023 @12:18 am ET
~293-494 nm
~538-741 nm
TEMPO First light and NRT checking showed that TEMPO is working very well!
[Credit: Heesung Chong]
[Credit: John Davis]

## Slide 5: Baseline and Threshold Measurements Requirements
* # of hourly measurements to be averaged to achieve required precision
Mission duration: 20 months for baseline, 12 months for threshold
Spatial resolution: < 60 km2 for baseline (4 native pixels coadded), < 300 km2 for threshold
AOD, SO2, and CHOCHO removed at KDP-C.
Species/Products | Required Precision | Temporal Revisit*
0-2 km O3 (Selected Scenes) Baseline only | 10 ppbv | 2 hour
Tropospheric O3 | 10 ppbv | 1 hour
Total O3 | 3% | 1 hour
Tropospheric NO2 | 1.0 × 1015 molecules cm-2 | 1 hour
Tropospheric H2CO | 1.0 × 1016 molecules cm-2 | 3 hour
Reduced list of baseline data products due to cost cap!

## Slide 6: TEMPO Data Products Baseline + SNWG TEMPO NRT
Level | Product | Algorithm | Major Outputs | A Priori (L2) | Res km2 * | Freq/Size | Val. Status (5/20/2024)
L0 | Digital counts | Raw to L0 | Reconstructed/reformatted DN |  | 2.0 x 4.75 | Daily/hourly | 
L1 | Irradiance NRT | SAO L0-1 | Calibrated & quality flags |  |  | weekly | Beta
 | Radiance NRT | SAO L0-1 | Geolocated, calibrated, viewing, geolocation & quality flags |  | 2.0 x 4.75 | Hourly, granule | Beta
 | City lights | SAO L0-1 | Geolocated & calibrated |  | 2.0 x 4.75 | Variable, granule | Beta
L2 | Cloud NRT | OMI O2-O2 | Cloud fraction, cloud pressure | GEOS-CF | 2.0 x 4.75 | Hourly, granule | Beta
 | O3 profile | SAO O3 profile | O3 profile, total/strat/trop/0-2 km O3 column, errors, a priori, AKs | Climatology+GEOS-CF | >= 8.0 x 4.75** | Hourly, granule | Unvalidated
 | Total O3 | TOMS V8.5 | Total O3, AI, cloud fraction | Climatology | 2.0 x 4.75 | Hourly, granule | Beta
 | NO2 NRT | SAO trace gas, BU strat./trop. sep. | SCD, strat./trop. VCD, error, shape factor, scattering weights | GEOS-CF | 2.0 x 4.75 | Hourly, granule | Beta
 | HCHO NRT | SAO trace gas | SCD, VCD, error, shape factor, scattering weights | GEOS-CF | 2.0 x 4.75 | Hourly, granule | Beta
L3 | Gridded L2 | SAO L2-3 | Same as L2 |  | 2 x 2 | Hourly, scan | 
* Spatial resolution at center of FOR. ** Might be at 8 x 9.5 km2
Research aerosols, SO2, ocean color products
Satellite Needs Working Group (SNWG) funded TEMPO NRT products (L2 products < 3 hours from observation time): 3/26/2024-3/25/2026, NOAA GeoXO team to produce TEMPO/GOES-R NRT aerosol products

## Slide 7: Algorithm/Data Products Development Timeline
First Light NO2 Images Release (8/24): updates to pre-launch (SDPC v4.0) (offline/development):
  Use initial wavelength grid for radiance from calibrated first light working solar irradiance
  No straylight correction and polarization correction
  Optimized Image Navigation and Registration (INR) for first light
  Optimization to clouds & NO2 algorithms
First official SDPC update: SDPC v4.1 (V1 data products) approved on 10/16, operational on 10/17, L0-1b, cloud, NO2, HCHO, total O3 produced and sent to ASDC
  INR: working well meeting science requirements.
  L0-1b: gain/non-linearity, bad pixel map, improved saturation flagging, Octant phase (odd/even)
  Further optimization in cloud and NO2
  Major changes to HCHO: radiance reference, and background/reference correction
  O3 profile not ready due to absolute radiometric calibration
SDPC v4.2 (V1): approved on 11/17, operational on 11/18
  INR: remove UV/Visible biases, accurate at subpixel level, tested to work for special observation
  Data processing pipeline: more robust, automatically recover from INR crash, other minor updates
  Used to reprocess TEMPO commissioning observations

## Slide 8
SDPC v4.3 (V2) & Level 1 release: approved on 2/23/2024, operational 2/26/2024
  Level 1 Beta Public Release:
    Scattering angle dependent BTDF correction, removing time- and across-track dependent biases
    Improved CCD image processing steps (electronic offset correction, smear correction, dark current correction after accounting for temperature dependence)
    Improved solar wavelength calibration, use latest solar irradiance wavelength for radiance
Algorithm/Data Products Development Timeline
  Critical updates to NO2, HCHO, and cloud algorithms: GLER interpolation issues, snow/ice, missing data due to cloud radiance wavelength calibration failure, NO2 tropopause layer selection bug, temperature correction in total NO2 AMF
  Change L3 resolution from to
[Credit: David E. Flittner]

## Slide 9
SDPC v4.4 (V3) & Level 2-3 release: May 20, 2024
  Improved Level 1 & new Level 1 city lights
    Add nominal geolocations for city lights & Improve the robustness for INR
    Improve FPA temperature sampling and temperature-dependent dark current correction
    Add straylight correction (1-D PSF)
    Add radiance wavelength calibration
  Improved Level 2 & 3 and likely ozone profile (UV only) product for public release
    Update GLER (v6.0->v6.1, snow free + 100% snow, quality flag 2-> 5, fill in gaps via interpolation)
    Perform retrievals up to SZA 90
    Update main data quality flag (AMF > 6 as suspect), Revisit convergence flag & AMF diagnostic flag
    Add temperature profile to output (for AMF)
    Cloud: SCD fitting optimization, SCD T correction, ECF/OCP iteration, wavelength shifts to ECF
    Ozone profile: Update the use of GEOS-CF meteorology and ozone profile + Derive soft calibration
After the May 2024 L2/3 public release --- end of baseline mission:
  Reprocessing for all data products (except for ozone profile product)
  Updates to science algorithms & calibrations as needed based on validations and feedback
  Update O3 profile retrieval with UV only
  Release UV/Visible to improve retrieval sensitivity to 0-2 km O3
Algorithm/Data Products Development Timeline
Power/cooling issues at our data center

## Slide 10: TROPOMI and TEMPO NO2
[Credit: Caroline Nowlan]

## Slide 11: TROPOMI NO2 Comparisons
11
PRELIMINARY!!
Courtesy of Barron Henderson, EPA
Overall, TEMPO tropospheric NO2 agrees well with TROPOMI
Biases between products can be due to differences in AMF inputs
Larger negative TEMPO bias in western U.S.?

## Slide 12: Pandora NO2 Comparisons
November 23-Jan 20
Courtesy of Prajjwal Rawat (NASA LaRC), Katherine Travis (NASA LaRC), James Szykman (EPA)
PRELIMINARY!!

## Slide 13: TEMPO and TROPOM HCHO (29-30 August 2023)
Google Engine S5P HCHO 0829
Google Engine S5P HCHO 0830
TEMPO HCHO 0829-0830 (scans close to S5P overpass)
TEMPO vs TROPOMI shows spatial agreement in HCHO columns. TEMPO shows small noise and almost no striping. Systematic biases are expected associated with AMF, radiance reference and background corrections.
[Credit: Gonzalo Gonzalez Abad]

## Slide 14: Pandora HCHO Comparisons
November 23-Jan 20
Courtesy of Prajjwal Rawat (NASA LaRC), Katherine Travis (NASA LaRC), James Szykman (EPA)
HCHO hotspots are captured well by both the measurements, irrespective of Pandora locations.
A moderate spatial correlation is observed between Pandora direct Sun HCHO and TEMPO HCHO column with larger dynamical range in the Pandora observations.
PRELIMINARY!!

## Slide 15: NO2 Tropospheric Column & HCHO Column Uncertainties
TEMPO NO2 & HCHO meets requirement for >90% of cloud-free scenes with no pixel coadding!
NO2 Median uncertainty = 0.46 × 1015 molecules/cm2 (SZA < 70°, all clouds)
Requirement
Coadd 4 pixels
Aug. 29-Sep. 1
SZA < 70°
All cloud fractions
All scans
Single pixel performance
Requirement
Coadd 12 pixels
Aug. 29-30
SZA < 70°
All cloud fractions
All scans
Single pixel performance
HCHO Median uncertainty = 5.5 x 1015 molecules/cm2 (SZA < 70˚, all clouds)

## Slide 16
Cloud fraction
Cloud pressure
Cloud Products (29 September 2023)
Saturation causes no retrieval under very cloudy conditions.
[Credit: Huiqun Wang]

## Slide 17: TEMPO O3PROF (3/28/2024 Scan 008)
Tropospheric O3 from TEMPO O3PROF
Tropospheric O3 from GEOS-CF
Tropospheric O3 from TROPOMI
Tropospheric O3 from EPIC
Dobson Unit
PRELIMINARY!
Note different tropopause pressure from EPIC/TROPOMI!
Earlier version
from 2 weeks ago!
[Credit: Junsung Park]
[Credit: Jerry Ziemke]

## Slide 18: TEMPO O3PROF (3/28/2024 Scan 008)
PRELIMINARY!
Surface to 2 km O3 from TEMPO O3PROF
Surface to 2 km O3 from GEOS-CF
Dobson Unit
[Credit: Junsung Park]

## Slide 19
TEMPO Total Ozone (V2):
Comparison with OMPS and OMI
Credit: Jerry Ziemke & Stacey Frith, NASA GSFC
OMPS and OMI within ±3 hr overpass with TEMPO with all data binned to 1o × 1o daily averages
20240328, S008
V2
V3
V3 – V2
CF < 0.3

## Slide 20
City Lights & Aurora
[Credit: Jim Carr]
Radiance derivation  Post-processing (de-speckling, de-streaking, etc.)  Composite
Clearest-Sky Composite 1–12 February 2024
Oxygen at 558 nm

## Slide 21
City Lights Spectral Classification
[Credit: Jim Carr]
Miami, Fl
Offshore Flaring
~1200 K Blackbody

## Slide 22: Summary
TEMPO commissioning and nominal operation have gone on very well
TEMPO is providing revolutionary hourly daytime atmospheric pollution measurements at high spatial resolution over North America
Most data products (L1b, cloud, NO2, HCHO, total O3) are in good quality at this early stage, showing that the TEMPO instrument and science algorithms are working very well.
We are on track to release the L2/3 data products to the public (likely including the UV only ozone profile product)
On track to release TEMPO data products that are acceptable to enable meeting baseline science requirements!
Thank you!
Acknowledgements: Funding from
NASA (Contract No. NNL13AA09C )

## Slide 25: Field of Regard
First light 8/2 field of Regard: 62.7 mins
(100 ms integration time, 26 coadds, 61.5 µrad)
Fields of regard characterization (FOR mapping) with different N-S SMA angles
Requirement
Performance
Optimized field of Regard in late Sep.: 59.75 mins
(100 ms integration time, 26 coadds, 64 µrad)
[Credit: Heesung Chong]

## Slide 26
First Light H2O SCD (2 August 2023)

## Slide 27
TEMPO AOD vs ABI AOD in the VA fire region
Credits: NOAA GeoXO Team, Pubu, Hai, Zigang and Shobha

## Slide 28: Introduction to TEMPO
NASA’s first Earth Venture Instrument (EVI) selected in 2012
PI: Kelly Chance, Smithsonian Astrophysical Observatory (SAO): Science team, ground systems, science data processing center
Instrument Project Management: NASA LaRC  SAO (Phase E)
Instrument Development: Ball Aerospace
Other Institutions: NASA GSFC, NOAA, EPA, NCAR, Harvard, UC Berkeley, St. Louis U, UAH, U Iowa, Sitting Bull College, RT Solutions, Carr Astronautics
International collaboration: Mexico, Canada, Cuba, Korea, U.K., ESA, Spain
NASA’s first host payload
  Mission Project Management: NASA LaRC
  Host Satellite Provider: Maxar Technologies
  Satellite Host: Intelsat (IS-40e)
  Launch: SpaceX
TEMPO: It’s about Time!

## Slide 29: TEMPO Operation
Nominal: Scan Field of Regard (FOR) in 1 hour
  ~ 2K N/S pixels ~1200 steps/hr
  2 4.75 km2 @center of FOR
Optimized scan: in the early morning and late afternoon, daylight portion, higher temporal resolution (~40 mins)
Special Observations (up to 25%):
  High-time scan: selected portion at higher temporal res. (e.g., <= 10 mins)
  Oversample to effectively increase spatial resolution
  Change FOR
  No Special observations before April release
Field of regard is optimized to cover both Puerto Rico and Canadian tar sands.
S5p-TROPOMI NO2 product oversampled by Kang Sun.
  Operate on geostationary communications satellite Intelsat 40e (IS-40e) at 91 ∘ W
https://weather.ndc.nasa.gov/tempo/green_paper.html
Request special observation

## Slide 30: TEMPO Software/Algorithm Teams
Operational Algorithm | Personnel
Instrument Operation Center (IOC) including Raw-L0 | John Davis
L0-1b | Heesung Chong, John Houck, Weizhen Hou, Xiong Liu, Dave Flittner, Jim Carr
Ozone profile | Junsung Park, Xiong Liu
Total ozone | GSFC / Junsung Park + Xiong Liu
Nitrogen dioxide | Caroline Nowlan, Gonzalo González Abad
Formaldehyde | Gonzalo González Abad, Caroline Nowlan
Clouds | Huiqun (Helen) Wang, Eun-Su Yang, Alexander Vasilkov, Joanna Joiner
Science Data Processing Center Operational Implementation & Processing Pipeline | John Houck

## Slide 31: Science Algorithms
Launch-ready Science Data Processing Center (SDPC) V4 software completed in Mar 2023
Algorithm mostly based on OMI heritage algorithms except for new L0-1b processor including Imaging Navigation and Registration (INR) using GOES-R by Carr Astronautics
SAO trace gas algorithm (HCHO, NO2): spectral fitting to derive Slant Column Densities (SCDs), calculate air mass factor (AMFs) and derive Vertical Column Densities (VCDs)
  NO2 requires stratospheric/tropospheric separation based on spatial filtering method (Geddes et al., 2018)
Cloud algorithm: SAO O2-O2 fitting + NASA GSFC’s O2-O2 cloud at ~477/466 nm
Total ozone algorithm: heritage TOMS V8.5, using ozone absorbing and non ozone absorbing pairs to derive total ozone column
Ozone profile algorithm: heritage SAO OMI O3 profile, using 290-340, 540-650 nm, retrieve O3 profile at 24 layers, including total, stratospheric, tropospheric, and 0-2 km O3
Main L1-2 algorithms updates include:
  NASA GMAO’s GEOS-CF trace gas profiles and meteorology
  Hourly resolved monthly mean Geometry-dependent Lambertian Equivalent Reflectivity (GLER) climatology

## Slide 32: First Light NO2 (2 August 2023)
Credit: NASA Scientific Visualization Studio
Notes: Caroline
- First mention these are from first-light. Got a lot of media attention.
I will talk about first light and describe the sources of NO2 as I go along on this slide: transportation, fires, lightning, soils
Mention how we can’t measure below clouds
Will point out these data are novel because we can measure every hour

## Slide 33: Including Visible to Improve Tropospheric Ozone Retrieval Sensitivity
This example is for solar zenith angle =25, viewing zenith angle 45, relative azimuthal angle 86, Signal to noise Ratio (SNR) with 4 pixels coadded
Add visible to improve retrieval sensitivity in the lower troposphere and help separate free tropospheric O3 from boundary layer O3
Under ideal conditions: 3-5 total Degree of Freedom for Signal (DFS) with up to ~1.5 in the troposphere, and up to ~0.5 DFS in 0-2 km
Adapted from OMI (Liu et al., 2010): Spectral fitting + VLIDORT + Optimal Estimation (OE) from Fitting windows: 293-345 nm, 540-650 nm
Retrieve partial O3 columns at ~24 layers (bottom layer is 0-2 km above the surface) as well as total, stratospheric, and tropospheric O3 columns, other trace gases, and auxiliary parameters.
A priori: a combination of tropopause-based climatology (Bak et al., 2013) with diurnally-resolved GEOS-CF data

## Slide 34
TEMPO Observation of Solar Eclipse
[Credit: Heesung Chong]