## Slide 1
Polar Resources Ice Mining Experiment-1
Project Manager: Dr. Jackie Quinn (NASA)
Principal Scientist: Dr. Janine Captain (NASA)
Lead Integration Engineer: Dr. Julie Kleinhenz (NASA)
Co-Scientists: Dr. Roberto Aguilar-Ayala (NASA), Dr. Kris Zacny (Honeybee Robotics)
Full Authorship: J.W. Quinn1, J.E. Captain1, A.S. Eichenbaum1, R. Augilar-Ayala1, J.E. Kleinhenz1, K.A. Zacny2, P.C. Chu2 , and V.R.Vendiola2, 1NASA (Mailstop UB-E, KSC, FL 32899 Jacqueline.W.Quinn@nasa.gov), 2Honeybee Robotics (2408 Lincoln Ave Altadena, CA 91001 kazacny@honeybeerobotics.com).

## Slide 2
  https://twitter.com/NASAMoon/status/1471889928762109953
Ice Mining on the Moon with PRIME-1

## Slide 3
Requirements
The Level-1 (L1) requirements below are designed to ensure meeting the PRIME-1 Mission-level Objectives. These requirements were further decomposed to develop the full set of requirements for MSolo and TRIDENT, which were included in their respective Preliminary Design Review submissions.
L1 Requirement 1: PRIME-1 shall operate on the surface at a lunar polar region.
L1 Requirement 2: PRIME-1 shall expose a subsurface regolith sample from up to a 1-meter depth drill hole.
L1 Requirement 3: PRIME-1 shall analyze the exposed subsurface regolith sample to detect water and other volatiles.
PRIME-1 Key Performance Parameters |  |  |  | 
Performance Parameter | Units | State of the Art | Threshold Value | Project Goal
KPP 1: Regolith sample-depth resolution | Number of linear depths along single drill hole1 | N/A2 | 3 | 5
KPP 2: Volatile species identification | Number of volatiles (#) | 1 (Hydrogen only) | 2 (Hydrogen and water) | >2 (light-weight volatiles under 70 amu)
KPP 3: Water detection accuracy for regolith3 | Percentage by mass water grade in regolith (%) | N/A2 | 24 | 14
Notes: Threshold linearly along a depth up to 0.6-m total. Project Goal linearly along a depth up to 1-m total. No drill samples for State of the Art. Orbital spatial scale is 10s of km at a depth of up to 1 meter, but only for hydrogen. Assumes 2.0-5.0% water by mass in the regolith which encapsulates ISRU’s definition of a critical cutoff concentration of water for harvesting purposes. Measurement accuracy of ± 50% |  |  |  | 

## Slide 5
TRL6 Drill Prototype
Auger and Percussion Drill Head
Drill String
Drill Linear Stage
Drill Deployment Stage
Brush Housing and Sample Delivery Chute
TRIDENT – Commercial Drill
TRIDENT (The Regolith and Ice Drill for Exploring New Terrains) subsystem includes the hardware to physically excavate/extract regolith from the lunar surface up to a depth of 1 meter.
Excavation device will be instrumented to measure forces/displacements in order to determine critical bulk properties of the regolith. This information will be used to understand the working environment and bound critical excavation parameters for future larger scale regolith mining equipment and processes.
TRIDENT captures regolith in 8-10 cm increments down to a depth of 1 meter. Material captured by the drill is transported to the surface to be analyzed by MSolo. TRIDENT measures strength of the lunar regolith as well as subsurface temperatures during drilling operations.

## Slide 6: TRIDENT Science Data
Cuttings cone (*):
Angle of Repose
Density at Dr of ~0%
Footpad sinkage provides (#):
Bearing capacity
Bit Temperature Sensor (#):
Subsurface Temp vs Depth
Heater (#):
Thermal Conductivity (with Temp. Sensor)
Drilling Power (#):
Material Strength vs. Depth
Loose ice grains vs ice cemented regolith
Parameter | Value
Bit Diam. (mm) | 25.4
Nominal Auger Spin (RPM) | 120
Auger Average Output Torque (N-m) | 5.5
Auger Average Power Consumption (W) | 87
Percussion Impact Energy (Joules/Blow) | 2
Nominal Percussion Rate (BPM)* | 972
Feed Stage Stroke (mm) | 1240
Maximum Drill Depth (mm) | 1020
Deployment Stage Stroke (mm) | 380
Z Stage Force Cont. (N) | 500
CBE Drill and Launch Locks Mass (kg) | ~22
CBE Avionics + Harness Mass (kg) | ~7
Engineering Specifications
TRIDENT

## Slide 7: MSolo is a modified-for-spaceflight commercial-off-the-shelf (COTS) Mass Spectrometer
Open Ion Source
Cross Beam
Ion Source
Modified Commercial Off The Shelf Mass Spectrometer
INFICON Quadrupole Residual Gas Analyzer
Open or Cross Beam Ion Source (COTS)
Electron impact ionization - Dual Y2O3/Ir filaments (COTS)
Faraday Cup and Electron Multiplier Detectors (COTS)
Calibration Gas System (KSC)
Chassis designed to build on instrument avionics and include spaceflight control computer (SHREC) and power board
MSolo
Mass Spectrometer observing lunar operations
Ruggedization for Spaceflight
Calibration Gas System
Thermal upgrades
Structural upgrades
Onboard computer designed
Avionics board redesign
New chassis to support COTS MS Boards, new power boards and onboard computer
Software designed to be compatible with RS422 and COTS firmware/operation

## Slide 8: PRIME-1 Regolith Cuttings Pile
The cuttings pile size increases with each bite, evenly falling into a cone shape on the surface
The lander partner provides regular camera imagery of the cuttings pile while operating. Images will be provided every minute during active operations, every 5min during analysis hold periods.
Lower Power
Stratigraphy is preserved in 8-10 cm “Bites”
Accurate material strength determination
More accurate downhole temperature
Reduced risk of freezing-in
Advantages of Bite Sampling

## Slide 9: MSolo Analysis Time
PRIME-1 will be able to implement a long MSolo analysis time, looking at the water signal decay which is used to:
  Understand the volatile diffusion and desorption from regolith which informs ISRU – i.e. desorption during excavation
  Apply the diffusion model developed using Earth-based TVAC conditions for quantification of PRIME-1 observed lunar water
Used to support the VIPER mission, whose timeline does not allow for a full signal decay
  The peak intensity will be used to interpret the water estimates using the model developed with PRIME-1 and ground test
Water Quantification Estimate:
TVAC tests correlate peak water signal with water flux.
Water flux is dependent on conical surface area of each bite.
MSolo Data from TVAC tests showing water signal decay (blue).

## Slide 10
Shackleton’s Connecting Ridge
Late 2024
Intuitive Machines Nova-C Lander
Falcon 9
PRIME-1 payload operations approximately 72 hours in duration
Video credit Angel Stickle/APL
Instantaneous lighting merge mosaic created by Jeff Leeburn/APL