## Slide 1
Towards Ultra-Narrowband and Wavelength-Agile Burst-Mode Molecular Filtered Rayleigh Scattering
Laser Applications to Chemical, Environmental, and Security Analysis 2024
The Meyer Research Group
| 1
Amanda M. Braun, Mikhail N. Slipchenko, Terrence R. Meyer
Purdue University
Paul M. Danehy, Neil S. Rodrigues
NASA Langley Research Center
Jason Leicht, Sukesh Roy
Spectral Energies, LLC

## Slide 2: Acknowledgements
NASA Space Technology Graduate Research Opportunity (NSTGRO20)
LaRC: William Holt Ripley, Dr. Ross Burns, Olivia Tyrell, Dr. Timothy Fahringer, Dr. Jian Gao, Steve Jones, Scott Bartram, Zachary Hunt
Dr. Jerome Braun
Dr. James Braun (no relation) and Alex Suppiah

## Slide 3: Why do we need optical diagnostics?
- Laser electronic excitation tagging (FLEET, PLEET)
- Schlieren/shadowgraphy
- Fluorescence-based (PLIF)
- Laser scattering (CARS, Raman, Rayleigh, DGV, PIV)
Surface Pressure
Surface Temperature
Mach Number
Hyper-X[2]
HIFiRE Flight 2 Vehicle [1]
Mach Number

## Slide 4: Why do we need optical diagnostics?
- Laser electronic excitation tagging (FLEET, PLEET)
- Schlieren/shadowgraphy
- Fluorescence-based (PLIF)
- Laser scattering (CARS, Raman, Rayleigh, DGV, PIV)
Surface Pressure
Surface Temperature
Mach Number
Hyper-X[2]
HIFiRE Flight 2 Vehicle [1]
Mach Number

## Slide 5: Why use Rayleigh scattering?
Particle Image Velocimetry
Technique
Velocity
Temperature
Pressure
Density
Doppler Global Velocimetry
Raman Scattering
Rayleigh Scattering
Unseeded
* Background interferences, weak signal levels, and difficulty making multi-parameter measurements
Notes: Unseeded technique

## Slide 6: What is Rayleigh scattering?
Incident Laser
Scattering Vector
Wave Vector
Laser Vector
Velocity Vector
Doppler Shift
Rayleigh Scattering
Flow Molecules
Notes: Explanation

## Slide 7: What is Rayleigh scattering?
Incident Laser
Flow Molecules
Scattering Vector
Wave Vector
Laser Vector
Velocity Vector
Doppler Shift
Rayleigh Scattering
Notes: Explanation

## Slide 8: Why use filtered Rayleigh scattering?
Incident Laser
Flow Molecules
Rayleigh Scattering
Rayleigh Scattering
Mie/Stray Scattering
Notes: Explanation

## Slide 9: Why use filtered Rayleigh scattering?
Rayleigh Scattering
Rayleigh Scattering
Mie/Stray Scattering
Filter
Gaseous Iodine
Flow Molecules
532 nm
Molecular
Filter
Notes: Explanation

## Slide 10: Why use filtered Rayleigh scattering?
532 nm
Rayleigh Scattering
Rayleigh Scattering
Mie/Stray Scattering
Filter
Molecular
Filter
Flow Molecules
High speed
High intensity
Narrowband
Wavelength tunable
Laser
Notes: Explanation

## Slide 11: Why use burst-mode filtered Rayleigh scattering?
Laser | Duration | Rate | 532 nm Pulse Energy | Average Power
Flashlamp Pumped Q-switched | Continuous | 10s of Hz | 0.50-1.00 J[3] | 10 W
Diode Pumped Q-switched | Continuous | kHz to MHz | 0.004 J (100 kHz)[4] | 400 W
Flashlamp Pumped Burst-mode | 1-20 ms per 10 s | kHz to MHz | 0.50-1.00 J (100 kHz) [5] | 0.10 W
Energy
Time
Energy
Time
10 s
Energy
Time
100 ms
[7] Koelling et al., 2022: 250 kHz visualization of tripped hypersonic flow.
[6]Wu et al., 2000: 500 kHz visualization of Mach 2.5 flow over a 14° Wedge.
Condensate-Enhanced Applications
Molecular Applications
[8] Krishna et al., 2021: 10 kHz 1D temperature of propagating premixed flame
[9] Creel et al., 2023: 250 kHz visualization of laser-spark pressure wave
Notes: Explanation

## Slide 12: Burst-mode Laser Architecture
Pulse Slicing
cw Laser Seed
Master Oscillator
SHG
Energy
Time
Repetition Rate
Time
Energy
Burst Duration
Duty Cycle
Energy
Time
1064 nm
Power Amplifier
Amp 1
Amp 2
Amp 3
Amp 4
Amp 5
Amp 6
What about the spectral characteristics?
Notes: Explanation

## Slide 13: FRS requires a spectrally pure laser source
[10] Barnes et al., 1993
High SP
Broadband Component
Broad Linewidth

## Slide 14: Methods to increase spectral purity
< OD 4 SP = 0.99986
Iodine Cell
Theoretically > OD 6!

## Slide 15: Methods to increase spectral purity
< OD 4 SP = 0.99986
Iodine Cell
Theoretically > OD 6!
Power Amplifier
Amp 1
Amp 2
Amp 3
Amp 4
Amp 5
Amp 6
Etalon
~ OD 6 SP = 0.9999987

## Slide 16: Demonstration of increased spectral purity
0
4096
Potential for kHz-MHz single-parameter measurements
Filtered
No Etalon
Filtered Etalon
0
4096
How can we achieve multi-parameter measurements?

## Slide 17: Intensity of filtered Rayleigh scattering
Rayleigh Scattering
Rayleigh
Filter
Laser
Filter
Background Scattering

## Slide 18: Intensity of filtered Rayleigh scattering
Rayleigh Scattering
Background Scattering
Rayleigh
Filter
Laser
Filter
1x Equation
2x Calibration Parameters
3x Unknowns

## Slide 19: Frequency-scanning FRS for a single pixel
Function of flow conditions,
Author | # Steps | # Avg. | Total time
[12]Forkey et al. (1996) | 30 | 30 | 50 (3) min.
[11]Boguszko et al. (2005) | 120 | 50 | 10 min.
[13]Doll et al. (2014) | 13 | 60 s | 12 min.
Can we reduce this measurement time?

## Slide 20: Method #1: Frequency-scanning burst-mode laser
Doppler global velocimetry
Planar laser induced fluorescence
[14] Fahringer et al. (2018)
[15] Burns et al. (2020)
[16] Rodrigues et al. (2023)
Potential to decrease measurement time to 10 ms or less

## Slide 21: Frequency-scanning burst-mode laser
Relative Frequency (GHz)
532 nm
SHG
1064 nm
Power Amplifier
cw Laser
Pulse Slicing
Function Generator
Master Oscillator
Function Generator Signal

## Slide 22: Frequency-scanning burst-mode laser
Relative Frequency (GHz)
Function Generator Signal
532 nm
SHG
1064 nm
Power Amplifier
cw Laser
Pulse Slicing
Function Generator
Master Oscillator
Wavemeter
Wavemeter Measurement

## Slide 23: Frequency-scanning burst-mode laser
Relative Frequency (GHz)
Function Generator Signal
532 nm
SHG
1064 nm
Power Amplifier
cw Laser
Pulse Slicing
Function Generator
Master Oscillator
Wavemeter
Wavemeter Measurement
Unfiltered
Unfiltered Burst Profile

## Slide 24: Frequency-scanning burst-mode laser
Relative Frequency (GHz)
Function Generator Signal
532 nm
SHG
1064 nm
Power Amplifier
cw Laser
Pulse Slicing
Function Generator
Master Oscillator
Wavemeter
Wavemeter Measurement
Unfiltered
Unfiltered Burst Profile
Iodine Cell
Iodine Cell
Filtered
Filtered Burst Profile

## Slide 25: Sensitive to the radial velocity component
532 nm
SHG
1064 nm
Power Amplifier
cw Laser
Pulse Slicing
Function Generator
Master Oscillator
Wavemeter
Unfiltered
Iodine Cell
Iodine Cell
Filtered
Iodine Cell
Unfiltered Camera
Filtered Camera
+ Doppler Shift
Laser Sheet
Schlieren
Flow
+ Velocity
Counts
0
1200

## Slide 26: Filtered Rayleigh scattering processing
Reference
Experiment

## Slide 27: Filtered Rayleigh scattering processing
Reference
Experiment

## Slide 28: Comparison with CFD results
Temperature
Radial Velocity
CFD[17]
Experimental
Pressure

## Slide 29: Comparison with CFD results
Density
CFD
Mean (RS)
Calculated
Temperature
Temperature
Radial Velocity
CFD [17]
Experimental
Pressure

## Slide 30: Five simultaneous P, T, and V measurements in 5-ms
Can we further reduce the measurement time?
Potential for 100s of Measurements

## Slide 31: Method #2: Generate “discrete” pulse frequencies
EOM
cw laser seed
Time
Energy
MHz
MHz
Energy
Time
MHz
Master Oscillator
SHG
Power Amplifier
+200 MHz AOM
Energy
Time
FA
Energy
Time
Pulse Slicing
Notes: Acousto-optic effect: send oscillating electric signal to PZ tranducer. Induces sound wave (RF frequency). Create a change in the index of refraction. Doppler shifted by the amount of the sound wave

## Slide 32: Method #2: Generate “discrete” pulse frequencies
EOM
cw laser seed
Time
Energy
MHz
MHz
Energy
Time
MHz
Master Oscillator
SHG
Power Amplifier
-200 MHz AOM
Energy
Time
Energy
Time
Pulse Slicing
+200 MHz AOM
FA
MHz
MHz

## Slide 33: Generation of four frequency-shifted pulses
50%
CW
EOM
1%
99%
Wavemeter
FA
50%
50%
50%
5
6
7
2
3
Master Oscillator
AOM1
AOM2
AOM3
AOM4
1
Energy
Time
0 MHz
1
Energy
Time
+200 MHz
2
Energy
Time
-200 MHz
3
Energy
Time
4
Energy
Time
7
Energy
Time
-300 MHz
6
+100 MHz
Energy
Time
5
-100 MHz
+300 MHz
4
-200 MHz
+200 MHz
-100 MHz
+100 MHz

## Slide 34: Overexpanded jet facility
Filtered Camera
532 nm
SHG
1064 nm
Power Amplifier
cw Laser
AOM System
Master Oscillator
Iodine Cell
Shadowgraph
+ Doppler Shift
Laser Sheet
Flow

## Slide 35: Visualization of the Doppler effect
1
2
3
4
1
2
3
4
Shadowgraphy
-V
+ Doppler Shift
+ V

## Slide 36: Fitting with four measurements
Average
Reference
Experiment

## Slide 37: Simultaneous temperature, pressure, velocity
t ~ 0 µs
t ~ 40 µs
t ~ 80 µs
Pressure
Temperature
Rad. Velocity
Calc. Density
Binned

## Slide 38: Centerline mean pressure and temperature
PR ~ 12
Theoretical Post-shock Conditions
Theoretical Exit Conditions

## Slide 39: Centerline mean pressure and temperature
PR ~ 12
PR ~ 13.5

## Slide 40: Centerline mean pressure and temperature
PR ~ 12
PR ~ 13.5
PR ~ 15

## Slide 41: Pressure, temperature, and velocity at 25 kHz
Potential for MHz Measurements
Pressure
Temperature
Rad. K Velocity
Calc. Density
How can we improve these results?

## Slide 42: How to find the optimal configuration?
Pressure
Absolute Relative Error
(GHz)
Range
Number of Frequencies

## Slide 43: How to find the optimal configuration?
1 atm, 300 K, 100 m/s
0.5 atm, 100 K,
-100 m/s
Can we keep the absolute relative error in below 2%?
Pressure
Temperature
Rad. K Velocity

## Slide 44: Conclusions
Improved Spectral Purity
High-stray scattering applications
Increased Frequency-scanning FRS rate by ~600,000x
Simultaneous in 1 ms
Potential for 100s of kHz
Simultaneous in 40 µs
Potential for MHz
Increased Frequency-scanning FRS rate by ~1,500,000x

## Slide 45: References
[1] Baurle, R. A. (n.d.). VULCAN-CFD applications. https://vulcan-cfd.larc.nasa.gov/WebPage/vulcan_apps.html
[2] “Hyper-X ED97-43968-1: Computational Fluid Dynamics (CFD) Image of Hyper-X Research Vehicle at Mach 7 with Engine Operating.” https://www.dfrc.nasa.gov/Gallery/Photo/X-43A/HTML/ED97-43968-1.html (accessed Oct. 02, 2022).
[3] “Spectra-Physics.” https://www.spectra-physics.jp/member/admin/document_upload/QuantaRay_PRO_LAB_INDI_datasheet.pdf
[4] “GX-series | EdgeWave.” https://www.edge-wave.de/web/en/produkte/short-pulse-systeme/hd-serie/ (accessed Oct. 02, 2022).
[5] J. Felver, M. N. Slipchenko, E. L. Braun, T. R. Meyer, and S. Roy, “High-energy laser pulses for extended duration megahertz-rate flow diagnostics,” Opt. Lett., vol. 45, no. 16, p. 4583, Aug. 2020, doi: 10.1364/OL.400831.
[6] P. Wu, W. L. Lempert, and R. B. Miles, “Megahertz Pulse-Burst Laser and Visualization of Shock-Wave/Boundary-Layer Interaction,” AIAA Journal, vol. 38, no. 4, pp. 672–679, Apr. 2000, doi: 10.2514/2.1009.
[7] F. R. Koelling, B. S. Leonov, and C. Limbach, “Filtered Rayleigh Scattering Visualization of Hypersonic Boundary Layer Trip Wake Flow at 250kHz,” presented at the AIAA AVIATION 2022 Forum, Chicago, IL & Virtual, Jun. 2022. doi: 10.2514/6.2022-3363.
[8] Y. Krishna, A. M. Mahuthannan, X. Luo, D. A. Lacoste, and G. Magnotti, “High-speed filtered Rayleigh scattering thermometry in premixed flames through narrow channels,” Combustion and Flame, vol. 225, pp. 329–339, Mar. 2021, doi: 10.1016/j.combustflame.2020.10.053.
[9] J. R. Creel, B. S. Leonov, and R. Miles, “Angle Optimized Filtered Rayleigh Scattering for the Imaging of Pressure Waves from Laser Generated Surface Sparks at 250,000 Frames per Second,” in AIAA SCITECH 2023 Forum, American Institute of Aeronautics and Astronautics. doi: 10.2514/6.2023-0350.
[10] N. P. Barnes and J. C. Barnes, “Injection seeding. i. theory,” IEEE J. Quantum Electron. 29, 2670–2683 (1993).
[11] M. Boguszko and G. S. Elliott, “On the use of filtered Rayleigh scattering for measurements in compressible flows and thermal fields,” Exp Fluids, vol. 38, no. 1, pp. 33–49, Jan. 2005, doi: 10.1007/s00348-004-0881-4.
[12] J. N. Forkey, N. D. Finkelstein, W. R. Lempert, and R. B. Miles, “Demonstration and characterization of filtered Rayleigh scattering for planar velocity measurements,” AIAA Journal, vol. 34, no. 3, pp. 442–448, Mar. 1996, doi: 10.2514/3.13087.
[13] U. Doll, G. Stockhausen, J. Heinze, and U. Meier, “Frequency scanning filtered Rayleigh scattering am HBK1,” presented at the Diagnostik i.d. Verbrennung, DIV10, Stuttgart, Oct. 2014. Accessed: Sep. 08, 2023. [Online]. Available: https://elib.dlr.de/91171/
[14] T. W. Fahringer, R. A. Burns, P. M. Danehy, P. M. Bardet, and J. Felver, “Pulse-Burst Cross-Correlation Doppler Global Velocimetry,” AIAA Journal, vol. 58, no. 6, pp. 2364–2369, Jun. 2020, doi: 10.2514/1.J059172.
[15] R. A. Burns, T. W. Fahringer, and P. M. Danehy, “Velocity measurements across an oblique shock using pulse-burst cross-correlation DGV,” in AIAA Scitech 2021 Forum, American Institute of Aeronautics and Astronautics. doi: 10.2514/6.2021-0120.
[16] N. S. Rodrigues, P. M. Danehy, N. Jiang, P. Hsu, J. Leicht, and S. Roy, “100 kHz High-Spectral-Resolution NO-PLIF Measurements for Compressible Flows,” in AIAA SCITECH 2023 Forum, National Harbor, MD & Online: American Institute of Aeronautics and Astronautics, Jan. 2023. doi: 10.2514/6.2023-0405.
[17] A. M. Braun et al., “Demonstration of Frequency-Scanning Burst-Mode Filtered Rayleigh Scattering for Multi-Parameter Gas-Phase Measurements,” in AIAA SCITECH 2024 Forum, in AIAA SciTech Forum. , American Institute of Aeronautics and Astronautics, 2024. doi: 10.2514/6.2024-1095.

## Slide 46: Backup Slides

## Slide 47: Burst profile using AOM-system
532 nm
SHG
1064 nm
Power Amplifier
cw Laser
AOM System
Master Oscillator
Wavemeter
Iodine Cell
Filtered

## Slide 48: Uncertainty in background constant estimates

## Slide 49: Model

## Slide 50: What is Rayleigh scattering?
Incident Laser
1 atm, 300 K, 0 m/s
0.75 atm, 350 K, 0 m/s
1.25 atm, 250 K, 0 m/s
Incident Laser
Scattering
Rayleigh Scattering
Flow Molecules
Notes: Explanation

## Slide 51: Same pixel with different fitted profiles
+10%
-10%
Pressure,
Temperature,
Velocity,
-10%
+10%
-50 m/s
+50 m/s

## Slide 52: Simultaneous P, T, and V in 1-ms
Can we further reduce the measurement time?
Scan 1
Scan 2
Scan 3
Scan 4
Scan 5

## Slide 53: Frequency-switching FRS for a single pixel
Fewer laser pulses with known laser frequency