## Slide 1: HWO Technology Development
Breann Sitarski

## Slide 2: Ultra-Stable Metrology
20 data sets per configuration, 100 seconds each, taken throughout a day, looking at concentric rings over ~3” flat in OAP configuration
Can achieve single-digit, picometer-level measurements at low (0.01 – 0.1 Hz) and mid (0.1 – 1 Hz) temporal frequencies for concentric rings on mirrors

## Slide 3: Orbiting Laser Guide Star
ORCAS at Keck Observatory provides some concept
  Concept is a highly-elliptical orbit with laser that points at Keck Observatory (Peretz+ 2024)
  LCRD pointed at Keck, and loop was able to close with high Strehl ratio
Laser guide star can provide:
  Reference PSF for PSF calibration
  Substantial photon count for focal plane wavefront sensing (common—path sensing)
    Could ease stability requirements by ~2 orders-of-magnitude (Clark, thesis)
LCRD concept
Open Loop
Closed Loop

## Slide 4: UV Coatings
Aluminum-based coatings can provide high reflectance (better than Al+MgF2) in the UV (i.e., Al+XeLiF) with excellent aging statistics
Challenges:
  Scaling up while maintaining high uniformity (2-3%) between segments
  Need to test surface roughness and coating-induced stresses
  Full characterization of polarization-induced aberrations
Al+XeLiF does better than Al+MgF2 and is only slightly worse than bare Al

## Slide 5
First on-sky closed-loop control of Keck primary mirror segments using a vZWFS (Salama+24)
POST closed-loop
Comparing vZWFS phasing with PCS phasing to determine optimal segment co-phasing technique for best AO performance
Vector-Zernike WFS: 2 simultaneous phase shifts for increased dynamic range
On-sky demonstration of Strehl improvements via post-AO ZWFS control of primary mirror
WFS architecture and control schemes are comparable to HWO, helping to verify and inform the HWO architecture
Working towards understanding interactions between primary mirror segment co-phasing and AO system