## Slide 1: Preliminary Assessment of Step Effects on the BOLT Geometry
Presented by:
Carey Scott
NASA Langley Research Center
Presented to:
AIAA Aviation
July 25, 2024
Co-authors:
Scott Berry & Frank Greene
NASA Langley Research Center
Kevin Basore & Stefan Wernz
Raytheon
Distribution Statement A. Approved for public release: distribution is unlimited.
Notes: BOLT is hypersonic flight test
Reduce words on screen
BOLT on flight configuration
Use takeaways – remove correlation bullet

## Slide 2: Motivation & Goals
The goals of this test include:
  Demonstration of a quantitative infrared thermographic test technique at LaRC.
  Complete a parametric study of forward and rearward facing 2-dimensional steps and their impact on the chord-wise transition location (x/L) of the boundary layer from laminar to turbulent in Mach 6 flow by varying flow conditions and step height, k.
Project Overview
Test Methodology
Preliminary Results
Discussion
Future Work
Why BOLT Step Test?
The Boundary Layer Transition (BOLT I) flight test article was designed with 2 different joints near the nose to accommodate the TPS and isolator materials.
There are differences in the CTE of the material on either side of the joint.
The difference in CTE is expected to cause a 2-dimensional step at the joint locations.
The step on the flight test article was designed to be rearward facing (RF).
Figure 1. BOLT I Flight Vehicle Design.
BOLT: BOundary Layer Transition
Hypersonic Flight Test
AFOSR funded study of hypersonic boundary layer transition in simple conical shapes to develop new physics-based transition prediction tools.

## Slide 3: Model Design
Model Design Concept:
The BOLT Step Test (BST) model utilized an aluminum ‘strongback’ for the main body and nose with a PEEK OML for the outer mold line (OML).
The nose was built as a separate piece with a set of slotted spacers to create offsets for the forward-facing (FF) or rearward-facing (RF) step configurations.
Figure 2. BST Model Design.
Project Overview
Test Methodology
Preliminary Results
Discussion
Future Work
Figure 3. BST Model Exploded View
BST Assembly:
PEEK OML
Al strongback
Al nose spacers (multiple)
  Creates steps in OML
  Center slot offsets
  0.005” increments
  1 spacer = 2 steps(+/-)
Figure 4. BST Nose and 0-Step Insert

## Slide 4: Model Fabrication
Model Configuration Values:
A single insert produced 2 step configurations by rotating the slotted inserts by 180 in roll axis. All step height measurements was along the model centerline.
Resulting step heights were scanned using an optical scanning microscope which lists a height measurement precision of 3.94 x 10-5 inches.
Significant deviation in as-built results from designed step heights. Primarily due to PEEK OML deformation in thin regions.
Project Overview
Test Methodology
Preliminary Results
Discussion
Future Work
BST Insert | Step Direction | kMeasured |  | Baseline %
 |  | (mm) | (in) | (kB=0.005-in)
IR-21b | RF | 1.718 | 0.0676 | 13.5 kB
IR-11b | RF | 1.101 | 0.0433 | 8.7 kB
IR-06b | RF | 0.438 | 0.0172 | 3.5 kB
IR-02b | FF | 0.076 | 0.0030 | -0.5 kB
IR-01a | FF | 0.089 | 0.0035 | -0.7 kB
IR-01b | FF | 0.157 | 0.0062 | -1.2 kB
IR-02a | FF | 0.272 | 0.0107 | -2.1 kB
IR-06a | FF | 0.777 | 0.0306 | -6.1 kB
IR-11a | FF | 1.409 | 0.0554 | -11 kB
IR-21a | FF | 2.033 | 0.0800 | -16 kB
Table 2. Step Height Values for As-Built Configurations
Note: Negative values denote FF steps.
Figure 5. BST Model on Optical Scanner Bench
Closest to a no-step case
Notes: Shelly’s paper for reference

## Slide 5: Test Facility
Langley Aerothermodynamic Laboratory (LAL):
Average run time for this test was 10 seconds.
Reynolds number sweeps from 1.05x106 /ft to 7.97x106 /ft were conducted for 10 step heights.
Project Overview
Test Methodology
Preliminary Results
Discussion
Future Work
Figure 7. BST Model in the test section. LongBOLT configuration is ~170% BOLT I length.
Figure 6. LAL 20-Inch Mach 6 facility in Hampton, VA. [1]
LongBOLT Extension
Notes: Use arrows / limit text…kB repeat here
Measurements across the centerline
Order of 3 BL height changes between CL vs leading edge.
Leading edge is very sensitive .

## Slide 6: Quantitative IR Test Technique
IR Thermography Workflow:
Define calibration coefficients of the Sakuma-Hattori equation for a single integration time of the camera over the range of expected temperatures.
Export the raw counts from the IR software for a pre-run frame and at frame 300 during the test entry.
Apply calibration equation to all pixels to get the transfer from
Counts > Temp(K) > Temp(C) then export as .csv files.
Import the temperature .csv files to IHEAT for processing to heat transfer and non-dimensionalize by Fay-Riddell film coefficient reference values.
Extract line cuts along regions of interest using the built-in IHEAT profiling tool.
Project Overview
Test Methodology
Preliminary Results
Discussion
Future Work

## Slide 7: Data Acquisition
Infrared Thermography Test Technique
Model temperature range (no-wind vs. wind-on) required custom radiometric calibration and temperature retrieval methodology.
Use Planckian version of Sakuma-Hattori equation as a basis for Signal to Temperature transfer function.
Project Overview
Test Methodology
Preliminary Results
Discussion
Future Work
IR Camera System Specs:
FLIR SC6701 SLS (LWIR)
FLIR 50mm Ge lens
11-in x14-in AR coated ZnSe Window
Integration time = 0.038 ms
Frame rate = 60 Hz
A | B | C | G
1.008 | 0.7235 | 6.368 | 1962.22
Figure 8. Temperature retrieval calibration curve provides greater dynamic range while imaging

## Slide 8: Raw IR Data – 83 Rotal Runs

## Slide 9: Raw IR Data – Baseline vs. Large FF Steps
Baseline step height:
kB = 0.005 inches
Closest to a no-step case

## Slide 10: Raw IR Data – Baseline vs. Large RF steps
Baseline step height:
kB = 0.005 inches
Closest to a no-step case

## Slide 11: Data Analysis
IHEAT Data Analysis Software
Aerothermal data processing package developed at LaRC.
Details of the IHEAT software are given by Mason, et al. [2]
Inputs to heat transfer calculations are given by Merski [3]
One-dimensional heat transfer results are output as heat transfer images.
Project Overview
Test Methodology
Preliminary Results
Discussion
Future Work
Convective heating film coefficient is represented by h in IHEAT output, definition is:
  where
    , where and
  Local value of is computed by IHEAT for all pixels from temperature-time history ().
  Local values are normalized by the Fay-Riddell correlation for stagnation point heat flux:
Figure 11. Raw IR images (top) and the resulting heat transfer images (bottom) for runs with k = -0.5kB.
Note: Color bar values are for the heat transfer images only (bottom row).

## Slide 12: Comparison with CFD - Longitudinal
Qualitative Technique Validation
Smooth OML (no step) cases were run for = 1, 2, 4, 5.6, and 8 x 106 / ft and used as a basis for comparison of the IR test technique with LAURA CFD solutions.
Line cuts were extracted and plotted against the wind tunnel results using h/hFR.
Project Overview
Test Methodology
Preliminary Results
Discussion
Future Work
Centerline
Baseline step height:
kB = 0.005 inches
Joint Edge

## Slide 13: Comparison with CFD – Spanwise Cuts for Reu = 2x106 ft-1
Qualitative Technique Validation
Smooth-wall CFD solutions are used as a basis for data validation.
Line cuts were extracted and plotted against the wind tunnel results using h/hFR.
Spanwise cuts shown here show the augmented heating at the lobes.
Project Overview
Test Methodology
Preliminary Results
Discussion
Future Work
Augmented heating at lobes
FF Step Height = -0.5kB
Augmented heating at lobes
LAURA CFD
CFD
Smooth wall
Reu = 2x106 ft-1
Experiment
Experiment
No-Step
Reu = 2x106 ft-1
CFD Smooth wall
Notes: Smooth CFD vs. ‘smooth’ experiment
Add joint location
Add text box with LAURA CFD not BLAYER

## Slide 14: Heat Transfer Data – Constant Re, Variable Step Height
Project Overview
Test Methodology
Preliminary Results
Discussion
Future Work
y/yref = 0
+1
CFD Smooth Wall
CFD
NOT TO SCALE
Step Location
Notes: Define L early on.
CL strong effect when FF
RF strong effect near leading edge

## Slide 15: Spanwise Cuts - Constant Re, Variable Step Height
LAURA CFD
LAURA CFD
0.2540
Notes: ADD bigger text
Descriptive titles
Change BLAYER to LAURA

## Slide 16: Spanwise Cuts - Constant Re, Variable Step Height
0.254
Notes: ADD bigger text
Descriptive titles
Change BLAYER to LAURA

## Slide 17: Summary
Project Overview
Test Methodology
Preliminary Results
Discussion
Future Work
Quantitative IR Thermography:
Significant forward progress was made toward quantitative IR thermographic test technique development at LAL.
This measurement technique offers potential cost, manufacturability, and supply chain benefits over the legacy phosphor thermography technique, but with previously undetermined accuracy.
BOLT Step Effects:
Forward-facing steps significantly disrupt the boundary layer, causing augmented heating forward of the step boundary, and more evenly distributed surface heating downstream.
Rearward-facing steps show reduced heating immediately downstream, suggesting boundary layer separation immediately aft of the step.
Observations suggest the region near the leading edge and the joint is highly sensitive to step effects.

## Slide 18: Next Steps
Project Overview
Test Methodology
Preliminary Results
Discussion
Future Work
Table 3. Approximate transition onset locations for k= -0.5kB as a function of Reynolds number.
Figure 12. ‘No-step’ transition data will be used as a baseline for comparing step effects for different configurations.
2D Step / Transition
Correlation Model:
Goal: Develop a step height vs transition onset correlation model for BOLT geometry.
BOLT Step Effects:
Continue data processing for additional Reynolds numbers and measure step heights near leading edge.
Investigate additional BOLT-derivative designs (i.e., Flat-BOLT, various nose shapes).
Explore use-cases for BST and BST-derivative models in other flow conditions.

## Slide 19: Next Steps: Flat-BOLT
Project Overview
Test Methodology
Preliminary Results
Discussion
Future Work
Benefits of Flat-BOLT Design:
Isolates the effect of the planform shape on leading-edge and acreage heating.
Permits optical measurements of the boundary layer such as Focused Schlieren and Focused Laser Differential Interferometry (FLDI).
Flat-BOLT acreage can host standard flat material coupons for testing

## Slide 20: Questions?
References:
[1] NASA Langley Hypersonic Experimental Aerothermodynamic Capabilities and Recent Contributions, AIAA Aviation 2024
[2] Mason, M. L. and Rufer, S. J., “Features of the Upgraded Imaging for Hypersonic Experimental Aeroheating Testing (IHEAT) Software,” AIAA 2016-4322, Jun. 2016. doi:10.2514/6.2016-4322.
[3] Merski, N., “Reduction and Analysis of Phosphor Thermography Data with the IHEAT Software Package,” presented at the 36th AIAA Aerospace Sciences Meeting and Exhibit, Reno,NV,U.S.A., 1998. https://doi.org/10.2514/6.1998-712

## Slide 21: Backup

## Slide 22: Test Design
Background
This investigation is focused on the 2-dimensional step at the joint between the stainless-steel isolator and the aluminum body (Joint 2). [Figure 1]
The BOLT Step Test (BST) model utilized a nose step location that accurately represents the step location on the BOLT I flight geometry. [Figure 2]
The intent of the present experiment is to provide a controlled data set to assist in flight test data analyses and provide data for future design considerations.
Additional comparisons to other BOLT-derivative geometries (i.e. Flat-BOLT) were conducted using similar model design principles and are presented in later sections for reference.
Figure 1. BOLT I Flight Vehicle Design.
Project Overview
Test Methodology
Preliminary Results
Discussion
Future Work
Figure 2. BST Model Design.
The BOLT Step Test (BST) was conducted at the 20-Inch Mach 6 Tunnel at NASA LaRC.
Table 1. 20-Inch Mach 6 Air Tunnel Test Conditions
Notes: Initial – 24 minutes –need to trim/
Trim slides for content – refer to content
Pathfinder test  include test dates
Acknowledge Drew’s am paper – refer to Drew’s talk
More results?

## Slide 23: Uncertainty Quantification
Project Overview
Test Methodology
Preliminary Results
Discussion
Future Work
Figure 6. LAL 20-Inch Mach 6 facility in Hampton, VA.
Heat Transfer Uncertainty
Temperature Uncertainty
Total Combined Standard Uncertainty with 95% confidence interval:

## Slide 24: Data Acquisition
Infrared Thermography Test Technique
Empirical measurements made for window transmission and PEEK emissivity values.
Project Overview
Test Methodology
Preliminary Results
Discussion
Future Work
Figure 9. Two methods of emissivity measurement were used. Convective and conductive heating methods provided data for ratio method of determination. Black electrical tape was used as a control.
Target
Sample
Control
Sample
Target
Sample
Heat Source
Blackbody Cavities
Figure 10. Window transmissivity and directional emissivity measurements help quantify uncertainty in
0.0255 &

## Slide 25: Uncertainty Quantification
Quantitative IR Thermography:
Inputs to the governing equations for temperature extraction and heat transfer are treated as type B uncertainties.
Uncertainty distributions & coverage factors are assigned conservatively.
Uncertainty input terms are the normalized standard deviations (), for each measured variable in percentage units.
All uncertainties are treated independently (no covariance is assumed).
Project Overview
Test Methodology
Preliminary Results
Discussion
Future Work
Heat Transfer Uncertainty
Temperature Uncertainty
Total Combined Standard Uncertainty with 95% confidence interval:
Notes: Add toback up