## Slide 2: Autonomous Robotic Manipulator Software (ARMS)
1 AUGUST 2024
Collin J Cresta
Robotics Engineer
Analytical Mechanics Associates - NASA

## Slide 3: Precision Assembled Space Structure
3 | #ascendspace
Notes: But first, an introduction into the project that has motivated this work and where most of the hardware testing of this system has occurred, the Precision Assembled Space Structure project out of Langley Research Center.

## Slide 4: The Structure
Backbone Truss Structure
2019 iSAT study concept
Backbone Structure assembly
TriTruss Module
Notes: In 2019 the iSat study produced this conceptual space telescope featuring a 20 meter mirror. The PASS project will perform a ground demonstration of robotic assembly of the back bone truss structure. The structure is shown here and is comprised of 37 of the TriTruss modules shown. And so I know I said it is Autonomous Robotic Assembly, and you might wonder why we need autonomy instead of human built or automated. Well this structure and others that will be assembled in space may be operating very far away from Earth where communications are spotty and may have delay on the order of seconds or even minutes. This means that teleoperation is not feasible and that the system will need to autonomously detect anomalies and react or shutdown and wait for human intervention.

## Slide 5: The Manipulator and End Effector
Notes: To allow for manipulation of the TriTruss modules there is an end-effector that was produced and shown here mounted on an ABB robotic manipulator. The combination of these 2 allows for modules to be moved around a work site.

## Slide 6: Robot at Work
Notes: Shown here is the assembly system at work. First the manipulator picks up a truss from a stowed position, then installing it into the central truss structure. I will break out the different segments of what is happening as we go along.

## Slide 7: Software Overview
8 | #ascendspace

## Slide 8: ARMS Overview
Robot Factory
Task and Agent Action Servers
Notes: We are going to look at 2 main parts of what make up the Autonomous Robotic Manipulation Software. The first is the robot factory, which is a configuration management tool that takes an input system definition and starts all of the software nodes required for that system to run. And the second is the Task and Agent Action servers that act on requests received, this is what commands the system to act on the environment.

## Slide 9: Software Dependencies
ROS 2
MoveIt 2
Gazebo
Notes: The software we have developed is built on top of ROS 2 and uses that as the communication framework for data, MoveIt 2 is used for its motion planning pipeline, and Gazebo for all simulation.

## Slide 10: Defining a Robotic Assembly System
11 | #ascendspace
Notes: Before we start assembling things, we need a way to define our system. As shown, we had a manipulator or robotic arm and an end effector for the PASS project, but various configurations require setting up various configuration files and launch systems and using this out of the box in ROS can be tedious.

## Slide 11: How many robots can you make?
A LOT!

## Slide 12: How many robots can you make?
A LOT!
Notes: Just to drive the point home, here you see some of the components that we have used for this project, often while planning things need to get moved around and rearranged. All of these changes cascade into various levels of configuration files if done traditionally.

## Slide 13: Robot Factory
Configuration management using URDF and XACRO
Once system configuration is built, it is launched
Notes: Our solution to this is to have a component library that consists of all of the manipulators, end-effectors, sensors and static models that we are using. Using the Unified Robot Description Format, XACRO and the tool we developed, the Robot Factory we can define any assembly system from a combination of components from the library. You can insert any element and attach it to any link in your defined system as part of the configuration. Robot Factory will then build the configuration files needed, and handle launching the software components of the system, like hardware controllers, MoveIt, and the action server.

## Slide 14: Modularity
Notes: It makes things very easy to plug components together like legos, I threw this into simulation in a few minutes.

## Slide 15: Agent Definitions
15 | #ascendspace
Notes: Agents are the parts of the system actually doing the work and interacting with the environment, we define two abstract agent interfaces, one is a manipulator, and the other is an end effector. These agents will receive and act on action requests sent from the command line, a mission script or from a task server.

## Slide 16: Manipulator
Action Types
  Move to Pose
  Move Link to Pose
  Move with Approach
  Servo
  Add Object
  Attach
  Detach
  Save Planning Scene
Modifiers
  Cartesian Motion
  Ignore Collision
  Path Preview
  Plan Only
Notes: The manipulator is typically a robotic arm but can really be any agent that is moving things around. It has several actions is can perform, but the key ones I will focus on is Move With Approach, there are also modifiers that can be sent with a request to change the behavior like requesting cartesian motion or that it allows you to preview the path and approve it before execution.

## Slide 17: Manipulator
Move To Pose
Notes: Move to pose, it takes in a pose target, and will plan a trajectory to get the end link of the manipulator to that goal.

## Slide 18: Manipulator
Move With Approach
Notes: Move With approach is most useful for the higher level tasks that we will discuss later. It solves the problem of trying to plan a two part motion, where the first part is a gross motion near the point of interest and the second is a cartesian path in a desired approach vector. Poor selection of the joint state that joins these two plans will result in an inability to complete the cartesian motion. If you look at a to b as one attempt, the starting joint state results in collision, while the c to d attempt is successful.

## Slide 19: Manipulator
Notes: You can see the planning of the cartesian motion in yellow and the orange robot is the joint state that joins the two goals.

## Slide 20: End-Effector
Grab
Release
Notes: The end effector agent is an interface, each end effector will need to have actions that it can perform overridden and filled in to act accordingly. Not all end effectors need to perform all overrides. Shown here is the Grab and release actions, intended for part grabbing.

## Slide 21: End-Effector
Join
Open/Close Alignment
Notes: The other actions of note are Closing/opening the alignment gripper and joining, the first is a set of features in a tool meant to pull a part into alignment with the grappled piece. The other main action is joining, which will join using the specified tool.

## Slide 22: Task Definitions
22 | #ascendspace
Notes: Tasks are actions that coordinate multiple agents in a system to perform complex operations. I am going to go over the pick and install actions today and are main parts used in the PASS project.

## Slide 23: Pick
Release
Move With Approach
Grab
Attach Object
Retreat (Move to Pose - Cartesian)
Notes: Pick consists of a series of steps executed sequentially, release grippers, move with approach of the manipulator, grab the object, and retreat away from the picked location.

## Slide 24: Install
Move With Approach
Force Servoing
Close Alignment
Join
Open Alignment
Load Test
Release
Retreat (Move to Pose - Cartesian)

## Slide 25: Applications to Projects
25 | #ascendspace

## Slide 26: Built On-orbit Robotically assembled Gigatruss
Notes: Here is another assembly problem that this software has been applied to, the built on orbit robotically assembled gigatruss, BORG for short, this assembly takes a strut by strut approach to complete cubic modules that can be combined to form larger assemblies. Shown in the video is the install procedure. The human interaction in this video was a stand in for a visual Servoing routine.

## Slide 27: Conclusion
ARMS enables
  Modularity
  Rapid Prototyping and Integration
  Multi-level Autonomy
Future work
Notes: ARMS provides a way to build robotic assembly systems to fit a mission using modularized components. Through this it enables rapid prototyping and integration testing with new configurations and components. And it completes these missions by using varying levels of autonomous actions available through the agents and tasks. For future work we would like to finish integration on the visual Servoing piece, as well as provide GUI interfacing for sending agent requests.