## Slide 1: IXPE Science Operations NICER/IXPE Workshop
2024-Jul-30
Allyn Tennant

## Slide 2: Preliminaries
IXPE was never intended to be fast response spacecraft
  Typical observations take about week, hence waiting a few days should make no difference
Neither SOC nor the MOC are 24/7 operations
  It is a low-cost mission with minimal direct interaction with the spacecraft
  Budgets are being squeezed
Forget everything you know about Swift and NICER
  Our drivers are totally different

## Slide 3: Objectives
This is a look “behind the curtain” of IXPE operations
  Make some of operations less mysterious
  Only indirectly will help you write better proposals
  Will not focus on issues of data analysis
We are spatially separated
  The Science Operations Center (SOC) is at Marshall Space Flight Center in the Central (US) time zone
  The SOC lead (me) remote works in the Eastern time zone
  The Mission Operations Center (MOC) is at Laboratory for Atmospheric and Space Physics (LASP) in the Mountain time zone
  The prime spacecraft contractor is at BAE (formally Ball) also in Mountain time zone
  The instrument team is in Italy

## Slide 4: Data Volume
IXPE generates more data per event than any previous X-ray mission
  Takes a picture of every electron track
  Limited on-board storage
    4 GB for event data
  Limited number of ground stations
    Malindi is prime
      Average use is every other pass
        I.e., 7.5 passes per day
    Singapore is backup
      Can be used a few times per week
      (can not be used at certain times of the day)
    Planning must allow for missed contacts
  Telemetry load is very important
    Totally drives planning for bright sources

## Slide 5: Ground Operations
IXPE operates with minimal ground interaction
  The spacecraft holds the observing plan for an entire week
  The plan includes all contact times
    When spacecraft flies over a ground station at a scheduled contact time it
      Turns on transmitter
      Transmits a block of data
      Resets the pointers
    Note, the spacecraft does this whether or not there is full two-way communications
      If ground station is not ready, then there will be a large gap in the data
      Since the spacecraft has reset pointers, it will not fill in gap, but continue on
      The MOC needs to find this gap and manually request a re-transmission before the data are overwritten

## Slide 6: Operations
There are often short gaps in the data
  Can be RF interference (lightning)
  Often due to the spacecraft transmitting on two antennae
    Can result in classic interference pattern in the signal strength
      Not a hard cutoff, but gradual degradation of the signal
    Resulted in an unexpected number of small files (100-1000s) early in the mission
      Greatly slowed SOC processing
  The MOC now predicts the times of destructive interference
    Weekly load will pause transmission of data during the worst intervals
  Can still get short gaps
    Since the predictions are a week in advance predictions can be slightly in error
    Trade off between getting as much data as possible when you can

## Slide 7: Re-transmissions
The MOC needs to identify all gaps in the data and request re-transmission of the missing data.
  Gap checker is now automated
  Re-transmission does require someone in the control center to
    Verify two-way communication
    Need to pause the current download
    Transmit commands to dump blocks of missing data
  Must occur during normal working hours
Even when the MOC has all the data, the SOC still sees gaps
  We then request that the MOC re-send the data
  This adds another couple of days to the collecting all the data

## Slide 8: Data Download Timeline
Worse case is it can take a week to get data from a bright source off the spacecraft
Allow another couple of days for MOC to find and fill gaps
Allow another couple of days for the SOC to request resend of any missing data
For long observations SOC processing can take several days
Can take up to two weeks to process data
  Often done in less time

## Slide 9: SOC Planning
The Long-Term Planning begins when SOC gets the target list
  Includes observing constraints
    Normal phase constraints such as
      Avoid X-ray eclipses
      Observe at peak of super orbital period
    Want to space out observations in time but not by too much
    Avoid times around full Moon
  Some checking of targets is performed
    Up to observer to get the numbers right
  Bright sources need to be broken up into “4 GB chunks”
    We call this “segmenting”
    Need to observe a faint source while on-board storage is read down
    Want to get back to bright source quickly
      Results in the faint target also being segmented
    Want all segments to occur in the same 6-month season
  Planning is a “packing problem”
    Need to lay out the full year to make sure last targets are visible at the end of the year
      Since ToO’s can change the plan, only 6 months are published

## Slide 10: Normal Planning Cycle
From the LTP, the SOC prepares a 3 week list of targets one week in advance
  This list is called an Instrument Activity Plan (IAP)
  IAP includes name, position, data rate and exposure times
    Does not contain observation start/stop times
  The MOC prepares a “slew report” for all 3 weeks
    The MOC plans slews to occur during Earth occultation of the target
    Provides feedback to SOC when observations begin and end
    For time critical observations we will adjust the exposure times to be consistent with LTP
    We only control to 6 hours
  The MOC also looks at how bright the upcoming targets are
    If a bright target is coming up, the MOC will request additional contacts for that week
    Ground station requests go in 3 weeks in advance
    The final list of contacts for the coming week comes back at about the same time
  The MOC plans the upcoming week
    Includes all spacecraft activities (contacts/slews/etc.)
    Plan is checked and approved by MOC, SOC and BAE

## Slide 11: The Planning Timeline
The SOC produces an IAP on Wed afternoon and submit to MOC on Thurs morning
The MOC produces the slew report by Friday
The MOC plans the upcoming week (12 UT on Thurs to 12 UT following Thurs)
The draft command load appears on Tues
  The command load is abstracted and posted at
    https://ixpe.msfc.nasa.gov/for_scientists/weekly.html
On Wed the commands for the entire week are loaded to spacecraft
  Goal is to have two chances to upload during working hours at MOC
At 12 UT on Thurs the new command load takes over control

## Slide 12: SOC stuff
For each contact, the MOC collects data from the ground station
  Then forwards all data to the SOC
    “Science” and Spacecraft data come in separate data streams
      Will contain separate gaps
      Will need both to process data
  Raw instrument data is sent to the Italian Team for health and safety monitoring
When data set is as complete, processing begins
  Apply detector corrections as provided by the instrument team
    Charging impacts the detector gain and depends on how bright the target is
      Bright targets charge faster
      Discharge occurs at a low rate all the time
      Need to integrate the charge history to get current charge state (hence the gain)
      Charging model is still not totally correct
  Actual boom motion was much larger than predicted pre-launch
    For bright sources, we apply an X-ray aspect solution
    We created a model for the boom motion which is applied
  Final level 1 and 2 products are produced
    SOC lead does a quick inspection of data before it is released

## Slide 13: ToO Considerations
ToO’s can impact the normal planning in 1 of 3 ways
  If the ToO is 3-4 weeks out, we just change the LTP
  If the ToO can start after 12 UT on the following Thurs we can tweak the IAP
  If the ToO impacts the planned or what's on the spacecraft, then the MOC must replan the load
A pre-approved ToO is considered must do
All other ToOs are considered to be Director Discretionary Time
  Subject to a review process including external scientists
  Review takes place in parallel with the planning
Friday afternoon is the worse time to submit a ToO
  Already planning the following week
Monday/Tuesday is better
  Very helpful if target can be observed the following Thurs
Depends on what is currently on the spacecraft
  If the ToO is bright and we just observed a bright target, may need to wait

## Slide 14: ToO Planning
In all cases the following key steps are needed
  The MOC is alerted that a ToO is being considered
  The coordinates and estimated count rates are checked
  We update our data base
  Figure out when the commands can be uploaded to the spacecraft
    Depends on contacts, for faint sources may not have a lot of choices
      May require a request for an additional contact
  The LTP is reworked in two phases
    First (before the IAP is submitted)
      Minimize disruption to overall plan
      Takes into account the amount of storage currently in use
      Add new target so that it does not violate the storage limits
    Second (after IAP is submitted to MOC
      Restore any cat A bumped targets
      Try to complete any observation that had been started
  IAP is created and provided to MOC

## Slide 15: Spacecraft Issues
Star tracker
  We have one star tracker with 2 heads
  Sometimes one head is searching for stars, the other head is restricted to 5 stars
  Has no noticeable impact on science quality
GPS
  Use for both timing and position
    Instrument has a very accurate oscillator
  Occasionally drops out
    Requires a GPS restart
    Early in the mission, this was a manual process
      Never occurred during a fast (<1 sec) pulsar
      We fill in GPS data using Two Line Elements (and added a note in the README file)
    The spacecraft now detects this condition and automatically restart the GPS
      GPS dropouts are now about a minute
      For these cases we do not back fill that data with TLE data
      Bad GPS times are not included in the Good Time Intervals

## Slide 16: Spacecraft issues
Battery issue
  Battery is used every orbit which results in battery wear
  Have reduced the heater power usage, increasing lifetime to 8 years post launch
  The entire team continues to look at ways to reduce wear
Fill Frame
  So far has happened twice, the spacecraft starts transmitting “fill frames”
  Telemetry contains no useful data, however
    Spacecraft is still executing the command load
    Spacecraft will accept ground commands
  Effectively required a reboot of the spacecraft
    Restoring spacecraft to normal operations requires almost a week
  Root cause not understood but BAE can simulate on the ground
    Has a potential “work around” to restore telemetry without the reboot
    Will be tested at next occurrence
    If successful, will automate recovery
  If data was not overwritten, it can be recovered off the recorder

## Slide 17: Early SAA entry
During geomagnetic storms
  A magnetic trough West of the the South Atlantic Anomaly (SAA) fills with particles
  IXPE enters this trough about 10 minutes prior to main SAA
    Totally different from the small rate increase seen just before SAA entry
  The detector count rate can reach very high levels
    To protect the detector the spacecraft detects this condition
    Instrument is commanded into SAA mode at this time
    Note, upon SAA exit the on-board load normally commands SAA mode off
  Other than slightly shortening the observation, has no impact on science

## Slide 18: Conclusions
IXPE operates with a very small team
  Nominal 40-hour work week
  The team is very dedicated and typically can be reached
A maximum amount is done on the spacecraft
  Does reduce flexibility
We try to accommodate as many science related requests as possible
  As in for all missions there are many trade offs that need to be considered
The primary task of the SOC is to help you get good science