## Slide 1: Self-Aligned Focusing Schlieren and OH Planar Laser-Induced Fluorescence Flow Visualization in a Dual-Mode Scramjet
Brett F. Bathel, Joshua M. Weisberger, Wayne E. Page
Advanced Measurements & Data Systems Branch
NASA Langley Research Center, Hampton, VA
Andrew Metro, Robert Rockwell, Chloe Dedic
Department of Mechanical & Aerospace Engineering
The University of Virginia, Charlottesville, VA
Nicholas Mejia, Bryan Schmidt
Department of Mechanical & Aerospace Engineering
Case Western Reserve University, Cleveland, OH
AIAA Paper 2024-3808
2024 AIAA Aviation Forum

## Slide 2: Presentation Overview
Motivation
  University of Virginia Supersonic Combustion Facility (UVASCF)
  Observe interesting physics using focusing schlieren technique that may not be captured by other measurement techniques (e.g., chemiluminescence, OH PLIF)
  Challenges
Self-Aligned Focusing Schlieren (SAFS)
  How it works, advantages over conventional schlieren and focusing schlieren methods
Experimental Setup
  SAFS and OH planar laser-induced fluorescence (OH PLIF)
Results
  SAFS, OH PLIF
  SAFS Dynamic Mode Decomposition
Summary

## Slide 3: Motivation
University of Virginia Supersonic Combustion Facility (UVASCF)
  Capabilities
    Electrically heated, continuous flow facility with stagnation temperatures up to 1200 K
    Mach 2 nozzle
    Optical access:
      Sides: Two-sided access for flow visualization and laser access
      Top: Ceiling access for laser access (PLIF, PIV, etc.)
  Research
    Flow/combustion physics: Fuel/air mixing, fuel injection strategies, combustion studies, etc.
    Measurement techniques: Wall pressure, PLIF, chemiluminescence, PIV, CARS, etc.

## Slide 4: Motivation
Advanced Laser-Based Imaging Techniques
  Chemiluminescence: CH*, OH*
  Laser-Based Measurements: PLIF (OH, CH2O, NO), CARS, PIV
High-Speed Schlieren Imaging
  Obtain time-resolved images of density gradients and turbulent structures not visible with species-specific measurements
  Use modal analysis techniques to isolate dominate flow structures and their frequencies
  Identify interesting physics not observed with other techniques
OH* Chemiluminescence
OH PLIF
?
?

## Slide 5: Motivation
Conventional Schlieren-Based Imaging
  Sensitive to 1st (schlieren) and 2nd (shadowgraph) derivatives of density ()
  Path integrated
Challenges
  Window defects, path-integration effects, HVAC thermals, tunnel boundary layers
  Variations in window refractive index resulting from thermal/mechanical stress
  Window flatness/parallelism
Shockwave/boundary layer interaction in Mach 10 flow

## Slide 6: Motivation
Conventional Focusing Schlieren
  Sensitive to 1st derivative of density
  Narrow depth-of-focus
  Successful application at UVaSCF with ramp fuel injector by Kouchi et al.1,2
Challenges
  Time-consuming alignment procedure
    Separate cutoff grid must be aligned to a separate source grid
  Typically requires two-sided optical access
    Large footprint
  Limited adjustability
  Sensitivity to vibration
  Projection methods could suffer from glare

## Slide 7: Self-Aligned Focusing Schlieren
Any
Linear Vertical
Right Circular
Outgoing Polarization:
Left Circular
Linear Horizontal
Returning Polarization:
Components3,4
  Condensing lens to focus/diffuse light (CD)
  Input light linearly polarized (LP1)
  Polarizing beamsplitter (PBS)
  Ronchi ruling grid element (RR)
  Polarizing Rochon prism (RP)
  Field lens (FL)
  Quarter-wave retarder
    Plate (QWP)
    Film (QWF)
  Retroreflective background (RBG)
  Linear polarizer (LP2) transmits horizontally polarized light
Imaging Optical Isolator
`
Schlieren Optics
Narrow depth-of-focus
Imaging large fields-of-view
Capable of high-speed acquisition
Schlieren-quality windows not required
Inherently self-aligned
Insensitive to vibration
Easily adjustable
    Scheimpflug imaging
Compact
Conventional
Focusing
Schlieren
Self-Aligned
Focusing
Schlieren

## Slide 8: Experimental Setup
SAFS Lens
Cavity
Injectors
OH PLIF
  20 Hz acquisition
  Q1(8) transition A2Σ+ → X2Π(1,0) band of OH
  PI-MAX4 1024i iCCD camera
SAFS
  110 kHz acquisition
  Cavitar Cavilux HF 640 nm illumination
  Phantom TMX 7510 CMOS camera
OH PLIF and SAFS Imaging Translation System
  3-axis translation stage with optical rails
  Visualization of injection location, cavity, cavity ramp
Flow
  C2H4 (ethylene) injection from B2 row of injectors
  φG = 0.18

## Slide 9: Experimental Setup
OH PLIF
SAFS
OH PLIF
  20 Hz acquisition
  Q1(8) transition A2Σ+ → X2Π(1,0) band of OH (283 nm)
  PI-MAX4 1024i iCCD camera
SAFS
  110 kHz acquisition
  Cavitar Cavilux HF 640 nm illumination
  Phantom TMX 7510 CMOS camera
OH PLIF and SAFS Imaging Translation System
  3-axis translation stage with optical rails
  Visualization of injection location, cavity, cavity ramp
Flow
  C2H4 (ethylene) injection from B2 row of injectors
  φG = 0.18

## Slide 10: Results
Fuel-Off, Flame-Off
Fuel-On, Flame-Off

## Slide 11: Results
Fuel-On, Flame-Off
Fuel-On, Flame-On
SAFS (110 kHz)
Regions not time correlated

## Slide 12: Results: Fuel-On, Flame-On
SAFS (110 kHz)
Regions not time correlated
OH PLIF (20 Hz)
Images not time correlated

## Slide 13: Results: Dynamic Mode Decomposition
Fuel-On
Flame-On
Mode 7 @ 1 kHz
Mode 6 @ 15.6 kHz
Mode 13 @ 19.0 kHz

## Slide 14: Summary
Schlieren-Based Imaging at the University of Virginia Supersonic Combustion Facility (UVaSCF)
  Benefits, challenges
Self-Aligned Focusing Schlieren (SAFS) for Flow Visualization at UVaSCF
  Working principle, advantages over standard focusing schlieren
Results
  SAFS and OH PLIF
  Mach 2 flow, φG = 0.18
    Fuel-Off, Flame-Off
    Fuel-On, Flame-Off
    Fuel-On, Flame-On
  SAFS modal analysis (Dynamic Mode Decomposition)

## Slide 15: Acknowledgements and References
Acknowledgements:
Transformational Tools and Technologies (T3) Project
Hypersonic Technologies Project (HTP)
Plume Surface Interaction (PSI) Project
References:
Kouchi, T., Goyne, C.P., Rockwell, R.D. and McDaniel, J.C., “Focusing-schlieren visualization in a dual-mode scramjet,” Experiments in Fluids, 56, pp.1-14, 2015.
Kouchi, T., Goyne, C., Rockwell, R., Reynolds, R., Krauss, R. and McDaniel, J., “Focusing-schlieren visualization in direct-connect dual-mode scramjet,” 18th AIAA/3AF International Space Planes and Hypersonic Systems and Technologies Conference, AIAA Paper 2012-5834, 2012.
Bathel, B.F. and Weisberger, J.M., “Compact, self-aligned focusing schlieren system,” Optics Letters, 46(14), pp. 3328-3331, 2021.
Weisberger, J.M. and Bathel, B.F., “Single source/cutoff grid, self-aligned focusing schlieren system,” Exp. Fluids, 63, 2022.
Patents:
Bathel, B.F. and Weisberger, J.M., “Compact, self-aligned projection focusing schlieren method and system,” US Patent #11,650,151, 2023.