## Slide 1: A Method of Compliance for Achieving Target Collision Risk in UTM Operations
✧ NASA Ames Research Center
*Metis Technology Solutions
✦ San Jose Sate University Research Foundation
◇ Universities Space Research Association
Moffett Field, CA
Min Xue✧
Aviation Forum, Aug. 1, 2024
Vincent Kuo*
José Ignacio de Alvear Cárdenas✦
Priyank Pradeep◇

## Slide 2
Target
(10-n NMACs per flight hour)
How to develop a method of compliance to show that a target UA-to-UA Collision Risk level can be achieved by core UTM services?
Safety Credit
(USS)
Safety Credit
(Intent sharing)
Safety Credit
(Strategic Conflict Detection)
Safety Credit
(Conformance Monitoring)

## Slide 3: Outline
Background
  Method of Compliance
  Reich Collision Risk Model
  ASTM USS Specification
Method of Compliance for Strategic Coordination Services
  Baseline ASTM requirements
  Volume-based Collision Risk Model
  Flow Diagram: test harness and data collection
Sensitivity Analysis
Conclusions and Future Work

## Slide 4: Background I: Method of Compliance
Advisory Circulars 107-2A:
“A method of compliance (MOC), or a means of compliance, is one method, but not the only method, to show compliance with a regulatory requirement”.
An MOC can help break down the initial requirement, substitute it with sub-requirements, and show that satisfying the sub-requirements is equal to satisfying the initial requirement.

## Slide 5: Sample MOCs in AC 107-2A
A small UA
  Does not exceed the applicable injury severity limit upon impact with a human being
  Does not contain any exposed rotating parts that would lacerate human skin
  Does not contain any safety defects
The small UA’s maximum kinetic energy calculated using:
is less than:
Category 2 : 11 ft-lbs
Category 3 : 25 ft-lbs
Speed limits
FAA-provided MOC
Kinetic energy limits
“Manufacture the small UAS so that the propellers are internal to the UAS, such as in a ducted fan configuration, then the rotating parts would not be exposed.”
FAA-provided MOC

## Slide 6: Background II: Reich Collision Risk Model
The Reich Collision Risk Model was developed to assess safety assessment for the North Atlantic Reduced Longitudinal Separation Minimum (RLongSM) project by providing a collision risk estimation.
Avg. relative passing speeds
Why the Reich model is not suitable for UTM at the current stage:
Requires adequate and representative traffic data to derive probabilistic distributions
Performs effectively only with parallel routes over extended ranges

## Slide 7: Background III: ASTM UTM USS Specification
ASTM F3548-21

## Slide 8: Outline
Background
  Method of Compliance
  Reich Collision Risk Model
  ASTM USS Specification
Method of Compliance for Strategic Coordination Services
  Baseline ASTM requirements
  Volume-based Collision Risk Model
  Flow Diagram: test harness and data collection
Sensitivity Analysis
Conclusions and Future Work

## Slide 9: Baseline ASTM Requirements
"Operational intents shall (OPIN0010) be constructed such that the UA’s actual position is inside an operational intent in the Activated state at least 95 percent of total flight time.”
Strategic Conflict Detection (SCD)
Operational Intent Conflict, not permitted
Operational Intent Conflict, permitted
"A managing USS shall (SCD0035) verify that before transitioning an operational intent to the Accepted state, it does not conflict with an equal priority operational intent when the regulation does not allow conflicts within the same priority level."
Method of Compliance
Operational Intent Creation and Modification (OICM)

## Slide 10: Outline
Background
  Method of Compliance
  Reich Collision Risk Model
  ASTM USS Specification
Method of Compliance for Strategic Coordination Services
  Baseline ASTM requirements
  Volume-based Collision Risk Model
  Flow Diagram: test harness and data collection
Sensitivity Analysis
Conclusions and Future Work

## Slide 11: Volume-base Collision Risk Model
Rectangular intent
Rectangular intent
What is the UA-UA collision risk?

## Slide 12: Volume-base Collision Risk Model: Collision Risk between Elliptical Shapes
Elliptical intent
Elliptical intent
Combined elliptical intent
Circular collision zone
Combined circular intent
Elliptical collision zone

## Slide 13: Volume-base Collision Risk Model: Collision Risk between Rectangular Cuboids
Rectangular intent
Rectangular intent
Circumscribed
elliptical intent
Inscribed elliptical intent
Circumscribed
elliptical intent
Inscribed elliptical intent
Lower bound of the collision risk
UA-UA collision risk
Upper bound of the collision risk

## Slide 14: Volume-base Collision Risk Model: Example

## Slide 15: Outline
Background
  Method of Compliance
  Reich Collision Risk Model
  ASTM USS Specification
Method of Compliance for Strategic Coordination Services
  Baseline ASTM requirements
  Volume-based Collision Risk Model
  Flow Diagram: test harness and data collection
Sensitivity Analysis
Conclusions and Future Work

## Slide 16: Flow Diagram: MOC for the Strategic Coordination Services
ASTM requirement
[OPIN0010]
OiMinConformance = 95%
[OPINxxxx]
Distribution Type = Normal
Volume-based Collision Risk Model
Test case
UA-UA collision risk
Volume-based Collision Risk Model
Strategic Conflict Detection Service
(target)
UA-UA collision risks
< TLS?
Fail
Pass
Operational/testing data
Conformance Data
Assumptions
New OPIN requirement
New SCD requirement
OIs are required not to conflict with each other
Test cases

## Slide 17: Outline
Background
  Method of Compliance
  Reich Collision Risk Model
  ASTM USS Specification
Method of Compliance for Strategic Coordination Services
  Baseline ASTM requirements
  Volume-based Collision Risk Model
  Flow Diagram: test harness and data collection
Sensitivity Analysis
Conclusions and Future Work

## Slide 18: Impact of Different SC Services
Deconflict without buffer
(Collision risk = 3.2x10-6)
Deconflict with buffer
(Collision risk = 7.5x10-7)
100 ft
4000 ft
3000 ft
100 ft
500 ft
Collision zone
R=10 ft
60 s
45o

## Slide 19: Impact of Layout of Operational Intents
100 ft
4000 ft
Collision zone
R=10 ft
100 ft
4000 ft
100 ft
Deconflict without buffer
(Collision risk = 2.1x10-4)
Deconflict with buffer
(Collision risk = 5.7x10-8)

## Slide 20: Impact of Operational Intent Size: larger intents
Deconflict without buffer
(Collision risk = 4.36x10-6)
500 ft
4000 ft
3000 ft
500 ft
Collision zone
R=10 ft
60 s
Deconflict with a 500-ft buffer
(Collision risk = 1.4x10-6)
500 ft

## Slide 21: Impact of Operational Intent Size: smaller intents
Deconflict without buffer
(Collision risk = 1.12x10-5)
Deconflict with buffer
(Collision risk = 4.48x10-7)
100 ft
2000 ft
1500 ft
100 ft
500 ft
60 s
45o

## Slide 22: Conclusions
An MOC for Strategic Coordination services is developed for nominal situations
An SCD service needs to include dynamic extra buffers
Test cases in the test harness need to consider the layout and size of operational intent volumes, as they play important roles in risk assessment
When the operational tempo is high, the SCD service reduces the tempo to mitigate the collision risk.
This MOC can serve as a proof while providing guidance on test harness and data collection.

## Slide 23: Future work
Strategic Conflict Detection (SCD)
Operational Intent Conflict, not permitted
Operational Intent Conflict, permitted
Method of Compliance
Method of Compliance
Off-nominal situations
Method of Compliance
Conformance Monitoring for Situation Awareness(CMSA)