## Slide 1: Random Micron Surface Roughness Effects on Swept Wing Boundary Layer Transition
Jenna Eppink
NASA Langley Research Center

## Slide 2: Experiment Setup
Panel | RMS (μm) | Peak-to-peak (μm) | Correlation length (μm)
Baseline | 0.42 | 1.79 | 822
TP1 | 8.64 | 39.36 | 172
TP2 | 4.78 | 20.68 | 384
TP3 | 13.93 | 66.21 | 92
TP4 | 16.92 | 65.85 | 317
TP5 | 8.78 | 20.84 | 876
Roughness panels of varying nano-particle formulations were fabricated and measured.
Testing was performed in the 2’x3’ Low Speed Tunnel.
PIV measurements were performed to capture the stationary crossflow amplitudes.
A three-axis traverse system was used to build up spanwise planes at various streamwise positions.
Wavelength Pre-multiplied Spectra

## Slide 3: Results
The results do not indicate a clear correlation between roughness RMS and stationary crossflow initial amplitudes.
No obvious correlation was observed between wavelength content and stationary crossflow mode wavenumber distributions.
More advanced roughness characterization is needed.
Stationary Crossflow Amplitudes
Baseline
TP1
TP5
TP4
TP3
Roughness RMS vs. Estimated Initial Amplitude (λ=8 mm)