## Slide 1: GPS Multipath Emulation using Software Generated Signals
Russell Gilabert, Julian Gutierrez, and Evan Dill
NASA Langley Research Center
DASC 2024
San Diego, CA
October 2nd, 2024

## Slide 2: Outline
Background
Experimental Setup
Results
Conclusions
Future Work

## Slide 3: Background
GPS works very will in open environments
However, performance can significantly degrade in urban areas
  Buildings block and reflect signals
    Reduced availability
    Multipath
This can be the largest error contributing to GPS performance
Urban Canyon

## Slide 4: Background
Fundamentally, GPS works by multilateration
GPS 101

## Slide 5: Background
Fundamentally, GPS works by multilateration
Each satellite broadcasts a stream of known Pseudo-Random Numbers (PRN)
Receivers compare this to a local stream to determine the range measurement
Under ideal circumstances, this give a sufficient range estimate*
101101011101000101001110101110101110001010001
101101011101000101001110101110101110001010001
Broadcast PRN
Receiver PRN
On Time
GPS Correlator
11010001010011101011101011

## Slide 6: Background
Multipath of the signal skews this measurement
On Time
101101011101000101001110101110101110001010001
Broadcast PRN
101101011101000101001110101110101110001010001
Bounce 1
101101011101000101001110101110101110001010001
Bounce 2
GPS Correlator

## Slide 7: Background
Multipath of the signal skews this measurement
The receiver correlates on the composite of the measurements it receives
Varies greatly depending on conditions
On Time
Delayed
101101011101000101001110101110101110001010001
Receiver PRN
101101011101000101001110101110101110001010001
Broadcast PRN
101101011101000101001110101110101110001010001
Bounce 1
Bounce 2
101101011101000101001110101110101110001010001
GPS Correlator

## Slide 8: Background
Simulation of multipath using generated signals can:
  Enable testing of receiver multipath resistance
  Gain insight on receiver’s operational limitations and behavior
  Assist in developing multipath mitigating technologies
Commercial GPS simulators exist but:
  Can be expensive
  Offer limited out-of-the-box tuning capabilities
Can cheaper, open-source tools be modified to add this capability?
GPS Simulation

## Slide 9: Experimental Setup
11010001010011101011101011
GPS Signal Generation
GPS-SDR-SIM
Open-source command line tool that allows the user to generate GPS signals
  Input: ephemeris (satellite orbits), coordinates
  Output: binary file containing the generated signals
Generates a binary file of simulated RF data that a GPS receiver would see if at that location
Can be played back on a real or software receiver
Modifications
Added the ability to:
  Clone satellite PRN’s
  Delay PRN by variable amount
Simulate composite multipath signal
On Time
Delayed

## Slide 10: Experimental Setup
GPS Receiver Simulation
GNSS-SDR
Open-source software to implement software defined GNSS receiver
  Input: binary file containing the generated signals
  Output: position estimate, RINEX observables
Can read .bin files of RF data that can be processed in software to generate pseudorange measurements and compute a solution
GNSS
SDR

## Slide 11: Experimental Setup
Overall Simulation Workflow
Input
RINEX Navigation File
Desired Position
Processing
GPS-SDR-SIM
with Modifications
GNSS-SDR
Output
RINEX Observation File
Position Solution
RINEX
Navigation File

## Slide 12: Experimental Setup
Test Scenarios
Various scenarios tested to validate the added GPS-SDR-SIM capabilities:
  Delayed signal
  Synchronous signal
  Multipath signal
G01
On Time
Delayed

## Slide 13: Experimental Setup
Test Scenarios
On Time
Delayed
G02
Various scenarios tested to validate the added GPS-SDR-SIM capabilities:
  Delayed signal
  Synchronous signal
  Multipath signal
Another satellite was placed in a matching orbit to compare results
G01

## Slide 14: Experimental Setup
Test Scenarios
Various scenarios tested to validate the added GPS-SDR-SIM capabilities:
  Delayed signal
  Synchronous signal
  Multipath signal
Another satellite was placed in a matching orbit to compare results
G01/G02
Tested using GNSS-SDR as the receiver
On Time
Delayed

## Slide 15: Results
Delayed Signal
20m delay on G01
No G01 cloned broadcast
Compared against G02 in same orbit

## Slide 16: Results
Delayed Signal
20m delay on G01
No G01 cloned broadcast
Compared against G02 in same orbit
Average measured delay of 20.089m

## Slide 17: Results
Delayed Signal
20m delay on G01
No G01 cloned broadcast
Compared against G02 in same orbit
Average measured delay of 20.089m

## Slide 18: Results
Synchronized Signal
0m delay on G01
0m delay on G01 cloned broadcast
Compared against G02 in same orbit

## Slide 19: Results
Synchronized Signal
0m delay on G01
0m delay on G01 cloned broadcast
Compared against G02 in same orbit
Average measured delay of 0.208m

## Slide 20: Results
Synchronized Signal
0m delay on G01
0m delay on G01 cloned broadcast
Compared against G02 in same orbit
Average measured delay of 0.208m

## Slide 21: Results
Multipath Signal
0m delay set on G01
20m delay on G01 cloned broadcast
Compared against G02 in same orbit

## Slide 22: Results
Multipath Signal
0m delay set on G01
20m delay on G01 cloned broadcast
Compared against G02 in same orbit
Average measured delay of 10.198m
0m 10m 20m

## Slide 23: Results
Multipath Signal
0m delay set on G01
20m delay on G01 cloned broadcast
Compared against G02 in same orbit
Average measured delay of 10.198m
0m 10m 20m

## Slide 24: Conclusions and Future Work
Conclusions
The modifications to GPS-SDR-SIM appear to be successful
Can duplicate PRN’s and add arbitrary bias
Overlapping signals introduce delay at receiver
Simulation confirms the multipath generation proof of concept
Future Work
Explore fast changing/variable rate multipath
Assess performance on GPS hardware receiver
Evaluate behavior of the receivers under a variety of multipath conditions
G01/G02

## Slide 25
Thanks!
Any questions?