## Slide 1
Quesst Mission and the X-59 Aircraft
Briefing for the Senior Capstone Design Class
Department of Mechanical and Aerospace Engineering
University of Virginia
“Converting customer needs to mission objectives and design requirements”
Craig Nickol NASA Langley Research Center
9/17/24
www.nasa.gov

## Slide 2: Presentation Topics
X-Planes
Customer Need: Barriers to Commercial Supersonic Flight
Sonic Boom 101
Requirements Development Process
X-59 Early Concept Evolution
Mission Overview
X-59 Aircraft Development
Current status
Illustration Credit: Lockheed Martin
www.nasa.gov

## Slide 3: X-Planes
Notes: Image credit: www.3djake.com/revell/bell-x-1-1rst-suipersonic, circa 1946

## Slide 4: X-Planes
Notes: Image credit: https://www.smithsonianmag.com/air-space-magazine/x-15-walkaround-22512890/
Circa 1959

## Slide 5: X-Planes
Notes: Image credit: https://en.wikipedia.org/wiki/Grumman_X-29
Circa 1984

## Slide 6: X-Planes
Notes: Image credit: https://en.wikipedia.org/wiki/Rockwell-MBB_X-31
1990

## Slide 7: X-Planes
Notes: Image credit: https://en.wikipedia.org/wiki/Lockheed_Martin_X-35
2000

## Slide 8: X-Planes
https://www.youtube.com/watch?v=DPd0OHrmCBc

## Slide 9
First supersonic flight: 1947
Introduction of supersonic commercial transports in 1970s brought the problem of sonic boom noise to public attention & showed sonic boom noise to be unacceptable
Supersonic overflight restrictions followed
  US: FAA Regulation (FAR) prohibits supersonic flight over US
  Worldwide: ICAO Assemble Resolution – “No unacceptable situation for the public due to sonic boom”
Restriction dramatically limited market potential for supersonic commercial flight
The creation of a market for supersonic commercial aircraft requires eliminating sonic boom as a barrier to overland flight
Barriers to Commercial Supersonic Flight
Sonic Boom Noise and Overland Flight Prohibitions
www.nasa.gov
Notes:                 New technology and design approaches are required to reduce or eliminate the noise from sonic boom
                An international certification standard based on acceptable sound levels must be developed to replace current overflight restrictions
1947 – Supersonic flight
1964 – Community study
1973 – Federal ban
2003 – Shaped Sonic Boom
2016 – Design of LBFD
2023 – LBFD community response test

## Slide 10: Vision for Commercial Supersonic Flight
An emerging potential market has generated renewed interest in civil supersonic aircraft
Evidenced by the appearance of several commercial programs despite lack of standards for en route noise or landing and takeoff noise, emissions
The vision of the Supersonics Community is a future where fast air travel is available for a broad spectrum of the traveling public.
Future supersonic aircraft will not only be able to fly overland without creating an “unacceptable situation” but will also be environmentally responsible, affordable and sustainable
Overland Flight Restrictions based on unacceptable sonic boom noise are viewed as the main barrier to this vision
Illustration Credit: Lockheed Martin
NASA plays a vital role in developing technology and the data that will enable this transformative new market
www.nasa.gov

## Slide 11: Overcoming the Barrier to Overland Supersonic Flight
New Environmental Standards are needed to open the market to supersonic flight
An En route Noise Standard is the biggest challenge
  Requires proof of new design approaches
  Must replace current prohibitions
  No relevant data exists to define limits
    Community data from large, diverse population is a requirement
  Standard must be accepted internationally
NASA’s Quesst Mission is specifically planned to generate key data supporting the development of en route certification standards based on acceptable sound levels
Illustration Credit: Lockheed Martin
www.nasa.gov

## Slide 12: SONIC BOOMS
NASA IS TURNING A BOOM INTO A THUMP

## Slide 13: What Makes a Sonic Boom?
Conical shock wave produces sonic boom at ground which moves with the airplane
Boom is created over entire length of supersonic flight path, just as a boat wake is continuous
Shock front
www.nasa.gov

## Slide 14: Sonic Boom Explained
Sonic Boom With Atmospheric Effects
Boom Signature Carpet

## Slide 15: Sonic Boom Basics
N-Wave Sonic Boom
Shaped Pressure Signal
www.nasa.gov

## Slide 16: NASA/DARPA Shaped Sonic Boom Demonstration (SSBD) Project 2003
Back-to-Back Flights of Modified and Unmodified F-5s
F-5SSBD
F-5E
Design
Flight Results
First-Ever Shaped Sonic Boom Recorded 27 August 2003
Notes: Chart from Tom Jones EAA AirVenture brief in Oshkosh, WI, July 28, 2017

## Slide 17
-
0.02
-
0.015
-
0.01
-
0.005
0
0.005
0.01
0.015
0.02
0.025
-
5
0
5
10
15
20
25
X
-
b
r (inches)
Comparison of Pre-test CFD and Wind Tunnel Measurements @ CL = 0.142
Pre-test CFD
Measured Data
Modern Design Tools are Ready for Shaped Boom Design (Tip to Tail)
CFD
Experiment
Why Now for X-59?
Notes: X-beta*r is a coordinate transformation; Same x location half a body length is the same at the ground
Chart from Tom Jones EAA AirVenture brief in Oshkosh, WI, July 28, 2017

## Slide 18: Why do we think the “Thump” is quiet enough?
Tests of increasing complexity have provided preparation and confidence
Ready to take the next step with flight testing over very large communities
Indoor human response and annoyance is the main concern for public acceptance
Laboratory Tests
Small Community Tests
Large Community Risk Reduction
Quiet Supersonic Flights 2018
Galveston, Texas

## Slide 19: Sonic Thump
www.nasa.gov
Notes: NASA's single-seat X-59 experimental aircraft will produce a barely audible sonic thump to people on the ground when cruising at supersonic speeds. In technical terms, the X-59's sonic thump will be around 75 Perceived Level decibels (PLdB) or less. PLdB is one of numerous scales, in decibels, that is used to understand human response to sounds and is used particularly for short duration sounds. Proving a sonic boom can be reduced to a sonic thump could enable a new fleet of quiet, commercial supersonic aircraft that can fly over land.
Additional detail if more technical audience: AESL metric uses a reference window of 1 sec. LAFmax metric (A-weighted, Fast, Sound Level) uses a reference window of 125 msec that tends to be more representative of rapid events like a sonic boom. For this comparison, PLdB will be compared to LAFmax metric which is the most representative comparison.
Aircraft ASEL (dB) LAFmax (dB) PL (dB)
Concorde 94 101 109
F-18 87 94 102
Demonstrator 60 66 75

## Slide 20: Introduction – Where did X-59 come from?
Answer: a lot of hard and excellent work by a lot of people! See “Brief History of Boom Reduction” in backup charts.
“Continuity of effort drives revolutionary achievement” Peter Coen
LBFD Concept Formulation Study
(CFS)
LBFD Concept Refinement Study
(CRS)
QueSST Preliminary Design
Mission Concept Review (MCR)
Mission Design Review (MDR)
Concept Development
Systems Requirements & Design Review (SRDR)
Aircraft Systems Requirements Review (ASRR)
Pre-Phase A
Concept Studies
Phase A
Concept & Technology Development
Phase B
PD & Technology Completion
NPR 7120.5 Project Phase
Preliminary Design Review (PDR)
MCR 9/2013
MDR 3/2014
SRDR 9/2015
ASRR 6/2016
KDP A/B 8/2016
PDR 6/2017
~$4M (Task
orders only)
~$10M (Task orders only)
KDP A/B
FY 17
$20.9M
(Task Order Base Effort)
The team did their homework which resulted in:
  Well grounded, concise and feasible requirements
  Government and industry teams with experience and understanding of the technical baseline
  Cost, schedule, and risk products to assist with full scale development planning

## Slide 21: Quesst Timeline
www.nasa.gov
Phase 2 – Acoustic Validation
Detailed ground and flight measurements
Validation of sonic boom signature and prediction tools
Phase 3 – Community Response
Community response overflights, ground measurements, and surveys over representative communities across the U.S.
Phase 1 – X-59 Aircraft Development
Aircraft design, fabrication, and ground test
Checkout and envelope expansion
First Flight 2024
2025
2026
Systematic Approach Leading
to Community Testing
Credit: Lockheed Martin
Credit: Lockheed Martin
Notes: Phase 1 Image
The X-59, unwrapped after transport back to Lockheed Martin’s Skunk Works facility in Palmdale, California, will now undergo final integration.
Credits: NASA/Lauren Hughes
Phase 2 Image
Juliet Page, a physical scientist with the Volpe National Transportation Systems Center, calibrates a microphone station during the CarpetDIEM flight series. The array featured high-fidelity microphones arranged in several configurations, giving researchers the ability to obtain accurate sound data and assess the loudness of the sonic booms, just as they will measure the quiet sonic thumps from the X-59.
Credits: NASA Photo / Lauren Hughes
Phase 3 Image
Suburb of the USA, filmed from a height, trees and houses.
Credits: Getty Images

## Slide 22: Requirements Flow for Preliminary Design
Level
1
2
3
Concept of Operations
Aircraft Specification and System Requirements Documents1, 2
Mission and Airworthiness Certification Requirements
NASA Airworthiness Criteria (NAC)1
Community Response Objectives (CST Project)
Aircraft Requirements and Assumptions (ARA)1
LBFD Needs, Goals and Objectives
4
Airworthiness Requirements and Criteria1, 2
Contractor Requirements,
Criteria and Specifications
NASA Requirements,
Criteria and Specifications
Assumptions1,2
Flight Systems
Aircraft Operations
Range Support
Systems Integration
and Testing
1Mutually agreed upon and consolidated during technical meetings (PDR, CDR, …)
2Contractor controlled documents with NASA review/approval
Interface Control Documents (ICDs)
Mission Level Requirements
Documents
Requirements,
Criteria and Specifications
Safety and Mission Assurance
Ground Support
Project
Plan

## Slide 23: Level 1: Needs, Goals, and Objectives
CST Objective / LBFD Need | LBFD Goals | LBFD Objectives
CST-Objective 1 – Conduct an initial low-noise sonic boom acoustic validation and community response overflight study to: 1) validate the community response test design and 2) establish community acceptance of the LBFD sonic boom signature noise level. | LBFD-Goal 1 – Design and build a LBFD aircraft with low-noise sonic boom signature characteristics acceptable to communities and traceable to future civil supersonic airliners. | LBFD-Objective 1 – Apply low-noise sonic boom design tools and technologies to design a LBFD aircraft that meets the LBFD mission and airworthiness certification requirements.
 |  | LBFD-Objective 2 – During Phase 1, build a LBFD aircraft and conduct the LBFD first flight within the baseline project budget and schedule.
 |  | LBFD-Objective 6 – During Phase 3, the LBFD aircraft shall perform the baseline mission with standard day environmental conditions using hydro-processed renewable jet fuel blends (JP-8/HRJ).
 | LBFD-Goal 2 – Acquire sonic boom signature data that will validate low-noise sonic boom design theory and improve the understanding and prediction of atmospheric effects on low-noise sonic boom signatures. | LBFD-Objective 3 – During Phase 1, demonstrate that the LBFD aircraft meets the LBFD airworthiness certification, safety, and performance standards throughout the flight envelope.
 |  | LBFD-Objective 4 – During Phase 2, measure and validate: 1) the near-field acoustic characteristics of the LBFD aircraft and 2) the atmospheric effects on the far-field and ground sonic boom signatures.
 | LBFD-Goal 3 – Demonstrate that the LBFD aircraft will produce a predictable range of low-noise sonic boom signatures appropriate for community response testing. | LBFD-Objective 5 – During Phase 2, conduct an initial low-noise sonic boom acoustic validation and community response overflight study to: 1) validate the community response test design and 2) establish acceptable sonic boom signature noise levels based on community response.

## Slide 25: Systems Engineering “V”

## Slide 26: X-59 Evolution – Early Concepts to Final Design
www.nasa.gov
C610 C611 C612
Concept Formulation
Concept Refinement
Preliminary Design
Detail Design
Illustration Credit: Lockheed Martin
Notes: NASA's single-seat X-59 experimental aircraft will produce a barely audible sonic thump to people on the ground when cruising at supersonic speeds. In technical terms, the X-59's sonic thump will be around 75 Perceived Level decibels (PLdB) or less. PLdB is one of numerous scales, in decibels, that is used to understand human response to sounds and is used particularly for short duration sounds. Proving a sonic boom can be reduced to a sonic thump could enable a new fleet of quiet, commercial supersonic aircraft that can fly over land.
Additional detail if more technical audience: AESL metric uses a reference window of 1 sec. LAFmax metric (A-weighted, Fast, Sound Level) uses a reference window of 125 msec that tends to be more representative of rapid events like a sonic boom. For this comparison, PLdB will be compared to LAFmax metric which is the most representative comparison.
Aircraft ASEL (dB) LAFmax (dB) PL (dB)
Concorde 94 101 109
F-18 87 94 102
Demonstrator 60 66 75

## Slide 27
X-59 Aircraft 3-View
Illustration Credit: Lockheed Martin
www.nasa.gov

## Slide 28
F-16 landing gear and other systems from high performance aircraft to minimize qualification cost and schedule
Overview of X-59 Aircraft Features
Fixed canard for nose-up trim at low-boom design point
T-38 aft canopy and ejection seat to minimize qualification cost and schedule
Large, unitized skins reduce parts count and manufacturing cost
Long nose to shape forward shock
Wing shielding to minimize impact of inlet spillage on sonic boom
External and forward visions systems for forward visibility
Single GE-F414 engine with standard nozzle to minimize cost and schedule
T-tail to minimize aft shock
Conventional tail arrangement to simplify stability and control considerations
X-plane approach that meets key requirements in a cost-effective design
Design Parameters
Length: 99 ft
Span: 29.5 ft
Speed: Mach 1.4 (925 mph)
Altitude: 55,000 ft
Illustration Credit: Lockheed Martin
www.nasa.gov

## Slide 29: X-59 QueSST Design
T-38 Rear Cockpit and Canopy Utilized on X-59
Saves Qualification and Testing Costs
X-59
NASA T-38
Notes: Slide from Brett Pauer SAFE Symposium Presentation, October 17, 2018 (Approved for Public Release – NASA DAA 61775)

## Slide 30: X-59 Aircraft Assessments
Credit: Lockheed Martin Corporation
Aerodynamic Performance
Handling Qualities
Structural Modeling
Sonic Boom
www.nasa.gov

## Slide 31: Wind Tunnel Validations
Low-and high-speed aerodynamic and Propulsion Airframe Interaction (PAI) wind-tunnel tests validate predictions and ensure readiness of the design
Photo Credit: Lockheed Martin
Photo Credit: Lockheed Martin
www.nasa.gov

## Slide 32
High Fidelity Computational Results (CFD)
Prediction Tools and Validation
In preparation for community response testing, NASA is creating a suite of prediction tools to support timely and accurate validation of the acoustic performance of the X-59 aircraft, rapid pre-flight exposure planning for Community Testing, and provide a foundation for future configuration design and certification analysis of supersonic aircraft.
Sonic Thump on the Ground
(75 PLdB Target)

## Slide 33: Acoustic Validation Test Planning and Execution
F-15 With Shock Sensing Probe
Advanced Air-Air Schlieren Imaging
Ground Recording Systems
Flight Planning
Plan and execute a test series to validate ground acoustic signature loudness is acceptable for community response testing and to gather airborne and ground data that will be used to anchor sonic boom propagation and acoustics models in a real atmosphere. Coordinate multiple ground and flight assets to efficiently gather multiple data types.

## Slide 34: Community Test Planning and Execution
Airfield and Community Selection
Survey Design and Analysis
Flight and Test Planning
Exposure Estimation
Community Engagement
Dose-Response Relationship
Plan and execute sonic boom tests with the X-59 aircraft over large non-experienced communities within the U.S. to provide a robust dose-response database of community annoyance
https://www.dreamstime.com/179235021
Image Credits: HMMH

## Slide 35: Manufacturing: First Chip Ceremony, November 13, 2018

## Slide 36: X-59 – Early Aircraft Fabrication and Integration
Photo credits: Lockheed Martin
Photo Credits: Lockheed Martin
www.nasa.gov

## Slide 37: X-59 Aircraft Fabrication and Integration
Photo Credits: Lockheed Martin (left and top right)
Photo Credit: General Electric
www.nasa.gov

## Slide 38: X-59 Aircraft Ground Testing in Ft. Worth
Preparing the Aircraft for Structural Testing
The Long Journey
Photo Credits: Lockheed Martin
www.nasa.gov

## Slide 39: X-59 Aircraft Ground Testing in Ft. Worth
Fuel Systems Testing
Structural Testing
Photo Credits: Lockheed Martin
www.nasa.gov

## Slide 40: System Installations and Checkouts
Photo Credits: Lockheed Martin
www.nasa.gov

## Slide 41: eXternal Vision System (XVS)
System components qualified for flight environment – imagery integrated with HUD symbology
System performance verified in flight test - guest pilots evaluated normal vision and XVS on see-to-avoid and see-to-follow tasks
Final component qualification, installation, and ground checkout in the X-59 aircraft completed
View of X-59 Cockpit with
XVS Image with HUD Symbology
Forward Vision System (bottom)
XVS Display
XVS Computer
XVS 4K Camera
(top)
XVS - enabling technology - combination of Ultra-High-Definition (UHD) sensor, display, and image processing technologies to provide the pilot with equivalent forward vison
www.nasa.gov
Notes: FVS - Enhanced Vision System (EVS) camera
XVS Processor takes inputs from the 2 camera systems and state/traffic/surveillance data (ADS-B, TCAS)

## Slide 42: X-59 Life Support and Crew Escape Systems
Hypobaric Chamber Testing
Photo Credit: KBR
Ejection Seat System
Canopy
System
  The Life Support System (LSS) provides the pilot with breathing oxygen at the right pressure, flowrate, and concentration to maintain the pilot’s well-being in any scenario, from normal flight missions to in-flight emergencies. Key components of this system were tested in a hypobaric chamber to simulate reduced pressure conditions that the pilots could experience at the higher altitudes.
NASA has worked with hardware vendors to ensure pilot safety by providing the hardware, checkout, and certification of the X-59 aircraft life support and crew escape systems
  The Crew Escape System (CES) provides the pilot with an integrated ejection seat and canopy systems to ensure pilot safety during normal and emergency flight and ground scenarios.
Credit: Martin Baker
www.nasa.gov
Notes: FVS - Enhanced Vision System (EVS) camera
XVS Processor takes inputs from the 2 camera systems and state/traffic/surveillance data (ADS-B, TCAS)

## Slide 43: X-59 Cockpit Simulations
Aircraft and cockpit simulations validate aircraft designs, systems, and performance – also used for pilot training and flight planning
Credit: Lockheed Martin Corporation
www.nasa.gov
Photo Credit: Lockheed Martin
Systems Integration Lab at Lockheed
Flight Simulator at NASA

## Slide 44: Control Room Preparations and Training
Control room preparations and display development have matured over the past year. Control room familiarization and training using the X-59 aircraft simulator to emulate flight operations and key sensor data has begun. Control room training is essential to ensure safe flight test and training for nominal and potential less-than-nominal scenarios.
Credit: Lockheed Martin Corporation
www.nasa.gov

## Slide 45
Photo Credit: Lockheed Martin
www.nasa.gov
Photo Credit: Lockheed Martin
Integrated Testing Outdoors, Run Stall 5 – August 2023
www.nasa.gov

## Slide 46
Photo Credit: Lockheed Martin
www.nasa.gov
Photo Credit: Lockheed Martin
X-59 Aircraft Rollout – January 2024

## Slide 47: Next Steps
Engine runs
Emergency engine restart system test
Electromagnetic Interference (EMI) test
Aircraft-in-the-loop integrated system testing
Low speed and high-speed taxi testing
First Flight

## Slide 48
Photo Credit: Lockheed Martin
www.nasa.gov
Quesstions?
Photo Credit: Lockheed Martin

## Slide 49: nasa.gov/quesst
www.nasa.gov