## Slide 1
Space Technology Mission Directorate
Game Changing Development Program
Caleb Adams, Distributed Spacecraft Autonomy (DSA) | Annual Program Review | September 10-12, 2024
Notes: Please provide pictures specific to your Project for each circle in this coversheet
Please make sure the pictures are Publicly Available and have been cleared by your Center

## Slide 2: Distributed Spacecraft Autonomy Overview
Needs Addressed by Project | 
GCD | Completion of project goals and objectives on time and in budget
SSTP | Demonstration of distributed autonomous technologies with small spacecraft
Project Goals | 
Goal #1 | Advance command and control methodologies for controlling a distributed space system as a single entity.
Goal #2 | Develop, mature, and demonstrate autonomous coordination between multiple spacecraft in the distributed space system.
Goal #3 | Develop, mature, and demonstrate approaches for adaptive reconfiguration and distributed decision-making across a distributed space system.
Project Objectives | 
Objective #1 | The DSA Project shall develop software to control a distributed space system.
Objective #2 | The DSA Project shall perform a technology demonstration of distributed space system software in flight.
Objective #3 | The DSA Project shall demonstrate the scalability of the distributed space system software in a simulation environment.

## Slide 3: Distributed Spacecraft Autonomy TRL Chart
FY19 | FY20 | FY21 | FY22 | FY23 | FY24 | FY25
3
Project Milestone
GCD (Key) Milestone
Controlled Milestone
TRL/SRL/MRL Progression
TRL
6
5
4
3
2
1
Project
Start
Network Communication
Commanding of the swarm as one entity
Ground interaction through one swarm asset
7
Closed-loop control by the swarm
Adaptive reconfiguration by distributed planning
PDR
CDA
Final
Launch
Final Report & Review
Release 1
Release 2
Release 3
Release 4
Release 6
Release 5
Coordination between multiple assets in the swarm
Release 7
Bathtub Period
Notes: Chart purpose: show TRL/SRL/MRL advancement over the project lifecycle schedule. Show TRL advancements as whole integer increases. Show how Key and Controlled milestones align with TRL advancement.
  TRL/SRL/MRL may not advance at each milestone. Often several milestones are required to produce a step increase in TRL/SRL/MRL.
There can be one, or more, of these charts per project as needed.
  For projects with fewer technical elements, the TRL/SRL/MRL data can be combined on one chart.
  For more complex projects, the TRL/SRL/MRL progression can separated into multiple charts by project technical area.
Show TRL, SRL, and MRL data for each technical element on the same chart.
  Delete TRL/SRL/MRL axis-labels that do not apply – e.g., remove SRL/MRL for projects/technical areas where SRL and MRL do not apply.

## Slide 4: Distributed Spacecraft Autonomy Technical Progress and Results

## Slide 5: Distributed Spacecraft Autonomy Technical Progress and Results
DSA-Starling represents the first demonstration of a fully autonomous distributed space mission. Specifically, DSA-Starling accomplished the following:
  First fully distributed autonomous operation of multiple spacecraft.
  First use of space-to-space communications to autonomously share state information between multiple spacecraft.
  First demonstration of fully distributed reactive operations onboard multiple spacecraft.
  First use of a general-purpose automated reasoning system onboard a spacecraft.
  First use of fully distributed automated planning onboard multiple spacecraft.

## Slide 6: Distributed Spacecraft Autonomy Technical Progress and Results
DSA-Starling consistently established a 3-spacecraft cross-link network
DSA’s Data Distribution Service (DDS)
Selected time from EP Sequence number 25 day 1:
  Grey is missing data at the time of analysis
  All spacecraft connect to network
  Accumulated telemetry packets demonstrate healthy network status

## Slide 7: Distributed Spacecraft Autonomy Technical Progress and Results
DSA Software is operating at 1Hz
Agents compute optimal plans locally from latest shared state information
Everyone solves the same optimization problem… does everyone get the same answer?
  Same answers: Consensus
  Different answers: non-consensus
Consensus is lost for a few valid reasons:
  One spacecraft sees something no one else does
  Communications delays
  Crosslink failures
Consensus lost
Spacecraft 3 covers GPSID 22 instead of 21.

## Slide 8: Distributed Spacecraft Autonomy Technical Progress and Results
  Max lag time was 46 seconds
  AVG time to recon 2.04 seconds
    Project Goal: 5 mins  we did way better
  Trade space:
    Need a fast response? Accept some non-consensus
    Need global consensus? Accept a slower response

## Slide 9: Distributed Spacecraft Autonomy Technical Progress and Results
DSA given pre-scheduled 2-day segments of runtime, called Experiment Periods (EP)
Failure was high in early attempts
  DSA ran on orbit only 16/28 (57.14%) on EP Opportunities
Success was high in the end
  80% of the last 5 runs successful
Success after Starling Platform Stability was 86.7%
Notes: We defined a successful run as the following:
• The DSA mission produced an outcome or delivered a product for execution on orbit.
• The DSA mission successfully ran on orbit and results were delivered.
• This increased the mission’s likelihood of meeting full success.
We define a loosely successful run as the following:
• The DSA mission missed an opportunity but was not set back according to our operational schedule.
• This did not change the mission’s likelihood of meeting full success.

## Slide 10: Distributed Spacecraft Autonomy Technical Progress and Results
KPP details in flight report
KPP 164: Date Uplink Reduction:
  Some uplink products required local commands
  Bus resets were occurring
  DSA only ran on 3 nodes
  A reduction of ~70% if run on all 4 nodes
KPP 165: Time to reconfiguration:
  Measurement of time until re-consensus
  Biggest success of DSA
KPP | State of the Art | Threshold | Project Goal | In Flight Results
Data Uplink Reduction ⬆️ | 50% | 66% | 75% | 49.3% - 61.3%
Time to reconfiguration ⬇️ | N/A | 22min | 5min | 2.04 – 6 seconds
Peer reviewed paper and detailed results:
Advancing Autonomy in Distributed Space Systems: Results From the Distributed Spacecraft Autonomy Experiment on Starling 1.0

## Slide 11: Distributed Spacecraft Autonomy Technical Progress and Results
Scalability Tested with Lunar Position, Navigation, and Timing (PNT) problem
Provide PNT to surface users
Assume non-dedicated assets
Limited resources and contacts
Scale two OoM (4 nodes to 100)
  Tested 24 and 60 nodes

## Slide 12: Distributed Spacecraft Autonomy Technical Progress and Results
Distributed Intelligent Spacecraft Simulation Test Rack (DISSTRACK)
LPNT algorithms validated and tested with 20-60 nodes on DISSTRACK (100 theoretical max)
100 flight-like computers
Build and test edge AI at scale
Complex Algorithms preempt mission design

## Slide 13: Distributed Spacecraft Autonomy Technical Progress and Results
Deployment times similar for incremental software updates
  Updating cFS tables
  Completely updating software (which is rare in I&T) does not scale
Timestamping is reliable across all currently tested nodes
  Usable for debugging
  NTP server may be considered in future
Localization method on 2-ISLs functions nearly as accurate as fully connected

## Slide 14: Distributed Spacecraft Autonomy Technical Progress and Results
DISSTRACK KPPs
KPP 43: Number of Homogeneous Spacecraft in Reactive Swarm
  Node stability significant issue
  Requiring 100% uptime of system for test was a technical blunder
  Recommend 5-10% buffer of extra nodes
KPP 166: Percent localization accuracy lost per node failure without intervention
  Planned to test with no-cost extension
KPP | State of the Art | Threshold | Project Goal | Test Rack Results
Number of homogeneous Spacecraft in reactive Swarm ⬆️ | 4 | 25 | 100 | 24 - 60
Percent localization accuracy lost per node failure without intervention ⬇️ | N/A | 50% | 25% | Not tested
DISSTRACK/LPNT work resulted in 4 peer reviewed publications

## Slide 15: Distributed Spacecraft Autonomy Transition/Infusion Status
Recently funded Ames CIF will use DSA Test Rack
DSA in discussion with SSTP regarding a DSA 2.0 Mission Concept
  Extend Autonomy into Scientific mission for TEC mapping (UCAR/NOAA/SSTP)
  Utilize existing DSA Comm App development
  Utilize autonomy matured on Starling 1.0
Additional funding from SSTP
  Opportunistic Software Experiments Satellite (OSE-SAT)
  OSE-SAT funded in FY24 (low cost)
  Utilizes DSA Comm App
  Utliizes DSA Scalability and Containerization
DSA 1.5 funded via SSTP through FY25
  Extended demonstrations of distributed autonomy on Starling

## Slide 16: <Project Name> Assessment Summary
Project Name | Performance |  |  |  | Comments
 | C | S | T | P | 
Annual | G | Y | G | G | Technical – Provide rationale for yellow and red color determination Cost – Schedule – Programmatic -
 | Oct | Nov | Dec | Jan | Feb | MYR | Apr | May | Jun | Jul | Aug | APR
C | G | G | G | Y | G | G | G | G | G | G | G | G
S | G | G | G | Y | G | G | G | G | G | G | Y | Y
T | G | G | G | G | G | G | G | G | G | G | G | G
P | G | G | G | G | G | G | G | G | G | G | G | G
If you had any reds or significant yellows throughout the year, please summarize the issue and how it was corrected, if applicable. If still an open issue, note what is needed to recover.