## Slide 1
PRE-LAUNCH ANALYSIS AND TEST OF THE OCEAN COLOR INSTRUMENT MODULATION TRANSFER FUNCTION
SPIE Sensors + Imaging
September 2024
SPIE Paper Reference 13192-17

## Slide 2: Modulation Transfer Function MTF
MTF is an evaluation of imaging performance that describes how well a system can resolve contrast within an image.
Mathematically, the Fourier Transform of an image response is the Optical Transfer Function (OTF)
  Each manipulation of the image can impact OTF
  OTF can go negative and represents a phase shift or aliasing, MTF is always positive
  The sum (Σ) effect of the MTF elements is the product of the Fourier transforms
MTF heads in one direction, down
  Design can limit its reduction but can not boost it back up
Chart: MTF
Chart: OTF

## Slide 3: OCI MTF Requirements
Fraction of Nyquist | Spatial Cycle Period | Requirement
0.0 | Uniform | 1.0
0.25 | 8 x GSD | 0.9
0.5 | 4 x GSD | 0.7
0.75 | 2.67 x GSD | 0.5
1.0 | 2 x GSD | 0.3
OCI MTF is specified in fractions of Nyquist
Nyquist for OCI is (GSD = 1.2km)
Cross track and along track MTFs are analyzed separately
1.2 km
1.2 km
Along Track
Cross Track Pattern
Nyquist Frequency
September 24
3

## Slide 4: OCI Design
Rotating telescope / half-angle mirror architecture
2 CCD spectrograph detectors (UVNIR)
  315-607 nm
  597-887 nm
Fiber fed multi-band SWIR detection assembly
  940, 1038, 1250, 1378, 1615, 2130, and 2260nm
September 24
4

## Slide 5: UVNIR MTF Networks
CCD Primary Contributors
Cross Track
  Image Velocity
  Jitter
Along Track
  Slit Size (effective pixel)
  Jitter
September 24
5

## Slide 6: SWIR MTF Networks
SWIR Primary Contributors
Cross Track
  MLA element size (effective pixel)
  Electronic Filtering
Along Track
  Slit Size (effective pixel)
  Jitter
September 24
6

## Slide 7: Pixel Size / MLA / Slit Contributions
  CCD pixels, SWIR MLA elements and slit opening are rectangular apertures
  Pixel / MLA / Slit similar analytically but different sizes / directions
*Pictures not to scale
September 24
7

## Slide 8: Image Velocity MTF
  Rectangular temporal aperture based on image displacement
Applicability to OCI
  This velocity happens for every pixel on the CCD in the TDI direction (x128)
  Conservative to assume TDI is instantaneous
  OCI sub-sampling ratio of 8:1 (CCD pixels : Science pixels)
  Relevant image displacement occurs at boundaries between science pixels
  Total image velocity represented by
GSD
September 24
8

## Slide 9: Electronics and Jitter MTF
Electronics MTFs
  Detectors, Low Pass Filters and Amplifiers all effect MTF
    Signal path through the electronics will vary the level or applicability in impact
  Effective 3dB frequency performance = , OCI MTF insensitive above 25kHz
Jitter MTF
  Movement occurring within a single integration period
  ;
  Jitter applicability
    Integration period =
    OCI sensitive to frequencies above 1.4 kHz
    Lower frequencies will manifest as a pointing error
September 24
9

## Slide 10: UVNIR MTF Analysis Results
Chart: UVNIR Cross-Track MTF
| 0 | 0.125 | 0.25 | 0.375 | 0.5 | 0.625 | 0.75 | 0.875 | 1 | 1.125 | 1.25 | 1.375 | 1.5 | 1.625 | 1.75 | 1.875 | 2
MTF RQMT | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3
Total | 1 | 0.98922 | 0.96386 | 0.92442 | 0.87269 | 0.81031 | 0.73959 | 0.66298 | 0.58424 | 0.50573 | 0.42988 | 0.35833 | 0.29321 | 0.23513 | 0.1846 | 0.14155 | 0.10607
Optics | 1 | 0.99662 | 0.99305 | 0.98868 | 0.98363 | 0.97732 | 0.96945 | 0.95947 | 0.94872 | 0.9369 | 0.92423 | 0.91012 | 0.89626 | 0.88196 | 0.86728 | 0.85142 | 0.8362
Stray Light | 1 | 0.99873 | 0.99494 | 0.98865 | 0.97987 | 0.96864 | 0.95499 | 0.93897 | 0.92062 | 0.89999 | 0.87715 | 0.85215 | 0.82506 | 0.79595 | 0.7649 | 0.73198 | 0.69729
Ghosting | 1 | 0.99883 | 0.99531 | 0.98948 | 0.98134 | 0.97093 | 0.95829 | 0.94344 | 0.92643 | 0.90731 | 0.88614 | 0.86296 | 0.83786 | 0.81088 | 0.7821 | 0.75159 | 0.71944
Image Velocity | 1 | 0.99799 | 0.99199 | 0.98206 | 0.96827 | 0.95077 | 0.92971 | 0.90529 | 0.87773 | 0.84726 | 0.81416 | 0.7787 | 0.74119 | 0.70193 | 0.66123 | 0.61941 | 0.57677
Carrier Diffusion | 1 | 0.99946 | 0.99786 | 0.99518 | 0.99144 | 0.98663 | 0.98076 | 0.97383 | 0.96585 | 0.95682 | 0.94674 | 0.93563 | 0.92349 | 0.91032 | 0.89615 | 0.88096 | 0.86479
Jitter | 1 | 0.99819 | 0.99279 | 0.98382 | 0.97136 | 0.95549 | 0.93633 | 0.91401 | 0.88869 | 0.86053 | 0.82974 | 0.79652 | 0.76109 | 0.72367 | 0.68451 | 0.64384 | 0.6019
Environment | 1 | 0.9998 | 0.99919 | 0.99818 | 0.99676 | 0.99494 | 0.99271 | 0.99008 | 0.98705 | 0.98362 | 0.97979 | 0.97556 | 0.97094 | 0.96592 | 0.96051 | 0.9547 | 0.94851
Mechanism | 1 | 0.9998 | 0.99919 | 0.99818 | 0.99676 | 0.99494 | 0.99271 | 0.99008 | 0.98705 | 0.98362 | 0.97979 | 0.97556 | 0.97094 | 0.96592 | 0.96051 | 0.9547 | 0.94851
Chart: UVNIR Along-Track MTF
| 0 | 0.125 | 0.25 | 0.375 | 0.5 | 0.625 | 0.75 | 0.875 | 1 | 1.125 | 1.25 | 1.375 | 1.5 | 1.625 | 1.75 | 1.875 | 2
MTF RQMT | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3
Total | 1 | 0.98255 | 0.94057 | 0.87658 | 0.79452 | 0.69935 | 0.59662 | 0.49207 | 0.3911 | 0.29827 | 0.21689 | 0.14898 | 0.095221 | 0.055121 | 0.027316 | 0.0096929 | 0
Optics | 1 | 0.99526 | 0.9903 | 0.98487 | 0.97871 | 0.97157 | 0.96318 | 0.95336 | 0.94219 | 0.92975 | 0.91615 | 0.90147 | 0.88583 | 0.86934 | 0.85317 | 0.83524 | 0.81668
Stray Light | 1 | 0.99753 | 0.99013 | 0.97785 | 0.96072 | 0.93881 | 0.91218 | 0.88092 | 0.84511 | 0.80486 | 0.76029 | 0.7115 | 0.65864 | 0.60185 | 0.54126 | 0.47704 | 0.40935
Ghosting | 1 | 0.99815 | 0.9926 | 0.98339 | 0.97054 | 0.95411 | 0.93413 | 0.91069 | 0.88383 | 0.85365 | 0.82022 | 0.78363 | 0.74398 | 0.70139 | 0.65595 | 0.60778 | 0.55701
Scrambler | 1 | 0.99992 | 0.9997 | 0.99932 | 0.9988 | 0.99812 | 0.99729 | 0.99631 | 0.99518 | 0.99391 | 0.99248 | 0.9909 | 0.98918 | 0.9873 | 0.98528 | 0.98311 | 0.98079
Slit | 1 | 0.99359 | 0.9745 | 0.94317 | 0.90032 | 0.84693 | 0.78421 | 0.71359 | 0.63662 | 0.55501 | 0.47053 | 0.38497 | 0.30011 | 0.21765 | 0.13921 | 0.066239 | 0
Jitter | 1 | 0.99819 | 0.99279 | 0.98382 | 0.97136 | 0.95549 | 0.93633 | 0.91401 | 0.88869 | 0.86053 | 0.82974 | 0.79652 | 0.76109 | 0.72367 | 0.68451 | 0.64384 | 0.6019
Environment | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Mechanism | 1 | 0.9998 | 0.99919 | 0.99818 | 0.99676 | 0.99494 | 0.99271 | 0.99008 | 0.98705 | 0.98362 | 0.97979 | 0.97556 | 0.97094 | 0.96592 | 0.96051 | 0.9547 | 0.94851
September 24
10

## Slide 11: SWIR MTF Analysis Results
Chart: SWIR Cross-Track MTF
| 0 | 0.125 | 0.25 | 0.375 | 0.5 | 0.625 | 0.75 | 0.875 | 1 | 1.125 | 1.25 | 1.375 | 1.5 | 1.625 | 1.75 | 1.875 | 2
MTF RQMT | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3
Total | 1 | 0.97621 | 0.92343 | 0.84726 | 0.75348 | 0.6497 | 0.5435 | 0.44052 | 0.34584 | 0.26233 | 0.19153 | 0.13352 | 0.087919 | 0.053392 | 0.028349 | 0.011092 | 0
Optics | 1 | 0.99572 | 0.99115 | 0.98669 | 0.98187 | 0.97676 | 0.9717 | 0.96629 | 0.96099 | 0.95571 | 0.95052 | 0.94492 | 0.93953 | 0.93414 | 0.92865 | 0.92261 | 0.9168
Stray Light | 1 | 0.99938 | 0.99753 | 0.99446 | 0.99018 | 0.9847 | 0.97804 | 0.97023 | 0.96128 | 0.95122 | 0.94007 | 0.92788 | 0.91466 | 0.90046 | 0.88532 | 0.86926 | 0.85234
Ghosting | 1 | 0.99883 | 0.99531 | 0.98948 | 0.98134 | 0.97093 | 0.95829 | 0.94344 | 0.92643 | 0.90731 | 0.88614 | 0.86296 | 0.83786 | 0.81088 | 0.7821 | 0.75159 | 0.71944
Filtering | 1 | 0.99416 | 0.97703 | 0.94968 | 0.91374 | 0.87113 | 0.82389 | 0.7739 | 0.72285 | 0.67209 | 0.62267 | 0.57533 | 0.53055 | 0.48862 | 0.44964 | 0.41363 | 0.3805
MLA | 1 | 0.99359 | 0.9745 | 0.94317 | 0.90032 | 0.84693 | 0.78421 | 0.71359 | 0.63662 | 0.55501 | 0.47053 | 0.38497 | 0.30011 | 0.21765 | 0.13921 | 0.066239 | 0
Jitter | 1 | 0.9988 | 0.99519 | 0.98922 | 0.98091 | 0.97033 | 0.95755 | 0.94267 | 0.92579 | 0.90702 | 0.8865 | 0.86435 | 0.84073 | 0.81578 | 0.78967 | 0.76256 | 0.7346
Environment | 1 | 0.99572 | 0.99115 | 0.98669 | 0.98187 | 0.97676 | 0.9717 | 0.96629 | 0.96099 | 0.95571 | 0.95052 | 0.94492 | 0.93953 | 0.93414 | 0.92865 | 0.92261 | 0.9168
Mechanism | 1 | 0.9998 | 0.99919 | 0.99818 | 0.99676 | 0.99494 | 0.99271 | 0.99008 | 0.98705 | 0.98362 | 0.97979 | 0.97556 | 0.97094 | 0.96592 | 0.96051 | 0.9547 | 0.94851
Chart: SWIR Along-Track MTF
| 0 | 0.125 | 0.25 | 0.375 | 0.5 | 0.625 | 0.75 | 0.875 | 1 | 1.125 | 1.25 | 1.375 | 1.5 | 1.625 | 1.75 | 1.875 | 2
MTF RQMT | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3
Total | 1 | 0.97521 | 0.92623 | 0.85522 | 0.7676 | 0.66921 | 0.56582 | 0.4631 | 0.36599 | 0.27826 | 0.20299 | 0.14023 | 0.090465 | 0.053501 | 0.02749 | 0.010274 | 0
Optics | 1 | 0.99419 | 0.98739 | 0.979 | 0.96929 | 0.95839 | 0.94626 | 0.93298 | 0.91863 | 0.90326 | 0.88802 | 0.87097 | 0.85208 | 0.83368 | 0.81602 | 0.79683 | 0.77737
Stray Light | 1 | 0.99873 | 0.99494 | 0.98865 | 0.97987 | 0.96864 | 0.95499 | 0.93897 | 0.92062 | 0.89999 | 0.87715 | 0.85215 | 0.82506 | 0.79595 | 0.7649 | 0.73198 | 0.69729
Ghosting | 1 | 0.99883 | 0.99531 | 0.98948 | 0.98134 | 0.97093 | 0.95829 | 0.94344 | 0.92643 | 0.90731 | 0.88614 | 0.86296 | 0.83786 | 0.81088 | 0.7821 | 0.75159 | 0.71944
Slit | 1 | 0.99359 | 0.9745 | 0.94317 | 0.90032 | 0.84693 | 0.78421 | 0.71359 | 0.63662 | 0.55501 | 0.47053 | 0.38497 | 0.30011 | 0.21765 | 0.13921 | 0.066239 | 0
Depolarizer | 1 | 0.99992 | 0.9997 | 0.99932 | 0.9988 | 0.99812 | 0.99729 | 0.99631 | 0.99518 | 0.99391 | 0.99248 | 0.9909 | 0.98918 | 0.9873 | 0.98528 | 0.98311 | 0.98079
Jitter | 1 | 0.99819 | 0.99279 | 0.98382 | 0.97136 | 0.95549 | 0.93633 | 0.91401 | 0.88869 | 0.86053 | 0.82974 | 0.79652 | 0.76109 | 0.72367 | 0.68451 | 0.64384 | 0.6019
Environment | 1 | 0.99274 | 0.98424 | 0.97375 | 0.96162 | 0.94799 | 0.93283 | 0.91622 | 0.89828 | 0.87908 | 0.86002 | 0.83871 | 0.8151 | 0.79211 | 0.77002 | 0.74604 | 0.72172
Mechanism | 1 | 0.9997 | 0.99878 | 0.99726 | 0.99514 | 0.9924 | 0.98907 | 0.98512 | 0.98058 | 0.97543 | 0.96969 | 0.96335 | 0.95641 | 0.94888 | 0.94076 | 0.93206 | 0.92277
September 24
11

## Slide 12: Testing Description
Testing was performed using a collimated scene projected into the OCI telescope
Time adjusted collections of the scene were superimposed to produce a detailed characterization of the OCI IFOV
The Fourier Transform of the IFOV was calculated for each direction
September 24
12

## Slide 13: CCD LSF Bench Test Results
Chart: Cross-Track UVNIR MTF Test Results (Fraction of Nyquist)
0.25 GLAMR Results | 0.96041 | 0.97022
0.5 GLAMR Results | 0.8623 | 0.88909
0.75 GLAMR Results | 0.72556 | 0.76586
1.0 GLAMR Results | 0.56415 | 0.61317
Chart: Along-Track UVNIR MTF Test Results (Fraction of Nyquist)
September 24
13

## Slide 14: SWIR LSF Bench Test Results
Chart: Cross-Track SWIR MTF Test Results (Fraction of Nyquist)
0.25 RQMT | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9
0.25 Test Result | 0.94463 | 0.91758 | 0.96825 | 0.92921 | 0.94638 | 0.94365 | 0.93551 | 0.94232 | 0.95721
0.5 RQMT | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7
0.5 Test Result | 0.84443 | 0.81589 | 0.86069 | 0.82301 | 0.8423 | 0.83948 | 0.80228 | 0.82556 | 0.84632
0.75 RQMT | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5
0.75 Test Result | 0.69821 | 0.67149 | 0.7063 | 0.66873 | 0.68868 | 0.68854 | 0.61853 | 0.65791 | 0.68624
1.0 RQMT | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3
1.0 Test Result | 0.52552 | 0.50016 | 0.53027 | 0.48857 | 0.50531 | 0.50882 | 0.41818 | 0.46423 | 0.49851
Chart: Along-Track SWIR MTF Test Results (Fraction of Nyquist)
0.25 RQMT | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9
0.25 Test Result | 0.92777 | 0.8978 | 0.9685 | 0.9023 | 0.9381 | 0.9513 | 0.9276 | 0.94727 | 0.95583
0.5 RQMT | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7
0.5 Test Result | 0.8072 | 0.77553 | 0.8504 | 0.7882 | 0.82123 | 0.8394 | 0.80773 | 0.8292 | 0.8399
0.75 RQMT | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5
0.75 Test Result | 0.63887 | 0.61583 | 0.67873 | 0.62583 | 0.65237 | 0.67647 | 0.63857 | 0.65973 | 0.6716
1.0 RQMT | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3
1.0 Test Result | 0.4548 | 0.44123 | 0.48663 | 0.44603 | 0.46627 | 0.49137 | 0.45253 | 0.471 | 0.4835
September 24
14

## Slide 15: Analysis vs Testing
UVNIR cross-track analysis and test results are in good agreement (sub-sampling advantage)
UVNIR along-track analysis shows better than expected performance
SWIR testing showed MTF performance worse in some bands than predicted by analysis
  Cause suspected to be extended tail response
  Flight data utilizes a correction, not yet in place for testing
 |  | UVNIR Along-Track (Wavelength average) |  | SWIR Cross-Track (Wavelength average) |  | SWIR Along-Track (Wavelength average) | 
 |  | MTF | % Diff from Analysis | MTF | % Diff from Analysis | MTF | % Diff from Analysis
0.25 Nyquist | Test | 0.95 | 3% | 0.94 | 2% | 0.94 | 1%
 | Test w/ Analytical Aperture | 0.94 | 2% | 0.92 | -1% | 0.91 | -2%
0.5 Nyquist | Test | 0.84 | 10% | 0.83 | 11% | 0.82 | 7%
 | Test w/ Analytical Aperture | 0.78 | 2% | 0.75 | -0.40% | 0.74 | -4%
0.75 Nyquist | Test | 0.69 | 24% | 0.68 | 24% | 0.65 | 15%
 | Test w/ Analytical Aperture | 0.57 | 2% | 0.53 | -2% | 0.51 | -10%
1.0 Nyquist | Test | 0.53 | 34% | 0.49 | 43% | 0.47 | 27%
 | Test w/ Analytical Aperture | 0.36 | 3% | 0.31 | -9% | 0.3 | -19%
Chart: UVNIR Cross-Track MTF Comparison
| 0.25 | 0.5 | 0.75 | 1
Test Results | 0.96041 | 0.8623 | 0.72556 | 0.56415
Analysis | 0.96386 | 0.87269 | 0.73959 | 0.58424
RQMT | 0.9 | 0.7 | 0.5 | 0.3
September 24
15

## Slide 16: Conclusions
Complex instruments can benefit from detailed MTF analysis.
Identifying the primary contributors can assist to focus resources and efforts toward most impactful elements.
Testing provides confidence in analysis and more robust verification of requirements.
Comparison of analysis with test results provides insight into test adequacy and nuance of instrument data collection.
September 24
16