## Slide 1
MITIGATING DECOMPRESSION SICKNESS FOR MOON AND MARS
1
Alejandro Garbino, MD, PhD, MPH, FAsMA
HRP Investigators’ Workshop
Tuesday January 28th, 2025

## Slide 2: Agenda
Moon and Mars?
What is Decompression Sickness
What causes it
What can be done to mitigate it
How can we test our plans
What is still to do in the future
Funding:
NASA Extravehicular Activity and Human Surface Mobility Program
NASA Human Research Program

## Slide 3: Decompression Sickness (DCS)
Decreasing ambient pressure causes release of nitrogen dissolved in tissues, which may result in DCS
  Grade IV VGE: Venous Gas Emboli “Silent bubbles” (no symptoms or clinical findings) can be detected by Doppler; Grade IV is the most severe form and is correlated with risk of DCS
  Type I DCS: Joint pain; single extremity tingling or numbness; mild skin symptoms
  Type II DCS: Central neurological or cardiopulmonary symptoms; can be life-threatening
Pre-EVA denitrogenation via oxygen prebreathe reduces DCS risk during EVA
Flight prebreathe protocols must be validated via human ground testing prior to operational implementation

## Slide 4: Fundamentals
↓pressure:
  tissues release nitrogen bubbles
  Too much bubbling: Decompression Sickness
    Type I DCS: Mild/Joint pain
    Type II DCS: Severe/life threatening
  Pre-EVA denitrogenation via oxygen prebreathe reduces DCS risk during EVA
High workload/ambulation = higher risk

## Slide 5: High Grade VGE

## Slide 6: Why Exploration Atmosphere?
Significantly increased frequency of EVAs is expected during planetary ops vs. ISS
  Up to 24 hrs / person / week
DCS risk is increased by ambulation and physical activity vs microgravity[1]
Apollo had 100% O2 cabin and zero EVA prebreathe
Current ISS prebreathe protocols would add significant timeline overhead and are NOT validated for planetary EVA
  Shuttle & ISS protocols are applicable to microgravity only
1Conkin J, et al. Venous gas emboli and ambulation at 4.3 psia. Aerosp Med Hum Perform. 2017; 88(4):370–376.

## Slide 7: Rationale for Exploration Atmosphere
Saturation Atmosphere | Microgravity Prebreathe* (h:mm) | Planetary Prebreathe*
14.7 psi, 21% O2 | 4:00 (resting) | 6:30-7:00 2
10.2 psi, 26.5% O2 | 0:40 | 3:00-3:30 3
8.2 psi, 34% O2 | 0:00-0:15 | 0:00-0:30 4,5
5.0 psi, 100% O2 (Apollo, Gemini) | 0:00 | 0:00
2 Abercromby et al. Suited Ground Vacuum Chamber Testing Decompression Sickness Tiger Team Report, (2019) NASA Technical Report. NASA/TP-2019–220343
3 Abercromby et al. Using the Shuttle Staged Prebreathe Atmosphere and Variable Pressure Spacesuits for Exploration Extravehicular Activity, (2018) AsMA.
4 Abercromby et al. Modeling Oxygen Prebreathe Protocols for Exploration EVA Using Variable Pressure Suits, (2017) AsMA.
5 Abercromby et al. Modeling a 15-min extravehicular activity prebreathe protocol using NASA׳ s exploration atmosphere (56.5 kPa/34% O2). Acta Astronautica, 109 (2015), pp.76-87.
Unvalidated estimates
(i.e., not yet available for flight use)
*Assumes 6hr EVA @ 4.3 psia and approximately equal DCS risk level
2021-2022
Notes: We’ve previously published and presented here the model-predicted implications of the exploration atmosphere and variable pressure suits as well as different EVA durations and frequencies.
This table shows the approximate prebreathe durations for microgravity EVA as compared with planetary EVA given the same saturation atmospheres, spacesuit pressure, EVA durations, and approximately the same DCS risk level. As you can see, our model estimates show a significant penalty associated with the higher metabolic rates and ambulation of planetary EVA as compared with microgravity.
[ANIMATION]
But while we have ground validation data and flight experience to show that these microgravity protocols are safe and about as efficient as possible, we don’t have the data to validate these model estimates. And we’re not going to be able to do EVAs on the moon or Mars until we do.
[NEXT SLIDE]

## Slide 8: What is NASA-STD-3001
NASA-STD-3001 requires human testing to
   15% incidence of Type I DCS (@95% CL)
   20% incidence of Grade IV VGE (@95% CL)
  No Type II DCS
Prebreathe study yields:
Statistical conversion to:
  % DCS risk and Confidence Limits at 5%-95%
  Confidence limits are driven by N moreso than actual risk
  Thus, reaching 3001 req’ts is contingent on sample size
NASA-STD-3001 does NOT address Cumulative Risk:
Loss of EVA is a mission risk – determined by mission
Artemis does not currently have mission-wide DCS risk

## Slide 9: Cabin Atmosphere Constraints
Exploration Atmosphere Working Group (2006, 2012): 8.2psia / 34% O2
  Compromise between flammability, hypoxia, DCS risk, prebreathe time
Increased Fire Risk
Increased Hypoxic Stress
DCS Risk
Prebreathe Time
EVA Suit Pressure

## Slide 10: How do we actually test?

## Slide 11: Historical NASA Testing

## Slide 12: Exploration Atmosphere Validation
Accept Criteria (per NASA-STD-3001):
   15% incidence of Type I DCS (@95% CL)
   20% incidence of Grade IV VGE (@95% CL)
  No Type II DCS
Reject Criteria
  > 15% incidence of Type I DCS (@70% CL)
  > 20% incidence of Grade IV VGE (@70% CL)
  Any Type II DCS
Neither
  Requires review and additional data
Test Series 1 (11 days)
Test Series 2 (11 days)
DSMB Review; Modify Prebreathe
Neither Accept nor Reject
Reject
Reject
Accept
Neither Accept nor Reject
Additional Test Series
Reject
Validated Prebreathe Protocol
DSMB: Data Safety Monitoring Board

## Slide 13: Prebreathe Validation Approach
What prebreathe is sufficient to meet NASA-STD-3001 standards in a Lunar/Mars environment?
  Equilibrate to Exploration Atmosphere: 8.2psi/34% O2 for 48 hrs (after 3hr O2 PB)
  Minimum prebreathe duration: 20 min ≥ 6.2psi
  Simulated EVA: 4.3psi/85% O2
  Simulate EVA workload: 6 tasks for 6hrs across workload ranges

## Slide 14: 20FT Chamber Overview
1st Floor – Science & EVA Activities
2nd Floor – Crew Quarters & Hygiene
3rd Floor – Stowage & Media Center

## Slide 15: 3rd Floor Configuration

## Slide 16: 2nd Floor – Crew Quarter Layout

## Slide 17: EVA Sim Stations

## Slide 18: EVA Simulation
EVA Sim Presented at AsMA 2022
see Estep et al.

## Slide 19: VGE Methods
Every 15 min:
  Subject lays on the cot in a left recumbent position
  The operator gels the Vivid iQ ultrasound probe and acquires an apical cross-section view of the heart and heart chambers (top)
    If the apical view is not easily visible, a parasternal long-axis view is imaged instead (bottom)
  Alternates with Doppler auscultation of L parasternal border

## Slide 20: Analysis and Scoring Methods
Ultrasound and Doppler Scoring
Ultrasound videos were scored based on number of VGE / bubbles present during imaging over 10 cardiac cycles (Modified Eftedal Brubakk Score, right).
Doppler audios were scored based on ‘bubble signals’, or audible peaks in doppler waveforms (Spencer Scale, left).
Data Analysis / Graphs
Scores for rests and leg flexes – left and right – were acquired via Vivid iQ Ultrasound w/ doppler wave acquisition application.
Scores between cross-graders (n=3 to 4 per crew member at each time point) were averaged for the resting and flexing periods.
Max scores and average scores of resting and flexing periods were graphed.
Data is represented by mean ± standard deviation.

## Slide 21: Results

## Slide 22: Test Campaign Summary
2005 – Initial proposal: 8.0psi/32% FiO2
2012:
  Updated to 8.2psi/34% FiO2 (to decrease hypoxic stress)
  Briefing to HEOMD – proceed with work on EA
2018 – Human validation studies in the building 7 20ft chamber green lit
2021 – Chamber readiness complete/initial HITL assessment
  2021-11: Overnight in Chamber (doors ‘closed’, no pressure change)
2022
  Feb: 1-day equipment validation (n=2)
  Mar: 3-day dress rehearsal (n=8)
    DCS x1
  Jun: 11-day test (n=8) “EA1”
    No DCS Type II
    Two DCS Type I cases; symptoms fully resolved with treatment
    One DCS Type l in Doppler Tech
    One VGE Grade IV
2023
  Mar: 3-day dress rehearsal (n=8)
    No DCS I/II
  Jun: 11-day test (n=8) “EA2”
    No DCS I/II
    One Asymptomatic LVGE
    One DCS Type l in external Doppler Tech

## Slide 23: Total Exposures
EA1 (2022):
  EVA 1: 6 subjects participated, 1 DCS case
  EVA 2: 4 subjects participated, no DCS*
    1 subject sat out EVA per protocol on ground level oxygen due to DCS on EVA1
    1 subject sat out EVA due to mask fit issues
  EVA 3: 5 subjects participated, no DCS
    1 subject sat out EVA due to mask fit issues
  EVA 4: 5 subjects participated, no DCS
    1 subject sat out EVA due to musculoskeletal issues
  EVA 5: 6 subjects participated, 1 DCS case
    1 subject excluded due to musculoskeletal issues
* DCS case in Doppler Technician – not a study subject
EA2 (2023):
  EVA 1: 6 subjects participated
    1 LVGE case removed
  EVA 2: 5 subjects participated, no DCS
  EVA 3: 5 subjects participated, no DCS
  EVA 4: 5 subjects participated, no DCS
  EVA 5: 5 subjects participated, no DCS
Finally Tally: 2 DCS cases, 50 exposures

## Slide 24: Total Exposures
EA3 (Nov 2023):
90min/4.3psia:
  EVA 1: 5 subjects participated, 1 DCS II case
150min/4.3psia:
  EVA 2: 4 subjects participated, no DCS
  EVA 3: 4 subjects participated, no DCS
  EVA 4: 4 subjects participated, no DCS
  EVA 5: 4 subjects participated, no DCS
EA4 (Sep 2024):
150min/4.3psia:
  EVA 1: 8 subjects participated, no DCS
  Accepted Protocol
20min/5.2psia:
  EVA 2: 8 subjects participated, no DCS
  EVA 3: 8 subjects participated, 1 DCS II case
50min/5.2psia:
  EVA 4: 7 subjects participated, no DCS
    1 drop out/1 escort; n=5
  EVA 5: 6 subjects participated, no DCS

## Slide 25: Summary – 8.2/34% Campaign
Accept Criteria (per NASA-STD-3001):
   15% incidence of Type I DCS (@95% CL)
   20% incidence of Grade IV VGE (@95% CL)
  No Type II DCS
Observed:
  DCS Type I: 2/50 = 4% (1.1%-13.5%)
  DCS Type II: 0
  VGE IV: 0
    (EB Grade 7: 1/50)
No Type II Cases
Two Type I Cases (out of 50 exposures)

## Slide 26: Summary – 9.6/28.5% Campaign
Accept Criteria (per NASA-STD-3001):
   15% incidence of Type I DCS (@95% CL)
   20% incidence of Grade IV VGE (@95% CL)
  No Type II DCS
4.3 psia:
  90 min: DCS Type II (rejected)
  150min: 1 VGE IV (accepted)
5.2 psia:
  20min: DCS Type II (rejected)
  50min: 11 exposures (inconclusive)
    EA-5 in Feb 2025

## Slide 27: Doppler – Max Spencer Grade
EA1
EA2

## Slide 28: Ultrasound – Max EB Score
EA1
EA2

## Slide 29: Future Directions
Testing Alternate Cabin
Testing Elevated Suit Pressure
HRP – AETHER Program (frequency, duration, etc)

## Slide 30: Conclusion
A 20 min prebreathe from a 56.5kPa (8.2 psi), 34% O2 atmosphere meets NASA-STD-3001 for EVAs at 30kPa (4.3psia)
  The observed DCS risk is 4% (1.1%-13.5%) per person per EVA
Doppler and U/S both show significant VGE stress during EVA
Will transition to allow E-B score as an alternative to Spencer Grade
Thank you!

## Slide 31: Backup/Reference

## Slide 32: Revised DCS Treatment Flow Diagram
Key:
Subj = Subject
Sx = Symptoms
DT = Doppler Tech
MO = Med Officer
SLO = Site-level O2 (8.2psia)
GLO = Ground-level O2 (14.7psia)
HBO = Hyperbaric O2
DSSMB = Diver and Suited Subject Medical Board
Subj placed on GLO Tx for 4+ hours.
Subj is removed from study, moved to hyperbaric chamber or Memorial Hermann for HBO Tx.
DCS diagnosis vetted by DSSMB within 36 hours.
Study is immediately stopped. Prebreathe protocol is re-assessed.
Study continues with (n-1) subjects.
Subj returns to main chamber after EVA Sim, misses next EVA. Subj held @ 14.7 outside chamber.
Subj placed on GLO Tx with check for Sx resolution within 10min and remain resolved.
Subject completes 4+ hour GLO Tx. MO does ~30min prebreathe. MO + Subj depress to 8.2, Subj moved to SLO. MO evaluates Subj for Sx recurrence at 8.2.
Symptoms (sx) resolved by 14.7 psia
Sx not
resolved
Type-II
Sx
Sx remain resolved
Sx recur within 4 hrs
Type-I / None
Type-II
No improvement in Sx @ 10min
Sx resolved by 10min
Subject starts 4+ hour GLO Tx, with MO monitoring for Sx recurrence.
Sx remain resolved
over 4 hrs
Sx recur
*Subj. travels solo in lock
START
Subj shows Sx during or after EVA Sim
Subj moved to 100% O2.
DT puts Subj in lock @ 4.3, repress to 14.7 in Man Lock*.
MO evaluates Subj for DCS Sx resolution @ 14.7.

## Slide 35: Timeline Implications
2 Abercromby et al. “Suited Ground Vacuum Chamber Testing Decompression Sickness Tiger Team Report”, 2018 NASA Technical Report
3 Abercromby, et al. “Using the Shuttle Staged Prebreathe Atmosphere and Variable Pressure Spacesuits for Exploration Extravehicular Activity”, 2018 AsMA.
4 Abercromby et al. “Modeling Oxygen Prebreathe Protocols for Exploration EVA Using Variable Pressure Suits”, 2017 AsMA.
Exploration conops are incompatible with multi-hour prebreathe durations
Timelines are notional and for purposes of comparison only
All prebreathe durations are model-based estimates [2-4]
Detailed depress profiles being worked with CX3

## Slide 36: EVA Simulation – Rationale for Tasks
61 exploration EVA tasks[2] were decomposed into 126 subtasks then characterized by functional requirements of each subtask
Categories:
  Body Positioning: Seated, Kneeling, Standing, Mobile, etc.
  Muscle Groups: Whole/Both, Upper, Lower
  Ambulation: None, Walking, Walking (terrain), Walking (slopes), Crawling, Climbing
  Loading Bearing: None, Carrying, Pushing/Pulling, Attached to Suit
  Loads: None, Minimal (<5 lbs), Variable, Heavy (>30 lbs)
  Upper Body Reach (Workspace): None, Standard, Extended
  Hand Usage: None, Fine Motor Skills, Grip Strength, Vibration, Shock, Other/Combination
  Task Occurrence: Rare (<10% of EVAs), Some (~30%), Many (~50%), Most (~75%), Nearly All (>90%)
  Task Duration (expected)
  Task Frequency: 1-2 times per EVA, Every 2 hours during EVA, Every hour during EVA, 1-30 minutes during EVA
2Coan D. Exploration EVA System Concept of Operations. NASA TR, EVA-EXP-0042 RevB. 2020
Chart: 
| Upper body | Lower body | Both Upper and Lower body | Minimal work
 | 23.8095 | 16.6667 | 52.381 | 7.1429
Notes: Patrick

## Slide 37: Pilot Data - Results
The average %VO2peak across all tasks was ~38% (1274 BTU/hr).
Avg = 38%

## Slide 38: Was the prebreathe within parameters?
*Transition from 6.2 psi to 5.4 psi (supersaturation point) added ~80-90 sec
Prebreathe Times:
EVA1: 20min 14 sec
EVA2: 20min 21 sec
EVA3: 20min 01 sec
EVA4: 20min 04 sec
EVA5: 20min 10 sec

## Slide 39: EB Score

## Slide 40: Research Goals
Primary Research Goal
  Prebreathe Validation (H3PO)
Secondary Research Goals
  Response/Recovery from Mild Exercise (H3PO)
  Visual Acuity and Contrast (H3PO)
  Acute Mountain Sickness Symptoms (H3PO)
  Performance during EVA Simulations (H3PO)
  Physiological Reponses of Hypobaric Hyperoxic Environment (Cardiovascular and Vision Lab)
  Hematology/Immunology/Inflammatory Response (Immunology Lab)
  Oxidative Damage (Nutritional Biochemistry Lab)
  Appetite and Food Intake Impacts (Space Food Systems Lab)
  Sleep Quality and Duration Impacts (Behavioral Health and Performance Lab)
  Neurocognitive and Functional Responses (Behavioral Health and Performance Lab)
  Habitability Acceptability (HFEL/CDSA)