## Slide 1: Temperature Boomlet Modeling and Analysis for Venus Environmental Descent
Joe Durante

## Slide 2: Outline
Introduction
  About me
  Internship objectives
DAVINCI Temperature Boomlet Modeling
  Mission Overview
  Thermal Model Methodology and Setup
  Convective analysis using Fluent
  Parasitic Heating Investigation
  Radiation Effects on Venus
  Platings and Optical Properties
  Adhesive Choices
  Final Conclusions and Future Work
Additional Work and Closing Remarks

## Slide 3: About me
Rising Junior Mechanical Engineering student at Georgia Tech
  From Ridley, PA
OSTEM Intern
Enjoy running, traveling, and cheering on Philly sports!

## Slide 4: Internship Objectives
Learn basics of spacecraft thermal control
Learn Thermal Desktop/SINDA/RadCAD
See day-to-day work of a thermal engineer
Learn thermal design, analysis and testing
Learn about conduction, convection, and radiation
Use FEMAP for high fidelity meshing
Learn ANSYS Spaceclaim/Fluent (CFD Software)

## Slide 5: Materials Used for Learning
Spacecraft Thermal Control Handbook
Fundamentals of Heat and Mass Transfer
  Mostly to understand convection
Brian's TD Guide
  Which includes Hume's videos/tutorial
Daniel's Project-specific tutorial
  Introductory Problem Set TD and HT.docx
NESC Academy
  Thermal videos and overall spacecraft videos
The Efficient Engineer
  YouTube videos to effectively teach the basics of important engineering concepts

## Slide 6: DAVINCI Mission Overview
DAVINCI stands for Deep Atmospheric Venus Investigation of Noble Gases, Chemistry, and Imagery
  First mission to Venus since the Soviet Vega program in 1985
  Set to launch in 2030
This mission will record data on the makeup of the Venus atmosphere as well as map out the cloud layer to better understand the origin and evolution of Venus
  This will help answer long-standing questions like if Venus was ever habitable, the atmospheric composition and surface interaction, and the surface properties.
There will be two flybys of Venus and then a full descent
  This descent will last approximately 1 hour, collecting valuable data throughout.
Challenges of the mission
  Temperature gets up to nearly 475 degrees Celsius (887 degrees Fahrenheit)
    Atmosphere is 96% CO2
  Crushing air pressure (92 bar)
  Clouds made of sulfuric acid

## Slide 7: Venus conditions
Wide variation in temperature, pressure, and radiative heat transfer throughout the descent
Probe initially starts warmer than atmospheric temperature before being ejected from probe flight system
  Probe flight system keeps the temperature around -20 degrees C.
Descent simulation data is used in analysis
  Used to calculate Reynolds number, Nusselt Number, and Convection coefficient
  Temperatures are around 230 K at the start of the descent, and end around 735 K.

## Slide 8: The DAVINCI Instruments
VISOR (Venus Imaging System for Orbital Reconnaissance)
CUVIS (Compact Ultraviolet to Visible Imaging Spectrometer)
VMS (Venus Mass Spectrometer)
VTLS (Venus Tunable Laser Spectrometer)
VASI (Venus Atmospheric Structure Investigation)
VenDI (Venus Descent Imager)
VfOx (Venus Oxygen Fugacity Student Collaboration Experiment)
In-situ measurement
Notes: DAVINCI will tackle these objectives…

## Slide 9: VASI System Overview
Temp. boomlet 2
Ø 33 in
Descent direction
Temp. boomlet 1
VfOx
Kiel tube
Main flange
Additive Manufacturing Prototype courtesy of Mitch Haglund
VASI, Venus Atmosphere Structure Investigation, is one of the scientific tools used in the DAVINCI Mission
  Goal is to measure pressure, temperature, and wind speed throughout the probe's descent
The VASI port is made up of two temperature sensors with protective titanium casings as well as a Kiel tube to measure pressure
  Temperature sensor is a PRT, to allow for accurate temperature readings
  Pioneer Venus used external PRTs, which failed during flight. Therefore, this casing is required to protect the sensor from the harsh Venus atmospheric conditions
VASI will measure wind speed and direction using accelerometers and gyroscopes installed in the descent sphere

## Slide 10: Temperature boomlet designs
The boomlet design must allow the PRT to effectively capture the temperature of the atmosphere to within 1 degree kelvin.
  This means the design must be optimized to stay structurally intact as well as allow for the most accurate temperature readings.
The goal is to maximize convection, since this is what will enable the boomlet and sensor to get to the true atmospheric temperature, while minimizing parasitic heat loads
These are the three initial designs
  Very small (Straight boomlets are 3mm in diameter )
PRT
Potting

## Slide 11: What are my project objectives?
Temperature Boomlet Performance | 
L2 Requirement | L3 Requirement
DAVINCI shall measure atmospheric temperatures with sampling interval <= 100 m, from prior to the first gas sample ingest and above 60 km altitude to <= 100 m above the surface. DAVINCI shall measure atmospheric temperatures with <= 0.5K relative precision, <= 1K absolute accuracy, over the expected range of 200 to 750K. | Temperature measurements shall be performed in the range of 200 to 750 K
 | Temperature measurements shall meet or exceed the accuracy requirement of ±1 degrees K.
 | VASI shall provide a minimum of two independent temperature sensors to measure the external temperature.
3D Thermal Desktop model of the VASI temperature boomlets.
  Transient model to capture the sensor response times and expected measured temperatures during Zephyr descent.
  Characterize errors due to extraneous heat inputs (radiation, conduction through boomlet stem, conduction through sensor wires, sensor self-heating, stagnation heating).
  Capture the response time impacts of various sensor mounting methods.
  Compare results with existing Engineering Equation Solver (EES) model.
  Provide suggestions to optimize the temperature boomlet thermal design.
Characterize VASI temperature boomlet convection coefficient using Fluent.
  Generate estimates for the convection coefficient of various boomlet designs as a function of Zephyr descent altitude.
  Provide estimated uncertainties in convection coefficient values.
Support VASI temperature sensor mounting trade.
  Research, design, and analysis support for determining the optimal temperature sensor mounting approach (adhesive vs mechanical mounting).
Investigate low-emissivity platings/coatings for the VASI temperature boomlet exterior surface.

## Slide 12: On to the model!
The boomlet designs are created to survive the mechanical loads while allowing for a fast response time to the sensor
  The basic boomlet is mostly used for design studies
  The straked boomlet (middle) and finned boomlet (bottom) are being investigated to be used as true designs.
Vortex-induced vibrations are an issue, which is why the strakes are included on the middle boomlet
  The third boomlet has a high natural frequency

## Slide 13: What are vortex-induced vibrations?
When fluid flows over a cylindrical structure, the flow around the cylinder slows and forms a boundary layer due to viscosity
At a separation point, the layer separates and forms a vortex in the wake behind the object
  This is called vortex shedding, and it occurs at a Reynolds number of at least 60
The vortices cause fluctuating lift and drag forces, which cause structural vibrations in the object
The frequency at which these vortices are shed can be estimated by the Strouhal number
  ~.2 for bare cylinders

## Slide 14: EES Model by Mitch Haglund
Model diagram
Mitch Haglund (Code 543) created his own 2D model using Engineering Equarion Solver (EES) to conduct thermal analyses of the initial boomlet designs. Based initial validation of TD model off of this
  Limitations in fidelity of the EES model. Cannot replicate some complex geometries of boomlets
  TD allows for complex thermal radiation modeling

## Slide 15: Using FEMAP
Due to the tight temperature sensing requirements, the model must be as geometrically close to the real designs as possible
Utilized FEMAP to do this, which allows for automatic meshing of parts of the boomlets.
  Thermal desktop allows for importing meshed parts from FEMAP
Could not accurately model the geometry of the adhesive in TD, and needed to model the complex strakes.

## Slide 16: Initial Model
First real thermal desktop design
  Had to get used to understanding node count, merging nodes, running case sets, and the general user interface
Modeled the convection using node to surface conductors
  Important to only select outer surface
  Used Venus descent properties to calculate Nusselt Number and convection coefficients. Uniform value around circumference.
Validated model with Mitch by looking at a basic transient case where the air is about 10 K cooler than the initial temperature of the boomlet

## Slide 17: Full descent comparison
This is the plot that is most important to the VASI team. It looks at the difference in temperature between the sensor and the atmosphere throughout the entire descent
Here is how the TD and EES models compared; they were quite close!

## Slide 18: Finned Model
The next task was to model the finned boomlet in TD
Decided the only parts that would need to be meshed in FEMAP were the holder and the adhesive. The adhesive has a geometry that cannot exactly be modeled in TD and meshing the holder allows for better control of the conductance to the inner boomlet.
For the creation of the boomlet in TD, separation of the cylinders between and under the fins allowed for accurate application of the convection only on the outer surface.

## Slide 19: Finned Model
M

## Slide 20: Straked Model
Modeled the straked boomlet in TD next
Used the straight boomlet from before, but this time used FEMAP to mesh the strakes, and then added them to the original model
  Had to increase the number of nodes along the boomlet to get the conductance between the strakes and the boomlet to be more accurate.
  The utilization of FEMAP was most important for this design, as this geometry cannot be made in TD

## Slide 21: Using Ansys Fluent
Nusselt number is a dimensionless value used to characterize the convection. It is the ratio of the convective heat transfer to the conductive heat transfer.
  Used the equation below for our descent calculations
Fluent allows for confirmation of the calculated values for the convection coefficient, as well as to see how the convective gradient forms around the circumference of the boomlets.

## Slide 22: Atmospheric Properties at Each Altitude
60km
  Velocity = 26.97 m/s
  Density = .454 kg/m^3
  Viscosity = 1.32 * 10^-5 Pa*s
  Conductivity = .0138 W/m-K
  Specific heat = .805 kJ/kg-K
30km
  Velocity = 33.52 m/s
  Density = 10.043 kg/m^3
  Viscosity = 2.39 * 10^-5 Pa*s
  Conductivity = .0335 W/m-K
  Specific heat = 1.014 kJ/kg-K
2.5km
  Velocity = 13.58 m/s
  Density = 57.99 kg/m^3
  Viscosity = 3.27 * 10^-5 Pa*s
  Conductivity = .0522 W/m-K
  Specific heat = 1.132 kJ/kg-K

## Slide 23: Straight boomlet comparison to Fluent
Altitude | Convection Coefficient from Hand Calcs | Convection Coefficient from Fluent | Percent Error
60km | 128.95 | 155.57 | 20.6% Greater
30km | 1400 | 1559.42 | 11.32% Greater
2.5km | 3063.15 | 3426.8 | 11.9% Greater
Altitude | Convection Coefficient from Hand Calcs | Convection Coefficient from Fluent | Percent Error
60km |  |  | 20.6% Greater
30km |  |  | 11.32% Greater
2.5km |  |  | 11.9% Greater

## Slide 24: Straked boomlet comparison to Fluent
Altitude | Convection Coefficient from Hand Calcs | Convection Coefficient from Fluent | Percent Error
60km | 128.95 | 136.45 | 5.81% Greater
30km | 1400 | 1776.7 | 26.9% Greater
2.5km | 3063.15 | 3843.1 | 25.5% Greater
Altitude | Convection Coefficient from Hand Calcs | Convection Coefficient from Fluent | Percent Error
60km |  |  | 5.81% Greater
30km |  |  | 26.9% Greater
2.5km |  |  | 25.5% Greater

## Slide 25: Finned boomlet comparison to Fluent
Altitude | Convection Coefficient from Hand Calcs | Convection Coefficient from Fluent | Percent Error | Fins Convection Coefficient
60km | 106.3 | 91.6 | 13.8% less | 90.6
30km | 1203.26 | 1464.65 | 21.7% Greater | 1600
2.5km | 2671.12 | 3350.33 | 25.4% Greater | 3
Altitude | Convection Coefficient from Hand Calcs | Convection Coefficient from Fluent | Percent Error | Fins Convection Coefficient
60km |  |  | 13.8% less | 
30km |  |  | 21.7% Greater | 
2.5km |  |  | 25.4% Greater | 

## Slide 26: Convection circumference effect
Studied effects of varying convection around the circumference of the boomlet.
  Kept the average values around the boomlet the same, but increased the ram direction half of the boomlet by the same percentage the opposite half decreased.

## Slide 27: Straight boomlet results
Almost no difference

## Slide 28: Finned boomlet
More significant differences here, so for future work the circumference differences should be explored more.
  Since the sensor will be placed at ram direction, this would only improve response
PRT
Potting

## Slide 29: Finned boomlet, importance of sensor location

## Slide 30: Characterizing Parasitic Heat Loads
Since convection allows for heat transfer of the true atmospheric temperature, it’s necessary to characterize any heating “errors”
  Some of these are shown to the right here
Thermal mass lag
Sensor self-heating
Thermal resistance between boomlet exterior and the sensor element
Conduction along the boomlet stem to the descent sphere
Conductance along the copper wire
Thermal radiation
Stagnation heating
1
2
3
4
5
6
7

## Slide 31: Characterizing Parasitic Heat Loads
Important
Not significant
Need to be investigated in the future
Thermal mass lag
Sensor self-heating
Thermal resistance between boomlet exterior and the sensor element
Conduction along the boomlet stem to the descent sphere
Conductance along the copper wire
Thermal radiation
Stagnation heating
Chemical Reactions
1
2
3
4
5
6
7

## Slide 32: Thermal mass lag
Thermal mass lag is especially demonstrated with the finned boomlet
  Hence why sensor placement is important

## Slide 33: Descent Sphere Temperature
DAVINCI team provided values for the average skin temperature of the descent sphere, but this is in reality variable around the whole outer diameter
  This study demonstrates how the descent sphere’s temperature can influence the sensor reading due to conduction from the boomlet to the DS

## Slide 34: Straked Boomlet, not a worry

## Slide 35: Radiation
Venus has a quite complex radiative environment
  Located at .72 astronomical units, the solar flux is around 2600 w/m^2 at the upper atmosphere, twice that of Earth
  However, the thick cloud layers absorb and scatter the incident light, significantly reducing the solar flux but still contributing significant diffuse solar flux
    This is reduced as altitude lowers
  Since atmosphere is 96% CO2, the greenhouse effect causes the surface heat to be absorbed
  This means in terms of thermal radiation, the boomlet is viewing temperatures above and below it at similar temperatures to the atmosphere.
Note: Zenith angle of 24 degrees during descent
  Dave Crisp (JPL) provided thermal radiation data from Venus descent simulation.

## Slide 36
51 km
48 km
57 km
70 km
230 K IR (e=1, blackbody
(“Planetary” IR)
(159 W/m2 Global)
512 K IR (e= 1)
(Planetary IR)
Bond Albedo (0.77)
(1800 W/m2)
Direct Solar impingement flux
(2622 W/m2)
Low
Middle
High
Diffuse Sky IR
510 K IR (e=1, blackbody)
3 K Space
Atmosphere temp
(variable with altitude)
Atmosphere temp
(variable with altitude, 503 K here)
735K Ground IR
1900 W/m2 Diffuse Solar
Aeroheat
~0 W/m2
(Global)
16500 W/m2
Atm Absorbed (Greenhouse)
~550 W/m2 diffuse solar flux
See Venus environment calculation.xls
for calculations
32 km
Cloud Layer
Clear
Thin
Haze
90 km
Thin Haze
Clear
Atmosphere temp
(variable with altitude, 230 K here)
Radiating absorbed heat
241 K IR (e= 1)?
(Planetary IR)
196.3 K Sky IR
~550 W/m2 diffuse solar flux
Credit: Shaun Thompson
Updated with data provided by Dave Crisp
516 W/m2 Direct Solar

## Slide 37: Modeling the Radiation in TD
Terrestrial Orbit
  Made by Shaun Thompson, updated data for VASI requirements’ case
  Did test runs to understand how TD models diffuse/direct/ground/sky values

## Slide 38: Result
Used emissivity of .55 and absorptivity of .4 (Bare Titanium According to Spacecraft Thermal Control Handbook)

## Slide 39: Straked boomlet emissivity study

## Slide 40: Finned boomlet emissivity study

## Slide 41: Finned Boomlet Absortivity Study

## Slide 42: Optical Properties
Titanium may react with the Venus environment which could lead to color changes
  This would affect the optical properties
Ideally want lower emissivity properties, but as shown by the results this is only really needed in the upper atmosphere
  In the lower atmosphere the IR radiation actually “helps” the boomlet’s temperature response time
Low absorptivity plating would also be nice, as that would reduce effects in the upper atmosphere significantly

## Slide 43: Adhesive Options
Many PRT mounting options are being investigated right now by Mitch Haglund and David Steinfeld
Cannot use epoxy due to outgassing
  Interior of DS is a vacuum
A copper foam press fit could be a great option
  Very low thermal mass, high conductance (10 w/m-k)
  Particles could be dangerous if they enter DS, so investigation will be done
Ceramic adhesive
  Low thermal mass and sufficient conductance (1.5 w/m-k)
  Hygroscopic (absorbs water)
Clamping restraint
  Strong mounting, moderate thermal mass
Clamp welded in place
End cap welded to boomlet tip

## Slide 44: Finned Adhesive conductivity

## Slide 45: Straked Adhesive Conductivity

## Slide 46: Future Design
Both boomlets have potential to be the design choice
  More investigation into number of fins, spacing of fins, diameter of fins could lead to a more optimal design.
  Finned boomlet improvement in thermal mass lag would greatly help under 40km.

## Slide 47: Conclusions and next steps
Finned Boomlet has the best response time in upper atmosphere, though not as accurate below 40km (still within .5K though)
  However, investigation should be conducted due to increased convection values according to Fluent
Radiative environment is very significant in the scope of temperature measurement requirements
Optical properties may be beneficial in terms of absorptivity, but not necessary for emissivity.
As design develops, the thermal models developed can be adjusted and tested.
Further Investigation
  Stagnation Heating
  Convection variance
  Titanium chemical reactions

## Slide 48: Additional Experiences and Closing Remarks
SSDIF Tour
  Thanks to Brian Parsons and Brian Comber for setting this up
Space Telescope Science Institute in Baltimore
  JWST Mission Operations Center
  Thank you to Bruce Barringer
DAVINCI Venus Chambers Tour
Supercomputer Tour
TARDIS 2.0 Work with Seth Abramczyk
  Along with Elliot Schwartz and Connor Riedman
Many OSTEM Networking and Professional Development events
Cube Sat Thermal Diagnosis
Thank you all for a great experience!
Highlighted on national intern day!

## Slide 49: Acknowledgements
Mentors: Daniel Bae and Seth Abramczyk
Kimberly Brown, Veronica Otero, and Branch 545 management for making this opportunity happen!
Thank you to Mitch Haglund (543) for his mentorship as well!
Additional Support from:
  Shaun Thompson
  David Steinfeld
  Xiaoyi Li
  Stephanie Vidal
  Ralph Lorenz (APL)
  Dave Crisp (JPL)
  Matthew Shacka
  Jordan Effron
  Brian Langbein

## Slide 50
Backup

## Slide 51: Finned Boomlet Wire Cond. Sens.

## Slide 52: Finned Boomlet Wire Cond. Sens.

## Slide 53: Finned Boomlet Wire Cond. Sens.

## Slide 54: Finned Boomlet Wire Cond. Sens.

## Slide 55: Radiation Sensitivity Study, before I knew rad

## Slide 56: Emissivity sensitivity, outdated radiation

## Slide 57: All three boomlets, with additional finned e = .1, outdated radiation