## Slide 1: Critical Awareness
Ryan Lawrence
NASA, Gateway SMA
9/24/2024

## Slide 2: Background / History
xEMU: FMEA process determined concerns with:
  Loss of Suit Lights
  Loss of Visibility through helmet
  Loss of Data Comm
  Loss of Voice Comm
  Loss/Corruption of Video
Key concern was that crew needed certain information to make safety critical decisions.
Led to determination that “critical awareness” was needed to keep crew safe.

## Slide 3: Purpose & Scope
This presentation aims at defining and understanding the concept of “critical awareness” and addressing its most common forms in human spaceflight.
The goal being to advance the acceptance of critical awareness as being a necessary part of safety and safety analysis in the Gateway community and other Spaceflight programs.

## Slide 4: What is Critical Awareness? Background:
When evaluating loss of component function, the spacesuit & Gateway safety teams had to examine what the effects would be due to loss of:
  Voice Communication
  Lighting
  Data
  Video
  Vision
None of which cause an immediate loss of life, but all can contribute to significant, and potentially catastrophic, effects if lost.
Historically, capturing these types of awareness in hazard space were either only partially addressed or completely taken for granted.

## Slide 5
Situational Awareness
Critical Awareness
Situational Awareness - can be defined simply as “knowing what is going on around us”,[i] or – more technically – as “the perception of the elements in the environment within a volume of time and space, the comprehension of their meaning and the projection of their status in the near future”
Critical Awareness – Types of situational awareness (SA) needed to keep an individual safe from critical or catastrophic harm.
(For safety analysis, it is the types of SA needed as hazard controls or to enable hazard controls.)

## Slide 6: Awareness Examples (EVA)
Situational Awareness:
Smell of suit
Taste of drinking water
Sound of Vent Loop fans
View of Earth
Making Science Observations
Critical Awareness:
See Display, Hear CWS, Comm with MCC,
Tactile switch feedback

## Slide 7: Now that we have defined “Critical Awareness”, let’s examine:
1. What is required to achieve it?
2. What forms does it take?
3. How does it impact safety?
4. How do we make sure it is available when needed?

## Slide 8: What is needed to achieve “critical awareness”?
As with any type of awareness, there are two ingredients:
  1. Inputs. Adequate Information from the surrounding environment to convey existing state/conditions.
  2. Cognition. Ability to process the inputs to form an adequate understanding about existing state/conditions.
Example: Low O2 while EVA
  Inputs: Audio: suit alarm and/or MCC verbal warning can be heard, Visual: Display info
  Cognition: Audio: crew understand what alarm means, MCC message is intelligible, Visual: Display information sufficient to convey problem.

## Slide 9: Critical Awareness: Inputs
What forms do the inputs take? Humans process inputs through their senses:
  Hearing – essential for voice comm, alerts, and other audio cues
  Seeing – reading displays, determining state & location & condition
  Feeling – tactile response; switch position, safe EVA translation, etc…
  Smelling – rarely used for safety, perhaps to detect fire/contamination (not appropriate for hazard controls)
  Tasting – rarely used for safety, (not appropriate for hazard controls)

## Slide 10: Critical Awareness: Cognition
How do crew understand environmental inputs
  Hearing – Intelligible speech, adequate volume, msg meaing
  Seeing – Intelligible displays, contrast & lighting – shape recognition
  Feeling – tactile feedback, sufficient to recognize state
Information Processing: (Leading to Cognitive Fatigue)
  Complexity
  Volume/Amount
  Speed

## Slide 11
What makes “awareness” so important for safety?

## Slide 12: What makes “awareness” so important for safety?
Just as the data a computer receives is vital to making critical calculations, so too is the information a human receives to critical decision making.
Sensor Input
Computer Processor
Calculated Decision
Computer
Ex.s
GNC
Press Cntrl

## Slide 13: What makes “awareness” so important for safety?
Just as the data a computer receives is vital to making critical calculations, so too is the information a human receives to critical decision making.
Enviro Input
Mental Processing
Informed Decision
Human
Ex.s
KOZ
Mate/
demate

## Slide 14: But How do we Determine What Inputs Are Needed for Safety?
Decision making that involves crew safety or mission success, is the touchstone of determining if inputs contribute to a level of awareness that is critical.
  Example:
    An EVA sharp edge. An operational control may inform the crew about a Keep Out Zone (KOZ).
    BUT…how does that translate to the crew?
      Crew have to be informed of KOZ
      Crew has a make decision on how to avoid it when translating in the area.
    Thus, a KOZ control requires knowledge and decision making that rely on situational awareness…(comm, vision, video for MCC,…).
    To ensure this awareness is achieved, that awareness must be protected and made reliable, by safeguarding them as controls.
Info
Info
Info

## Slide 15: Understanding how information is used to make decisions
Example: Car Back-Up Camera
Situation: Driver to drive car backwards, driveway to road.
Info Needed: Situational awareness of what is behind the car while backing up
Consequence: kids and vehicles in area; impact in worst-case = fatal
Importance of Information: Driver requires adequate awareness to drive safely and prevent impact events which have the potential for catastrophic effects
Used: Video display primary, mirror/direct sight secondary

## Slide 16: Understanding how information is used to make decisions
Example: Car Back-Up Camera
In this example:
  Situational enviro assessed
  Decision consequences evaluated
  Information used to make decisions and take action identified
Result: inputs used to achieve critical awareness identified
Video
Mirror
Direct Visual

## Slide 17: Understanding how information is used to make decisions
Example: Car Back-Up Camera
These inputs can now be assessed for effects of failure. (ex. Erroneous data)
Note: In this example, the 3 input paths are redundant, but redundancy doesn’t affect the potential severity of the negative outcome.
Any of the three could be used and result in the negative outcome.
Video
Mirror
Direct Visual

## Slide 18: Understanding how information is used to ensure safety
Summary
  Here, critical decisions require critical awareness
  Critical awareness is derived from adequate inputs.
  Appreciating which inputs are used/ or have the potential to be used in critical decision making.
Video
Voice
Data

## Slide 19: Understanding how info is used to make decisions
EX. EVA Video and Voice Comm
Is EVA Video used to help make critical decisions? Is it in the decision path?
Video is used in decision making to keep crew safe.
Crew Translates
MCC sees near KOZ
MCC call up to avoid
Crew takes different path
MCC notices tether tangle
MCC call to adjust tether placement

## Slide 20
Summary
  Critical decisions may require critical awareness
  Critical awareness is derived from adequate inputs.
  Adequate inputs = adequate information
  Assessing situations, the potential consequences, and the information used to make critical decisions leads to identification of sources of information that lead to critical awareness
Situation Analysis
Needed (Critical) Awareness
Required (Critical) information