## Slide 1: Synthesis Methods to Auralize Rotor Noise for Transitional Flight
Siddhartha
Krishnamurthy
Applied Acoustics Branch
NASA Langley Research Center
Hampton, VA, USA
Fall 2024 Acoustics Technical Working Group Meeting
October 9, 2024
Co-Investigators:
Brian C. Tuttle (Analytical Mechanics Associates)
Aric R. Aumann (Analytical Services and Materials)
Stephen A. Rizzi (NASA Langley)
Leonard V. Lopes (NASA Langley)
Stefan J. Letica (NASA Langley)
D. Douglas Boyd, Jr. (NASA Langley)

## Slide 2: Auralizations can help understand human response to Urban Air Mobility (UAM) vehicles in transitional flight

## Slide 3: For auralization, sound is synthesized near aircraft (presentation focus) before propagating to a ground observer
Direct Path
Reflected Path
Ground Observer
Synthesized Sound
NASA Auralization Framework (NAF) performs sound synthesis and propagation

## Slide 4: Methods exist to synthesize loading and thickness (tonal) noise and broadband self noise
Blade Thickness & Loading
Blade Self Noise
Self Noise 1/3 Octave Band Spectral Time History

## Slide 5: Blade aerodynamics and geometry data are needed for acoustic predictions, which are then used to synthesize sound
Acoustic Predictions
:
Propagate Synthesized Sound
Complete Auralization
Flyover Sound Synthesis
Input Blade Data
:
:
At/Near Source
At Ground Observer

## Slide 6: NASA Auralization Framework (NAF) Formulation 1A (F1A) Synthesis Plugin generates loading and thickness noise
NAF F1A Synthesis Plugin
Blade loadings, motions, geometry
Audible Loading and Thickness (Tonal) Noise
Vehicle Flight Path
Inputs
Output

## Slide 7: For transitional flight sound synthesis, combine blade aerodynamics and geometry data from many flight conditions
NAF F1A Synthesis Plugin
Interpolated Blade loadings, motions, geometry
Audible Loading and Thickness (Tonal) Noise
Vehicle Flight Path
Inputs
Output
Trimmed State 2 Data
Trimmed State N Data
Trimmed State 1 Data
ANOPP2 Series of Periodic to Aperiodic Interpolated Data (ASPAID)
:

## Slide 8: Loading and thickness noise synthesized for transitional flight from interpolated blade loading, motion, and geometry
NASA Urban Air Mobility (UAM) Quadrotor Reference Vehicle
Constant 40 KTAS Airspeed, 5 Degree Climb
Airspeed changing from 40 KTAS to 60 KTAS, 5 Degree Climb

## Slide 9: Methods exist to synthesize broadband self noise hemisphere predictions into sound
Observer
Exaggerated illustration shows single flight condition

## Slide 10: Self noise predictions are interpolated between different hemispheres for transitional flight synthesis
Observer
Trimmed State
Trimmed State

## Slide 11: Self noise synthesized for transitional flight from interpolated source noise hemispheres
NASA Urban Air Mobility (UAM) Quadrotor Reference Vehicle
50 KTAS, 10 deg Climb to 90 KTAS Level Cruise
50 KTAS, 10 deg Climb Only

## Slide 12: Departure and approach maneuvers with changing flight conditions auralized with self noise
NASA Urban Air Mobility (UAM) Quadrotor Reference Vehicle
Departure Sound Pressure Level (SPL) Time History

## Slide 13: Methods developed to synthesize rotor loading and thickness noise and broadband self noise for transitional flight
Future work includes:
  Complete departure and approach auralizations with loading and thickness noise
  Prepare public release of NAF Modulated Broadband Synthesis Plugin for transitional flight
Experimental data on rotor transitional flight anticipated in the coming year (2024-2025) for comparisons with auralizations
This work is in support of NASA’s Revolutionary Vertical Lift Technology Project of the NASA Advanced Air Vehicles Program
Questions?

## Slide 14: Image Sources
All images in this presentation were provided internally by NASA or generated by presenter