## Slide 1: Synergistic TEMPO Air Quality Science
Presented by Laura Judd, NASA LaRC
Contributions from:
John Hair, Rich Ferrare, Amin Nehrir, Rory Barton Grimley—LaRC
Scott Janz & John Sullivan—GSFC
Daniel Jensen—JPL

## Slide 2
Above shows maps of the geographical regions/dates sampled in June-August 2023 during STAQS.
Purpose: To integrate TEMPO satellite observations with traditional air quality monitoring to improve understanding of air quality science for increased societal benefit
The NASA DC8 for NOAA AEROMMA and GCAS on the Gulfstreams flew together all flight days except 2.
All STAQS data are publicly available at the QR code above.
2 PGN
3 TOLNet
9 PGN
4 TOLNet
6 PGN
2 PGN
1 TOLNet
2 PGN
3 TOLNet
Notes: Red dates are those that coincide with TEMPO data.

## Slide 3
Above shows maps of the geographical regions/dates sampled in June-August 2023 during STAQS.
All STAQS data are publicly available at the QR code above.
Platform | Instruments | Parameters | Sampling Strategy included Raster patterns over city of interest
JSC GV (123.4 hours) | GCAS | Column NO2 and HCHO | 
 | HSRL2 | Profiles aerosol characteristics/ozone and mixed layer heights | 
LaRC G-III (147.3 hours) | HALO | Column methane + HSRL aerosol characteristics and mixed layer heights | 
 | AVIRIS-NG (swapped for GCAS after Aug 15) | Many—but the primary for this mission being methane and CO2 emissions estimates | 
9 PGN
4 TOLNet
6 PGN
2 PGN
1 TOLNet
2 PGN
3 TOLNet
Notes: Red dates are those that coincide with TEMPO data.

## Slide 4
GEOCAPE Airborne Simulator (GCAS)
Data Products:
NO2 column density: 250 m x 550 m
  Has a nearly 1:1 relationship with the PGN Pandora observations (within 25% according to DS).
  Comparisons indicate a slight high bias in GCAS of ~1E15 like due to reference assumptions.
HCHO column density: 750 m x 1250 m
  PGN correspond in magnitude with GCAS HCHO but with poor correlation. Results differing dramatically between direct-sun and sky scan comparisons.
GCAS is an airborne UV-VIS pushbroom spectrometer meant to satellite measurements like those from TEMPO, GEMS, TROPOMI
Contacts: Scott Janz—scott.j.janz@nasa.gov
Laura Judd—laura.m.judd@nasa.gov

## Slide 5
PSPI NO2-01: Distinguish high NO2 urban areas from nearby rural areas for three select urban-rural scene combinations.
TEMPO
Validation
Notes: If you’ve looked at the TEMPO validation document, All results are centered around these PSPIs. Product specific performance indicators. This talk is centered around how GCAS addresses some of them indicators.

## Slide 6
PSPI NO2-07: Assess bias, precision, and uncertainty of the tropospheric NO2 product over areas of interest using data gathered during targeted field campaigns.
Colored points represent the density cloud of individual pixel coincidences in each regional domain.
Coincidence criteria:
+/- 30 minutes
GCAS > 75% mapped TEMPO Pixel
TEMPO qa=0
TEMPO cloud effective fraction < 0.15
White dots represent the median of each dataset for all pixels mapped in a TEMPO scan with the interquartile ranges represented by the black bars.
Statistic represent all coincidences
(not individual overpasses)
High bias, I think is due to the cloud retrieval these days, but in need of further investigation.
SC r2=0.68
SC r2=0.61
SC r2=0.89
SC r2=0.71
If only looking at the precision < 1e15
NYC:r2=0.52 n=1328 m=0.68
Chicago: r2=0.65 n=884 m=0.74
Toronto: r2=0.49 n=264 m=0.66
California: r2=0.83 n=4151 m=1.04

## Slide 7
High Spectral Resolution Lidar - 2 (HSRL2)
Data Products
Aerosol Products at 355, 532, and 1064 nm
  Backscatter
  Depolarization
  Extinction/AOT
  Aerosol Type (e.g., smoke, dust, urban, marine,…)
Ozone profile
Surface weighted ozone/aerosol products
Mixed layer heights
Aerosol Backscatter
Aerosol Extinction
Ozone
Aerosol Depolarization
Near surface aerosol backscatter
Near surface ozone
~ 200 km (15 min)
HSRL2 is a nadir-viewing airborne high spectral resolution lidar (HSRL) designed to measure aerosol properties as well as ozone profiles.
HSRL2 flew with GCAS during STAQS.
Contacts: John Hair– Johnathan.W.Hair@nasa.gov
Taylor Shinger— taylor.j.shingler@nasa.gov

## Slide 8: Airborne HSRL measurements are used with machine learning algorithms to derive surface (and profile) PM2.5 concentrations
We used hourly surface PM2.5 measurements within 10 km and 15 minutes of near-surface airborne HSRL measurements to train machine learning models to derive surface PM2.5 from airborne HSRL measurements
Measurements from four NASA/LaRC airborne HSRL systems acquired during 172 flights between 2010-2024 (including STAQS) were used to train models
Approximately 1400 measurements used to train algorithms (80% of data)
Approximately 360 measurements then used to test algorithms (20% of data)
Exponential Gaussian Process Algorithms consistently gave best performance (lowest root-mean-square errors, highest correlations)
Models that used only aerosol optical thickness (AOT) and mixed layer height (MLH) performed poorly
Models that used multiple HSRL measurements of aerosol extensive and intensive parameters performed well
Poor performance
Good performance
Credit: Rich Ferrare (LaRC)

## Slide 9: Spatial/Temporal/Vertical Variability of PM2.5 derived from HSRL-2 measurements over New York City on July 26, 2023 during STAQS
Surface PM2.5
(morning)
Surface PM2.5
(midday)
Surface PM2.5
(afternoon)
PM2.5 (14:15-14:28 UT)
PM2.5 (16:45-17:05 UT)
PM2.5 (19:22-19:40 UT)
Credit: Rich Ferrare (LaRC)

## Slide 10
4𝜆 935 nm water vapor differential absorption lidar (DIAL)
  Carroll et al. 2022, AMT
2𝜆 1645 nm methane integrated path DIAL (IPDA)
  Barton-Grimley et al. 2022, AMT
532 nm high spectral resolution lidar (HSRL), 1064 nm backscatter
  Hair et al. 2008, Applied Optics
H2O DIAL
HSRL
CH4 IPDA
HSRL
CH4 IPDA, H2O DIAL, Doppler Winds, HSRL
HALO – Cross-Cutting DIAL and HSRL
Relative Humidity (DIAL)
Aerosol Optical Properties (HSRL)
H2O Differential Absorption Lidar
CH4 Integrated Path Differential Absorption (IPDA)
HALO on G-III
STAQS Co-Leads:
Amin Nehrir (amin.r.nehrir@nasa.gov)
Rory Barton-Griley (rory.a.barton-grimley@nasa.gov)
Notes: HALO is a cross-cutting lidar that supports 5 of the 6 NASA Earth Science Focus areas between methane, water vapor, and aerosol/cloud measurements. HALO has three configurations, water vapor/HSRL, methane/HSRL, and third configuration which has h20, ch4 and additional winds. CH4/HSRL which was flown for STAQS.
Third configuration with combined combined water vapor. Methane and winds coming online in the next two years
To-date, focus has been directed towards better quantifying strong CH4 point sources, but regional diffuse fluxes are still the largest contributor to the anthropogenic CH4 budget . HALO is the only lidar in the world with capability for HSRL and CH4 DIAL to measure both diffuse fluxes across different environments and point sources.

## Slide 11
Broad city scale enhancements observed between AM and PM flights
Many small point sources identified from landfills, power plants, and wastewater plants
Good correlation with in-situ CH4 DC-8 observations
AM – Mixing Layer Height
PM – Mixing Layer Height
AM - XCH4
PM - XCH4
STAQS – New York AM/PM Flights – City Enhancement

## Slide 12
AM - XCH4
PM - XCH4
Broad city scale enhancements observed between AM and PM flights
Many small point sources identified from landfills, power plants, and wastewater plants
Good correlation with in-situ CH4 DC-8 observations
DC-8 in-situ
DC8 CH4 Data – C/O NOAA CSL– AEROMMA 2023
STAQS – New York AM/PM Flights – Point Sources

## Slide 13
AVIRIS-NG
AVIRIS-NG is an airborne VIS-SWIR imaging spectrometer retrieving methane/CO2 emissions using an iterative matched filter technique.
Emission rate estimates from the noted plumes below and imagery will be publicly available soon.
Credit: Daniel Jensen, JPL
Contacts: Daniel Jensen—daniel.j.jensen@jpl.nasa.gov
Andrew Thorpe—andrew.k.thorpe@jpl.nasa.gov
Notes: Middlesex Landfill

## Slide 14
Tropospheric Ozone Lidar Network (TOLNET)
Contact: John Sullivan –john.t.sullivan@nasa.gov
Fernando Chouza—keil@jpl.nasa.gov
8 Lidars in three major domains!
New compact system deployed and tested!
Contributions to model evaluation
Contact: Jerrold Accdan—acdan@wisc.edu
Notes: Middlesex Landfill

## Slide 15
All STAQS data are publicly available at the QR code and will eventually be findable through Earthdata Search through ASDC
Thanks for listening!
Feel free to contact me at
Laura.m.judd@nasa.gov

## Slide 16
Satellite Validation: TROPOMI with STAQS GCAS NO2
Notes: This slide shows application of methods developed for TROPOMI validation in Judd et al. 2020 (https://doi.org/10.5194/amt-13-6113-2020) to STAQS data in four different cities and with TROPOMI’s updated NO2 product (v2.5).
Maps show an example overpass of coincident data. GCAS, as you can see, is more spatially refined.
The scatter plot represents the spatially degraded GCAS data to the TROPOMI pixel footprint.
TROPOMI and GCAS correlate extremely well. The only major offsets occur over very polluted scenes in NYC (previously seen as well). Higher scatter in Chicago may be attributed to increased cloud coverage during those flight days, but more investigation may be needed.