## Slide 1: Common Cause Failures Dominate and Defeat Redundancy
Harry W. Jones, Ph.D., MBA
NASA Ames Research Center

## Slide 2: Overview of common cause failures (CCFs)
Common cause failures occur when several malfunctions are produced by a single event or process.
  They can eliminate all the redundant components and disable a system.
Redundancy is used when the single unit failure probability is too high.
  Systems with high reliability requirements often use extensive redundancy.
  Redundancy improves reliability unless the failures are not independent.
Common cause failures defeat redundancy.
  No amount of redundancy can reduce the total failure probability below the common cause failure probability.
Common cause failures dominate redundancy.
  Failures of highly redundant systems are usually common cause failures.

## Slide 3: Cause and impact of common cause failures (CCFs)
Common cause failures can be due to specification, design, manufacturing, operations, or maintenance problems that affect all units.
  CCFs typically account for one tenth of all failures.
If the failure probability is low and CCFs are significant, adding more than two or three redundant units does not increase overall reliability.
CCFs can be reduced by using diverse components, technologies, and manufacturers and by avoiding shared control, power, or location.
  External events and commonalities may still cause CCFs.

## Slide 4: Common cause failures - several components fail for the same reason
Common cause failures are either same event failures, where the cause is one external happening, or same manner failures, where the systems fail in the same way for the same reason.
The reliability gain from redundancy
  If all the redundant systems have probability of failure F, and if the failures are independent,
  the probability that N redundant systems fail is FN.
If this result holds, increasing N can give an arbitrarily low failure probability.
This is unrealistic - common cause failures can disable all the redundant systems.
  Common cause failures violate the assumption of independent failures.
  Common cause failures defeat redundancy.

## Slide 5: Common cause failures dominate redundancy
Redundancy decreases the overall failure probability, but the relative portion of common cause failures increases.
Common cause failures are the main cause of system failure in nuclear power plants and in modern technological systems.
  Nuclear power plants have highly redundant designs to minimize the probability of failure.
  The monitoring, control, warning, and safety systems are highly redundant.
Common cause failures dominate the failure probability in high reliability systems.

## Slide 6: The beta factor model of common cause failures
The single system failure probability is F.
The fraction of the single system failure probability due to common cause failures is ß.
The failure probability of a system with N redundant subsystems is = ((1- ß) F) N + ß F
  ((1- ß) F) N is the probability that all N redundant units fail due to independent events.
  ß F is the common cause failure probability.
The probability that all N redundant units fail approaches zero for N large.
The common cause failure probability is a lower bound on the system failure probability.
The beta factor model shows how common cause failures can dominate and defeat redundancy.

## Slide 7: The expected range of beta factors
The beta factor is the probability that a failure has a common cause.
  The beta factor is 0.01 to 0.10 with prevention of common cause failures, but it can reach 0.20 or 0.30 with low effort.
When data is not available, the beta factor can be estimated by assessing attention to common cause failures.
  Some factors - safety culture, management effectiveness, budget and schedule constraints, training effectiveness, maintenance program, and industry failure history.
System type | Low beta | High beta
Safety systems | 0.001 | 0.25
Hardware systems | 0.01 | 0.10
Nuclear power plant equipment | 0.01 | 0.22
Electrical equipment | 0.01 | 0.30
Average | 0.01 | 0.22

## Slide 8: The beta factor limits redundancy failure reduction
The common cause failure probability, b F, is a lower bound on the redundant system failure probability.
The failure probability for N redundant subsystems is FN = ((1- ß) F) N + ß F
  Taking logarithms and solving for the required number of redundant systems N,
  N = log (FN - ß F)/log [(1- ß) F]
The required redundant system failure probability FN must be greater than ß F, since ß F is the minimum possible overall failure probability.
  If the beta factor is constant, a higher individual unit failure probability, F, requires higher redundancy N.
  If the beta factor is constant, a higher individual unit failure probability, F, produces a higher redundant system failure probability at any specific redundancy N.
  Small variations in the beta factor do not have much effect on the required redundancy N.

## Slide 9: The required redundancy N for beta = 0.10
 |  | FN, the desired redundant failure probability |  |  |  |  | 
F, unit failure probability |  | 0.01 | 0.05 | 0.1 | 0.2 | 0.3 | 0.4
 | 0.40 | no go | 5 | 3 | 2 | 2 | 1
 | 0.30 | no go | 3 | 3 | 2 | 1 | ok
 | 0.20 | no go | 3 | 2 | 1 | ok | ok
 | 0.10 | no go | 2 | 1 | ok | ok | ok
 | 0.05 | 2 | 1 | ok | ok | ok | ok
 | 0.01 | 1 | ok | ok | ok | ok | ok
The effect of FN, the desired redundant failure probability, and F, the single unit failure probability, on N, the required redundancy, for ß = 0.10.
  no go: ß F > FN, so the required FN cannot be achieved.
  Redundancy is needed, N > 1, if F > FN
  ok: F < FN, so FN is already achieved with N = 1.

## Slide 10: The beta factor limits the maximum useful redundancy N
Example – set the total failure probability with N redundant units, FN, equal to twice the common cause failure probability, FN = 2 ß F.
    This is 2 times the lower bound FN = ß F.
As ß decreases, the maximum useful redundancy increases.
  High levels of redundancy are useful only for low ß and high F.
  A high common cause factor ß > 0.2 would limit useful redundancy to N = 2 or 3.
 |  | ß, common cause failure ratio |  |  |  |  |  | 
F, unit failure probability |  | 0.01 | 0.05 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5
 | 0.40 | 7.5 | 5.0 | 3.8 | 2.5 | 1.8 | 1.3 | 1.0
 | 0.30 | 6.0 | 4.0 | 3.2 | 2.2 | 1.7 | 1.3 | 1.0
 | 0.20 | 4.8 | 3.3 | 2.7 | 2.0 | 1.5 | 1.2 | 1.0
 | 0.10 | 3.8 | 2.8 | 2.3 | 1.8 | 1.4 | 1.2 | 1.0
 | 0.05 | 3.0 | 2.3 | 1.9 | 1.5 | 1.3 | 1.1 | 1.0
 | 0.01 | 2.0 | 1.6 | 1.5 | 1.3 | 1.2 | 1.1 | 1.0

## Slide 11: Design for single thread reliability
Design for Reliability (DfR) should be integrated into the standard system design process.
  Defining requirements including reliability.
  Reliability modeling, analysis, and prediction.
  Allocating the system level reliability requirement to the different subsystems.
  Improving reliability by reducing complexity, redesigning subsystems, and selecting more reliable components.
Improving reliability can have rapidly increasing costs and diminishing returns.
  Reliability can reach a practical limit.
Redundancy is the fall back solution.

## Slide 12: Redundant system design
The simplest form of redundancy is providing complete spare systems,
  Either online hot spares or stored replacements.
Sometimes spare components are provided.
  This requires difficult troubleshooting and repair.
Adding redundancy may be more cost effective than improving reliability.
  The level and impact of common cause failures must be considered.
Safety critical systems are designed to be ultrareliable using redundancy.
  The more redundancy, the more likely that system failures will be due to common cause failures.

## Slide 13: Reducing common cause failures – diverse redundancy
Common cause failures can occur due to errors in system specifications, design, manufacturing, installation, operations, and maintenance.
Common cause failures are reduced by eliminating the coupling mechanisms, shared factors, and complex interactions that make failures dependent rather than independent.
  Use different technologies, designers, and manufacturers.
  Provide different design, hardware, software, procedures, operators, maintenance, location, and environment.
  Provide separation and shielding between components, signal channels, wiring, piping, and material flows.
Diversity does not cure errors in the original system specification, such as mistaken performance requirements or unanticipated environment or use.

## Slide 14: Summary - common cause failures limit redundancy
Redundancy may not produce the expected operational reliability.
  Common cause failures may be unexpected or underestimated.
  Fault detection and using spares may fail.
Design for one-fault or two-fault tolerance may decrease reliability.
  The increased design complexity adds failure modes.
Common cause failures dominate and defeat redundancy.
  Improving single thread reliability should be first priority.
  Redundancy is problematic but often necessary.