## Slide 1: Four problematic methods in reliability analysis
Harry W. Jones, Ph.D., MBA
NASA Ames Research Center

## Slide 2: Overview and Outline
Some basic methods used in reliability analysis are problematic.
  They produce incorrect and overoptimistic predictions.
  Favorable forecasts are often invalidated by testing and operational experience.
The problematic methods in reliability analysis include
  estimating the system failure rate as the sum of component failure rates,
  assuming that reliability growth continues forever during testing,
  overestimating the benefits of redundancy, and
  using the fault tolerance count instead of a detailed reliability analysis.
The inevitable optimistic bias should be corrected by realistic analysis that reflects experience.
  Repeated surprising poor performance suggests willful blindness.
Rigorous methods and impartial critical reviews are needed to improve reliability analysis.

## Slide 3: Reliability Prediction Errors
A common early estimate of the system failure rate sets it equal to the sum of component failure rates.
  This is a best case lower bound, but it ignores integration and system level problems.
Using the sum of component failure rates has been severely criticized.
  The published component failure rates are not trustworthy.
  The assumed constant failure rate ignores infant mortality and wear out.
  There are many system level failures due to problems in requirements, design, interfaces, manufacturing, operations, and software.
There is no standard accepted method for predicting system reliability.
  Predictions vary greatly in detail, completeness, basis in data, and dependability.
Component based reliability prediction methods can produce extremely inaccurate results.
  The predicted reliability can be tens or hundreds of times higher than the actual reliability.

## Slide 4: The Problem of Inaccurate Reliability Predictions is Well Known
“Reliability predictions have been the subject of much discussion ...
  Some articles have proclaimed them to be valueless.”
Using parts reliability to estimate system reliability has been defended.
  “(T)he practice has been to use part failure rates as a proxy, meaning that if a system has a high part failure rate it will probably have a proportionately high failure rate due to unanalyzed causes.” “It is useful for gross estimation of the achievable reliability and for assessing alternatives.”
However, the results are often highly unsatisfactory.
  “Recent research shows that these methods have produced highly inaccurate results when compared to actual test data… The ratio of predictions to demonstrated values ranges from 1. 2:1 to 218:1”
Reliability prediction “methods have been criticized as flawed and leading to inaccurate and misleading results. …
  the U.S. National Academy of Sciences has recently discredited these methods.”

## Slide 5: Cause and Cure of Reliability Prediction Errors
Reliability predictions are usually too high.
This can be explained as overoptimistic analysis and unrealistic advocacy.
  “Initial reliability estimates are invariably better than demonstrated.”
  “When “selling Congress on a system, it may seem to be politically smart to use the optimistic reliability estimates.”
Reliability predictions can be improved by basing them on the actual performance of similar systems.
  “Since field data on a similar-system is the best starting-point for quantification of the new-system reliability, it should be used to the maximum extent possible.”

## Slide 6: Over-optimistic Reliability Growth Projection
It is usually assumed that reliability growth can continue forever.
  But instead the failure rate usually reaches a constant steady state.
The reliability bathtub curve shows infant mortality, constant failure rate, and wear out.
  Reliability growth occurs only while infant mortality is being corrected.
The common failure pattern is short infant mortality followed by a constant failure rate.
  If the final constant failure rate is subtracted from the total failure rate, the infant mortality failure rate remains.
  A surprising result is that the remaining infant mortality failure rate often declines simply as n/t.
  The early failure count due to infant mortality is simply being averaged out over an increasing time period.
Applying the usual reliability growth model for an increasing test time gives n(t)/t = k t-a.
  The reliability growth exponent, a = 0 to 1, gradually decreases as the test time increases.
  As the test time gets longer, it creates a mistaken impression of indefinitely continuing reliability growth, although at an ever-decreasing reliability growth rate.

## Slide 7: The Duane-Crow and abcd Reliability Growth Models
The Duane-Crow reliability growth model:
Failure rate = n(t)/t = k t-a.
  k is a constant. The reliability growth rate is a.
  The model implies the failure rate can decrease forever but instead it usually reaches a constant low value.
The abcd model adds a second time period with a constant failure rate.
  n(t)/t = a t-b + c from t = 0 to td
  = c + d after td, where d = a td-b
Notes: The term a t-b describes the initial reliability growth period that continues out to time td and c is the constant long term failure rate. The parameter d represents an additional constant failure rate due to remaining correctable but accepted failure modes. After the reliability growth process is terminated, the failure rate n(t)/t = c + d.

## Slide 8: Reliability Growth Rate Projections Are Unrealistic
The usual Duane-Crow model has the cumulative failure rate of n(t)/t = k t-a, where a is the reliability growth exponent.
  The Duane log-log plot is of data Crow used illustrate reliability growth.
For the first three failures, the red dotted line has a = 0.62, showing rapid early reliability growth.
  If this continued, the failure rate n(t)/t would decline to 0.1 at 50 hours.
The blue dotted line fit to the full data set has a = 0.28.
  If this much slower reliability growth continued, n(t)/t would decline to 0.1 at about 500 hours.
This reliability growth projections are unrealistic.
  The data shows a roughly constant cumulative failure rate after 50 to 100 hours.
Chart: Cumulative failure rate
| 0.7 | 3.7 | 13.2 | 15 | 17.600000000000001 | 25.3 | 47.5 | 54 | 54.5 | 56.4 | 63.6 | 72.2 | 99.2 | 99.6 | 100.3 | 102.5 | 112 | 112.2 | 120.9 | 121.9 | 125.5 | 133.4 | 151 | 163 | 164.7 | 174.5 | 177.4 | 191.6 | 192.7 | 213 | 244.8 | 249 | 250.8 | 260.10000000000002 | 263.5 | 273.10000000000002 | 274.7 | 282.8 | 285 | 304 | 315.39999999999998 | 317.10000000000002 | 320.60000000000002 | 324.5 | 324.89999999999998 | 342 | 350.2 | 355.2 | 364.6 | 364.9 | 366.3 | 373 | 379.4 | 389 | 394.9 | 395.2
n(t)/t | 1.4286 | 0.54054 | 0.22727 | 0.26667 | 0.28409 | 0.23715 | 0.14737 | 0.14815 | 0.16514 | 0.1773 | 0.17296 | 0.1662 | 0.13105 | 0.14056 | 0.14955 | 0.1561 | 0.15179 | 0.16043 | 0.15715 | 0.16407 | 0.16733 | 0.16492 | 0.15232 | 0.14724 | 0.15179 | 0.149 | 0.1522 | 0.14614 | 0.15049 | 0.14085 | 0.12663 | 0.12851 | 0.13158 | 0.13072 | 0.13283 | 0.13182 | 0.13469 | 0.13437 | 0.13684 | 0.13158 | 0.12999 | 0.13245 | 0.13412 | 0.13559 | 0.1385 | 0.1345 | 0.13421 | 0.13514 | 0.13439 | 0.13702 | 0.13923 | 0.13941 | 0.13969 | 0.13882 | 0.13928 | 0.1417
 | 1.4286 | 0.54054 | 0.22727 | 0.1

## Slide 9: Reliability Growth Rate Projections Are Misleading
The reliability growth exponent, a, is usually large, approximately 1, for early testing, as infant mortality failures are corrected.
  As the test period is extended into the period of constant failure rate, the reliability growth exponent, a, gradually declines toward zero.
If the usual Duane-Crow reliability growth model with n(t)/t = k t-a, is fitted to the cumulative failure rate data, it can be used to estimate the test time needed to achieve any specific lower failure rate, even zero or negative failure rates.
  These projections are extremely misleading since reliability improvement becomes increasingly difficult and the failure rate usually becomes constant after the initial period of infant mortality.
This is an obvious well known problem that is not explained in reliability growth analysis.

## Slide 10: Common Cause Failures Limit the Gains of Redundancy
The benefits of redundancy can be overestimated because of two significant problems.
  Redundancy adds new failure modes in the systems that monitor failures and replace components.
  Redundancy can be defeated by common cause failures.
Common cause failures occur when several system components fail due to a single incident or one precipitating factor.
  Common cause failures limit redundancy.
No level of redundancy can reduce the probability that the redundant system will fail to less than the probability of a common cause failure.
  Common cause failures may comprise ten percent of all failures and can limit the useful amount of redundancy to one or two spares per component.

## Slide 11: Redundancy Can Increase Reliability, Up to a Limit
If common cause failures are neglected, the reliability gain from redundancy appears large.
  If the redundant components all have the probability of failure F, and the failures are independent, the probability that the N redundant systems all fail is FN.
  If F is less than one, FN approaches zero for N large.
  It seems possible to achieve an arbitrarily low failure probability by continuing to increase redundancy.
This is unrealistic because common cause failures can damage all the redundant components.
The beta factor, ß, is the fraction of all the failures that are common cause failures.
  If the single system failure probability is F, the common cause failure probability is ß F.
  The total failure probability of a system with N redundant subsystems is FN = ((1- ß) F) N + ß F.
  The first term is the probability that all N redundant units fail, and it approaches zero for N large.
The total failure probability cannot be reduced below ß F, the common cause failure probability, no matter how much redundancy is used.

## Slide 12: The Failure Probability Decrease With Redundanccy
The beta factor can be 0.01 to 0.10 if common cause failures are eliminated, but it can reach 0.20 or 0.30 if they are not removed.
The figure shows that when the beta factor is high, ß = 0.3, (red and blue) increasing the redundancy reduces the failure probability very slowly and the failure probability remains above ß F.
  Redundancy beyond N = 2 or 3 gives little improvement.
When the beta factor is low, ß = 0.01, increasing the redundancy reduces the failure probability rapidly and the failure probability becomes relatively small.
  Redundancy beyond N = 3 improves failure probability.
Common cause failures limit the potential gains of redundancy.
Underestimation of the effect of common cause failures can lead to an overconfidence in redundancy.
Chart: Failure probability decrease with redundancy
| 1 | 2 | 3 | 4 | 5
F = 0.3, ß = 0.3 | 0.3 | 0.1341 | 0.099261 | 0.091945 | 0.090408
F = 0.3, ß = 0.01 | 0.3 | 0.091209 | 0.029198 | 0.010781 | 0.0053109
F = 0.1, ß = 0.3 | 0.1 | 0.0349 | 0.030343 | 0.030024 | 0.030002
F = 0.1, ß = 0.01 | 0.1 | 0.010801 | 0.0019703 | 0.0010961 | 0.0010095

## Slide 13: Using Fault Tolerance to Gain Reliability
NASA has used a fault tolerance requirement to improve safety since the beginning of the space age.
  A one-fault tolerant system can operate after one failure.
  NASA continues to require one-fault tolerance for catastrophic events.
A design for fault tolerance can actually reduce safety.
  Fault tolerance requires adding complexity and new failure modes.
  Reliability should be checked by direct analysis.
Currently both probabilistic reliability analysis and fault tolerance are required by NASA.
  Analysis is sometimes neglected in favor of fault tolerance.

## Slide 14: The Four Problematic Methods Are Too Optimistic
The four problematic methods in reliability analysis all produce unrealistically high estimates of system reliability.
Optimistic reliability and safety assessments have been described as “fantasy plans” that “make wildly optimistic and unrealistic statements.”
  The creation of fantasy plans seems instinctive and unintentional, due to an optimism bias.
  Fantasy plans are usually not deliberately created to deceive people, but can have that effect.
  And there may be cases of “willful blindness”and “strategic misrepresentation.”
Favorable errors in reliability prediction are systematic and predictable.
  They seem due to the optimism bias rather than random mistakes.
  Such errors persist and seem impossible to correct, even when they are frequent and well known.
  Understanding our biases does not correct them.

## Slide 15: Need for Open Communication and Critical Thinking
Organizational performance is improved by open communication and discussion.
  Everyone should feel free to ask questions and raise problems.
This is more necessary in reliability and safety, which are important but hard to discuss.
  It is not easy to say that reliability is poor or that reliability estimation methods don’t work.
The natural reluctance to raise problems may be why overoptimistic reliability estimates and unreliable estimation methods are not corrected.
Steps to encourage open discussion are to conduct critical reviews, establish red teams, appoint a devil’s advocate, use diverse expertise, directly create challenges, and develop counter arguments.
  Team members should be encouraged to speak up about potential risks and failure modes, develop critical thinking, and include multiple perspectives.

## Slide 16: Reference Class Forecasting
Reference class forecasting can provide a realistic reliability assessment by using historical data.
  It uses Nobel prize winning theories of decision-making in Daniel Kahneman’s book, Thinking, Fast and Slow.
The three basic steps in reference class forecasting are:
1) identifying the reference class of similar past projects,
2) organizing the data on the reliability, cost, environment, and other attributes of the projects,
3) predicting the new project’s reliability based on its multidimensional similarity to the past projects.
Project data should include attributes related to reliability, such as cost, environment, mass, design iteration, etc.
The reliability of each past project and its similarity to the new project are used to estimate the new project reliability.

## Slide 17: Summary & Conclusions
The problematic methods used in reliability analysis involve estimating the failure rate, modelling reliability growth, implementing redundancy, and using fault tolerance.
While these methods are traditional, widely accepted, and often required, they are well known to be unsatisfactory and seem to reflect overoptimism and favorable bias.
Using actual data on the reliability results of similar projects can provide more realistic reliability analysis.