## Slide 1: Modeling Reliability Growth
Harry W. Jones, Ph.D., MBA
NASA Ames Research Center

## Slide 2: Reliability Growth Modeling and Testing
The reliability growth process consists of testing a system, experiencing failures, finding the failure causes, and redesigning the system to remove them.
Reliability growth data often show a high initial failure rate due to infant mortality followed by a later constant low failure rate.
  A two part failure rate model with an initial exponential decline followed by a constant failure rate usually fits the data.
  This is more realistic than the traditional model which has the exponential decline without the final constant failure rate.
The cost of reliability growth increases with the number of failure modes and the time needed for them to occur and be removed.
  Reliability growth testing has diminishing returns, since it takes longer for the less probable failures to occur and be removed.

## Slide 3: Reliability Growth Modeling Overview
A simple two phase model of reliability growth is introduced.
A group of rapid early failures is followed by a constant failure rate.
  The cumulative failure rate n(t)/t due to N early failures can decline as rapidly as N/t or N t -1 .
  n(t)/t declines more slowly if more failures occur.
9 of 14 data sets conform to the model
  Reliability growth is approximately as n(t)/t = 1/t or t -1.
  There are substantial final failure rates , ~ 10 - 20% of maximum.
  5 of the 14 data sets show no reliability growth.

## Slide 4: The Bathtub Curve and Reliability Growth
The blue real time failure rate has “infant mortality,” random failures during useful life, and wear out.
The red cumulative failure rate is n(t)/t, the total number of failures up to time t divided by t.
The initial decline of the cumulative failure rate, n(t)/t, is usually described as reliability growth.
More than two-thirds of all systems show infant mortality and then a constant failure rate, but no end-of-life aging period.
Chart: Failure rates
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40
Real time failures | 3.5 | 3 | 2.5 | 2 | 1.5 | 1.2 | 0.9 | 0.7 | 0.6 | 0.55 | 0.52 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.52 | 0.55 | 0.6 | 0.7 | 0.9 | 1.2 | 1.6 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5
Cumulative failure rate, n(t)/t | 3.5 | 3.25 | 3 | 2.75 | 2.5 | 2.2833 | 2.0857 | 1.9125 | 1.7667 | 1.645 | 1.5427 | 1.4558 | 1.3823 | 1.3193 | 1.2647 | 1.2169 | 1.1747 | 1.1372 | 1.1037 | 1.0735 | 1.0462 | 1.0214 | 0.9987 | 0.97875 | 0.9616 | 0.94769 | 0.93852 | 0.93714 | 0.94621 | 0.968 | 1.0013 | 1.0481 | 1.1073 | 1.1776 | 1.2583 | 1.3483 | 1.447 | 1.5537 | 1.6677 | 1.7885

## Slide 5: Modeling Reliability Growth
The orange curve shows three failures occurring before t = 1.
  In this case n(t)/t = 3/t = 3 t -1.
  The reliability growth curve has the exponent - 1.
The blue curve shows ten failures occurring before t = 6.
  The reliability growth curve has the exponent - 0.81.
The red curve has the same ten failures occurring before t = 6 plus a constant failure rate of 0.5 failures per unit time.
  Here the reliability growth curve has the exponent - 0.50.
Chart: Cumulative failure rate, n(t)/t
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40
Failures t = 1 to 6 & constant | 3.5 | 3.25 | 3 | 2.75 | 2.5 | 2.25 | 2 | 1.8125 | 1.6667 | 1.55 | 1.4545 | 1.375 | 1.3077 | 1.25 | 1.2 | 1.1562 | 1.1176 | 1.0833 | 1.0526 | 1.025 | 1 | 0.97727 | 0.95652 | 0.9375 | 0.92 | 0.90385 | 0.88889 | 0.875 | 0.86207 | 0.85 | 0.83871 | 0.82812 | 0.81818 | 0.80882 | 0.8 | 0.79167 | 0.78378 | 0.77632 | 0.76923 | 0.7625
Failures t = 1 to 6 | 3 | 2.75 | 2.5 | 2.25 | 2 | 1.75 | 1.5 | 1.3125 | 1.1667 | 1.05 | 0.95455 | 0.875 | 0.80769 | 0.75 | 0.7 | 0.65625 | 0.61765 | 0.58333 | 0.55263 | 0.525 | 0.5 | 0.47727 | 0.45652 | 0.4375 | 0.42 | 0.40385 | 0.38889 | 0.375 | 0.36207 | 0.35 | 0.33871 | 0.32812 | 0.31818 | 0.30882 | 0.3 | 0.29167 | 0.28378 | 0.27632 | 0.26923 | 0.2625
Failures before t = 1 | 2.5 | 1.25 | 0.83333 | 0.625 | 0.5 | 0.41667 | 0.35714 | 0.3125 | 0.27778 | 0.25 | 0.22727 | 0.20833 | 0.19231 | 0.17857 | 0.16667 | 0.15625 | 0.14706 | 0.13889 | 0.13158 | 0.125 | 0.11905 | 0.11364 | 0.1087 | 0.10417 | 0.1 | 0.096154 | 0.092593 | 0.089286 | 0.086207 | 0.083333 | 0.080645 | 0.078125 | 0.075758 | 0.073529 | 0.071429 | 0.069444 | 0.067568 | 0.065789 | 0.064103 | 0.0625

## Slide 6: Modeling the Crow Data Set
The Crow data set has the expected reliability growth pattern, with infant mortality, a rapidly declining cumulative failure rate, and a final constant failure rate.
  If the final constant failure rate is subtracted from the cumulative failure rate, the cumulative failure rate due to infant mortality rapidly declines to zero.
  The cumulative failure rate minus the final constant failure rate declines nearly as 1/t or t -1,
A power law curve fit shows that the reliability growth exponent is 0.96, showing nearly maximum reliability growth.
Chart: Crow data, first 10 failures, cumulative failure rate
| 0.7 | 3.7 | 13.2 | 15 | 17.600000000000001 | 25.3 | 47.5 | 54 | 54.5 | 56.4
n(t)/t -0.135 | 1.2936 | 0.40554 | 0.092273 | 0.13167 | 0.14909 | 0.10215 | 0.012368 | 0.013148 | 0.030138 | 0.042305

## Slide 7: Modeling 14 Data Sets (Crow Plus 13)
Reliability growth following the two phase model occurs in 10 of the 14 data sets.
  9 sets have the reliability growth exponent between 0.93 and 1.18.
  The final failure rate is between 2.4% and 28.7% of the initial failure rate, average 17%.
  One 27 failure set shows little reliability growth, final failure rate 53% of initial failure rate.
In the other 4 data sets, there was no reliability growth.
  The final failure rate is 2 to 5 times the initial failure rate.
The model fits but there is an issue.
Number of failures | Reliability growth exponent | Final failure rate %
56 | 0.99 | 9.8%
41 | 1.01 | 9.4%
27 | 0.49 | 53%
27 | 0.93 | 3.7%
19 | 1.07 | 6.9%
16 | 1.14 | 18.1%
15 | 0.93 | 2.4%
10 | 1.18 | 17.5%
8 | 1.17 | 28.7%
7 | 1.10 | 19.3%

## Slide 8: Reliability growth exponent greater than 1.0? No!
A reliability growth exponent greater than 1.0 is impossible.
  n/t cannot decline faster than as 1/t or t -1.
The chart shows two curves.
  The upper blue 1/t with a power law curve fit of x -1.
  The lower red 1/t - 0.2 with a power law curve fit of x -1.15.
The problem is over correction.
  A cumulative failure rate decline faster than 1/t or t -1 is caused subtracting too large a long term constant failure rate.
Chart: Cumulative failure rates
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
n(t)/t | 1 | 0.5 | 0.33333 | 0.25 | 0.2 | 0.16667 | 0.14286 | 0.125 | 0.11111 | 0.1 | 0.090909 | 0.083333 | 0.076923 | 0.071429 | 0.066667
n(t)/t - 0.2 | 0.98 | 0.48 | 0.31333 | 0.23 | 0.18 | 0.14667 | 0.12286 | 0.105 | 0.091111 | 0.08 | 0.070909 | 0.063333 | 0.056923 | 0.051429 | 0.046667

## Slide 9: How Long Does Reliability Growth Continue?
For this check, the end of reliability growth was defined as the time when the cumulative failure rate fell below twice the final failure rate.
The number of failures during this reliability growth period varied from 2 to 12 with an average of about 6.
Except for two cases, the reliability growth period was between 25 and 50% of the total test time.
  Two varied more widely, due to very long testing in the 56 failure Crow data set and the long clock time of the 10 failure data set.
Total number of failures | Number of failures during reliability growth | Percent of failures during reliability growth
56 | 5 | 8.9%
41 | 10 | 24.4%
27 | 12 | 44.4%
19 | 5 | 26.3%
16 | 4 | 25.0%
15 | 7 | 46.7%
10 | 7 | 70.0%
8 | 2 | 25.0%
7 | 3 | 42.9%

## Slide 10: Reliability Growth Testing and Model Fitting
Reliability growth testing observes and corrects failure modes, records the failure times, and computes the cumulative failure rate.
  If reliability growth occurs, the two-phase model fits the data.
  An example uses the first five failures in the Crow data set.
A series of trial model fits is shown in Table 4.
Successively approximating, the final estimate for the assumed constant failure rate is 0.1965 and the reliability growth exponent is 0.998.
The first five data points of the Crow data set show that reliability growth follows the two-phase model.
  An initial exponential failure rate decline is followed by a constant failure rate.
Trial number | Assumed constant failure rate | Reliability growth exponent
1 | 0.0000 | 0.546
2 | 0.2200 | 1.227
3 | 0.1100 | 0.706
4 | 0.1600 | 0.836
5 | 0.1900 | 0.961
6 | 0.1950 | 0.989
7 | 0.1970 | 1.001
8 | 0.1960 | 0.995
9 | 0.1965 | 0.998

## Slide 11: Conclusion
The first tests of a new system often find an unexpectedly high initial failure rate.
  This infant mortality can be caused by mistaken requirements or errors in design.
During reliability growth, the failure modes are identified and removed.
  The difficulty and cost of reliability growth process depend on the number and probability of the failure modes.
The higher probability failure modes tend to occur and be removed earlier, producing rapid initial reliability growth.
  Continued testing often reveals a continuing long term constant failure rate.
A two part failure rate model with an initial exponential decline followed by a constant failure rate usually fits the data.