## Slide 1: Using Airborne Passive Microwave Observations for Cloud and Precipitation Science
Presenting author: Corey G. Amiot1
Co-authors: Timothy J. Lang2, Clay B. Blankenship2, J. Brent Roberts2, Rachael A. Kroodsma3, Benjamin T. Johnson4, Mircea Grecu3, and Ian S. Adams3
1NASA Postdoctoral Program, NASA Marshall Space Flight Center
2NASA Marshall Space Flight Center
3NASA Goddard Space Flight Center
4UCAR Joint Center for Satellite Data Assimilation
NPP Symposium Presentation
November 2024

## Slide 2: Purpose
Clouds and precipitation affect global water cycle and energy budget (e.g., Reid et al. 2023)
Compared with spaceborne sensors, airborne sensors can provide finer-scale data and dedicated sampling
  Resolve finer-scale atmospheric features
  Some drawbacks, including limited horizontal and vertical coverage
Results from airborne campaigns may be applicable to spaceborne platforms
  E.g., frequency overlaps between airborne and spaceborne radiometers
Source: Lang et al. (2021)
Background & Radiometers
Radiometer Data Mergers & Testing
Applications & Ongoing Analyses

## Slide 3: Passive Microwave Observations
All surfaces with temperature > 0 K emit radiation; however, exact emission efficiency (emissivity) might not be known in advance
Assume surface is a perfect emitter of radiation (i.e., a blackbody); observations can be reported as a brightness temperature (Tb) value
Surfaces that have a lower emissivity will yield a lower Tb due to these assumptions, all else being equal
Includes reflected + scattered radiation
  Example of oceanic scene on right
Source: NASA GPM (2024)
Background & Radiometers
Radiometer Data Mergers & Testing
Applications & Ongoing Analyses

## Slide 4: Passive Microwave Retrievals
Integrated and near-surface atmospheric properties may be retrieved using brightness temperature (Tb) combinations from microwave frequencies (e.g., Wilheit and Chang 1980; Wentz and Spencer 1998; Wentz and Meissner 2007; Hong and Shin 2013)
Lower frequencies become attenuated less quickly
Higher frequencies increasingly sensitive to precipitation, clouds, and water vapor
Retrievals include: columnar cloud liquid water path (CLW), total precipitable water vapor (WV), and 10-m wind speed over water (WS) (e.g., Wentz and Meissner 2000, 2007; Biswas et al. 2017; Amiot et al. 2021)
Example of AMPR retrievals during OLYMPEX/RADEX
Background & Radiometers
Radiometer Data Mergers & Testing
Applications & Ongoing Analyses

## Slide 5: Overview of Radiometers
Advanced Microwave Precipitation Radiometer (AMPR), NASA MSFC
Covers 10.7–85.5 GHz
90° cross-track scans beneath aircraft
Retrieves: cloud water and ice contents, precipitation, atmospheric water vapor, and near-surface ocean winds
Conical Scanning Millimeter-wave Imaging Radiometer (CoSMIR), NASA GSFC
Covers 50.3–183.31 GHz
Conical and cross-track scans
Retrieves: info about clouds and precip, both liquid and ice
Source: GHRC (2023)
Source: Kroodsma et al. (2023)
Source: NASA ASP (2024)
Compact Scanning Submillimeter-wave Imaging Radiometer (CoSSIR), GSFC
Covers 170.5–684.0 GHz
Conical and cross-track scans
Retrieves: info about clouds, especially sensitive to ice
Background & Radiometers
Radiometer Data Mergers & Testing
Applications & Ongoing Analyses

## Slide 6: Merging Radiometer Data
CoSMIR/CoSSIR for background lattice
  Narrower swath during OLYMPEX/RADEX
  Applies for cross-track and conical mergers
Identify flight segments of interest and use nearest-neighbor method to match AMPR pixel with CoSMIR/CoSSIR pixel
  Find tandem flights when on separate aircraft
Keep track of properties for all pixels
  E.g., resolution, EIA, beamwidth, etc.
Right: conical CoSMIR (top) and original AMPR (bottom) Tb data along with the remapped AMPR Tb data (middle)
  Top two panels would go into merged product
Background & Radiometers
Radiometer Data Mergers & Testing
Applications & Ongoing Analyses

## Slide 7: Merging Radiometer Data
AMPR-CoSSIR merger during ~90-min flight segment from IMPACTS 2023
Background & Radiometers
Radiometer Data Mergers & Testing
Applications & Ongoing Analyses
Mean clear-air Tb differences between 85-GHz AMPR and 89-GHz CoSMIR generally < 2 K (<3 K) for cross-track (conical) data mergers

## Slide 8: Applications of Merged Dataset
Better understanding of processes often unresolved with spaceborne radiometers
  However, results may be applicable to spaceborne platforms
Can combine retrievals and Tb data with radar reflectivity to gain more in-depth perspective on given cloud and/or precipitation region
  Powerful when examined in environmental context (e.g., from atmospheric soundings)
Relevance to Earth Science Decadal Survey and NASA’s 2022 Strategic Plan
  GPM, INCUS, and AOS missions
Background & Radiometers
Radiometer Data Mergers & Testing
Applications & Ongoing Analyses

## Slide 9: Ongoing Analyses
Geophysical retrievals (e.g., cloud liquid water and near-surface winds) using adapted radiative transfer model + 1DVAR
Examine and quantify trends in these retrievals and Tb around edges of precipitation regions
Finalize applications across four NASA airborne campaigns
This work has been supported by an appointment to the NASA Postdoctoral Program at NASA Marshall Space Flight Center, administered by Oak Ridge Associated Universities under contract with NASA
Contact email: corey.g.amiot@nasa.gov
Background & Radiometers
Radiometer Data Mergers & Testing
Applications & Ongoing Analyses