## Slide 1: Innovations in Distributed Spacecraft Autonomy
Caleb Adams
Project Manager (DSA) ; Deputy Project Manager (Starling)

## Slide 2: Multi Spacecraft Missions
MagCon
CYGNSS
SWARM
Pléiades Neo
LISA
SunRISE
ESCAPADE
EZIE
BRITE
HelioSwarm
OLFAR
Notes: These missions have become more prevalent due to
the decreased launch costs and development costs per
vehicle. MSS/DSM can involve heterogeneous space-
craft, consisting of different types, or homogeneous
spacecraft, all the same type. These are also refered to as constellations
Within the category of all Space Missions there exists Multi Spacecraft Missions
Multi Spacecraft Missions are: systems that
utilize multiple spacecraft to accomplish mission
objectives

## Slide 3: DSA+Starling

## Slide 4
All Spacecraft Missions
[1] An Overview of Distributed Spacecraft Autonomy at NASA Ames; C Adams, B Kempa, M Iatauro, J Frank, W Vaughan - Proceedings of the Small Satellite Conference, 2023
Multi Spacecraft System (MSS)
Notes: Other NASA programs call them DSM ”a mission that involves multiple
spacecraft to achieve one or more common goals
However, it is important to note that a MSS does
not necessarily imply distribution or autonomy. The
Concept of Operations (ConOps) for MSS may sim-
ply include the production of tasks and commands
by ground operators, who simply command each
Spacecraft
NASA’s HelioSwarm mission.2 In this mission, oper-
ators pre-compute plans for all spacecraft, which are
then sent to a central hub spacecraft.

## Slide 5
All Spacecraft Missions
Multi Spacecraft System (MSS)
Autonomous Multi Spacecraft System (A-MSS)
[2] Starling CubeSat Swarm Technology Demonstration Flight Results; S Miller, C Adams, N Alem, H Cannon, R Grashuis … ; Proceedings of the 38th Annual Small Satellite Conference, 2024
Notes: When autonomy is added to a MSS, we have Au-
tonomous Multi-Spacecraft Systems (A-MSS). An
A-MSS allows one of the spacecraft within the system
to assume decision authority. Adding autonomy to a
MSS offers various advantages, including addressing
latency, bandwidth constraints, mission complexity,
and transient or temporally limited events of interest.
Moreover, autonomy enables the operation of space-
craft as a collective rather than as individuals.
The
Reconfiguration and Orbit Maintenance Experiments
Onboard (ROMEO) experiment phase of the Starling
1.0 mission7 is one such example.

## Slide 6
All Spacecraft Missions
Autonomous Multi Spacecraft System (A-MSS)
Distributed Space System (DSS)
Multi Spacecraft System (MSS)
[3] Design and testing of autonomous distributed space systems; N Cramer, D Cellucci, C Adams, A Sweet, M Hejase …; 35th Annual Small Satellite Conference, 2021
Notes: Finally, Distributed Space Systems (DSS) represent
a type of A-MSS where decision authority itself is
distributed across all spacecraft in the system

## Slide 8: Local Observations

## Slide 9: Distributing Observations

## Slide 10: Distributing Decision Authority

## Slide 11: What about state mismatch?

## Slide 12: Reactivity > Mismatch
We don’t want to miss an opportunity to react!
Reactivity is the highest priority
How long does it take for everyone to sync back up?

## Slide 13: Consensus
Notes: When every node things all the other nodes are doing what they’re actually doing, that’s consensus
When someone is doing something different than what others thing, it’s
When everyone is sync’d back up – that’s consensus

## Slide 14: Non-Consensus
Notes: When every node things all the other nodes are doing what they’re actually doing, that’s consensus
When someone is doing something different than what others thing, it’s
When everyone is sync’d back up – that’s consensus

## Slide 15: Time until re-consensus
Δt
time++
[4] Advancing Autonomy in Distributed Space Systems: Results From the Distributed Spacecraft Autonomy Experiment on Starling 1.0; C Adams, M Iatauro, B Kempa, R Levinson, J Frank… ; 38th Annual Small Satellite Conference, 2024
2 – 6 seconds on average!

## Slide 16: Resilient Autonomy
DSA proved resilience
Handles node drop outs live
Operated with 2 or 3 out of 4 sats
Responds to new information and stabilizing system
No human operation required
No pre-scheduled actions
time++
✅
✅
✅
❌
❌
❌
✅
✅

## Slide 17: Scalable Autonomy
No loss in reactivity when adding nodes to swarm
DSA consensus scales linearly
Tested in Lunar, Position Navigation, and Timing scenario
Tested 2 orders of magnitude in simulation
  24 node test
  60 node test
[5] Scheduling PNT Service Requests from Non-dedicated Lunar Constellations; Samantha Niemoeller; Jeremy Frank, Roland Burton, Richard Levinson, Nicholas Cramer; IEEE Aerospace Conference 2022
[6] Development of a High-Performance, Heterogenous, Scalable Test-Bed for Distributed Spacecraft; C Adams, B Kempa, W Vaughan, N Cramer; IEEE Aerospace Conference 2023

## Slide 18: DSA 1.0 Firsts in Space
First demonstration of fully distributed reactive operations onboard multiple spacecraft.
First use of space-to-space communications to autonomously share state information between multiple spacecraft.
First use of fully distributed automated planning onboard multiple spacecraft.
First fully distributed autonomous operation of multiple spacecraft.
First use of a general-purpose automated reasoning system onboard a spacecraft.
DSA-Starling represents the first demonstration of a fully autonomous distributed space mission. Specifically, DSA-Starling accomplished the following:

## Slide 19: Continued Experimentation DSA 1.5 on Starling 1.5

## Slide 20: DSA enables Earth Independent Operations
Tomography
Transient Plume Events
Lunar Crater and Ejecta Detection
🔍
🔍
🔍
🔍

## Slide 21: Thank You!
Caleb.A.Adams@nasa.gov