## Slide 1
The LuNaMaps Team | AGU24 | December 10, 2024

## Slide 2: Outline
Introduction
Building Digital Elevations Models
Pre-built Maps
Map Validation
TRN Validation
Synthetically Enhanced Digital Elevation Models

## Slide 3: Outline
Introduction
Building Digital Elevations Models
Pre-built Maps
Map Validation
TRN Validation
Synthetically Enhanced Digital Elevation Models

## Slide 4: The Need for Better Lunar Map Products
TRN
Powered Descent Initiation
Ref. Map
Descent image
Hazard Detection
3D Digital Elevation Map
Currently there are no lunar orbiters that can provide navigation solutions to landers or surface assets
Landers must rely on Terrain Relative Navigation (TRN) for precision landing
TRN systems use a reference map to localize the spacecraft in lunar coordinates
Hazard Detection and Avoidance (HDA) systems can quickly scan surface for hazards and perform divert maneuvers
HDA system development needs realistic terrain models
Divert to hazard-free site
Controlled landing

## Slide 5: Outline
Introduction
Building Digital Elevations Models
Pre-built Maps
Map Validation
TRN Validation
Synthetically Enhanced Digital Elevation Models

## Slide 6: Ames Stereo Pipeline
A suite of free and open-source automated geodesy and stereogrammetry tools designed for processing stereo images captured from satellites (around Earth and other planets), robotic rovers, aerial cameras, and historical images, with and without accurate camera pose information.
ASP produces cartographic products, including digital terrain models (DTMs, synonymous with digital elevation models, DEMs), ortho-projected images, 3D models, and bundle-adjusted networks of cameras. These data products are suitable for science analysis, mission planning, and public outreach.

## Slide 7
Bundle-adjust (BA) images (iterate)
Select subset for optimal coverage
Register images to a priori DEM (IA)
Compute Shape-from-Shading (SfS) DEM
Pre-process images and down-select
Start from input LDEM/SLDEM at 5-100 m/pix
Find overlapping images (shapes)
Calibrate and project on DEM
Filter bad and shadowed images
Identify images and calibrate
SFS DEM @ target resolution + ancillary products (validation)
Set paths, crs, target resolution, region of interest
Main steps of our SfS pipeline
Semi-automated Ground Track Digital Elevation Model Construction
Semi-automated pipeline of python scripts, USGS ISIS + Ames Stereo Pipeline (ASP) wrappers, and geospatial libraries (gdal, xarray, geopandas)
Published and ongoing applications to the Moon and Mercury
Successfully applied to large (e.g., 16x16 km, 300x300 km) regions and 2500+ LROC or MDIS NAC images
Can run in distributed environment
Notes: Can we get the same plot for Connecting Ridge site?

## Slide 8: Outline
Introduction
Building Digital Elevations Models
Pre-built Maps
Map Validation
TRN Validation
Synthetically Enhanced Digital Elevation Models

## Slide 9: Pre-built maps
The project built high-quality digital elevation models of the lunar surface at key points of interest.
Cleaned and higher-resolution LOLA DEMs of the south pole:
  80o – 87o south 20 m/pix: https://pgda.gsfc.nasa.gov/products/90
  87o – 90o south 5 m/pix: https://pgda.gsfc.nasa.gov/products/81
  Specific Sites 5 m/pix: https://pgda.gsfc.nasa.gov/products/78
1 m/pix shape from shading DEM of the Apollo 16 site:
  Will soon be available at the Planetary Data System (PDS) Cartography and Imaging Sciences Node Annex
Additional sites may be released after evaluation of data sensitivity

## Slide 10: Outline
Introduction
Building Digital Elevations Models
Pre-built Maps
Map Validation
TRN Validation
Synthetically Enhanced Digital Elevation Models

## Slide 11: Map Validation
Compare maps from generated using different techniques/data sets.
For more details visit poster “Exploring the Effect of Map Distortion on Optical Terrain Relative Navigation” in session G31B on
Tools available open source at https://github.com/nasa-jpl/landmark_tools

## Slide 12: Outline
Introduction
Building Digital Elevations Models
Pre-built Maps
Map Validation
TRN Validation
Synthetically Enhanced Digital Elevation Models

## Slide 13: LuNaMaps TRN Validation Pipeline
Goal: Determine if it’s possible to derive concrete metrics or parameter ranges that relate DEM quality to TRN system performance.
  Use a combination of camera images and lidar measurements
  Use different TRN algorithms and implementations and different simulation pipelines
  Use different quality maps and different kinds of map errors and deformations
Maps
Create Lunar digital elevation maps of varying quality using LOLA altimetry data
Measurements
Test various TRN methods on the maps to generate results
Estimation
Analysis
Complete parametric runs to see how map quality affects TRN performance
Use observed and computed measurements in filter to generate state estimations

## Slide 14: Vira – Rendering Tool
SLDEM2015 + LDEM60S DEMs wrapped with WAC albedo
Bennu rendered with OSIRIS-Rex SPK/CK kernels
67P SPC Maplets Level-of-Detail System
Textured Saturn with Rings
Lunar Descent Images

## Slide 15: Outline
Introduction
Building Digital Elevations Models
Pre-built Maps
Map Validation
TRN Validation
Synthetically Enhanced Digital Elevation Models

## Slide 16: LuNaSynth: Synthetic Lunar Terrains for Autonomous Navigation
Enhance lunar digital elevation maps (DEM) to create high resolution maps for autonomous navigation
  Sculpt craters into the DEM using current best empirical distributions of crater profile and crater placements
  Add a rock field from empirical rock distributions in representative terrains. Use procedural rocks and scanned rocks models from Apollo missions and terrestrial lunar analog sites.
Implementations available at https://github.com/nasa-jpl/lunasynth and https://github.com/NeoGeographyToolkit/synthterrain
Sample output
Rendered terrain
Rock field ground truth
Detailed DEM
Base DEM
Rendered Terrain
Terrain Creation Process
December 10, 2024
AGU24
16

## Slide 17: Generation Process: from large scale DEM to regolith detail
Examples of desired level of detail
Example of existing level of detail
December 10, 2024
AGU24
17