## Slide 1
NASA’s Exploration and In-Space Services (NExIS) Division OSAM-1 and Related Propellant Transfer Subsystem Progress through FY 2024
Presentation
Graham K. Webster and Peter A. Knudtson
NASA Goddard Space Flight Space Center
Thomas J. Aranyos, Brian M. Nufer, Amy M. Felt, and Syrus Jeanes
NASA Kennedy Space Center
January 2025
The author of this document is an employee of the U.S. government, and it was created as part of the author’s official duties. It is not subject to copyright protection in the United States, under U.S. copyright law. Therefore, this document is declared a work of the U.S. government.
Published by the American Institute of Aeronautics and Astronautics, Inc., with permission.

## Slide 2: Introduction & Overview
NASA’s Exploration and In-Space Services (NExIS) Division has been developing technologies for the on-orbit servicing of satellites for decades (Hubble servicing missions)
On-Orbit Servicing, Assembly and Manufacturing mission 1 (OSAM-1) had plans to robotically refuel a heritage satellite on-orbit (a.k.a. non-cooperative)
  Future plans of the OSAM-1 flight hardware will not be discussed
The OSAM-1 Space Infrastructure Dexterious Robot (SPIDER) payload is designed to assemble a 3-meter communications antenna
OSAM-1 Propellant Transfer Subsystem (PTS) development supports the nascent in-space refueling ISAM goals
  Reference “National In-Space Servicing, Assembly, and Manufacturing Implementation Plan” (Dec 2022 from White House Office of Science and Technology Policy)
ISAM fluid transfer technology shortfalls still exist and are actively being addressed at NASA

## Slide 3: What is ISAM?
Enabling in-space…
Close Inspection
Small inspectors diagnose anomalies, enabling corrective action and in-space repair operations. Small satellite inspectors launch “on need.”
Seeker Test Flight, 2019 )
Free-Flyer Capture and Relocation
Commercial servicers perform autonomous capture of active spacecraft and uncontrolled debris, relocating them to new operational, disposal or salvage orbits.
OSAM-1
Delivery and Aggregation
Commercial launch and high-efficiency in-space transportation systems deliver commodities and cargo to assets in multiple orbits, enabling frequent and lower-cost resupply and client relocation.
Gateway Deep
Space Logistics
Maintenance & Repair
US Spacecraft launch with standard interfaces enabling frequent upgrades. Commercial servicers conduct planned and on-demand manufacturing, repair and maintenance. Human exploration spacecraft refurbished and recertified in space.
Mars Transportation
System
Refueling and Fluid Transfer
Spacecraft launch with standard in-space fueling (and other) accommodations. Commercial servicers provide fueling on-demand in multiple orbits and planetary surfaces.
Persistent Platform or “Instrument Hotel“
(JPL)
Installation and Upgrade
Great Observatories and platforms in multiple orbits enable hosting of operational and experimental instruments and payloads. Commercial servicers provide delivery, installation and hosting services.
Roman Space Telescope
Manufacturing and Assembly
Purpose-built in-space systems enable audacious new science, exploration, and commercial-ization of space: a 20-meter space telescope discovers signs of life on extrasolar planets; an outer planets human exploration mission departs aboard an in-space assembled craft; manufacturing products for use in space and on Earth provide a stimulus to the U.S. economy.
Rotating Space Station
Great Observatories
All activities depicted not currently funded or approved. Depicts “notional future” to guide technology vision.
3

## Slide 4: ISAM Efforts Past, Present, and Future
4
Notes: Good progress to date has been made on in space refueling from 1985 till present from NASA – Shuttle Program , Orbital Express, Space Station (w/ RRM-3 and Russian refueling) , Gateway, and OSAM-1 missions. The KSC effort has been supporting GSFC collaboratively for in-space refueling starting in 2010 (under vision of Frank Cepollini-”Cepi” request for help, who was the father of Hubble Service missions). Over $30M has been expended to date to support Restore-L and to OSAM-1 mission in propellent transfer subsystem development efforts. This effort has kick started a new way of approaching less launch fuel capacity required and in-space maneuver w/o regret possibilities such that the National ISAM plan issued by Whitehouse (weblink at top) discusses commercial in-space refueling (both for in orbit and on surface) as the new normal.

## Slide 5: OSAM-1: On-Orbit Servicing, Assembly & Manufacturing
Transfer ~30 gallons of hydrazine
https://www.youtube.com/watch?v=gverl0Ypf0k
OSAM-1 Mission (nasa.gov)
  The Propellant Transfer Subsystem (PTS) forms one of the principal subsystems of OSAM-1, providing demonstration of critical technologies for in-space fluid transfer
    For the OSAM-1 mission, the primary focus is on hydrazine, although the technologies developed are extensible to other storable hypergols
  SPIDER added in April 2020 for the assembly element of the mission to verify the capability to construct large spacecraft structures in orbit
    Assembles a functional communications antenna
Notes: KSC focus has been the fluid transfer servicing portion of the mission ( a propellant resupply of approx. 30 gallons of hydrazine –equivalent of small SUV tank refill ) Although it can also image, rendezvous, capture, reposition, mechanically service etc. In 2020 assembly and manufacturing to demonstrate robotic capability to construct large spacecraft structures in orbit was added and mission renamed from Restore-L to OSAM-1. Web links on page will take you to videos for further info if interested.

## Slide 6: OSAM-1: On-Orbit Servicing Concepts
OSAM-1 is analogous to the fuel truck on the ground (with six degrees of freedom control on orbit)
The PTS is analogous to the familiar gas station pumping, metering, and control system
A Hypergol Refueling Tool (HRT) with a Quick Disconnect (QD) interfaces with existing client propulsion system on-orbit
  Similar to a Liquefied Natural Gas (LNG) type automobile refill end effector (but robotically mated)
AIAA S-157, In-Space Storable Fluid Transfer Standard planned for release very soon
Propellant Transfer Vehicle
Propellant Transfer Subsystem (PTS)
Propellant Transfer Interface
Space Vehicle (SV)
Hypergol Refueling Tool / QD
RRM #3
Typical client interface
Notes: OSAM-1 overall concept is for capability to refuel heritage or planned clients in orbit, first starting with hydrazine replenishment of an end of life LandSat-7 client (a US govt asset). KSC collaborative effort was focused on the hose reach and pumping and metering station of these subassemblies. The Hose Management assembly release to client does a serial staged waypoint dance with GSFC provided robotic arm and transfer end effector (or Hypergol refueling Tool) enroute to attach to client interface.
NASA PTS team has also participated on the ongoing AIAA interface development committee consisting of govt and industry team members for release in 2023 of a first of its kind in-space fluid transfer standard also addressed in the White House ISAM plan goals.

## Slide 7: OSAM-1 Spacecraft and PTS Hardware
Source: Maxar Website
Propellant Transfer Subsystem (PTS)
Hose Management Assembly (HMA)
Propellant Transfer Subsystem (PTS)
Hydrazine Transfer Sub-Assembly (HTSA)
Propellant Transfer Subsystem (PTS)
Hydrazine Tanks
Space Vehicle (SV)
Servicing Payload (SP)
Propellant Transfer Subsystem (PTS)
Vent Thruster Sub-Assembly (VTSA)
Spacecraft Bus

## Slide 8: Payload PTS Subassemblies
Transfers propellant safely & reliably to an on-orbit client satellite
  TRANSFER
    Manages pressures and flow rate
    Mil-Spec propellant (transfers approx. 30 gal to L7)
  SAFETY
    Minimize propellant release
    Maintains servicer and client propellant tanks within temperature constraints
    Performs leak checks on self & client fluid interface connection
  RELIABILITY
    Robust design
    Well tested / proven heritage components
    Accurate heritage pressure transfer operational technique
Designed for heritage client/refueling
OSAM-1 PTS designed for cooperative refueling
Spacecraft bus supplies hydrazine & helium to Servicing Payload
HTSA
HMA
VTSA
HRT
(by Tools)
Propellant Transfer Subsystem (PTS)
Hose Management Assembly (HMA)
Hydrazine Transfer Subassembly (HTSA)
Vent Thruster Subassembly (VTSA)
Reference: PTS Implementation Plan, RL-PTS-PLAN-0167

## Slide 9: OSAM-1 Propellant Transfer Subsystem (PTS)
SV
FM
STB
Test
Servicing Payload PTS
Vent Thruster SubAssembly (VTSA)
Hydrazine Transfer SubAssembly (HTSA)
Hose Management Assembly (HMA)
Motor
HMA PFU
LV
PT
Pin Puller
RDSA
RDSA
*Most component subcontracts >3 years for design, fabrication, qualification, and acceptance
CV
Qualification / Acceptance Testing / Analysis / Certification for HMA |  | 
- TVAC | - Full Sun | - Bend Radius
- Thermal Protect | - Full Darkness | - Twist/ Torque Cycles
- Vibe | - Press Cycle Life | - Cycle Contamination
- EMI/EMC | - NDE / CT scans | - Space Charging (LEO)
- DC magnetics | - Ascent Vent | - Proof / Precision Leak
- Radiation | - Structural loads | - Precision Cleanliness
Notes: The PTS Payload consists of 3 main subassemblies – a Hose management Assembly, a Hydrazine Transfer Subassembly, and a Vent Thruster Subassembly. Most components seen in the bottom row feeding higher level subassemblies above required 3 + years design / fab/ test to flight environments and unique mission requirements before integration / test into their designated main subassemblies. Parallel Engineering Test Units at both the component and subassembly level were also critical to enable design verification and any redesign / rework as required on this R&D program effort. And early testing included not only typical environmental but zero -G flight and neutral buoyancy pool specialty tests to confirm design. The HMA has over 10+ years development / test efforts associated to achieve a unique twist compliant convoluted SST hose assembly without use of any seals that meets extremes of in-space transfer environments / use. The Flowmeter was built & tested with GFE electronic boards to meet qual levels for reliable space environments at high accuracy levels (≤ 1% error) for required flow rate ranges at varying viscosities.
After 3+ years of Fab /Qual/Acceptance Testing PTS Installation / Test to Servicing Payload was Completed Feb 2023

## Slide 10: Hose SubAssembly (HSA) Torque/Twist Qualification Test Summary with Flight-Grade ETU
Twist angle qualified with extra % hose length deployed before next waypoint robo stop distance planned
Chart: HSA Outside HMA Trace Length (in)
| 28.25 | 28.25 | 57.78 | 87.3 | 110 | 110
Twist Angle Limit | 0 | 60 | 90 | 100 | 100 | 0
Torque and twist allowable (inner hose and HSA) changes depending on deployed length per the envelope shown
  Note that the HSA can bend out of plane (this is different than twisting)
  Unique capabilities for SST convoluted annealed hose and specialty wrappings / wiring / thermal protection
Reference Documents:
  HMA ETU Functional Tests: OSAM1-PTS-RPT-0267, OSAM-1 PTS HSA Mechanical Loading Assessment
  HMA ETU Functional Tests: OSAM1-PTS-RPT-0469, HMA ETU HSA Twist Test Report
  Inner hose qualification test report: RL-PTS-RPT-0241, PTS Flex Hose Qual Test Report
Example of Out of Plane HSA
Bending but Zero Torsion on HSA
150 Reverse Cycles
Notes: The final qualified test results for ConOPS uses are summarized below. Note that the Hose Subassembly consists of a unique annealed, 100% x-rayed, SST inner convoluted braided hose wrapped with thermal layers, wiring, heaters and an outer conduit that is thermal coated, marked, and has charge dissipation capabilities. The graph shows that the HSA is qualified with margin for up to 60 to 100 degrees of twist dependent on the hose length deployed for cumulative Robot planned next waypoint movement. Image in upper right shows a typical worst case heritage client satellite reach and access required for which this design satisfies.

## Slide 11: HMA Early Proof of Concept Testing Mechanical Design Validation Testing
2012
2013
2014
2015
2016
Hose tests in Zero-g & NBL
End to End Refuel Demo
2017
HMA-Vibe/
Launch lock tests
RL-PTS-RPT-0180
RL-PTS-TN-0031
RL-PTS-RPT-0055
STB Hose Deploy
RL-PTS-RPT-0120
HMA Hose EMI/EMC
RL-PTS-TN-0053
RL-PTS-WOA-0012
RL-PTS-PROC-0160
Coating Abrasion
11
Ref | Test | Technology Demonstrated | Test Venue
RL-PTS-WOA-0012 | End-to-End Refueling | Demonstrate ability for Propellant Transfer Assembly (PTA) to transfer propellant to the demo Landsat-7 (L7) (water used) through the HMA | GSFC & KSC
RL-PTS-RPT-0055 | Hose and Nozzle Tool Neutral Buoyance Testing | Characterize the motion of the hose in a zero-g environment Validate the slack amounts keep torque under limits | SSL
RL-PTS-TN-0031 | Hose Assembly Vacuum Testing | Verify normal and upset case performance of design for a hypergolic fluid transfer hose exposed to space environments Validate fluid stays within 5 degrees C during flow as referenced from the temperature at its point of entry. | GSFC
RL-PTS-TN-0020 | Hose Manipulation Trajectory and Loads Test | Characterize hose trajectories to investigate potential hose load concerns, including slack management, in test and Demo L7 hose deploy/retract ops, use of visual indicator feedback | GSFC/27N GSFC (29/150) GSFC (GSSCC)
RL-PTS-RPT-0180 | Vibe test hose assembly (for launch locks) | Vibe testing of hose assembly in box constraints for worst case load environments predicted (no launch locks required) | KSC
RL-PTS-RPT-0120 | HMA Box & Tool Stowage Configuration Study | Assess robotic movements of HRT/hose assembly with different box configurations & tool stowage configurations – Decision: Maintain baseline | GSFC
RL-PTS-PROC-0160 | Thermal Coating Abrasion Test | Assess adhesion of CCAg/ITO thermal coating on conduit surface during hose deploy. Determine if contam level & performance meet requirements. | GSFC
RL-PTS-TN-0053 | HMA Hose EMI/EMC | Determine HMA hose susceptibility to EMI /EMC/reduce risk to development schedule | KSC
Notes: Early development included TVAC tests to down-select outer coatings of the conduit. And neutral buoyancy, zero-g testing, along with robotic coordinated ConOPS established the initial twist & torque goals and limits, then were followed by typical standard environmental tests for vibe, EMI and cycle life.

## Slide 12: ETU HMA Testing
2018
2019
CSA Launch Loads Vibration Re-Test
RL-PTS-TN-0085
Redesigned PT cradle
Increased roller compression
HMA Abrasion Risk Reduction Test
RL-PTS-RPT-0103
Nickel coating of BSA
Add exit guide rollers to RDSA
HMA Contingency –Pullout Force tests RL-PTS-RPT-0131
Robo extraction low force lbf range of best case angles 15-25°
HMA ETU Launch Survivability Vibration Risk Reduction Test RL-PTS-RPT-0210
All components performed nominally
Functional checks verified performance pre/post test
Ascent Vent ETU
Risk Reduction Test RL-PTS-RPT-0262
All components performed nominally
No noticeable change in mechanical characteristics of hose
TVAC of 1-m reference HSA verified no change in thermal performance (ref: RL-PTS-RPT-0238)
Notes: Development continued on a flight like Engineering Test Unit to feed lessons learned to the flight product.

## Slide 13: ETU HMA Testing (cont.)
2019 Contd.
2020
HMA ETU TVAC and Abrasion Test
OSAM1-PTS-RPT-0323
Modify HSA exit bracket to reduce debris
All components performed nominally
HMA ETU Abrasion Test
OSAM1-PTS-RPT-0365
Verified new HSA exit bracket
Passed contamination
HMA ETU HSA Compression Test OSAM1-PTS-RPT-0448
Verified HSA performance at bend radii < 6"
HMA ETU HSA Twist Test
OSAM1-PTS-RPT-0469
All components performed nominally
Showed HSA can bend up to 100°or to a torsion of 21 in-lb.
2021
HMA ETU 200 Cycle Mechanical Assessment
OSAM1-PTS-RPT-0336
All components performed nominally
Demonstrated 4x life for RDSA and HSA
13
Notes: Further ETU level testing closed all potential open technical risk items

## Slide 14: System-Level Testing in Servicing Testbed
Servicing testbed (GSFC)
  High fidelity mockup with many OSAM-1 subsystems
  Full size Landsat 7 mockup with fluid interface panel
Hypergolic Refueling Tool (HRT) EDU w/HMA on ATDS
Landsat 7 and Payload Mock-up
Notes: For OSAM-1, the architectural approach used for the ONT and its QD are preserved. For the EDU, the HRT and QD were tested at a MEOP of 650 psig and leak rates measured were in the 1 x 10-6 sccs/GHe range. Because the CSV and QD share a lot of the same design elements, lessons learned from the CSV development and flight program were incorporated into the QD flight design.

## Slide 15: HMA: Motion Operations
The HMA motion conceptual operations (waypoint serial dance planned motion events) with the robot arm were investigated in simulated ConOps lights out condition at GSFC ROC testbed
The trajectory of the flexhose is monitored by suitable conduit markings to validate deploy / retract lengths along with position telemetry received from the HMA motor
The Vision Subsystem situational awareness camera provides additional guidance on the hose trajectory

## Slide 16: HMA Activities Prior to Turnover for SP Install (Final Weld, Vibe, TVAC and EMI / Elect Checks)
Weld of HRT to CSA in Bldg 11
Tested >37 Gs
Precision Welds
TVAC tested extremes of full sun or extreme darkness
HMA Trial run EDU install in STB
HMA w/ HRT (EMI lab)
HTSA EMI filter pin rework
EMI Test filter box
EMI filter protection added / tested
VTL - Vibe Test Setup
Notes: The last year of OSAM-1 for HMA involved final weld, vibe, TVAC, and EMI / elect checks of HMA prior to it being board approved for turnover for PL install Dec 16, 2022. Unit was Vibe tested to 37 G’s at KSC in June 2022, and then onto GSFC for precision welds in a tight assembly configuration with HRT integrated and all passed NDE / proof tests, was then TVAC tested for extremes of full sun / darkness, an EMI filter protection was added / tested to harnessing, and also in parallel a trial mockup run installation in GSFC Payload testbed of the ETU was conducted.

## Slide 17: Vent Thruster Subassembly (VTSA)
A heritage thruster was utilized for the VTSA
VTSA allows GHe and GHe / N2H4 mixtures to be vented to space as part of nominal and off-nominal ConOps to minimize contamination of surrounding surfaces
The first PTS flight weld was completed on the VTSA along with I&T activities at flight subassembly level

## Slide 18: PTA: Flow Meter Development
Flow meter produces pulses based on turbine blade rotation rates
Flow meter development was met with some initial challenges related to manufacturing techniques for the internal GFE electronics board rated for space environment
  Flight unit builds are now complete and providing excellent calibration accuracy (≤ 1% error) for required flow rate ranges at varying viscosities
  Flight unit (and spare) received and incorporated into the flight HTSA
OSAM-1’s flow meter performance enables an accurate propellant transfer, and is extensible to future on-orbit fluid transfer operations or propulsion systems
  Analysis shows pVT is an adequate rough comparison backup for mass transfer determination
Applicable for all in-space incompressible single-phase fluids
NASA GFE Printed Circuit Boards
turbine pulse counter
(EEE rated, radiation hard, etc.)
Flight Unit
Body
Sensor
Notes: The turbine type flowmeter flight hardware using GFE qualified electronics board was delivered in 2021 and all performance was at or above qual tested levels.

## Slide 19: PTA: Flow Meter Uncertainty
Qualification and flight flow meters meet accuracy requirement (≤ 1% uncertainty) across required flow rate (0.1 – 1.0 GPM) and N2H4 kinematic viscosity (0.7 – 1.3 cSt) ranges
Flow meter performance enables OSAM-1 propellant transfer and is extensible to future on-orbit fluid transfer operations (for incompressible / storable fluids)
  Not applicable for two phase fluids
  Worst case predicted transfer mass uncertainty is 1.1%
Qualification flow meter passed all testing (RL-PTS-RPT-0053/-0065/-0066/-0067/-0085)
Flight flow meters passed all testing (OSAM1-PTS-EIDP-0191)
Flight unit RFM-N-001 calibration data
Notes: The qual and flight units have all shown below 1% uncertainty as seen in referenced test reports. This gear turbine technology is extensible to any on-orbit incompressible / storable fluid, but not applicable for two phase applications.

## Slide 20: PTA: GHe and Water Leak Flow Testing
The relationship between GHe leak rates and water leak rates was experimentally investigated for arbitrary leak sizes covering a wide range of flow rates with the aid of a needle valve (see AIAA-2019-3437 for GHe leak study)
The water leak rate data could then be scaled to propellant leaks for flight application

## Slide 21: PTA: Water Evacuation Testing
Trapped fluid evacuation and venting characteristics of planned ConOps were ground-tested with small and large volumes using a low-level vacuum
  Planned vent ConOps duration to trace vapor levels verified via test, including trapped filter fluid release
The data were theoretically correlated to hydrazine use (AIAA-2020-3036)
SV: Solenoid Valve
SLV: Simulated Latch Valve (solenoid)
LV: Latch Valve
PT: Pressure Transducer
QD: Quick Disconnect
FM: Flowmeter
FDV: Fill Drain Valve
Ref Reports: RL-PTS-REVW-0143 PTS Manifold Depressurization and Evacuation Test and Analysis Results (Feb 2019)
AIAA-2020-3036 External Depressurization & Evacuation of Water from a Typical Transfer Subsystem (June 2020)
OSAM1-PTS-RPT-0100 PTS Post-Servicing Evacuation and Venting Test Results Rev A update (Feb 2022)
2-D simulation test mockup of Payload PTS (KSC)

## Slide 22: PTA Activities Prior to Turnover for Installation (Final Weld, Vibration, TVAC, and EMI / Electrical Checks)
HTSA Acceptance Testing
  Certification of flight hardware also included dozens of requirements verification evidence approvals
Approx. 2,000 PTS configuration management approved documents (drawings, procedures, test reports work orders, acceptance data packages etc.) over the development timeline (some hundreds of pages in length)
VTSA Acceptance Testing
VTSA Bracket, tubing, and electrical assembly
HTSA EMI Testing – EMI Filter Added/Tested
PTS Requirement Burndown
Typical prop system weld NDE, proof, & elect / control functional
HTSA Vibe Testing – Full environmental testing and post workmanship vibe
Notes: The HTSA and VTSA sub-assembles also completed all final weld, vibe, TVAC and EMI/Elect Checks at GSFC by Jan 27, 2023 with formal certification turnover scheduled for Feb 09.
Total PTS team documents issued /approved in GFSC mission configuration management total approx. 2,000 to feed Requirements Verification before Turnover. Although not as much fun as fab & test, detail certification paper for requirements verification closeout was performed throughout FY 2022 and continues into FY 2023 with over 40 final requirements verification to be closed after integrated Payload installation/ test.
So lessons learned 12 plus years later for myself nearing end of career, is you never know what next challenge / opportunity lies around the corner (as I was merely asked to attend a quick tagup with a GSFC manager in my division manager‘s absence for that day about possible help to GSFC satellite servicing test efforts in May of 2010). And I have had the privilege to lead and work with a team of the highest level talent at both KSC and GSFC, many key players too numerous to all mention by name from NE (some who have moved on to bigger/ better things) and handful that have remained through the end of development, but my sincere thanks to all 60 plus key players at both KSC and GSFC that enabled this effort to be successful over the past 12 years.
And lastly a paid political announcement for “Bytes with The Boss” series, if you are interested in further details of the OSAM-1 Propellant Transfer System and of spin-off development technologies for closing gaps for future in-space fluid transfer, you will want to join my colleague Brian Nufer presentation on Feb 15 at noon. Brian has been an integral key lead engineer for OSAM-1 and general refueling studies also for over 12 years.
Thanks -Any questions?

## Slide 23: PTS: Integration into Servicing Payload
The PTS was integrated into Servicing Payload in Feb 2023 and handed over to the Space Vehicle by end of CY 2023
  Documented the processes related to payload level integration and testing
The relevant integration and test flow schematic is shown on the left, incorporating formal test / verification plans at component, subassembly, Servicing Payload and Space Vehicle levels of development

## Slide 24: PTS: Integration into Servicing Payload and SV
Assembled SV

## Slide 25
The Future

## Slide 26: ISAM Fluid Transfer Investment Summary
Cooperative client fuel servicing of a client bladder/diaphragm tank (ORS & OE)
Cooperative client fuel servicing of a client PMD tank (OE)
Cooperative client fuel and oxidizer (bi-prop) servicing (GW, ISS, & Mir)
Non-cooperative client fuel servicing of a client bladder or diaphragm tank (OSAM-1)
Non-cooperative client fuel servicing of a client PMD tank
Non-cooperative client fuel and oxidizer (bi-prop) servicing
Cooperative or non-cooperative servicing of a high pressure GHe/GN2 system
Cooperative or non-cooperative servicing of a high pressure, super critical xenon system (GW)
Cooperative or non-cooperative servicing of a cryogenic system (Starship)
Mir, Salyut 6, ISS (Progress, ATV, etc.)
ORS on STS-41G, Orbital Express, FARE II & II, ALFE, VTRE, TPCE/TP, SFMD, RRM, and others
SpaceX Starship
Gateway
OSAM-1
Mars transit vehicle
Lunar/Mars surface fluid transfer systems
Transfer pumps (Lunar Flashlight & DoD)
Fluid transfer coupling (RRM)
Turbine flow meter, flexible servicing hose, hypergol refueling tool, & cooperative servicing valve (OSAM-1)
Refuelable orbital debris removal spacecraft (SBIR)
Commercial fluid interfaces (Orbit Fab, NG, VACCO, etc.)
In-space propellant tank venting (SBIR & CoECI)
Coriolis flow meter, xenon and helium compressor, variable output regulator, and flexible fluid adapter (NASA AXCIS ECI); titanium bellows accumulator
Optimize fluid transfer assembly (NASA AXCIS ECI)
Mission Pull:
Technical Development:
System Types:
1
2
3
4
5
6
7
8
9
10
“Idea”
“Operational”
“Flight Proven”
22
TRL
“Difficult”
“Easy”
19
18
24
10*
15
16
11
*Russian
Mission Pull
#
#
Tech. Dev.
System Types
#
26
www.nasa.gov/spacetechpriorities
1
2
3
8
4
7
9
17
20
12
13
11
21
5
6
14
11
13
23

## Slide 27: AXCIS Project Overview
The Advancement of Exploration Components for In-Space Servicing (AXCIS) is an Early Career Initiative (ECI) project that aims to complete the design for an optimized servicing system needed for near future missions by rapidly developing a specific suite of gap technologies with commercial partners followed by component and system level environmental testing.
The AXCIS gap technologies include:
Seal-Less, Mechanically Compliant, Fluid Adapter (starting TRL 3)
High Accuracy Coriolis Mass Flow Meter (starting TRL 3)
Helium Compressor (starting TRL 3)
Xenon Compressor (starting TRL 2)
Variable Output Regulator (starting TRL 3)
Through commercial partnerships, the team will develop flight-like prototypes/engineering development units (EDUs) and perform various applicable environmental and system level tests at KSC & GSFC (following GEVS, GSFC-STD-7000) to verify and validate the designs, bringing all gap technologies to a TRL 6 at project completion.
The AXCIS project is a two-year project that will end at the end of FY25

## Slide 28: AXCIS Seal-Less Fluid Adapter Technology Summary
What is it?
  An additively manufactured, seal-less (no dynamic seal), mechanically compliant fluid adapter or leak-proof joint technology being designed and manufactured by Quadrus Corporation.
How does it work?
  Having no seals or soft goods, this technology can be used with hypergolic oxidizer (nitrogen tetroxide) systems while allowing for movement in any vector within a full hemisphere about the hinge for pitch, roll, and yaw.
  Can be used in conjunction with any fluid interface where misalignment may be a concern or as a flexible joint (i.e. robotic arm).
What gaps does this technology address?
  Primary STMD Shortfall 1224 (storable prop. resupply)
Specifications:
  MEOP: 500 PSIG
  Footprint: ~6” OD, 14” Length
  Mass: ~4.73 lbs (without actuation components)
Previous development efforts prior to AXCIS:
  SBIR Phase I (looking at concept and materials compatibility)
  SBIR Phase II (developing preliminary single rotational stage prototype)
*Partial closure
^Modifications required for closure

## Slide 29: AXCIS High Accuracy Coriolis Mass Flow Meter Summary
What is it?
  A multi-variable (telemetry output) device that provides direct measurement of mass flow, density, and temperature for liquids, slurries, and gases.
How does it work?
  A Coriolis flow meter measures mass flow rate using motion mechanics. The technology is based on the principle that inertia created by the fluid flow causes the meter’s tubes to twist proportional to the mass flow rate.
  Can be used in both liquid and gas systems and can perform well under certain two-phase flow conditions.
What gaps does this technology address?
  Primary STMD Shortfall 1224 (storable prop resupply)
Specifications:
Previous development efforts prior to AXCIS:
  FY22 Independent Research and Technology Development (IRTD) (developed Mark 1 Printed Circuit Board (PCB) design)
 | Xenon | Helium | Liquid
MEOP (psig) | 3263 | 6000 | 2200
Footprint (in) | 9 x 8 x 3 | 11 x 7 x 2 | 11 x 7 x 2
Mass (lbs) (without transmitter) | 10.8 | 5.4 | 5.0
*Partial closure
^Modifications required for closure

## Slide 30: AXCIS Helium and Xenon Compressor Summary
What is it?
  A relatively small footprint, multi-stage, positive displacement, piston compressor.
How does it work?
  Each stage of the multi-stage compressor consists of a custom designed piston assembly that is used to step up the outlet pressure. Stage 1 is designed to increase pressure from 300 to 600 PSIA, Stage 2 increases pressure from 600 to 1000 PSIA, and Stage 3 increases pressure from 1000 to 4000 PSIA.
  For the AXCIS project, a single compressor EDU is being designed to work with both xenon and helium (schedule/cost savings).
What gaps do these technologies address?
  Primary STMD Shortfall 1506 (pressurant resupply)
  Primary STMD Shortfall 1138 (electric prop. resupply)
Specifications:
  MEOP: 4000 PSIG
  Footprint: ~12” width x 22” Length
  Est. mass: ~65 lbs (EDU), ~55 lbs (Flight)
Previous development efforts prior to AXCIS:
  SBIR Phase I (analytical model, preliminary design)
  SBIR Phase I (developing preliminary single stage prototype and performing preliminary testing)
*Partial closure
^Modifications required for closure

## Slide 31: AXCIS Variable Output Regulator Summary
What is it?
  A modified COTS ground hand regulator that allows for remote pressure adjustment.
How does it work?
  Where a typical hand knob is installed on the top of the regulator bonnet, a gear box and motor are attached to the regulator pressure adjustment shaft. Limit switches are used to signal the motor when the regulator is fully open or fully closed to prevent damage to the motor and regulator.
  Can be used to service pressurant tanks with the capability to adjust set pressure between clients.
What gaps does this technology address?
  Primary STMD Shortfall 1138 (electric prop. resupply)
  Primary STMD Shortfall 1224 (storable prop resupply)
  Primary STMD Shortfall 1506 (pressurant resupply)
Specifications:
  MEOP: 6000 PSIG (High Pressure, Low pressure)
  Outlet Pressure Range: 50-6000 PSIG (High P), 50-500 PSIG (Low P)
  Footprint: ~3” OD, 7” Length (High P), ~2” OD, 5.5” Length (Low P) (without actuation components)
  Mass: ~6.6 lbs (High P), ~3.3 lbs (Low P) (without actuation components)
Previous development efforts prior to AXCIS:
  NASA KSC/GSFC joint study with electronic regulator testing
*Partial closure
^Modifications required for closure
Low Pressure
High Pressure

## Slide 32: AXCIS Test Integration Outlook
Functional Testing (KSC)
  July 2024 – Sept. 2025
EMI/EMC Testing (KSC)
  Mar./Apr. 2025
Vibe/Shock Testing (KSC)
  May 2025
System Level TVAC (GSFC)
  July 14-25, 2025 (Scheduled)

## Slide 33: Conclusion
OSAM-1 designed and built to perform first non-cooperative hydrazine transfer in space
OSAM-1 PTS assembly completed
  Extensive functional testing of PTA and HMA were carried out at flight ETU physical and / or functional levels, and in special testbeds mimicking flight conditions /operations
  Subassembly qualification and acceptance level testing prior to payload installation in February 2023
  Integrated PTS to payload subsystem avionics control testing completed 2023
  Integration to space vehicle (bus) and acceptance / contingency testing completed in 2024
  OSAM-1 technologies and intellectual property could be considered for commercial licenses and / or agreements through NexIS On-Orbit Servicing Technologies Contacts (see Backup)
  Hardware designs extensible (with design specific modifications) for other prop storables
  Springboard for other govt agencies and commercial efforts in support of White House ISAM National Strategic Plan: https://www.whitehouse.gov/wp-content/uploads/2022/12/NATIONAL-ISAM-IMPLEMENTATION-PLAN.pdf
Further ISAM technology gaps for other variables and commodities are in progress by NASA, DOD, and commercial ventures to raise TRL needed for future routine prop replenishment needs (at levels of funding support available)
  NASA focus gap list is contained here: www.nasa.gov/spacetechpriorities
NASA ExIS/OSAM Team: Fluid Transfer documents - Summary Index IP master index available upon request
Notes: I will now turnover presentation to Brian Nufer to discuss efforts on Vacuum Evacuation testing and analytical modeling

## Slide 34
Backup Charts
To learn more about the NASA Technology Transfer Program and how it facilitates collaborations between NASA researchers and external parties for mutual benefit, visit https://technology.nasa.gov/network.
To arrange further technical discussion of specific on-orbit servicing technologies and backup detail reports, contact Tammy Brown (tammy.l.brown@nasa.gov) of GSFC.

## Slide 35
Acronym List
ATDS | Advanced Tool Drive System
CCB | Configuration Control Board
ConOps | Concept of Operations
CSA | Clamshell Assembly of HMA
cSt | centistoke
CT scan | Computed Tomography scan
CV | Check Valve
DOD | Department of Defense
EEE | Electrical, Electronic and Electromechanical
EMC | Electromagnetic Compatibility
EMI | Electromagnetic interference
ETU | Engineering Test Unit
FDV | Fill-Drain Valve
FM | Flow Meter
GEO | Geosynchronous Equatorial Orbit
GFE | Government Furnished Equipment
GHe | Gaseous Helium
GN2 | Gaseous Nitrogen
GPM | Gallons per minute
GSFC | Goddard Space Flight Center
H/W | Hardware
HFCS | Hybrid Flight Computing System
HMA | Hose Management Assembly
HRT | Hypergol refueling tool
HSA | Hose Sub Assembly
HTSA | Hydrazine Transfer SubAssembly
I&T | Integration and Test
ISAM | In-Space Servicing Assembly and Manufacture
ISS | International Space Station
JPL | Jet Propulsion Laboratory
JSC | Johnson Space Center
KSC | Kennedy Space Center
LEO | Lower Earth Orbit
LV | Latch Valve
MEOP | Maximum Expected Operating Pressure
MMH | Monomethyl Hydrazine
N2H4 | Hydrazine
NASA | National Aeronautics and Space Administration
NBL | Neutral Buoyancy Lab
NDE | Non-Destructive Evaluation
NExIS | NASA’s Exploration and In-Space Services
NTO | Nitrogen Tetroxide
OE | Orbital Express
ORS | Orbital Refueling System (on STS-41G)
OSAM | On-Orbit servicing, Assembly, and Manufacturing
PFU | Protoflight Unit
PMD | Propellant Management Device
PSU | Payload Servicing Unit
PT | Pressure Transducer
PTA | Propellant Transfer Assembly
PTS | Propellent Transfer Subsystem
PVT | Pressure Volume Temperature
QD | Quick Disconnect
RDSA | Roller-Drive SubAssembly
ROC | Robotic Operations & Control
RRM3 | Robotic Refueling Mission #3
SBIR | Small Business Innovation Research
SPIDER | Space Infrastructure Dexterous Robot
SSCO | Satellite Servicing Capabilities Office
SSPD | Satellite Servicing Projects Division
SST | Stainless Steel
STB | Servicing Test Bed at GSFC
SV | Solenoid Valve
TRL | Technology Readiness Level
TVAC | Thermal Vacuum
VTL | Vibe Test lab
VTSA | Vent Thruster SubAssembly
WM | Workmanship
WSTF | White Sands Test Facility

## Slide 37
UNUSED BACKUP

## Slide 38: PTS Assembly /Test Efforts to Flight HW Acceptance
HTSA Electrical Install & Test
HTSA Vibe & EMI Tests w/ Pre &-Post Test (w/ rework)
May/June
Nov
May
Feb 9, 2023
Turnover to SPINT
VTSA
Accept Test Complete
Vent thruster Subassembly (VTSA)
Hydrazine Transfer SubAssembly (HTSA)
OSAM-1 Propellant Transfer Subsystem major sub-assemblies were qualified & validated
with installation into Servicing Payload completed Feb 2023
Hose Management Assembly (HMA)
HMA Vibe Test @ KSC
HRT Weld Integration & Heater / Thermistor / Harness Install & Test
HMA TVAC Test (8 Cycles) + vibe + HSA Marking
Feb
Turnover to SPINT
Dec 16 , 2022
May
June
Sept 22
2021
HMA HTSA Thermal HW & Test
HTSA Mechanical Panel Fabrication
HMA
EMI / EMC
Test
HSA Weld Integration CSA / PT / SV (NDE / leak test)
Major component / Sub-element fab / test and qual to flight requirements / environments - complete
Notes: The planned remaining PTS acceptance testing can be seen in below block diagrams and is on track to support Payload installation and test in Summer of 2022.

## Slide 39: Satellite Servicing Extensibility
  The core technologies being developed for OSAM-1 are extensible to many space system architectures and future mission needs
    In-space fluid transfer progress is focus of this presentation
39

## Slide 40: Summary of HMA ETU and PFU Verification/Test
Over 9 years of development & test for unique combined capabilities, environments, & contingencies
Terms:
ETU: Engineering Test Unit (design and functionality to near flight like without full flight pedigree)
PFU: Protoflight Unit (to be tested at slightly higher levels than normal flight article acceptance tests)
Reference historical detail reports available upon request
Reference extracted from full suite of PTS verification tests in Technical Memo: OSAM1-PTS-TN-0763
Notes: We now switch gears to a summary discussion of some of the unique capabilities involving the Hose Management System and the Flowmeter. The HMA full suite of capabilities were developed over 9 years, based on serial funding. This effort not only involves typical space environmental qual & cycle life, but also special features for unlimited sun or blackout exposure and contamination along with operational twist & torque limits for the operational use. Development efforts as seen in next 3 slides, evolved from crude prototypes then onto ETU and finally Proto-flight articles. Note that the detail test and analysis reports available are shown in green text for remainder of the presentation.

## Slide 41: OSAM-1 PTS Evacuation and Surge Test Campaign
Full Test Setup
PT8
PT04
Tool
QD
FDV
PT2
PT1
Temp. Probe
Hose
SV1 to Client FDV
2-D layout, near exact replica of flight system plumbing
cc: Cubic centimeter
FDV: Fill and drain valve
FM: Flow meter
HMA: Hose management assembly
HTSA: Hydrazine transfer subassembly
PL: Payload
PT: Pressure transducer
PTS: Propellant transfer system
QD: Quick disconnect
SV: Solenoid valve
TT: Temperature sensor
Bus/PL Interface
Vent Thruster (Simulator)
Flexhose
PT8
PT7
Temp. Probe TT-21
PT6
PT9
SV2
SLV8
HMA
HTSA
FM1
Temp. Probe TT-20
Tool/QD and TT-15
FDV
HTSA
SV2
SV2
SV1
SV2
SV1
Notes: The test campaign was performed using a high-fidelity flight-like ground setup with water to simulate the hydrazine. The test assembly is an exact replica of the flight plumbing bends, lengths, and inner diameters and includes simulators for all components with two of the solenoid valves being flight EDUs. These two EDU solenoid valves contain an inlet and outlet filter to protect the sensitive valve seat from contamination. The goal of the evacuation and vent testing was to remove the liquid from the plumbing through a simulated vent thruster which was connected to a vacuum source during testing. The plumbing is shown in the images above with the orange representing the large volume that includes the flex hose and the green highlighting the small volume between SV1 and the client FDV.

## Slide 42: PTA: Flow Meter System-Level Use Uncertainty
There are 4 primary sources of error in transfer mass measurement when using the PTS flow meter:
  PSU pulse counting: PSU counts pulses digitally (so no A to D), therefore error contribution is negligible
  Propellant temperature measurement: PSU analysis shows worst case thermistor measurement uncertainty of ± 0.59C (calc of transfer mass by PSU requires density calc (using temp telemetry with its own inaccuracies)
  Volumetric flow rate measurement: Flow meter maximum volumetric flow rate uncertainty is ± 1%
  HFCS time-tagging: Negligible contribution to transfer mass uncertainty
Worst case predicted transfer mass uncertainty is 1.1% (primarily due to flow meter error), easily meeting 10 kg max uncertainty requirement across full range of transfer mass
Verified system level use with all stacked errors meet high precision mission needs (RL-PTS-TN-0099)
Notes: Testing and analysis at integrated Payload system level predicts a transfer mass uncertainty of 1.1 % accounting for all major stacked input errors.

## Slide 43: PTS and Refueling Tool Development Test
Full propellant transfer system with pumps, flow meters, bellows accumulator, etc.
Oxidizer Nozzle Tool (ONT) and ATDS with robotic arm
Tested with NTO at KSC with telerobotic ops from GSFC
ONT w/QD
Telerobotic client interface mating, NTO transfer, and disconnect
Notes: The Oxidizer Nozzle Tool implemented this new architectural approach. It was successfully used to perform tele-robotic dinitrogen tetroxide transfers at Kennedy Space Center while being controlled by the operator and engineer located at Goddard Space Flight Center. The ONT and its QD are the basis for the “Refueling tool and quick disconnect” patent filing granted in August of 2021.

## Slide 44: Refueling and Fluid Transfer Technology Development (NASA)
Potential Government Funding & Partnership Opportunities
Small Business Innovation Research (SBIR) - https://www.sbir.gov/
Government Contract Solicitations - https://sam.gov/
NASA Solicitation and Proposal Integrated Review and Evaluation System (NSPIRES) - https://nspires.nasaprs.com/external/
NASA TechPort (need to apply for access) - https://techport.nasa.gov/opportunities
44

## Slide 45: ISAM GAPS Other Related Fluid In-Space Efforts Required beyond OSAM-1
Cooperative client* fuel servicing of a client bladder/diaphragm tank (ORS on STS-41G, OE)
Cooperative client fuel servicing of a client PMD tank (Orbital Express)
Cooperative client fuel and oxidizer (bi-prop) servicing (Gateway, ISS, Mir, & Salyut 6)
  Assume oxidizer tank is PMD or metal bellows-type; NTO bladder/diaphragm not feasible unless mission is on the order of days
Non-cooperative client fuel servicing of a client bladder or diaphragm tank (OSAM-1)
Non-cooperative client fuel servicing of a client PMD tank
Non-cooperative client fuel and oxidizer (bi-prop) servicing
  Assume oxidizer tank is PMD or metal bellows-type; NTO bladder/diaphragm not feasible
Cooperative or non-cooperative servicing of a high pressure GHe/GN2 system
  Less difficult if blowdown transfer, but will be very lengthy process
Cooperative or non-cooperative servicing of a high pressure, super critical xenon system (Gateway)
  Challenges with phase changes
Cooperative or non-cooperative servicing of a cryogenic system (SpaceX Starship)
  Including storage with zero / negligible boil-off
*Cooperative client – A spacecraft that was designed to enable on-orbit servicing
“Easy”
“Difficult”
Flight Proven
No Flight Heritage

## Slide 46: In-Space Fluid Transfer Shortfalls
https://www.nasa.gov/spacetechpriorities/
Priority #111 of 187
Priority #100 of 187
Priority #50 of 187

## Slide 47: AXCIS Alignment to ISAM
Spacecraft fluid and pneumatic gas servicing systems are required for future programs such as Gateway, OSAM, Artemis, DoD, U.S. commercial, Martian Transit, and Lunar / Martian surface.
  Programs typically do not have the resources (schedule) for R&D efforts. AXCIS intends to help these programs by advancing key technologies.
“On-orbit servicing, assembly, and manufacturing” is a “Critical and Emerging Technology” in the “Space Technologies and Systems Subfield” per the National Science and Technology Council, Executive Office of the President of the United States, February 2022 Critical and Emerging Technologies List Update Report.
Executive Office of the President of the United States, April 2022 ISAM National Strategy Report stated six strategic goals, three directly applicable to AXCIS: “(1) advancing ISAM research and development… (3) accelerating the emerging ISAM commercial industry… and (6) inspiring a diverse future workforce as a potential outcome of ISAM innovation.”
NASA recently stood up the Consortium for Space Mobility and ISAM Capabilities (COSMIC), a nationwide coalition to invigorate a domestic in-space servicing, assembly, and manufacturing (ISAM) capability. AXCIS aligns with the goals of COSMIC.

## Slide 48: AXCIS Technologies Delivery Schedule
 | AXCIS Technology | Partner | Contract Mechanism | Anticipated Delivery Date
 | 1) Seal-less, mechanically compliant, fluid adapter | Quadrus Corp. | SBIR Phase II E Direct Award | January 2025 (On Track)
 | 2) High accuracy Coriolis mass flow meter | Emerson Micro Motion / Chase Defense Partners | Sole Source FFP Contract | Delivered September 2024
 | 3 & 4) Helium / Xenon Compressor | Flight Works, Inc. | SBIR Phase III Direct Award | February 2025 (On Track)
 | 5) Variable Output Regulator | Premier Industries | FFP Contract | January 2025 (On Track)
 | FFP = Fixed Firm Price |  |  | 

## Slide 49: AXCIS TVAC System Test Plan
Technology | Model | Liquid Transfer | Liquid Pressurization | High Pressure Helium Transfer | High Pressure Xenon Transfer
1) Seal-less, mechanically compliant, fluid adapter | Flexible Fluid Adapter | X |  |  | 
2) High accuracy Coriolis mass flow meter | Coriolis Flow Meter (Liquid) | X |  |  | 
 | Coriolis Flow Meter (Helium) |  | X | X | 
 | Coriolis Flow Meter (Xenon) |  |  |  | X
3 & 4) Helium / Xenon Compressor | Helium/Xenon Compressor |  |  | X | X
5) Variable Output Regulator | Low Pressure Variable Output Regulator |  | X |  | 
 | High Pressure Variable Output Regulator |  |  | X | X

## Slide 50: Examples of Intellectual Property Analysis & ConOPS Bi-Propellant and GHe In-Space Transfer Model
Thermodynamic and fluid transfer models created to study efficiencies and ensure safety while holding reasonable timeline
  GHe transfer, client tank venting, and propellant transfer
  Bipropellant resupply to PMD-type client tanks requires ullage venting prior to propellant transfer for large % refill
Venting model anchored to existing data; however, they would benefit from further validation prior to practical application
Model utilized for study with external partner and for Gateway program with minor changes to initial conditions
Generic Propellant & Helium Transfer System
Notes: Thermodynamic fluid transfer models were created to study propellant and pneumatic gas transfer for a generic servicer and client system as shown in the image. The propellant transfer modeling package includes tank venting and filling from a propellant management device-PMD-style tank, along vent interface and plume modeling.

## Slide 51: GHe Transfer (Charging) & Blowdown Model
Gaseous helium transfer from the servicing vehicle to the client was modeled to determine pressure and temperature changes in COPV’s
  Helium transfer (charging) causes the servicer tank temperature to decrease (due to expansion) and the client tank temperature to increase (due to compression)
  The helium transfer assumes use of an electronic regulator controller with a redundant fast valve / orifice for maximum efficiency, reliability, and safety protection
Model predicts pressure, temperature, flow rate, pressurization rate history, and the overall transfer (charging) time
Generic Helium Transfer System
Helium properties
COPV geometry
Heat transfer constants
Initial pressure
Initial temperature
Orifice parameters
Valve cycle timing
Model Inputs
Pressure profiles
Temperature profiles for helium and tank walls
Flow rate
Mass transferred
Pressurization rate
Energy
Model Outputs
Notes: The gaseous helium transfer model uses the geometry and thermal properties from a typical COPV along with the properties of the gas to determine the system heating during pressurization and the cooling during static, no-flow conditions. It assumes an electronic regulator is used that can adjust to any desired outlet pressure but could easily be modified to any servicing vehicle design.

## Slide 52: Client Tank Filling & Venting Application of the Integrated Model
Two techniques studied in detail:
Multiple sequential vents then fill
  Vent ullage for 6 to 45 seconds (or other) until minimum temperature or target pressure is reached (vapor pressure + x psi)
    Results in a lower starting pressure before liquid fill
  Fill until maximum pressure reached, allow cooling, and then fill again until maximum pressure reached
  Does not require interface with ullage and fill FDVs simultaneously
Single short vent, single fill, repeat
  Vent ullage for 6 to 75 seconds (or other) until minimum temperature is reached
  Shorter vent/fill timeline by ~10 to 20% depending on system design (with optimized trades)
  Repeat until fill is complete (maximum pressure reached)
  Requires interface with ullage and fill FDVs simultaneously
Generic Propellant Transfer System
Propellant properties
Tank geometry
Heat transfer constants
Initial pressure
Initial temperature
Initial propellant mass
Orifice/venturi parameters
Fill/vent valve cycle timing
Model Inputs
Pressure profiles
Temperature profiles of tank wall, propellant, and ullage mixture
Flow rates
Mass vented
Mass transferred
Propellant/ullage volume
Pressurization and depress rates
Energy
Ullage mass fractions
Model Outputs
Notes: The venting model discussed was then added to the larger model that also includes the propellant fill. These two models work in concert together to form the overall MMH and N2O4 propellant transfer models. The model incorporates inputs such as the propellant tank geometry and thermal characteristics along with the initial conditions of the propellant. It outputs pressure, temperature, flow rate, mass transferred and many other variables as a function of time. The model can be utilized to perform trade studies and to analyze the servicing timeline. We chose to focus on two techniques for performing a propellant transfer operation. The first involves a series of relatively short vents of the propellant tank to a set pressure and then filling it with propellant. The second performs a single short vent and then a single propellant fill that is then repeated.

## Slide 53: Typical GEO Bi-Prop Results for Client Tank Venting & Filling Comparison of Two Primary Modes of Propellant Transfer
Method 1: Multiple sequential vents then single fill
The tank is vented to a set pressure (margin) above the vapor pressure of the liquid or until a low temperature limit is reached
  Potential impact to NO content in NTO
It takes several cycles for venting the tank to the desired set pressure subject to given constraints prior to filling
Propellant transfer takes a few cycles thereafter
Method 2: Single vent, single fill, repeat
Heating during ullage compression is accompanied by ullage cooling in each transfer cycle
It takes several cycles for the given propellant to be safely transferred
100%
0%
50%
100%
0%
~70%
Venting
Prop Filling
Venting and Prop Filling
Notes: The model output graphs shown here summarize some of the key features for the two methods mentioned. One key difference between the two techniques is that the first one does not enable a full propellant load unless the venting operation is repeated. You can see in the sample graphs that you can setup the model to run until certain predetermined cutoffs are met like a low or high temperature.

## Slide 54: Prior Hardware Development Investments by NExIS (SSPD, SSCO…)
2012 2013 2014 2017 2020 2022
Seal-less N2O4 Pump Tests (KSC)
Testing of prototype micro pump with CFC-113 and N2O4 MON-3.
2012
H/W Development
Flow Meter Technologies
Test of multiple ground units with various fluids (including hypergolics) to determine feasibility for on-orbit propellant transfer.
2012 - 2016
H/W Development
Bellows Accumulator
Titanium bellows accumulator development with industry partner to enable pressure manipulation of a propellant transfer system.
2012-2013
H/W Development
Modified Prototype Pump Development
Reliability enhanced prototype pump through testing with CFC-113 and NTO MON-3 with other pumps in parallel.
2013 - 2015
H/W Development
Xenon Transfer Compressor
Test of various ground unit pump/compressor technologies to enable efficient on-orbit transfer.
2014 - 2016
Development Testing
On-Orbit Transfer Flow Meter
Development of high accuracy flight-rated unit for N2H4 propellant transfer.
2017 - 2021
H/W Development
Torque-Compliant Metal Convolute Flex Hose
Metal convolute flex hose qualification tested compliant to multi-cycle twist / torque / bend values for prop transfer.
2017 - 2020
H/W Development
N2O4 MON-3 Mechanically Compliant Interface
Device to allow for seal-less pitch, roll, and yaw compliance with N2O4 MON-3.
2020 - Future
H/W Development
On-Orbit Helium Servicing Technologies
Development of electronic regulator and compressor hardware and modeling tools to perform efficient on-orbit helium servicing.
2020 - Future
H/W Development
Flight Coriolis Flow Meter
Development of electronics able to withstand space environment and maintain high accuracy of sensor to use with any fluid (including hypergolics) for on-orbit propellant transfer.
2022 - Future
H/W Development

## Slide 55: Example of some Key Prior Related Test Campaign Investments by NExIS (SSPD, SSCO…)
2012 2013 2015 2016 2017 2018 2019 2020 2021
Client Interface Leak Testing
Testing of worst-case leakage at client interface and GHe to liquid leakage correlation.
2017 - today
Development Testing
WSTF Materials Testing and Client FDV Testing
Testing of new materials with N2O4 MON-3 and MMH along with Peacekeeper FDV testing.
2012 - 2016
H/W Development
GSFC Servicing Testbed
Full scale client mockup with PTS functional test setup and robotic arm simulators.
2015 - today
Con Ops Development
Vacuum Venting Testing
ASME hypergolic propellant / vacuum rated for liquid jet dispersion test vessel.
2019 - today
Development Testing
On-Orbit Bi-Propellant Transfer Modeling
Transient thermal-fluid model of N2O4 MON-3 and MMH propellant transfers to study system temperature, pressure, and flow rate.
2020 - today
Concept Evaluation
Propellant Transfer Subsystem CFC-113 and NTO Testing
System-level tests with flight-like ETU flow meter, pump, bellows accumulator, and linear control valve.
2013-2014
H/W Development
KSC OSAM-1 PTS Testbed
End-to-end functional and volumetric simulator of flight PTS used for flow, pressure surge, and evacuation/vent testing. Utilized to validate con ops and verify PTS requirements.
2018 - today
Development Testing
2013-2015
H/W Development
ROSE
Reconfigurable Operational Spacecraft for Science and Exploration using repurposed Peacekeeper hardware.
2016 - today
H/W Development
HMA Vibe, EMI/EMC, Thermal, Shock, & Ascent Venting
Qualification testing of unique hose management assembly for the OSAM-1 (and other prop servicing missions).