## Slide 1: Fluidic Fence Flow Control on a 30° Swept Wing in Compressible Freestreams
Evan J. McFadden & Jeffrey P. Bons
The Ohio State University
Mechanical and Aerospace Engineering
2025 AIAA SciTech Forum, Jan. 6th – 10th

## Slide 2: Motivation

## Slide 3: Swept Wing Design
Designed for high-speed flight
Drag rise at high subsonic Mach numbers weakened by sweeping the wing
Complicated stall patterns in low-speed flight
Susceptible to sudden pitch break and loss of lift
Dependent on Mach number
[Hoerner, 1965]
[Harper and Maki, 1964]

## Slide 4: Fence-type flow control methods
Passive control techniques and high lift devices can modify the pitch performance
An active ‘fluidic fence’ via slot blowing mimics passive fence benefits
  Lower drag penalty, can be actuated ‘as-needed’
CM
α
+
0
–
0°
40°
[Pratt and Shields, 1952]
[Walker and Bons, 2018]

## Slide 5: Fence-type flow control methods
Obstruction of spanwise flow on suction surface improves flow on outboard wing
Lift increment over wide range of α, especially with VGJs
ΔCL
α (°)
[McFadden et al, 2023]
[McFadden et al, 2022]
Fluidic fence
M = 0.05
Re = 105
α = 15°

## Slide 6: Study Objectives
Test the performance of a streamwise row of vortex generating jets in compressible freestreams for enhanced AFC utility
Evaluate how performance scales with AFC cost metrics at higher Mach numbers

## Slide 7: Methods

## Slide 8: Model Details
30° Swept Wing
AR=4.3, no taper
NACA 643-618 airfoil along true chord, c
Active flow control at 70% span
Test article for previous AFC studies, experimental and computational

## Slide 9: Active Flow Control Method
20 vortex generating jets (VGJs)
1mm diameter, placed 5 diameters apart
60° skew, 30° pitch (relative to local surface curvature)
  Leading edge jet constrained to 90° skew
Flat face specified as inlet BC
60° skew
30° pitch
5mm
TOP
SIDE
FRONT

## Slide 10: CFD Methods
NASA’s FUN3D-FV RANS Solver
Adaptive mesh refinement with Sketch-to-Solution, refine function
  Mesh adapted on gradients in the scalar flow metric of Mach number
  18 mesh adaptations for final meshes that contained 180 million tetrahedral cells
Negative Spalart-Allmaras one-equation turbulence model (SA-neg-RC)
  Handling of negative values
  Rotation/curvature corrections
Riemann-invariant farfield boundary conditions 100 ceff away from wing
Symmetry plane at wing root to model full wing in free flight
Total pressure boundary conditions applied to VGJ inlet faces for AFC
Hierarchical Adaptive Nonlinear Iteration Method (HANIM)
  Preconditioner, generalized conjugate residual (GCR) method, and CFL adaptation

## Slide 11: Test Matrix
4 freestream Mach number setpoints, 2 angles of attack at each (5° & 10°)
  First Mach number matched low-speed wind tunnel conditions
Targeted a constant mass flow coefficient (CQ) at each setpoint
 | M = 0.051 | M = 0.30 | M = 0.5 | M = 0.7
Mach | 0.051 | 0.300 | 0.500 | 0.700
Temperature (K) | 300 | 300 | 300 | 300
Velocity (m/s) | 17.8 | 104.2 | 173.6 | 243.1
Re | 1.0e5 | 5.8e5 | 9.7e5 | 1.4e6
Angles of attack | 5°, 10° | 5°, 10° | 5°, 10° | 5°, 10°
PRAFC | 1.05 | 2.54 | 4.21 | 4.83
CQ | 0.0024 | 0.0027 | 0.0029 | 0.0028
Cµ | 0.0223 | 0.0138 | 0.0074 | 0.0065
Cπ | 1.374 | 0.130 | 0.084 | 0.056
VR | 4.62 | 2.54 | 1.26 | 1.14

## Slide 12: Results

## Slide 13: Low-Speed (M = 0.05) Results
Baseline:
Spanwise flow development
Trailing-edge separation
AFC:
Flow improved on outboard wing section
  ~7% lift enhancement at each angle of attack
Entrainment, streamlines turning towards fluidic fence
V∞
ΔCL = 7.7%
ΔCD = 7.9%
ΔCM = 42.8%
ΔCL = 6.7%
ΔCD = 12.4%
ΔCM = 86.3%

## Slide 14: Baseline wing performance
V∞
Spanwise flow development more rapid with Mach
  TE separation line moves forward on chord
Cl drop-off with span intensifies with M

## Slide 15: AFC wing performance
Obstructs inboard spanwise-oriented flow
Outboard attached flow
Shock-induced separation significantly reduced
Smaller local AFC impact
  Linked to constant CQ
V∞
ΔCL = 5.7%
ΔCD = 9.9%
ΔCM = 31.5%
ΔCL = 5.0%
ΔCD = 10.7%
ΔCM = 51.5%
ΔCL = 3.0%
ΔCD = 9.9%
ΔCM = 22.3%
ΔCL = 3.2%
ΔCD = 10.9%
ΔCM = 47.1%
ΔCL = 2.1%
ΔCD = 10.0%
ΔCM = 25.8%
ΔCL = 3.8%
ΔCD = 6.3%
ΔCM = 82.8%

## Slide 16: Section lift distributions
ΔCl highest for low M
  Monotonic with Mach until shock-induced separation becomes relevant
Inboard losses due to blowing
Lift enhancements highest immediately surrounding VGJs
Effect of wingtip vortex re-introduced for M = 0.7, α = 10°
Baseline Lift Distributions
ΔCl due to AFC

## Slide 17: Force Coefficient Summary
Lift and drag always increase with actuation
Pitching moment more negative with actuation
Normalizing with Cµ demonstrates high Mach effectiveness
  Cµ is expensive

## Slide 18: Local changes in pressure coefficient
ΔCp further aft for higher Mach
Region of decreased pressure gets smaller with Mach
Saturated streaks of ΔCp from movement of SS shock
V∞
ΔCl due to AFC

## Slide 19: Change in Shock Location for M = 0.7
Baseline
α=5°
AFC
α=5°
Baseline
α=10°
AFC
α=10°

## Slide 20: Conclusions
Streamwise row of VGJs tested computationally at freestream Mach numbers of 0.05, 0.3, 0.5, and 0.7 at constant CQ
Flow improvements found outboard of control, as with previous studies
  Consistently decreased pitching moment, good for control
Increments in lift decreased with Mach number, effect of CQ
  7.7% to 2.1% ΔCL at α = 5°
  6.7% to 3.8% ΔCL at α = 10°
Change in pressure coefficients found further aft on suction surface with M
Intriguing interplay with suction surface shock at M = 0.7
  Potential for other applications with shock features, reducing separation

## Slide 21: References
Hoerner, S. F., Fluid-Dynamic Drag, published by the author, Bakersfield, CA, 1965, Chap. 15.
Harper, C. W. and Maki, R. L., "A Review of the Stall Characteristics of Swept Wings," NASA TN D-2373, 1964. https://ntrs.nasa.gov/citations/19640014908.
Pratt, G. L., and Shields, E. R., “Low-Speed Longitudinal Characteristics of a 45° Sweptback Wing of Aspect Ratio 8 with High-Lift and Stall-Control Devices at Reynolds Numbers from 1,500,000 to 4,800,000,” National Advisory Committee for Aeronautics Research Memo NACA R&M L51J04, 1952. https://ntrs.nasa.gov/citations/19930086963.
Walker, M. M. and Bons, J. P., "The Effect of Passive and Active Boundary-Layer Fences on Swept-Wing Performance at Low Reynolds Number," in 2018 AIAA Aerospace Sciences Meeting, Kissimmee, FL, 2018. https://doi.org/10.2514/6.2018-0793.
McFadden, E. J., Brandt, P. J. and Bons, J. P., "Swept-Wing Active Flow Control with a Streamwise Row of Vortex Generating Jets," AIAA Journal, vol. 61, no. 3, pp. 1142-1150, 2023. https://doi.org/10.2514/1.J062302.
McFadden, E. J., Brandt, P. J. and Bons, J. P., “The Effect of Spanwise Location of a VGJ Fluidic Fence on Swept Wing Performance,” in AIAA Aviation 2022 Forum, Chicago, IL, 2022. https://doi.org/10.2514/6.2022-3468.

## Slide 22: QUESTIONS

## Slide 23: Backup Slides

## Slide 24
Increasing Re from 105 to 106
Leading-Edge Sweep and Reynolds Number Variation For Fluidic Fence Active Flow Control
VGJ Fluidic Fence @ Re=1,000,000
Benefits generally decrease at higher freestream Reynolds number
Note: CFD computes decrements to lift performance at high angles of attack

## Slide 25: Active Flow Control System Costs
AFC cost metrics for required air supply
Design complexity = $$
Added weight = $$
Impact on cruise drag and fuel burn = $$
Goal: Minimize AFC cost, maximize AFC utility
Mass flow coefficient:
Momentum coefficient:
Power coefficient:

## Slide 26: Sketch-to-Solution
3 mesh adaptations per target complexity before doubling cell count
Metric field:
M is the adaptation scalar (Mach)
H is the reconstructed Hessian matrix of M, the adaptation scalar
Ct is the target mesh complexity, correlated to number of grid points
p = 2, d = 3
“A mesh conforming to MLP provides optimal control of the scalar field interpolation error in the p norm. A lower p norm targets weaker variations of the scalar field and a larger p norm targets rapid variations of the scalar field.”