## Slide 1
Dr. Jim Clark
Dr. Dolan Highsmith
The Aerospace Corporation & NASA CARA
35th Space Flight Mechanics Meeting
Kaua’i, Hawaii, Jan 19-23, 2025
Decision Aid for Conjunction Risk Mitigation by Differential Drag

## Slide 2: What is differential drag?
Propagation assumes a particular drag area.
Changing a satellite’s drag has a net propulsive effect!

## Slide 3: Why does CARA Analysis need a decision aid?
CARA’s missions are seeing more and more conjunctions.
Missions without propulsion want to explore their options for collision risk mitigation.
(Missions with propulsion want to explore their options!)

## Slide 4: The Δ-B-Cs of differential drag
To compare satellites consistently, we use delta-BC:
Delta-BC =
So, Delta-BC of 2  3x drag area
Can be negative, to represent decreasing drag area.
Can be time-averaged to encompass duty cycles, etc.
BC: Ballistic Coefficient = (area/mass)

## Slide 5: Can my satellite use differential drag?
~4,300 historical conjunctions with Pc > 1E-4 at TCA-3 days.
Using CARA’s Maneuver Trade Space (MTS) tool, propagate with different delta-BCs. Final Pc < 3E-6?
There seems to be a clear breakpoint in the 500-600 km range, around delta-BC of 2.
Zooming in, 560 km is (close to) the 50% point.
Pc: Probability of collision
TCA: Time of Closest Approach

## Slide 6: Validation
To validate MTS’s analysis, we compared to another NASA mission that uses drag for risk mitigation. (Delta-BC = 2.2, perigee ~520 km, ~48-hr maneuvers)
In most cases: qualitative agreement, tending conservative

## Slide 7: Validation
Of the 16 conjunctions we identified, 11 were remediated, which is consistent with expectations!
The one “optimistic” error was from a plan that was superseded by a shorter one (true negative).
Predict \ Actual | Remediated | Not Remediated
Remediated | 7 | 1*
Not Remediated | 4 | 5

## Slide 8: Application – Mission Design Support
A mission with very large solar panels asked us to evaluate differential-drag for risk mitigation.
Orbit not yet fixed, 500-700 km
Unfortunately, their mission constraints restrict their time-averaged delta-BC.
Theoretical max efficacy…
…Actual efficacy.
… 8 9 10
0.68

## Slide 9: Other considerations
Positive vs. negative delta-BC
  Usually more ‘upside’ going positive, but if the mission doesn’t have much delta-BC and has to make the most of it, CARA can advise them how to best reduce collision risk.

## Slide 10: Conclusion
A mission:
  Perigee below ~560 km
  Able to triple its drag area
  For 3 days straight
  (or a greater factor for less time)
Can count on differential drag to remediate many high-interest conjunction events.
This is a very high bar to clear! Much higher than formation maintenance, etc.
CARA is exploring other aspects of differential drag:
  What efficacy is ‘worth pursuing’ vs. acceptable as a substitute for propulsion?
  What counts as remediation?

## Slide 11: Diff-drag efficacy, 3 days, 100% duty cycle

## Slide 12: Diff-drag efficacy, 2 days, 100% duty cycle

## Slide 13: Diff-drag efficacy, 1 day, 100% duty cycle

## Slide 14: Diff-drag efficacy, 3 days, 30% duty cycle

## Slide 15: Evaluation of differential drag
~4,300 historical conjunctions with Pc > 1E-4 at TCA-3 days.
Take that state, propagate with different delta-BCs, compare to original
  Should be close to the historical DB value at delta-BC = 0
  Mostly ‘more is more’, but some conjunctions behave a little differently…

## Slide 16: Evaluation of differential drag
~4,300 historical conjunctions with Pc > 1E-4 at TCA-3 days.
Take that state, propagate with different delta-BCs, compare to original
  Should be close to the historical DB value at delta-BC = 0
  Mostly ‘more is more’, but some conjunctions behave a little differently…

## Slide 17: Evaluation of differential drag
~4,300 historical conjunctions with Pc > 1E-4 at TCA-3 days.
Take that state, propagate with different delta-BCs, compare to original
  Should be close to the historical DB value at delta-BC = 0
  Mostly ‘more is more’, but some conjunctions behave a little differently…