## Slide 1: Average Heat Flux Measurements in a Gaseous Detonation-Based Rocket Engine
Matthew A. Maybee1, Michaela R. Hemming1, Kaito J. Durkee1, Justin M. Byers1
Joseph Hernandez-McCloskey2, Kunning G. Xu1, John W. Bennewitz1, Thomas Teasley3
1The University of Alabama in Huntsville (UAH)
2The University of Texas San Antonio
3NASA Marshall Space Flight Center
AIAA SciTech 2025 – January 9
This material is a work of the U.S. Government and is not subject to copyright protection in the United States.

## Slide 2: Overview
Introduction / Motivation
  Overview
Hardware
  Heat-sink hardware
  Calorimetry hardware
  Coolant channel geometry sizing
Experimental Methods
  Heat flux determination
  Methodology
Experimental Results
  Operational map
  Heat Flux
  Wave dynamics
Conclusions

## Slide 3: Motivation
Realizing the benefits of rotating detonation rocket engines (RDRE) will be accompanied with increased thermal loads
Heat flux levels must be measured to develop thermal management strategies for RDRE
  Long duration firing times are required, necessitating actively cooled hardware
Objective: Obtain average axial heat flux measurements in an actively cooled RDRE as a first step towards the development of thermal management strategies
+J. W. Bennewitz, et al. Experimental validation of rotating detonation for rocket propulsion. Scientific Reports, 13(1):14204, August 2023.

## Slide 4: Hardware Configurations
Hardware specifications:
  76.8 mm annulus (OD)
  6.65 mm annular width (63.5 mm OD center body)
  Chamber length: 76.2 mm
  Additively manufactured (AM) out of GRCop-42
  Three configurations tested
Three hardware configurations investigated
Hardware comprised of three modular components:
  Outer body
  Inner body
  Expansion nozzle
  Propellant manifold

## Slide 5: Calorimetry Testing Methodology
Objective: Provide axially resolved average heat flux distribution using long duration firing of calorimetry hardware
Axial heat flux distribution obtained through 18 circumferential internal channels
Target firing times used to achieve steady state operation:
  Straight center body: 3.5 s
  Constricted center body: 4.5 s
CTAP
Inlet
Outlet
Temperature rise across hardware and measured mass flow rate used to determine heat flux

## Slide 6: Coolant Channel Geometry Sizing
Heat flux of 23.6 MW/m2 assumed (Micka et al.1)
Initial outlet temperature set to be coolant saturation temperature at working pressure
Temperature rise across hardware decreases until
Objective: Determine the coolant channel geometry to achieve mass flow rate required required to cool combustor wall
Heat Transfer Coefficient:
Required Heat Transfer Coefficient:
[1] Micka et al., AIAA Propulsion and Energy 2021 Forum, AIAA 2021-3685, 2021.

## Slide 7: Design Overview
Channel Dimensions: 2.54 x 3.05
  Rib width increases to 1.78 above CTAP
  Parallelogram cross section due to AM
  30º overhang angle
Inlet/Exit 180° ± 20° apart
  Outlet: 9 7.04 mm ID brazed tubes
CTAP
Outlet
Inlet
2.54
1.27
1.27
3.05

## Slide 8: Inlet and Outlet Manifolds
Inlet Manifold
Exit Manifold
Injector Face
Three inlet manifolds supply coolant to 18 channels
Coolant exits hardware through nine brazed tubes
Flow Direction
Uncooled Center Body

## Slide 9: Axial Stations
Measurements taken at nine axial stations 0.01 mm apart
One CTAP measurement
  Chamber pressure () measured at
Two center bodies tested:
  Straight center body (top)
  Constricted center body (bottom)
Throat located at for constricted geometry
throat

## Slide 10: Experimental Setup
Cooling water supplied by pressure fed system at 12.4 MPa
  Provides coolant mass flow rate of 2 kg/s
Engine mounted to 22 kN thrust stand
Critical flow orifices for propellant mass flow measurement
Diagnostics per axial station:
  Pressure (static pressure transducer)
  Temperature (T-type thermocouple)
High-speed imaging (Phantom TMX 5010)

## Slide 11: Constricted Center Body RDRE Firing
Constricted Center body configuration test:
  Total mass flux = 240 kg/m2-s, = 1.1
  Firing time: = 4.5 s

## Slide 12: Operational Map
Operational map for tests with calorimetry outer body
Total mass flux varied from 103-310 kg/m2-s at 1.1
6 conditions performed with the straight center body (= 3.5 s) and 4 with the constriction (= 4.5 s)
High Flux Case
Low Flux Case

## Slide 13: Outlet Temperature Temporal Histories
Thermal steady state reached for outlets 2-8
Outlets 1 & 9 do not fully reach steady state due to lack adjacent cooling channel
Data averaged over analysis period highlighted in red
Analysis Window

## Slide 14: Heat Flux Determination
Heat flux corrected for varying mass flow rates amongst channels
Heat flux calculated accounts for heat transfer between channels
Tout,
Mass Flow Rate:
Energy Balance:
Heat Flux Definition:

## Slide 15: Heat Flux Comparison
Low Flux: = 103 kg/m2-s, = 1.1
High Flux: = 240 kg/m2-s, = 1.1
Heat flux ranges from 5 to 18 MW/m2
Higher heat flux for constricted geometry
Constricted geometry, has local maximum at detonation front and throat

## Slide 16: Straight Channel Heat Flux Distributions
Total mass flux ranges from 103-310 kg/m2-s at 1.1
Heat flux ranges from 5.75-11.25 MW/m2
Increased heat flux at = 0.17-0.47
Heat flux decreases past detonation zone along axial direction

## Slide 17: Constricted Geometry Heat Flux Distributions
Increased heat flux loading for constricted geometry (7.5 - 17 MW/m2)
Total mass flux ranges from 103-240 kg/m2-s at 1.1
Sharp increase in heat flux at = 0.17-0.37, likely the axial location of detonation
Heat flux increases due to throat located at = 0.77
Difference in heat flux scaling between:
  (1) Detonation region
  (2) Flow expansion region
1
2

## Slide 18: Conclusions
Axial heat flux distribution experimentally determined for a water-based rotating detonation rocket engine calorimeter
Hardware tested at a total mass flux of 103-310 kg/m2-s at 1.1 for CH4/O2
Hardware tested with a straight and constricted center body:
  Straight center body:
    Average heat flux: 5−12 MW/m2
    Location of maximum heat: 𝑥/𝐿 = 0.27 (near detonation zone)
  Constricted center body:
    Average heat flux: 6−18 MW/m2
    Location of maximum heat flux: 𝑥/𝐿 = 0.77 (near physical throat location)
Heat flux scaling differs between near injector and flow expansion regions

## Slide 19: Acknowledgments
This work is sponsored by the National Aeronautics and Space Administration (NASA) Marshall Spaceflight Center (MSFC) under NASA CAN grant 80NSSC24M0062.
The authors would like to thank Dr. David Lineberry and Tony Hall for their invaluable support with testing, as well as Raj Dave, Garrett Cobb, and the students of the Advanced Propulsion, Energy, and Combustion Science Laboratory.

## Slide 20
Thank you
Questions?

## Slide 21
Backup Slides

## Slide 22: Heat Flux sensitivity to Operating Mode
Change in wave dynamics observed for constricted center body case
Station 1 outlet temperature reaches steady state, then exhibits an increase in slope
This behavior corresponds with the wave mode transitioning from a one wave rotating mode to a one wave counter-propogating mode

## Slide 23: Measurement Repeatability
Station 1 temperature response for increasing firing time

## Slide 24: Water Flow System
Water flow system from tank, through hardware, to atmosphere
H20 Tank volume [gal] | Mass flowrate [lbm/s] | Volumetric flowrate [gal/s] | GallonsH20 per 10 s test | Number of tests
60 | 9.0-12.6 | 1.1-1.5 | 11 - 15 | ~4-6

## Slide 25: Internal Channel Geometry
Cooling channels locally raised to create room for CTAP hole
  Tear drop cross section normal to the combustor wall
Cooling channels travel circumferentially 160º, 180º, and 200º to outlets

## Slide 26: Outlet Mass Flow Rate Measurement Rationale
Pressure, temperature measurement 10 diameters upstream of orifice to atmosphere
  Orifice sized to keep pressure measurement within PT measurement range (0-500 psig)
  K-Type TC to minimize uncertainty
Orifice calibrated via catch and weigh to determine prior to use
Coolant mass flow rate, , for each axial station determined using:
From Hardware
To ATM

## Slide 27: 20241031 dataset 5 side view

## Slide 28: 20241031 dataset 7 side view

## Slide 29: 20241031 dataset 7 top view

## Slide 30: 20241029 dataset 20 side view

## Slide 31: 20241029 dataset 20 top view

## Slide 32: 20241031 dataset 4 side view

## Slide 33: 20241031 dataset 4 top view