## Slide 1
Ben Nikaido
NASA Ames Research Center
Garth Hobson, PhD
Naval Postgraduate School
AIAA SciTech, Jan 6 – 10, 2025
Published by the American Institute of Aeronautics and Astronautics, Inc., with permission.
RANS Predictions of Inlet/Isolator Unstart at Mach 4

## Slide 2: Outline
Introduction
SWBLI V&V
Inlet/Isolator Model
Backpressure Mechanisms
Results
  Numerical Backpressure
  Louver Backpressure
Conclusions

## Slide 3: Research Goals
  Predict shock train position and unstart limits for future tests
    Flow control implementation
    Kulite® placement
  Investigate validity of 2D simulation simplification for this aspect ratio duct (2.4)
  Compare results from:
    Different 2-equation turbulence models
    Solution advancement schemes
    Two CFD solvers

## Slide 4: CFD Codes and Turbulence Models
OVERFLOW (2.4b)
  Finite difference solver for structured, overset grids
  Up to 6th order spatial accuracy
CREATE-AV Kestrel KCFD (v18.3)
  Finite volume (cell-centered) solver for general unstructured grids
  2nd order spatial accuracy
Both codes using HLLE++ (inviscid flux) and Kato-Launder for turbulent production variable formulation
Turbulence models:
  Wilcox k – ω [OVERFLOW]
  Menter Baseline (BSL) [Kestrel]
  SST [Both OVERFLOW and Kestrel]

## Slide 5: SWBLI V&V
Mach 5 impinging shock by Schulein[1] et. al. β =14°
DLR Ludwieg Tube Wind Tunnel Facility (RWG, Tunnel B)
Schematic of experiment
OVERFLOW Mach Contours
Shock Generator
Isothermal Wall (300K)
To = 410 K
Po = 21.2 bar
Re = 40e6 / m

## Slide 6: SWBLI V&V
Impingement point
(Exp.)
(Exp.)
Separation bubble

## Slide 7: Inlet/Isolator Model
Acap = 1.5 in2
L = 12 in, d = 0.625 in
Flow Conditions
M∞ = 4.0
To = 525°R (292 K)
Po = 250 PSI
Re = 2.35e6 / in

## Slide 8: Inlet/Isolator Model Shadowgraph
Started
(Unbackpressured)
Unstarted

## Slide 9: Backpressure Methods - Flaps
𝝳 = 17°
𝝳 = 18°
< 1°of flap angle between fully started and unstarted
No shock train formation

## Slide 10: Analytic Startablity Limits
Courtesy [2]
Used by permission
𝝳
17°
18°

## Slide 11: Backpressure Methods - Louver
Novel ”louver” mechanism
  Provides controlled and uniform static backpressure increase in space-constrained tunnel
  Allows pre-combustion shock train
  Maintains startability
Deflection Angle Convention
Rendering of Louver Valve. Currently in Additive Manufacturing

## Slide 12: Grids
3D OVERFLOW grid w/louvers
20M nodes
Triple-fringe
Connectivity by Pegasus
Supersonic
Extrapolation
(Specified P for
Numerical
Backpressure)
Freestream
Y - symmetry
M∞

## Slide 13
Results:
Numerical Backpressure
Outflow static pressure increased from 1 ≤ P4/P∞ ≤ 30
Each simulation successively continued from lower backpressure solution

## Slide 14: OVERFLOW URANS 2D (Mach) Increasing P4/P∞
k - ω
SST

## Slide 15: STLE Detection
xSTLE
xSTLE
L
L
2D solutions: Line probes just above boundary layer. STLE where most upstream M < 1 location
3D solutions: Surfaces just above boundary layer on ramp, cowl, and sidewall surfaces

## Slide 16: STLE location vs. Backpressure Ratio
STLE vs. Backpressure Ratio
2D Steady and 2D Time-Accurate
STLE vs. Backpressure Ratio
2D Steady and 3D Steady

## Slide 17: OVERFLOW 2D Time Resolution Study
STLE vs. Backpressure Ratio
STLE location vs. Iteration (time-marching)
P4 / P∞ = 7

## Slide 18: Mach Contours (Time-averaged)
P4/P∞ = 18

## Slide 19: Standard Deviation of Mach, Contours
P4/P∞ = 18

## Slide 20: Separated Flow Isosurfaces
P4/P∞ = 15

## Slide 21
Results:
Numerical Backpressure
Louver angle 𝜽 increased from 0°to 60°
Each simulation successively continued from lower backpressure solution

## Slide 22: OVERFLOW URANS 2D (Mach) Increasing 𝜽
k - ω
SST

## Slide 23: STLE location vs. Louver Rotation Angle

## Slide 24: Mach Contours (Time-averaged)
𝜽 = 35°

## Slide 25: Conclusions
Large difference in STLE location and unstart due to turbulence modeling
Temporal resolution affects STLE position and unstart
2D vs 3D difference in STLE position and unstart
  Span asymmetry
  Sidewall/corner separation
2D simulations show 25% difference in critical unstart backpressure
Surprising difference between OVERFLOW and Kestrel SST
SST predicts earliest unstart, concurrent with Reardon et. al. [3]
Optimal Kulite placements on ramp and cowl walls
Louver range of at least 0° ≤ 𝜽 ≤ 35° for stable shock train

## Slide 26: References
[1] Schulein, E., Krogmann, P., and Stanewsky, E., “Documentation of two-dimensional impinging shock/turbulent boundarylayer interaction flow,” Tech. rep., 1996.
[2] Rising, C. and Sosa, J., “Exploration of the Influence of Various Backpressure Mechanisms to Inlet Unstart,” ICCFD, Kobe, Japan, July 2024
[3] Reardon, J. P., Schetz, J. A., and Lowe, K. T., “Computational Analysis of Unstart in Variable-Geometry Inlet,” Journal of Propulsion and Power, Vol. 37, No. 4, 2024/12/01 2021, pp. 564–576.
[4] Di Stefano, M. A., Hosder, S., and Baurle, R. A., “Effect of turbulence model uncertainty on Scramjet Isolator Flowfield analysis,” Journal of Propulsion and Power, vol. 36, 2020, pp. 109–122.

## Slide 28
Backup Slides

## Slide 29
Hypersonic Airbreathing Propulsion

## Slide 30: Unstart

## Slide 31: Isolator Shock Trains
* Matsuo et. al.

## Slide 32: Backup