## Slide 1
A Workflow to Rapidly Interrogate Multiscale Model Simulation Results Across Multiple Length Scales
Trenton M. Ricks, Brett A. Bednarcyk, Steven M. Arnold, Evan J. Pineda
NASA Glenn Research Center (GRC), Cleveland, OH
Transformational Tools and Technologies (T3) Project
AIAA SciTech 2025 Forum, Orlando, FL
January 9, 2025

## Slide 2: Vision 2040
A Roadmap for Integrated, Multiscale Modeling and Simulation of Materials and Systems
Nine Identified Key Element Discipline Areas
2040 Vision State:
A cyber-physical-social ecosystem that impacts the supply chain to accelerate model-based concurrent design, development, and deployment of materials and systems throughout the product lifecycle for affordable, producible aerospace applications
cyber-physical-social ecosystem
NASA CR 2018-219771
https://ntrs.nasa.gov
Provides a public/private investment strategy for the design of fit-for-purpose materials and structures

## Slide 3: Why Should You Care About Multiscale Visualization?
Many materials have mechanisms and features at multiple length scales
  Allows a detailed interrogation of driving forces at appropriate subscales for a given mechanism
  Example problems in this presentation demonstrate this
Verification and validation of constitutive, damage, and failure models requires detailed visualization capabilities
  Becomes even more essential for multiscale problems
Most visualization tools show results at only one scale
  Q: how can you trust results and know they are accurate?
Allows users to leverage large amounts of data generated during an analysis to make better informed decisions
Multiscale visualization allows users to rapidly perform trade studies on individual methods

## Slide 4: NASA Multiscale Analysis Tool (NASMAT)
Successor to MAC/GMC and FEAMAC toolsets
A framework designed to support massively multiscale modeling
    Solves real, large-scale, non-linear, thermo-mechanical problems
Modular design to support “plug-and-play” capabilities
    Operational components categorized into NASMAT procedures
Developed for enhanced interoperability
    Integrates with 3rd party structural analysis codes (e.g., FEA)
  Library of constitutive laws/damage models
Ideal for “design with” or “design of” the material
  Enables Integrated Computational Materials Engineering (ICME)
  Developed to support Vision 2040

## Slide 5: Multiscale Recursive Micromechanics (MsRM)
Level 1
Level 2

## Slide 6: A Brief History of Micromechanics and Multiscale Analysis at NASA GRC*
1992
1996
1987
MOC
1991
Aboudi Book
GMC
MAC/GMC 2.0
2002
MAC/GMC 4.0
2013
Book Pub.
2001
HFGMC
MAC 1.0
1994
GMC - 3D
1995
FEAMAC 1.0
1997
FEAMAC 2.0
2003
HyperMAC
2005
2018
NASMAT 1.0
GrantaMAC
2011
NASA Funded
1992 – 2002: Development of basic tools/theories/methods
Inelastic deformation/constitutive model development
Fiber-matrix debonding/interfaces
Fatigue, creep fatigue
Laminate dominated
Focus shift:
Woven/braided composites
Multiscale
Visualization tools
Damage/failure
2016
NASMAT Dev. Starts
2020
NASMAT 2.0
2021
Book Pub.
2022
NASMAT 3.0
2024
NASMAT 4.0
1993
*Limited to our research group, not including seminal work of others (C. Chamis)
1999
MAC/GMC 3.0
MSGMC
2009
MACE Est.
2010
MACPOST
FEAMAC-Pre/Post

## Slide 7: A Brief History of Micromechanics and Multiscale Analysis at NASA GRC
1992
1996
1987
MOC
1991
Aboudi Book
GMC
MAC/GMC 2.0
1999
MAC/GMC 3.0
2002
MAC/GMC 4.0
2013
Book Pub.
2001
HFGMC
MAC 1.0
1994
GMC - 3D
1995
FEAMAC 1.0
1997
FEAMAC 2.0
2003
HyperMAC
2005
MSGMC
2009
2018
NASMAT 1.0
GrantaMAC
2011
NASA Funded
MACE Est.
2010
2016
NASMAT Dev. Starts
2020
NASMAT 2.0
2021
Book Pub.
2022
NASMAT 3.0
2024
NASMAT 4.0
1993
Pace of Methods Development and Application Has Far Exceeded Visualization Capabilities!
Detailed Visualization Limited to Two Scales!
MACPOST
FEAMAC-Pre/Post
Notes: Legacy visualization tools rely on paid software licenses
Implications for model validation

## Slide 8: NASMAT PrePost
A Solution for Efficiently Visualizing Multiscale Modeling Results
Utilizes state-of-the-art visualization tools not dependent on paid software licenses
Able to generate NASMAT models and incorporate legacy tools
Can ingest large datasets and quickly visualize results at multiple scales
Separate user-interface and utility functions for flexibility
Requirements
Features/Capabilities
Two example problems shown that capture relevant features across multiple length scales
Python development primarily utilizing PyQt5, VTK, H5py packages
Standardized functions for developing NASMAT inputs and processing NASMAT outputs
Able to seamlessly transition between results at multiple length scales
User-interface separated from “guts” of code to allow standalone result viewing
Converter to input VTU/VTI geometries from tools such as TexGen or PuMA
Support utility to add NASMAT Abaqus results to NASMAT H5 file for viewing

## Slide 9: Thermoplastic Terrestrial Point Design Collar
Support collar and beam concept, adapted from hardware for Roman Space Telescope Deployable Aperture Cover
Fused deposition printing fills in layers with a specified raster pattern
Composite additive manufacture (AM) of collar sub-element
PEEK matrix + ~10 vol% discontinuous carbon fiber
Bednarcyk, B.A., Mulhearn, W.D., Kaleel, I., Pineda, E.J., Steele, P.E. “Multiscale Modeling of Short fiber Additively Manufactured Composites,” presented at the ASME ASME Aerospace Structures, Structural Dynamics, and Materials Conference, April 29 – May 1, 2024, Renton, WA.
Notes: Features occurring at different scales in a multiscale analysis.

## Slide 10: Multiscale AM Problem Setup
90°
90°
0°
0° frame
Level 1
Layered AM composite with framing
Micro voids in printed filaments
[effective]
Macro voids between print passes
Level 2
Printed filament with macro voids between print passes
Level 3
Printed filament with as-measured fiber lengths and angles
Level 4
RUC with 2 short fibers
frame
NOTE: Overall void content in model = 21.9%
Level 3
Level 4
Level 4
Level 4
Level 5
0° frame

## Slide 11: Thermoplastic AM Composite Visualization with NASMAT PrePost
Green Arrow
RUC 2-direction
Blue Arrow
RUC 3-direction

## Slide 12: Thermoplastic AM Composite Visualization with NASMAT PrePost
Green Arrow
RUC 2-direction
Blue Arrow
RUC 3-direction

## Slide 13: Heatshield for Extreme Entry Environment Technology (HEEET)
HEEET designed to be part of the thermal protection system for re-entry spacecraft
HEEET comprised of two 3D woven layers:
  Recession and Insulation (IL)
Blended carbon and phenolic fiber tows
Four tows twisted to form a yarn
Yarns are woven to create preform
Preform infused with a highly porous phenolic resin
  Inter-yarn porosity (local): 0.846
  Intra-yarn porosity (local): 0.552
Optical microscopy and x-ray computed tomography (CT) data obtained and analyzed
Image from: Fahy, W.P., Chang, A., Wu, H., and Koo, J.H. “Recent Developments of Ablative Thermal Protection Systems for Atmospheric Entry”, AIAA SciTech 2021, 19–21 January, 2021.
Images from: Gasch, M. (2019) “Heatshield for Extreme Entry Environment Technology (HEEET) Thermal Protection System (TPS)” MS&T19, Portland OR.
Recession Layer
Insulation Layer
Within Tows
Carbon Fiber (white)
Phenolic Fiber (dark gray)
Matrix:
Porous Phenolic
Ricks, T.M., Bednarcyk, B.A., Fraile Izquierdo, S., Abbott, L.J., & Aboudi, J. “Multiscale and Multifidelity Modeling of a 3D Woven Composite Thermal Protection System,” in the proceedings of the American Society for Composites Thirty-Ninth Technical Conference, October 21-23, 2024, San Diego, CA.

## Slide 14: HEEET-IL Problem Setup
Weave geometry and properties utilized from previous work*
17x26x26 subvolume grid generated in TexGen and solved with HFGMC3D
Blended carbon and phenolic fiber tows modeled with a 21x21 subvolume grid and solved with HFGMC2D
Inter-tow and intra-tow porosity modeled using spherical Mori-Tanaka
Applied mechanical strain in warp-direction
Subvolume elimination method used for failure
  Max strain failure criterion (carbon fiber)
  Hashin stress-based failure criterion (phenolic fiber and matrix)
*Bednarcyk, Brett A., et al. "Effect of Damage Progression on the Thermal Conductivity of 3D Woven Composite Thermal Protection System Materials." AIAA SCITECH 2023 Forum.
*Izquierdo, Sergio Fraile, Andrew P. Santos, and Lauren J. Abbott. "Certification by Analysis of Woven TPS: Fiber-and Weave-Scale Modeling." NASA Ames EDL Summer Series. 2023.
Inter-tow Porous Matrix (Level 2)
Blended Fiber Tow (Level 2)
Intra-tow Porous Matrix (Level 3)
HEEET-IL Weave (Level 1)
Warp direction

## Slide 15: HEEET-IL Visualization with NASMAT PrePost
Red Arrow
RUC 1-direction
Green Arrow
RUC 2-direction
Blue Arrow
RUC 3-direction

## Slide 16: HEEET-IL Visualization with NASMAT PrePost
Red Arrow
RUC 1-direction
Green Arrow
RUC 2-direction
Blue Arrow
RUC 3-direction

## Slide 17: HEEET-IL Visualization with NASMAT PrePost
Red Arrow
RUC 1-direction
Green Arrow
RUC 2-direction
Blue Arrow
RUC 3-direction

## Slide 18: What happened to the Intra-tow Matrix Results?
HEEET-IL multiscale model included calculations for intra-tow porous matrix (including failure)
Entire problem took 3.7 hrs to run on a single CPU
Level 3 results not able to be efficiently output
  Methods to judiciously output results required
Inter-tow Porous Matrix (Level 2)
Blended Fiber Tow (Level 2)
Intra-tow Porous Matrix (Level 3)
HEEET-IL Weave (Level 1)
1 larger RUC (HF3D)
4720 RUCs (HF2D)
4720x172 = 811,840 unique Level 3 RUCs!
Real-time results viewing is less of a problem than outputting results to view
Circle size represents computational complexity
172 RUCs (MT)
6772 RUCs (MT)

## Slide 19: Summary and Conclusions
Developed a new open-source Python tool for visualizing multiscale model simulation results generated with NASMAT
Demonstrated workflow for two large multiscale analysis problems
Modern software visualization packages can efficiently handle large multiscale datasets
Data output limitation is a key challenge for visualizing multiscale results
  Methods under development to judiciously output relevant data
Version 1.0 specific to NASMAT, intent to generalize to allow multiscale visualization from other tools
NASMAT PrePost expected to be posted to NASA Github (open-source) in Spring 2025

## Slide 20: Acknowledgments
Software development supported by the NASA Aeronautics Research Mission Directorate’s Transformational Tools and Technologies Project
Example applications supported by the NASA Space Technology Mission Directorate’s Thermoplastics Development for Exploration Applications and Entry Systems Modeling projects
Request NASMAT via the NASA Software Catalog
- new version released Sept. 2024