## Slide 1: ISRU Overview for SPIE PW 2025
Desmond O’Connor
desmond.oconnor@nasa.gov
NASA Johnson Space Center
SPIE PW 2025

## Slide 2: ISRU
What
Definition
Scope
Why
Launch costs
Sustainability
Where
Moon/Mars
How
Resources
Technologies
Involvement

## Slide 3: What is ISRU?
In-Situ Resource Utilization
Where you are
A useful material
Making Something from said material
“Using what you have to make what you need”
Notes: By definition:
  In-Situ:
    Where you are
  Resource:
    A useful material
  Utilization:
    Making something out of said materials
Using what you have where you are to make what you need.

## Slide 4: Scope
What does NASA want to do?
NASA’s Focus:
  Short term:
    Consumables (H2/O2/CH4/Water)
    Using regolith directly (berms/shielding/roads)
  Long term:
    Refining metals
    Manufacturing
https://www.melodieyashar.com/#/lunar-landing-pad/

## Slide 5: Why pursue ISRU?
LOX
ISRU Propellant Production Plant
CO2
H2O
LCH4
Kleinhenz, J. E., & Paz, A. (2017). An ISRU propellant production system for a fully fueled Mars Ascent Vehicle. In 10th Symposium on Space Resource Utilization (p. 0423).
An Oxygen-only propellant production plant on Mars could make ~3 times its own mass in oxygen in 480 days
An LOX/LCH4 propellant production plant on Mars could make ~ 18 times its own mass in propellant in 480 days
Notes: Terrestrial propellant alone (Lox and Methane propellant mass, not including additional tankage) is
18x the mass of a Lox/LCH4 ISRU landed mass
4x the mass of a LOX ISRU landed mass
10-20 tons of propellant per ton landed on Mars

## Slide 6: ISRU Technology Impact on Earth
Image Credit: NASA
Water electrolysis can be used to produce hydrogen at a large scale
Hydrogen reduction of iron oxides is being used to make steel with no carbon emissions
Solar-carbothermal reduction and molten regolith electrolysis can be used to produce silicon with no carbon emissions
Sabatier process can convert carbon dioxide and hydrogen into methane
Carbon dioxide and water can be used to make plastics

## Slide 7: In-Situ Resource Utilization
The Moon
Oxygen – Lunar regolith is ~45% oxygen
Water Ice- Located at the poles
Metals – Iron, Aluminum, Titanium, Magnesium
Metalloids – Silicon
Regolith – Can be used as a construction material
Solar Wind Volatiles – Helium 3 can be used for nuclear fusion
Abundant solar energy
Image Credit: NASA
Mars
Oxygen – Can be extracted from CO2 atmosphere
Water in Regolith – Anywhere on the surface
Water Ice – Under the surface in some locations
Metals – Iron, Aluminum, Titanium, Magnesium
Metalloids - Silicon
Regolith – Can be used as a construction material
Notes: Analysis of Luna 24 samples showed the samples contained ~0.1% water by mass
Clementine indicated the presence of water ice at the poles based on the response of radar interactions with the surface
Lunar Prospector detected hydrogen using a neutron spectrometer and estimated the content of water ice to be 300 million metric tons
Chandrayaan-1 puts the estimate at 600 million metric tons
In 2008, an analysis of Apollo samples indicated the presence of water, with some debate over whether is was terrestrial contamination
LCROSS provided definitive proof of water in cabeus crater

## Slide 8: Water on the Moon
1994 : Clementine indicated the presence of water ice at the poles based on the response of radar interactions with the surface
1998: Lunar Prospector detected hydrogen using a neutron spectrometer and estimated the content of water ice to be 300 million metric tons
2008: Chandrayaan-1 puts the estimate at 600 million metric tons (240,000 Olympic swimming pools)
2009: LRO/LCROSS provided definitive proof of water ice in Cabeus crater
Image Credit: NASA/GSFC
Image Credit: UCLA/NASA/JPL/GSFC
Notes: Analysis of Luna 24 samples showed the samples contained ~0.1% water by mass
Clementine indicated the presence of water ice at the poles based on the response of radar interactions with the surface
Lunar Prospector detected hydrogen using a neutron spectrometer and estimated the content of water ice to be 300 million metric tons
Chandrayaan-1 puts the estimate at 600 million metric tons
In 2008, an analysis of Apollo samples indicated the presence of water, with some debate over whether is was terrestrial contamination
LCROSS provided definitive proof of water in cabeus crater

## Slide 9: LRO/LCROSS
Lunar Reconnaissance Orbiter (LRO)
  Launched June 18, 2009
  Still active
Lunar Crater Observation and Sensing Satellite (LCROSS)
  Launched June 18, 2009
  Centaur crashed into the surface of Cabeus crater at 11:31 UT October 9th, 2009
  LCROSS crashed into the surface 4 minutes later after analyzing the impact plume
  LRO analyzed plume from orbit
Colaprete, A., Schultz, P., Heldmann, J., Wooden, D., Shirley, M., Ennico, K., ... & Sollitt, L. (2010). Detection of water in the LCROSS ejecta plume. science, 330(6003), 463-468.

## Slide 10: Water on Mars
Image Credit: NASA/JPL-Caltech
Notes: Overlay of water equivalent hydrogen abundances and a shade relief map derived from MOLA topography. Mass percents of water were determined from epithermal neutron counting rates using the Neutron Spectrometer aboard Mars Odyssey between February 2002 and April 2003.
Image Source: https://mars.jpl.nasa.gov/odyssey/gallery/latestimages/20030724a.html

## Slide 11: Water on Mars
A cross-section of underground ice is exposed at the steep slope that appears bright blue in this enhanced-color view from the HiRISE camera on NASA's Mars Reconnaissance Orbiter. The scene is about 550 yards wide. The scarp drops about 140 yards from the level ground in the upper third of the image.
Image Credit: NASA/JPL-Caltech/UA/USGS

## Slide 12: Water on the Moon
2H20
2H2 + O2
Water electrolysis can be used to convert water into hydrogen and oxygen using an electric current from a solar panel or other source of power
Oxygen gas can be used for breathing
Oxygen and hydrogen gas can be used to run a fuel cell
Liquid hydrogen and liquid oxygen can be used as rocket propellant
Saturn V , Space Shuttle , and SLS all use LOX/LH2 propellant
Image Credit: NASA

## Slide 13: Lunar Water Utilization
Excavation
10 Tonnes (10,000kg) of oxygen per year is considered a full-scale production rate
Extraction
Water will need to be extracted from the regolith for processing
Heating the regolith will cause water to sublimate, so it must be done in a controlled fashion
Purification
Volatile contaminants (CO, H2, H2S, NH3, SO2, CH3OH, CH4, CO2) and particulate must be removed and conductivity reduced for PEM electrolysis
Electrolysis
Different system can be used for electrolysis including PEM, SOE, or Alkaline stacks.
Liquefaction/Storage
Propellants need to be liquefied for storage and use.
Assuming 5% water ice, with an excavation depth of 5 cm, it would take ~67% of the area of a football pitch to produce 15 Tonnes of water
5% and 5cm deep
Conductivity | Resistivity
0.056 | 18
0.063 | 16
0.071 | 14
0.083 | 12
0.100 | 10
0.133 | 7.5
0.200 | 5
0.500 | 2
1.000 | 1
1.333 | 0.75
2.000 | 0.5
4.000 | 0.25
10.000 | 0.1
20.000 | 0.05
40.000 | 0.25
100.000 | 0.01
200.000 | 0.005
500.000 | 0.002
1000.000 | 0.001
2000.000 | 0.0005
5000.000 | 0.0002
10000.000 | 0.0001
Cathode
Anode
Solid Oxide
H2O
O2
H2
-
+
HYDROGEN LIQUEFACTION |  | 
Oxygen Mass | 10 | tonnes
LOX/Fuel Ratio | 6 | 
H2 Mass Required | 1.67 | tonnes
Mass of 20W/20K crycooler | 106.3 | kg
Fuel Liquefaction Thermal Lift Required | 429 | W
Number of Cryocoolers Required | 22 | 
Mass of Cryocoolers & Radiators | 2.34 | tonnes
Return on Landed Mass in 1 year | 0.71 | 
RASSOR
LADI
Notes: Excavation
10 Tonnes (10,000kg) of oxygen per year is considered a full-scale production rate until more information becomes available on lunar landers
10 Tonnes of oxygen per year requires 15 Tonnes of water
Assuming 5% water ice, with a density of 1.25 g/cc and an excavation depth of 5 cm, it would take ~67% of the area of a football pitch to produce 15 Tonnes of water
Extraction
Water will need to be extracted from the regolith for processing
Heating the regolith will cause water to sublimate, so it must be done in a controlled fashion
This is an auger-dryer system developed at JSC for continuous water extraction from regolith
The auger geometry uses regolith at the inlet and outlet to create a plug, preventing water vapor from escaping during processing
Purification
Tap water has conductivity of 100-200 microsiemens/cm^2, PEM electrolyzers require high grade DI water (<0.1 cond)
Lunar water will also include volatiles and other contaminants (namely mercury and ammonia) that must be removed to prevent damage to electrolyzer stacks
  Freeze distillation can be used to separate water from most volatiles
Electrolysis
Water must be split into H2/O2 for use a propellant or reactant
Most used technologies are Proton Exchange Membrane (PEM) or Solid Oxide Electrode (SOE)
Both have flight heritage
  The O2 generator on ISS is PEM
  MOXIE on the Perseverance rover
SOE operates at high temperatures, does not require deionized feed water, provides dry low pressure O2
PEM requires lower temperatures, needs very pure feed water, can provide high pressure O2
Liquefaction
One of the biggest challenges with using water to make propellant is hydrogen liquefaction. Using the current state-of-the-art liquefaction technology, it would take 2.34 Tonnes worth of liquefaction hardware to produce 1.67 Tonnes worth of liquid hydrogen per year.

## Slide 14: Oxygen from Regolith – Chemical Composition
Loftus, D. J., Tranfield, E. M., Rask, J. C., & McCrosssin, C. (2008). The chemical reactivity of lunar dust relevant to human exploration of the Moon.
Examples of Lunar Regolith Chemical Composition
The darker areas of the Moon are called Mare
The lighter areas of the Moon are called Highlands
Ruess, F., Schaenzlin, J., & Benaroya, H. (2006). Structural design of a lunar habitat. Journal of Aerospace Engineering, 19(3), 133-157.
Image Credit: NASA

## Slide 15: Oxygen from Regolith – Hydrogen Reduction
Fe0 + H2
Fe + H2O
Image Credit: ISRO/NASA/JPL-Caltech/Brown Univ./USGS
Notes: Left: Image from NASA’s Moon Mineralogy Mapper, an instrument on the Indian Space Research Organization's Chandrayaan-1 mission.
Blue shows the signature of water, green shows the brightness of the surface as measured by reflected infrared radiation from the sun and red shows an iron-bearing mineral called pyroxene.
Right: Video of reduced tephra (Soil found on Mauna Kea) being removed from ROxygen reactor during 2008 field demonstration

## Slide 16: Oxygen from Regolith : Solar-Carbothermal Reduction
2H2O
Solar Concentrator
Physical Sciences Inc.
Carbothermal Reactor
Orbitec (Now Sierra Space)
Heat
Excavator
Canadian Space Agency
Tephra
Water Electrolysis
Johnson Space Center
O2
LOX
H2O
Liquefaction
Johnson Space Center
Propulsion
Johnson Space Center
Heat
Plume
Sintered Pad
Physical Sciences Inc.
NORCAT
Si0 + C H4
Si + CO+ 2H2
CO + 4H2
CH4+H2O
2H2O
2H2 + O2
Notes: Left: ROxygen electrolyzer and gaseous oxygen storage in the foreground. Solar Concentrator in the background
Upper Right: Melted tephra produced with solar concentrator
Lower Right: Sintered tephra using solar concentrator

## Slide 17: Carbothermal Reduction Demonstration (CaRD) Prototype
Prototype Reactor tested in Thermal-Vacuum
Integrated Test with Solar Concentrator

## Slide 18: Molten Regolith Electrolysis (MRE)
MRE uses high voltage current to reduce Fe, Si, and Al
Generates oxygen as well as pure metals
No chemicals required, just power
MRE Reactor Cross Section

## Slide 19: Moon to Mars
Modified Lunar Carbothermal Concept
O2 Liquefaction & Maintenance
O2 Dryer
Inlet Hopper
Soil Excavation
Water Electrolysis
Condenser
Outlet Hopper
Spent Soil Disposal
Water Cleanup
Carbothermal Reactor
H2O
CH4
H2
H2O
O2
CH4, CO, H2, CO2
CH4
Sabatier Reactor
Carbon
Water from Icy Regolith
CH4 Liquefaction & Maintenance
CH4 Dryer
CH4
Methane Pyrolysis
Common to Mars ISRU
If we bring carbon to the Moon
1) We can test all of the technologies required to produce propellant on Mars
2) We can utilize hydrogen from water by feeding water into a system that is already in place to extract oxygen from regolith
3) It will much easier to liquefy and store methane than hydrogen.
Common to Mars ISRU and Life Support Systems
HYDROGEN LIQUEFACTION |  | 
Oxygen Mass | 10 | tonnes
LOX/Fuel Ratio | 6 | 
H2 Mass Required | 1.67 | tonnes
Carbon Mass Required (tonnes) | 0 | tonnes
Mass of 20W/20K crycooler | 106.3 | kg
Fuel Liquefaction Thermal Lift Required | 429 | W
Number of Cryocoolers Required | 22 | 
Mass of Cryocoolers & Radiators | 2.34 | tonnes
Return on Landed Mass in 1 year | 0.71 | 
METHANE LIQUEFACTION |  | 
Oxygen Mass | 10 | tonnes
LOX/Fuel Ratio | 3.6 | 
CH4 Mass Required | 2.78 | tonnes
Carbon Mass Required (tonnes) | 2.08 | tonnes
Mass of Cryotel GT | 3.1 | kg
Fuel Liquefaction Thermal Lift Required | 169 | W
Number of Cryocoolers Required | 8 | 
Mass of Cryocoolers & Radiators | 0.065 | tonnes
Return on Landed Mass in 1 year | 1.30 | 
Notes: This image was produced for the Evolvable Mars Campaign and has already cleared the DAA process

## Slide 20: Instrumentation Challenges in ISRU
Common Instrumentation and Analysis
  Measurement of regolith composition before and after processing
    Monitoring input/output composition to evaluate system efficiency and efficacy
  Water quality monitoring
    Conductivity/resistivity
    Contamination
      Particulate
      Specific elements (Hg, NH3, Acids)
  Water Flow and Level
    Water separation
  Moisture Content Monitoring in Product Streams
    O2/H2/CH4
Instruments that can survive hostile environments
  High-Radiation
  Single Event Upsets
  Vacuum
  Large temperature swings from processes and environments
  Dust tolerance within the process and in the environment
  O2 Rich, corrosive, high current processes
Instrumentation that can maintain calibration or be recalibrated remotely

## Slide 21: How to get involved
Small Business Innovation Research / Small Business Technology Transfer (SBIR/STTR)
Provides funding for ideation and prototype development
Limited matching funds available
Phase I submissions are currently open and will close “early March 2025”!
https://www.nasa.gov/sbir_sttr/

## Slide 22: NASA Technology Taxonomy
Identifies and organizes technology gaps relevant to NASA
Also contains information on NASA funded projects in each technology
Prioritized shortfalls can be found at https://techport.nasa.gov/strategy
https://techport.nasa.gov/taxonomy

## Slide 23
Thanks for listening! Questions? Comments?
desmond.oconnor@nasa.gov
SBIR/STTR:
https://www.nasa.gov/sbir_sttr/
Tech Taxonomy:
https://techport.nasa.gov/taxonomy
Internships:
https://www.nasa.gov/learning-resources/internship-programs/