## Slide 1: Informatics and Decision Support Technology Roadmap IEEE SMC-IT/SCC 2025
NASA JSC/Geraldo Cisneros
This document has been reviewed for Proprietary, CUI, and Export Control (ITAR/EAR) and has been determined to be non-sensitive. It has been approved for public release via the NASA Scientific and Technical Information (STI) Process DAA #20250001045

## Slide 2: Informatics & Decision Support Roadmap Purpose & Scope
Purpose
Identify shortfalls/gaps, shortfall/gap closure strategies, and candidate investments to mature Informatics and Decision Support technologies in support of M2M Program risk mitigation activities, enable and enhance crew insight to system performance, decision making, and computer-human interaction.
In this first publication, scope of the Informatics and Decision Support Roadmap is limited to Deep Space Crew Displays and Audio Systems. Future publications will expand scope to other capabilities.
Scope
Deep Space Crew Displays
  Develop high availability radiation-tolerant display systems capable of withstanding the harsh radiation environment of deep space and meeting the needs of various systems with differing use cases and requirements.
  Implement a radiation-tolerant graphics processing architectures that feature radiation tolerant by design components and single event fault interrupt mitigation software and middleware
  Evaluate and characterize the display and optics trade space to better understand and catalog their capabilities and benefits as they pertain to human spaceflight
  NASA-STD-3001 Vol 2, Human Factors, Habitability, and Environmental Health, specifies visual display parameters for spacecraft displays: NASA-STD-3001 Vol 2
  Avionics Radiation Hardness Assurance (RHA) Guidelines, specifies current state of NASA’s RHA best practices: Avionics Radiation Hardness Assurance (RHA) Guidelines
Deep Space Audio Systems
  Develop robust audio processing hardware capable of withstanding high-radiation environments and ensuring consistent and reliable audio performance in space.
  Implement advanced voice control systems and Speech-To-Text (STT) technology for seamless communication between crew members and ground control, enhancing operational efficiency and preserving communication records.
  Design and deploy intuitive audio interface devices tailored for space environments, providing clear and effective communication tools for crew members during missions.
2

## Slide 3
Priorities for Informatics & Decision Support
  Develop, enable, and integrate advanced avionics & informatics technologies for deep space exploration
    BENEFIT: Enhances the safety, efficiency, and success rate of deep space missions, ensuring precise information exchange and robust system operations in the challenging environment of deep space.
  Identify and integrate radiation mitigation technologies and strategies for informatics systems
    BENEFIT: Protects critical informatics systems from harmful space radiation, thereby ensuring the longevity and reliability of mission-critical data and communication systems, ultimately safeguarding mission integrity and crew health and safety.
  Identify and enable informatics technologies that promote crew autonomy and self reliance
    BENEFIT: Promotes reduced dependence on ground control, empowering astronauts to make informed decisions, manage unforeseen issues independently, and maintain mission continuity in real-time, which is vital for long-duration deep space missions.
  Develop and integrate reliable spacesuit audio systems for crew safety and mission success
    BENEFIT: Ensures reliable contact between the crew and mission control, facilitating timely updates, emergency responses, and seamless coordination, which are critical for maintaining crew safety and achieving mission objectives in deep space.
  Determine more cost-effective verification methods for speech-intelligibility
    BENEFIT: Ensures clear and accurate communication among crew members and between crew and mission control, enhancing operational efficiency, reducing misunderstandings, and preventing costly errors, thereby contributing to the overall success and safety of space missions.

## Slide 4: Informatics & Decision Support Key Observations
Deep Space Crew Displays
No readily available radiation-tolerant solutions exist that meet Artemis performance and reliability requirements for safety critical crew
  High-Performance Space Computer (HPSC) is a promising radiation-tolerant solution, but is itself a technology development activity with flight-ready delivery in 18+ months
  HPSC may not be a one-size-fits-all solution, each Program/Project will need to assess specific application and potentially determine alternatives to HPSC
Targeting Display panel gap closure in 2-3 years
  NASA screen/pixel radiation characterization and body of knowledge report completed in FY24.
  Anticipate industry collaboration to prototype full display with multi-layer software mitigation
Feasibility for the development of an EVA Heads-Up Display (HUD) has increased
  An RFI conducted by the Joint AR project collected several feasible proposed solutions capable of developing a suit integrated heads-up display within a reasonable timeframe. This SBIR Phase 1 will further increase TRL for suit integrated heads-up displays
  Implementation of optics solution with a helmet bubble form factor and radiation performance and characterization of projector systems are forward work
Deep Space Audio Systems
Pursue Industry engagement /collaboration for implementing a radiation-tolerant audio system compatible with spacecraft network interfaces
For EVA audio, alternatives to current EVA communication design (”snoopy cap”) continue to have issues with echo
  Echo cancellation technology development needs attention and funding
Lack of Speech recognition testing standards makes future requirements development difficult
  Modern systems depend on Earth-based cloud computing, not feasible for spaceflight

## Slide 5: Informatics and Decision Support Roadmap – STMD Shortfalls and ESDMD Gaps
https://techport.nasa.gov/framework
Envisioned Futures Charts - Advanced Informatics - Human Interfaces
https://www.nasa.gov/moontomarsarchitecture/
Moon2Mars Architecture Definition Document
https://www.nasa.gov/spacetechpriorities/
Civil Space Shortfalls
STMD Shortfall ID | Shortfall Title
Avionics 1541 | Intuitive and Efficient Human Robot Interaction for Safe Teaming and Remote Supervisory Control
Avionics 1550 | Crew Audio/Visual Interfaces for Long Duration Missions Beyond LEO
Avionics 1551 | Distributed Avionics to Enable Improved Performance and SWaP Efficiency
Avionics 1552 | Extreme Environment Avionics
Avionics 1553 | Foundational Technologies for Future Avionics Devices and Systems
Avionics 1554 | High Performance Onboard Computing to Enable Increasingly Complex Operations
Avionics 1555 | Next Generation Avionics Architectures
ESDMD Architecture- driven Gap ID | Gap Title
0201 | Extreme Environment Computing
0202 | High Performance Onboard Computing
1004 | Trustworthy Autonomy for Planning and Decision-making

## Slide 6: Mid to High Level TRL NASA Informatics & Decision Support Investments
1. DEEP SPACE CREW DISPLAYS TRL FY POTENTIAL INFUSION TARGET
  High Performance Space Computing (HPSC) 6 2022-25 GW, LTV, PR, HLS, Habitats
  Joint AR EVA Display - STAR 4 2020-23 xEVAS, LTV, HLS, Habitats
    2024 – JETT5 Testing Completed
  Radiation Tolerant & Reliable Electronic Displays 4 2021-23 GW, xEVAS, LTV, PR, HLS, Habitats
    2022: Total Ionizing Dose Radiation Testing Completed
    2023: Single Event Effects Radiation Testing Completed
  Radiation Tolerant Displays 6 2024-25 GW, xEVAS, LTV, PR, HLS, Habitats
    2024: Display Prototype Development
2. DEEP SPACE AUDIO SYSTEMS
  Acoustic Echo Cancellation 7 2022-25 xEVAS, PR
  Audio Systems 7 2024 GW, xEVAS
  Bone Conduction Evaluation 6 2022-23 xEVAS, PR
  ASO, IRIS 4 2020-22 xEVAS
  Pratt Bone Conduction Headsets 4 2024-25 xEVAS, PR
6

## Slide 7: DEEP SPACE CREW DISPLAYS
STAR
HPSC
Radiation Tolerant Displays System
Display/Optics Evaluation and Characterization
POC: JSC EV/Geraldo Cisneros
Revised: Fall 2024
Deliverables & Milestones
RTD architecture configs defined for various system use cases
System prototype dev complete with flight like components and vendor supplied display
Radiation Tolerant System Reference Design
Joint AR participation in JETT5 Analog Test
STAR Software Releases
    STAR Engine Released (Dec ‘23 – US Only Release)
  6. HPSC Dev Kits Available (Q2 ‘25)
Decision Points
  Assess infusion potential to pursue maturation to TRL 6
  Infuse into Programs/Projects (c-f below)
  Infuse into xEVAS
  Infuse into PR
  Infuse into LTVS
  Infuse into GW
Candidates Under Evaluation
Rad-Mat - Radiation hardened polymer material for displays
a
#
Rad Tolerant & Reliable Electronic Displays
KPPs: Display Performance (see page 18) FOM: Radiation Tolerance (see page 19)
1
6
A
Joint AR EVA Display
C
xEVAS Impl
c
CLPS 19D Firefly (2025):
Radiation Tolerant and Reliable Electronic Displays – Radiation & Performance Characterization of Pixel Displays
Radiation-Tolerant Displays (RTD) –
  Industry development of rad tolerant display panel
  Industry development of rad tolerant smart head system
  Total Ionizing Dose
  Single Event Effects
Robust Multicore Middleware
High Performance Space Computer (HPSC) – TRL 6
Joint AR EVA Display
Space Technology Application Renderer (STAR) Graphics Engine
2024 SBIR Phase I Selections
  Exploration Extravehicular Mobility Unit Spacesuit Heads-Up Display – SBIR Phase I
  Multifocal Augmented Reality Visual Informatics System – SBIR Phase I
  Holographic Enabled Display for xEVA – SBIR Phase I
Industry Development
5
4
4
6
2
4
5
3
Project Impl
b
FY24 SBIR Phase I
xEVAS Impl
c
H
RMM SBIR
RMM SBIR Phase III
6
Risk-Bounded, Goal-Driven AI
xEVAS Impl
c
LTV Impl
e
PR Impl
d
(Shortfalls: 1541, 1550, 1551, 1552, 1553, 1554, 1555)
(ESDMD Tech. Gaps: 0201, 0202)
SBIR Phase II
SBIR Phase III
a

## Slide 8: NASA Funded Deep Space Crew Displays Investments
Task Bar Name | Description & Status | Start | Finish
High Performance Space Computing (HPSC) | The objective of HPSC is to develop a next-generation flight computing system that addresses computational performance, energy management and fault tolerance needs of NASA missions through 2040 and beyond. | 2022 | 2025
Joint AR EVA Display | The Joint AR project worked to develop a space suit augmented reality display and control system reference design to promote crew autonomy and help meet the demands of future EVA missions in deep space. This project also produced a custom, NASA built, graphics engine known as STAR. | 2019 | 2023
Spacesuit Technology Application Renderer (STAR) | STAR is a low-power, high-performance, zero-dependency graphics engine developed by NASA for next-generation human exploration missions. STAR is light weight and feature's fault mitigation capabilities. STAR has been open sourced to US citizens. | 2021 | 2023
Rad Tolerant & Reliable Electronic Displays (2REDPANDAS) | The Radiation Tolerant and Reliable Electronic Displays project was an early career initiative which took foundational steps towards the development of displays in deep space. This project characterized the performance and metrology of several pixel panel display technologies before and after their exposure to radiation. Complete, radiation characterization and test results collected and available for knowledge transfer | 2021 | 2023
Radiation Tolerant Display System (RTD) | Radiation Tolerant Displays aims to partner with industry to develop a reference design for a display and computer system that can withstand and mitigate the effects of radiation in deep space. The project seeks to develop a system that is scalable to meet the needs of various lunar assets and their respective use case. Fully funded, working toward architecture down selection, display system prototyping, and vendor selection processes. | 2024 | 2025
8

## Slide 9: NASA Funded Deep Space Crew Displays Investments (Cont’d)
Task Bar Name | Description & Status | Start | Finish
Risk Mitigation Middleware (RMM) | The significance of this Risk Mitigation Middleware (RMM) innovation is that it is the only feasible technology that provides a path to enabling these types of missions by allowing high-performance COTS processors to operate with a high degree of fault tolerance without the need for rad-hard electronics, and thus simultaneously meets advanced mission criticality and performance requirements | 2021 | 2023
Exploration Extravehicular Mobility Unit Spacesuit Heads-Up Display | To address NASA’s need for an augmented reality (AR) display system for EVAs, This SBIR awardee proposes to develop a new Exploration Extravehicular Mobility Unit (xEMU) Spacesuit Heads-up Display (xHUD) based on innovative integration of laser projectors and wave guide pupil expander combiner (WPEC) optics. 2024 SBIR Phase I Awardee. | 2024 | 2025
Multifocal Augmented Reality Visual Informatics System | This proposed technology, the Multifocal Augmented Reality Visual Informatics System (MARVIS), is a spacesuit-integrated, head-decoupled, solid-state, augmented reality (AR) system designed to provide astronauts with an immersive, informative visual interface that significantly enhances decision-making capabilities and situational awareness (SA) during EVAs. 2024 SBIR Phase I Awardee | 2024 | 2025
Holographic Enabled Display for xEVA | This proposed technology aims to develop a Heads-In Display coupled to information systems and potentially Augmented Reality processors and sensors. The proposed solution can bridge the technology gap that exists with state-of-the-art AR displays that can’t simultaneously provide the metrics of eye relief, field of view, brightness and resolution needed in a spacesuit helmet display. 2024 SBIR Phase I Awardee | 2024 | 2025
Risk-Bounded, Goal-Driven AI for Human Planetary Exploration | When planning an EVA, flight operations identifies goals and decides traverse paths and timelines given the constraints and risks of a mission. This proposal will mature risk-bounded, goal-driven AI methods for generating mixed traverse and activity planning for crewed Lunar and Martian exploration. | 2025 | 2025
9

## Slide 10: Proposed Deep Space Crew Displays Investments
Task Bar Name | Description & Status | Start | Finish
Display/Optics evaluation and characterization | Create and expand body of knowledge and subject matter expertise pertaining to display mediums, form factors, and metrology and determine the best techniques for verifying and validating displays for human spaceflight. | 2025 | 2028
10

## Slide 11: Deep Space Audio Systems (Shortfalls 1541 and 1550)
Bone Conduction Eval
KPP: Speech Intelligibility (see page 20)
KPP: Speech Recognition Accuracy (see page 20)
FOM: Radiation Tolerance (see page 21)
STT Perf & Test Standards
Local (non-Cloud) STT models
Speech Recognition - Lunar Demo Ops
Speech Recognition, NLP, Voice Assistant for Mars
Voice for Autonomous Operations
Core Spacecraft Audio System
Acoustic Echo Cancellation
POC: JSC EV/Geraldo Cisneros
Revised: Fall 2024
ASO, IRIS
BCE
xEVAS Impl
a
PR Impl
b
1
Deliverables & Milestones
Callisto Payload flown on Artemis I, demonstrated voice control
Completed thermal vacuum testing
JETT 5 Analog Test
  Usefulness of real-time transcripts spawned EMSS product called Talky-Bot that is now used for ISS operations and will be part of the suite of tools provided by the EMSS team for Artemis
Decision Points
  Infuse into xEVAS
  Infuse into PR
Candidates Under Evaluation:
#
1
5
4
A. Acoustic Echo Cancellation
  CHP SCLT Acoustic Monitoring and Control Roadmap
  Voice communication in a space suit requires ambient noise suppression and echo cancellation to achieve the required speech intelligibility level. This is particularly challenging if the mic and speaker are mounted in the helmet rather than integrated into a “comm cap.”
B. Bone Conduction Evaluation
  See EHP PLSS Avionics and Power Roadmap
C. Speech recognition and speech-to-text
  IRIS began the effort to make a custom, built-in-house speech recognition software.
D. Pratt Institute Bone Conduction (BC) Headsets
2
xEVAS Impl
a
a
Pratt BC
D
EMSS Talky-Bot
Real-Time Transcripts
3
xEVAS Impl
a
A

## Slide 12: NASA Funded Deep Space Audio Systems Investments
Task Bar Name | Description & Status | Start | Finish
Acoustic Echo Cancellation | Development and evaluation of technology that identifies and eliminates echo in audio communication systems. This is crucial for ensuring clear and uninterrupted crew voice transmission in where signals may be reflected and captured again leading to disruptive feedback. | 2022 | 2025
Bone Conduction Evaluation (BCE) | Investigation of bone conduction audio transducers to eliminate acoustic coupling of inbound/outbound audio in space suits. Includes custom design of bone conduction headsets optimized for long term wear comfort, fit and adjustability as well as optimization of transducer selection, placement and amplifier design. | 2022 | 2023
Autonomous Systems and Operations(ASO), Intelligent Response and Interaction System (IRIS) | IRIS began the effort to create a custom speech recognition software by building upon existing speech recognition software. IRIS prototypes had the capability to understand wake words and translate speech to text when in an environment with very little noise pollution. | 2020 | 2023
Pratt Institute Bone Conduction Headset | Pratt institute is investigating the potential of bone conduction earphones equipped with moisture-proof transducers. This innovative approach aims to resolve the audio coupling issues encountered in space suit communications. | 2024 | 2024
EMSS Talky-Bot | The real-time transcripts, used during JETT 5 Analog testing, were so useful that they spawned a new EMSS product called Talky-Bot that is now used for ISS operations and will be part of the suite of tools provided by the EMSS team for Artemis. | 2024 | 2025
12

## Slide 13: Proposed Deep Space Audio Systems Investments
Task Bar Name | Description & Status | Start | Finish
STT Performance & Test Standards | Establishing benchmarks to assess the accuracy, speed, adaptability, and user experience of speech-to-text engines, with a specific focus on comparing cloud-based and local STT engines for their integration and compatibility across various platforms. | 2025 | 2026
Local (non-cloud) STT models | Focuses on creating STT models that operate locally, emphasizing the development of an efficient, accurate, and adaptable system capable of processing STT without cloud connectivity. | 2025 | 2028
Bone Conduction Eval (Cont’d) | Investigation of bone conduction audio transducers to eliminate acoustic coupling of inbound/outbound audio in space suits. Includes custom design of bone conduction headsets optimized for long term wear comfort, fit, and adjustability; as well as optimization of transducer selection, placement, and amplifier design. | 2025 | 2026
Speech Recognition for Lunar Demo Ops | Evaluation of control of non-critical systems using voice control. Also includes use of speech-to-text for communication via long latency communication channels. | 2026 | 2029
Speech Recognition, NLP, Voice Assistant for Mars | Expanded application of system control via voice and continued assessment of speech-to-text application for communication over long haul comm links. | 2030 | 2036+
13

## Slide 14: Deep Space Crew Displays - KPPs Display Performance
NASA-STD-3001, Volume 2, RevisionD, Human Factors, Habitability, and Environmental Health, specifies visual display parameters for spacecraft displays (right).
Display performance requirements vary by how the display is used. Table 10.4-2 represents performance goals for display technologies that may be considered for infusion.
NASA display standards do not encompass unique display form factors such as augmented reality, virtual reality, and projector-based displays. NASA STD-3001, and M2M GUI Standards (50040) are two relevant documents for displays. There are international display standards that are widely accepted by all projector, TV, and display companies which may be more applicable for unique form factors.
Metric | Minimum | Maximum | Context | Notes
Peak white luminance | >100 cd/m2 | -- | Emissive displays | 400 cd/m2 or higher preferred
Ambient contrast ratio | 100:1 | -- |  | 1000:1 or higher preferred
Color gamut area | 0.17 | -- | Color displays | Fraction of CIE 1976 u’v’ chromaticity space
Viewing angle | -/+45 deg | as defined by task analysis |  | Four-point viewing angle (left, right, up, down), contrast and color gamut criteria met
Spatial resolution | 32 pixels/deg | -- | Image and video displays | 64 pixels/deg or higher preferred
Frame rate | 60 Hz | -- | Video displays | 60Hz is an absolute minimum to avoid flicker, but 90Hz should be the minimum for any display used for active control
Moving edge blur | -- | 15 ms |  | Using metric GET (preferable) or BET; use average of five equal lightness levels, including white and black
Number of colors | 224 (1,627,716) | -- | Image and video displays | 
 | 212 (4,096) | -- | Text and graphics displays | 
Number of gray levels | 28 (256) | -- | B/W image and video displays | 
Except where noted, metrics are as defined as in International Committee on Display Metrology (ICDM), Display Measurement Standard (DMS 1.0), or Video Electronics Standards Association (VESA) Flat Panel Display Measurements (FPDM 2.0). Further details on metrics may be found in chapter 10, Crew Interfaces, of the HIDH. |  |  |  | 
Table 10.4-2 Visual Display Parameters
From NASA-STD-3001 Vol 2 Rev D

## Slide 15: Deep Space Crew Displays - FOM Radiation Tolerance
Radiation tolerance is the driving FOM for this gap, with an overall goal to maximize display reliability
  Displays are composed of the pixel or projector technologies, driver circuitry, rendering pipeline, and computing/networking controllers
  Reliability requirements vary by use case, function, and the overall spacecraft displays and controls architecture. Radiation tolerance requirements vary by mission environment and duration.
  This gap targets displays used by crew to perform safety-critical tasks with short time-to-effect hazards in the Lunar vicinity or Lunar surface
RT Design Goal 1: Destructive Single Event Effects (SEEs) Immunity
  Up to Linear Energy Transfer (LET) of 60 MeV-cm2/mg
  SEE characterization of performance, failure modes
RT Design Goal 2: Non-destructive SEE Immunity
  Minimize probability of down time
  Minimize duration of down time
RT Design Goal 3: Total Ionizing Dose (TID) Tolerance
  100Krads(Si), TNID and ELDRs considered
  TID characterization of performance, failure modes
Notional Lunar Mission Description Displays are operated only during crewed periods | Example Spacecraft
30 days in Lunar orbit Crewed for full mission | Orion
15 years in Lunar orbit Crewed for 30 days annually | Gateway
10 years on Lunar surface Crewed for 20 days annually | Lunar Rover
10 years in Lunar orbit Crewed for 20 days annually, transported to/from Lunar Surface | Space Suit
3 months in Lunar orbit Crewed for 20 days on Lunar surface | Lunar Lander
Reference: SLS-SPEC-159
Cross-Program Design Specification for Natural Environments (DSNE)

## Slide 16: Deep Space Audio Systems - KPP
Speech Intelligibility KPP
  Speech intelligibility refers to the ability of a person to correctly identify speech in accordance with a standardized testing method
  NASA-STD-3001 Vol 2 Human Factors, Habitability, and Environmental Health specifies speech intelligibility requirements for audio systems:
  10.5.3.7 Speech Intelligibility: For critical communications, the system shall ensure 90% English word recognition, using ANSI/ASA S3.2-2009, Method for Measuring the Intelligibility of Speech over Communication Systems.
Speech Recognition KPP
  Speech recognition accuracy refers to the performance of a hardware and software system in recognizing human spoken words. In Human Spaceflight this may be used for a variety of commanding or speech-to-text applications such as voice transcription when real-time voice is impractical.
  Speech recognition solutions with a performance minimum of 90% accuracy may be considered for infusion in some spaceflight applications.
  Significantly higher accuracy, >99%, would be required for speech recognition to be considered for critical commanding.
  Notes
  There are no industry standard performance metrics or test methods for speech recognition systems. Word error rate may be used to assess speech to text performance but is not suitable for systems that directly execute commands from speech.
  Spacecraft speech recognition engines cannot rely on Earth-based servers due to communication delays. This necessitates a novel “offline” speech recognition architecture that deviates from modern commercial implementations.
  KPP: The above NASA-STD-3001 Speech Intelligibility requirement is an appropriate target, although specific use cases and operational design may ultimately determine a higher or lower accuracy requirement

## Slide 17: Deep Space Audio Systems - FOM Radiation Tolerance
Radiation tolerance is the driving FOM for this gap, with an overall goal to maximize audio system reliability
  Voice communication and annunciation of caution and warning via spacecraft Audio systems are critical spacecraft functions
  Radiation tolerance requirements vary by mission environment and duration
RT Design Goal 1: Destructive Single Event Effects (SEEs) Immunity
  Up to Linear Energy Transfer (LET) of 60 MeV-cm2/mg
  SEE characterization of performance, failure modes
RT Design Goal 2: Non-destructive SEE Immunity
  Minimize probability of down time
  Minimize duration of down time
RT Design Goal 3: Total Ionizing Dose (TID) Tolerance
  100Krads(Si), TNID and ELDRs considered
  TID characterization of performance, failure modes
Notional Lunar Mission Description Displays are operated only during crewed periods | Example Spacecraft
30 days in Lunar orbit Crewed for full mission | Orion
15 years in Lunar orbit Crewed for 30 days annually | Gateway
10 years on Lunar surface Crewed for 20 days annually | Lunar Rover
10 years in Lunar orbit Crewed for 20 days annually on Lunar Surface | Space Suit
3 months in Lunar orbit Crewed for 20 days on Lunar surface | Lunar Lander
Reference: SLS-SPEC-159
Cross-Program Design Specification for Natural Environments (DSNE)

## Slide 18: BACK-UP

## Slide 19: Tips for Reading Roadmaps
FY20 | FY21 | FY22 | FY23
Activity Name
Proposed Activity
Investment Name
White background indicate activities that are under evaluation but are not yet confirmed or fully funded.
Each box represents an activity or set of activities and the length of the box denotes the duration of the activity.
Color codes and icon keys are located in the bottom left corner of each slide.
  The color of each box represents the activity is planned/funded and the platform where the activity takes place (not the platform where the technology will be enabled). In this example the activity takes place on the ground although it may be the development of hardware for flight.
Boxes that end in an arrow indicate activities without a defined end date or where the hardware will go into regular operation after a demo.
1
2
8
4
9
ABC
See XYZ Roadmap for more information
Play button icons show “touchpoints” between roadmaps.
5
A
CLPS lander icon indicates manifested H/W related to activity.
The shape of each box represents the
source of funding. NASA ESDMD, NASA
STMD, or Industry. See legend below for
shapes.
3
Activity Name
6
Objectives (FOMs/KPPs):
Performance measures that define the required capability
Capability objectives, FOMs, or KPPs are located in the bottom right corner.
7
Lunar orbit
Ground
Lunar surface
Notes
ISS / LEO
Decision point
Deliverable/Milestone
Funded
Unfunded
Artemis missions
STMD
ESDMD
Industry
Risk
Touchpoint
#
TRL
Act
Act
19
Notes: 19

## Slide 20: Life Cycle of Technology Integration
20
Review capability/technology challenges
Identify activities to mitigate risks and close shortfalls
Periodically assess project/activity status
Decide on Infusion
Implement in Flight Program and/or Flight Project
Initiate Technology transfer to sponsor commercialization or spinoff
D
Flight Project
Implementation
Program Funded Risk Reduction Activity
STMD Funded Tech Dev Activity
Industry / Partnerships
Shortfall Title/#
Technology maturation and demonstration to enable Mars occurs in parallel and follows similar life cycle
D
STMD Activity
Industry Activity
(Iterative, but not necessarily a serial process)
Funded Activity
Proposed Activity
Y
N
Commercialization/Spinoff
Architecture
Standards/Req’s
Risks
Shortfalls & Tech Integ (Roadmap)
Infusion (Flt Projects)
Flight & LL
Objectives

## Slide 21: Definitions & Acronyms
2D | 2-dimensional | HSM | Human Surface Mobility
2REDPANDAS | Radiation tolerant and Reliable Electronic Displays: a Preliminary Assessment Necessary for Deep-spaceflight Applications | HUD | Heads Up Display
AR | Augmented Reality | Hz | Hertz
ASO | Autonomous Systems and Operations | ICDM | International Committee on Display Metrology
AV | Audio Visual | IRIS | Intelligent Response and Interaction System
BET | Blur Edge Time | IT | Information Technology
C&DH | Command & Data Handling | Joint AR | Joint Augmented Reality
CHP | Crew Health & Performance | JETT | Joint EVA and Human Surface Mobility Test Team (JETT)
CIE | International Commission on Illumination | KPP | Key Performance Parameters
COTS | Commercial Off the Shelf | LCD | Liquid Crystal Display
DMS | Display Measure Standard | LED | Light Emitting Diode
DSM | Deep Space Missions | LET | Linear Energy Transfer
EVA | Extravehicular Activity | NLP | Natural Language Processing
EHP | EVA & HSM Program | OLED | Organic Light Emitting Diode
ELDRs | Enhanced Low Dose Rate Sensitivity | PCD | Portable Computing Device
ESDMD | Exploration Systems Development Mission Directorate | PR | Pressurized Rover
FOM | Figure of Merit | RT | Radiation Tolerant
FPDM | Flat Panel Display Measurements | SCLT | System Capability Leadership Team
GCD | Game Changing Development | SEE | Single Event Effects
GET | Gaussian Edge Time | STMD | Space Technology Mission Directorate
GPC | Gateway Portable Computer | STT | Speech to Text
GSS | Gateway Support Server | TID | Total Ionizing Dose Tolerance
GW | Gateway Program | TNID | Total Non-Ionizing Dose
HIDH | Human Integration Design Handbook | TTS | Text to Speech
HLS | Human Lunar Systems Program | VESA | Video Electronics Standards Association
HPSC | High Performance Space Computer | xEVAS | Exploration EVA Services contract
HRP | Human Research Program |  |