## Slide 1
NASA’s Rotating Detonation Rocket Engine Development
2025 AAS Conference, February 1, 2025
Thomas Teasley ER13 Combustion Devices | NASA Marshall Space Flight Center
This material is a work of the U.S. Government and is not subject to copyright protection in the United States.

## Slide 2: Introduction
Project Goal: Identify and understand operability requirements, design requirements, and scalability of RDRE hardware.
Methane, Kerosene, Liquid Hydrocarbon, Hydrogen fuels tested to date.
Elevated pressure conditions demonstrated with detonations.

## Slide 3: Major Tests at NASA MSFC
Several Scales Tested.
H2/LOx, LH2/LOx, GCH4/GOx, LCH4/LOx, RP/LOx.

## Slide 4: Major Tests at NASA MSFC
RP/LOx (direct injection)
Strong single wave detonation observed.
L/L injection yielded extremely high dynamic loads and high entrainment.
Direct calorimetry extremely difficult with one wave and with sooting of the wall.
Next steps are dual regen with methane heat flux profiles assumed.
LH2/LOx (dual-regen)
Only deflagration observed.
Hydrogen is viable for annular combustion chambers.
Not the end of the story for hydrogen/oxygen RDRE.
There are other things that can be done to coax detonation and the community should not give up on it.

## Slide 5: Critical Technology Elements
RDRE can be broken up into 4 Critical Technology Elements
CTE 1: Thrust Chamber – Cooling passages, initial nozzle geometry, pressure vessel.
CTE 2: Injector – Sets system pressure loss and mixing environment.
CTE 3: Nozzle Extension – Yields performance in vacuum, dictates packaging.
CTE 4: Powerhead – Adapts systems requirements, provides power, and overall pressure budget.

## Slide 6: Critical Technology Elements
Confluence of Manufacturability and Scale Validation
As the thrust class increases, so does the ease of manufacturability, to a limit.
Once you exceed a certain thrust class, the manufacturability becomes a challenge.
The high the thrust class, the lower the overall confidence in scalability.

## Slide 7: Experimental Activities
Thrust class and scalability.
Propellant and conditioning.
  Propellant type.
  Phase at injection.
  Temperature at injection.
  Pre-burned condition.
Annulus Geometry.
  Wall contouring.
  Annulus gap width.
  Area Contraction.
  L* and L’.
Injection parameters.
  Element scheme.
  Element density.
  Injection pressure loss or momentum balance.
  Orifice geometry.
  Manifold acoustics and coupling.

## Slide 8
Experimental Efforts
Heat Transfer.
Vibrational Environments.
Hardware Geometry.
Operability Success

## Slide 9: Chamber Geometry – Calorimetry for Heat Transfer

## Slide 10: Use of Bimetallic Capabilities
AM L-PBF GRCop-42.
Monel K500 / GRCop-42 bimetallic injector – Quadrus Corp.

## Slide 11: Test Data – Vibratory Environment
Triaxial Load Cell
Accelerometer
V1
V2
Single wave mode environments are extreme.
Both triaxial load cell and accelerometer data corroborate extreme vibrational environment.
This is observed on other scales and with other propellants.
2+ wave environments are far less severe.

## Slide 12: Test Data – Vibratory Environment
V1
V2

## Slide 13
Test Data – Hardware Geometry is Critical
Martinez et al. 2024; Experimental Study of a Watercooled GOX/RP-1 Rotating Detonation Rocket Combustor for Application to Ox-Rich Staged Combustion Engine Cycles

## Slide 14
Two Birds – One Stone
Leveraging every opportunity possible to partner with other projects.
RAMBO, SBIR, STTR activities.

## Slide 15
High Pressure Demonstration
Multi-wave modes have been measured at elevated pressures with RP-1 and Methane fuels, 750 psia and 1250 psia respectively.
NASA 1250 psia test.

## Slide 16: Summary
Challenges Moving Forward
Heat Transfer - known heat flux scaling.
Vibratory Environment – Multi-mode operation.
1. We have a plan and test /computational activities will elucidate these challenges.
2. Successful demonstration of the TDM project operating conditions.
3. Leveraging collaborations to involve industry, academia, and government.
4. Sharing these data as broadly as possible with collaborators.

## Slide 17
Contact:
Thomas Teasley
NASA MSFC
thomas.w.teasley@nasa.gov