## Slide 1: Automation of Mission Operations & Testing with Digital Twins
D. Cody Cutright, Systems Engineer, TMC Technologies
February 12, 2025

## Slide 2: Who is NASA IV&V?
NASA Katherine Johnson Independent Verification and Validation Program
  Ensuring Class A Mission success since 1993
  Full Development Lifecycle
    Software Requirements, Design, Code, Test, I&T
  Located in West Virginia
JSTAR Team
  The Jon McBride Software Testing & Research Laboratory
    Named for WV’s first astronaut
  Specialized subset of IV&V Facility
  Experts in modeling, simulation, and digital twins of NASA missions

## Slide 3: What Does JSTAR Do?​
Experts in software only simulation of hardware
Experts in hardware emulation
We provide simulated hardware so flight binaries can be executed, unmodified, on commodity hardware
  This enables unique, challenging, and otherwise difficult to create test cases
  Virtual testbeds allow development to proceed without immediate access to a flatsat
  In some cases, code can essentially be finalized prior to hardware integration
  Shortens development timelines
FSW, Physics, Avionics

## Slide 4: How do you design, test, and operate efficiently?

## Slide 5: Traditional NASA Life-Cycle Phases
Pre-Phase A: Concept Studies
A: Concept & Technology Development
B: Preliminary Design & Technology Completion
C: Final Design and Fabrication
D: System Assembly, Integration & Test, Launch & Checkout
E: Operations & Sustainment
F: Closeout
Based on NPR 7123.1
Traditionally, sub-system software begins here.
FSW integration with sub-systems and system-wide testing here.
Notes: For mission testing and operations, where is the bottleneck?

## Slide 6: C & D Overviews
C: Final Fabrication & Design “To complete the detailed design of the system (and its associated subsystems, including its operations systems), fabricate hardware, and code software.”
D: System Assembly, Integration and Test, Launch
“To assemble and integrate the system (hardware, software, and humans), meanwhile developing confidence that it is able to meet the system requirements. Launch and prepare for operations. Perform system end product implementation, assembly, integration and test, and transition to use.”

## Slide 7: Why not start mission operations and testing in phase C?
Working towards a finalized design
Have a good idea of subsystems that will be selected early on in Phase C
Definite list of subsystems and manufacturers at the end of Phase C
You know the basics of everything, including flight software
  Start with a skeleton framework of subsystem applications and simulators, and iterate as more information becomes available
  There’s no need to wait for hardware to begin software, if you have an ICD and specifications!

## Slide 8: Benefits of starting early
Digital twins shift the traditional software development cycle
Greatly increase test resources and opportunities
Shifting Left—Building Systems & Software Before Hardware Lands (intel.com)

## Slide 9: More benefits
Digital twins allow for earlier…
  operator competency
  fault detection & correction scenario testing
  nominal concepts of operations / DITL
  system-wide integration for data products that drive additional software (e.g. ML for representative spacecraft data)

## Slide 10: Which disciplines can benefit?
Developers
Software development environment
Early development opportunities before hardware arrives
I&T
Enables end-to-end testing early
Manipulate hardware models
Operations
Dry-run scenarios
Day in the life testing
IV&V
Risk reduction testing and mission assurance
Hardware modeling and fault injection
New Personnel
Training platform that you cannot break
Easily run lab tests to demonstrate faults
Researchers
Integrate and demonstrate new technologies
V&V
Increases available test resources
Code coverage
Exploratory testing
New uses and users reported regularly!

## Slide 11: Simulation To Flight 1
Born of Simulation To Flight 1 (STF-1)
  West Virginia’s first spacecraft
Partnered with WVU and leveraged existing NASA GSFC efforts
Demonstrated digital twin capabilities to improve mission processes
Provided an open-source solution for researchers and technology development
Resulted in the NOS3 platform
  Initially a framework
  Now a design reference mission
De-orbited in 2024, after 5 operational years

## Slide 12: NOS3 Simulation Example
Hardware Models
Flight Software
Time Sync
Dynamics
Ground Software
Flight Software
Time Sync
Ground Software
Dynamics
Hardware Model

## Slide 13: NOS3 Architecture
Combination of multiple pieces of open-source software
  A virtual spacecraft!
  Learn on, do research, baseline as your own
Flight Software
  Core Flight System (cFS)
  F’
Ground Stations
  Ball Aerospace COSMOS
  JPL AMMOS Instrument Toolkit
  OpenC3 COSMOS
  YAMCS
Dynamics / Visualization
  42
NOS Engine
  Communication protocols
  Hardware abstraction layer
  Component simulators

## Slide 14: NOS3 Architecture
NOS3 enables cross compiling for your flight and simulation targets
  HWLIB enables selection of build type via flags at compile time
FSW
Software Bus
CAM
GPS
Inst.
Radio
Hardware Library
Data Providers
42 Spacecraft Dynamics Simulator
Ground Station Software
SIM
CAM
GPS
Inst.
Radio
NASA Operational Simulator (NOS)
Time synchronized across all modules
Engine
Sim Terminal
Time
NOS
Engine
UDP
UDP

## Slide 15: Design Reference Mission
NOS3 benefits have been proven across multiple missions
Each mission develops several hardware specific applications
  Due to licensing concerns these are not available outside of NASA for re-use
Missions often become so specific that implementations require a complete understanding
  No easy method of training or baselining for new efforts
To provide a baseline for advanced development in NOS3 a complete mission is required
  Generic components and interfacing was the first step to resolve this

## Slide 16: NOS3 Development Flow
Checkout
Review
README
Template
Checkout HW Testing
Simulator
Checkout w/ Simulator
Application
Application w/ Simulator
Application HW Testing

## Slide 17: Developers
Robert J. Brown, Systems Engineer, TMC Technologies, NASA IV&V
D. Cody Cutright, System Engineer, TMC Technologies, NASA IV&V
Donovan R. Ice, Systems Engineer, TMC Technologies, NASA IV&V
John P. Lucas, Systems Engineer & JSTAR Deputy Lead, NASA IV&V
Justin R. Morris, Computer Engineer & JSTAR Lead, NASA IV&V
Scott A. Zemerick, Chief Engineer, TMC Technologies, NASA IV&V

## Slide 18: JSTAR In Review
JSTAR is a Digital twin factory
Digital twins provide a capability
  Highly flexible environments to support development and risk reduction testing
Digital twins shift the software timeline
  Less reliance on hardware schedules
  Increased test opportunities and resources
Points of Contact
  David.C.Cutright@nasa.gov
  Justin.R.Morris@nasa.gov