## Slide 1: Evaluating Crewed Lunar Landers
Steven Carothers (NASA)
Mark Updegrove (Intuitive Machines)
March 2025

## Slide 2: Agenda
Apollo
  Lunar Landing Overview
  Lunar Flying vs Aircraft Flying
Artemis
  Architecture and Overview
HLS and the HCLS
  Lunar Lander Simulation
Vehicle Evaluation
  Flying Qualities vs. Handling Qualities
  Handling qualities evaluations with test pilots
  Cooper-Harper Chart
  Performance Criteria
Key Findings
Summary

## Slide 3: APOLLO

## Slide 4: Lunar Landing Overview
Apollo 16
Flight Deck

## Slide 5: Lunar Landing Overview

## Slide 6: Lunar Landing Overview
Manual Control:
100 ft altitude
36 ft range
Dallas to Wichita in 11.5 minutes!
Ignition:
50,000 ft
Mach 6.5
Dallas
Wichita

## Slide 7: Lunar Flying vs Aircraft Flying
Ways to fly terrestrial aircraft
  Constant altitude
  Constant airspeed
  Constant climb/descent rate
  Constant flight path angle
  Usually land on prepared surface at a controlled location
None of the above are true with a lunar lander

## Slide 8: ARTEMIS

## Slide 9: Artemis
Moon to Mars Architecture
  Ultimate goal: access to Mars via the Moon
  Lunar outposts in South Pole Region
  Access to surface via Near Rectilinear Halo Orbit (NRHO)
Multiple Elements
  Orion – Transport crew between Earth and NRHO
  Gateway – Small Station in NRHO
  HLS – Transport crew between NRHO and Lunar surface
  Others – Launch systems, rovers, suits, etc.

## Slide 10: Artemis
Multiple Vehicle Providers
  SpaceX
  Blue Origin
Modern lander designs leveraging modern technology
  Emphasis on reusability
  No size constraints
  Fuel optimal trajectories
  Advanced avionics
  What are the impacts to piloting?

## Slide 11: Mission Overview

## Slide 12: HLS and the HCLS

## Slide 13: Purpose
Evaluate handling qualities of potential lunar lander designs
Prototype crew displays
Evaluate inceptor types and characteristics
Evaluate control modes
Evaluate effects of propellant slosh
Evaluate different trajectory designs
Develop processes and tools for evaluating handling qualities
HCLS = HLS Crew Compartment Office Lander Simulation
Notes: Evaluate ≈ Explore

## Slide 14: Descent Guidance
Fully automated descent from a Low Lunar Orbit (LLO) through touchdown
Primary Phases of Flight
  Braking
  Approach
  Terminal Descent
Automated Guidance
  Apollo
  Reference Trajectory Tracking
Translational Guidance
Steering
PID
Plant
+
-

## Slide 15: Manual Control
Manual control available at any point during descent
Planform Guidance Modes
  Rate Command with Attitude Hold (RCAH)
  Attitude Command with Velocity Hold (ACVH)
  Translation Rate Command with Position Hold (TRCPH)
Vertical Guidance
  Auto Rate of Descent (ROD) uses a look-up-table based on the reference trajectory altitude
  Manual Control via Translational Hand Controller (THC)

## Slide 16: Facilities
Simulation, Exploration, and Analysis Lab (SEAL)
Motion Table

## Slide 17: Facilities
SEAL Workstation (1 of 2)
THC
Primary Flight Display
Navigation Display
RHC
External Views

## Slide 18: Capabilities
Customize control power, bandwidth, and max attitude rate
Customize rotational hand controller characteristics
Customize propellant slosh parameters
Force landing site redesignation
Add navigation biases to vehicle
Set lighting conditions for a specific day
Simulate terrain based on Lunar Reconnaissance Orbiter data
Add extra large rocks to landing zone
Immediate analysis via detailed reports

## Slide 19: Primary Flight Display
Guidance Diamond
  Available in auto and manual control
  Visual pitch and roll guidance
  Fly-to symbology
  Multiple methods to drive diamond
Altitude Above Field Level tape
Altitude rate scale
Mini-map
Boresight
Guidance Diamond
Notes: Trajectory Following PID
  Calculates acceleration required to track reference trajectory
  Uses feedforward acceleration term
  Fades to time-based constant acceleration command
Explicit Constant Acceleration
  Calculates constant acceleration at each time step
Explicit Cubic Solution
  Calculates cubic polynomial solution at each timestep

## Slide 20: Navigation Display
Overhead view centered on ownship
Predictive position symbology
  Based on rotorcraft displays
  Decoupled from the guidance system
  Pilot uses the RHC to position the cue over the desired landing point
Altitude Above Field Level tape
Altitude rate scale
Attitude Determination Indicator ball
Velocity Vector
Position Predictor
Landing Target

## Slide 21: Navigation Display
Overhead view centered on ownship
Predictive position symbology
  Based on rotorcraft displays
  Decoupled from the guidance system
  Pilot uses the RHC to position the cue over the desired landing point
Altitude Above Field Level tape
Altitude rate scale
Attitude Determination Indicator ball
Velocity Vector
Position Predictor
Landing Target
Notes: Explain this example describing the situation to help them picture the relationship between the symbols.

## Slide 22: Vertical Rate Command
Discrete THC inputs change the commanded vertical velocity by 10% of the current vertical velocity
For small vertical rates, discrete THC inputs change the commanded vertical rate by a minimum of 0.1 m/s
Continuous THC inputs slew the commanded vertical rate indicator along the vertical rate scale
Slewed commanded rate will stop at zero
Release THC and resume inputs to cross zero
Can return to vertical rate command to auto

## Slide 23: VEHICLE EVALUATION

## Slide 24: Flying Qualities vs. Handling Qualities
Flying Qualities
  Stability and control of vehicle (flight control system, structure, aerodynamics)
  Quantitative measurement of vehicle response to specific pilot inputs
Handling Qualities
  Flying qualities plus task demands, pilot controls, and crew displays
  Qualitatively evaluated by test pilots via comments and ratings
We’ll address Handling Qualities in this presentation.

## Slide 25: Evaluators
HLS astronauts (pilots and non-pilots)
Military test pilots
  Test Pilot School graduates
  Fixed-wing, rotary-wing, tilt-rotor, vectored thrust
US Coast Guard helicopter pilots
MQ-9 Reaper operators
HLS team members from all disciplines
Private pilots, non-pilots, VIPs
Moonwalkers: Jack Schmitt and Charlie Duke

## Slide 26: Execution: Formal Evaluation Sessions
Begin only when pilots no longer getting significantly better at the task
Evaluate similar scenarios seen in familiarization session
Get pilot comments during and immediately after each run
Compare performance to desired and adequate performance criteria
Get more pilot comments
Get Cooper-Harper rating

## Slide 27: Cooper-Harper Chart
Level 1
Level 2
Level 3

## Slide 28: Cooper-Harper Guidance & Definitions

## Slide 29: Cooper-Harper Ratings: Misuses
Evaluating too many things at once
No clearly defined initial conditions
Poorly defined task
Poorly defined (or undefined) performance criteria
No way for pilots to know how well they’re performing in real-time
No feedback after task regarding how well performance criteria was met
No “recalibration” runs (i.e., frog in the boiling pot)
Giving half ratings, especially between Levels
Averaging ratings

## Slide 30: Lunar Lander Performance Results
Task: Guidance Tracking
  Keep boresight on diamond
    “Thing on the thing”
  Primarily in pitch axis
  Follow to landing
Performance Criteria
  Desired
    ≤3 deg of cue ≥90% of the time
  Adequate
    ≤ 6 deg of cue ≥90% of the time
Boresight
Guidance Diamond
Notes: Trajectory Following PID
  Calculates acceleration required to track reference trajectory
  Uses feedforward acceleration term
  Fades to time-based constant acceleration command
Explicit Constant Acceleration
  Calculates constant acceleration at each time step
Explicit Cubic Solution
  Calculates cubic polynomial solution at each timestep

## Slide 31: Lunar Lander Performance Results
Pilot Compensation
Tracking test throughout trajectory
Arrival for Terminal Descent
Touchdown Conditions
Average of all scores

## Slide 32: Lunar Lander Performance Results
Quickly generate report for pilot evaluations
40+ page PDF generated in less than a minute

## Slide 33: Lunar Lander Key Findings: Overall
Flying credentials are not a good predictor of lunar lander performance.
Correct mental model of vehicle dynamics is critical.
Correct understanding of display symbology is critical.
A good position-predictor cue is critical for a manual landing.
Rotary-wing pilots generally did better than fixed-wing, single seat fixed-wing pilots.
Low gain pilots had better results.

## Slide 34: Lunar Lander Key Findings: Manual Piloting
Manual piloting requires most of the pilot’s attention.
Once off trajectory, it is increasingly difficult to get back on trajectory.
PIO manifests with 20-30 second periods (overshoot landing site).
Controlling translation and vertical rates simultaneously requires extra practice.
Lunar lander flying techniques are counter to fixed-wing techniques.
Lunar lander stick input techniques are not like rotary-wing techniques.
Landing is mainly a heads-down activity.
It is possible to land without guidance attitude cues.

## Slide 35: Summary
Define desired and adequate performance criteria beforehand.
Define performance criteria for the entire run, not just the end.
Pilots need a way to evaluate their performance in real-time. This drives pilot compensation.
Quickly generate reports after each run.
Main benefit of Cooper-Harper ratings is to elicit comments from pilots.
Ask for ratings for specific tasks, not one rating for the whole trajectory.
Use multiple evaluation pilots with various backgrounds.
Displays can have a huge impact on handling qualities.
Practice the process before conducting formal evaluations for certification.