## Slide 1: Multi-Functional Flash Lidar Software for Precision Safe Landing
Paul Brewster
NASA Langley Research Center
2025 Flight Software Workshop
3/24/2025

## Slide 2: Precision Safe Landing
Safely land on the Moon
  Within vehicle tilt limits
  Clear of dangerous objects such as rocks and boulders
  Clear of craters
Precisely land on the Moon
  Detect vehicle position relative to known features on the Moon
  Measure altitude from the surface
Constraints
  Proposed future missions are to the hazardous Southern Polar regions
  Current Lunar surface data is insufficient
  Lighting near the Southern Pole is difficult
  Calculations are time sensitive with no abort options

## Slide 3: Landing Conops

## Slide 4: Flash Lidar
Performance
  A laser pulse is spread to cover an area of interest
  An array of detectors produces a Range Image from a single laser pulse
  Laser pulses at 20Hz
  Multiple Range Images are combined to create a Digital Elevation Map at 1Hz
Advantages
  Does not have the lighting issues of a Visual Camera
  Does not have the pointing and motion issues of a Scanning Lidar
  Does not require external hardware (IMU, gimbal, etc.)
Disadvantages
  Limited Resolution, but can be overcome in software
  Processing Power (although also applies to Visual Cameras and Scanning Lidar)

## Slide 5: Multi-Functional Flash Lidar
Hazard Detection
  Creates a Digital Elevation Maps and Hazard Maps
  Laser pulse spread to fully cover the area of interest
  The full detector array is illuminated
  Maximum Range is 1km
Hazard Avoidance
  Tracks the relative motion of the vehicle to the identified hazards
  System configured as in Hazard Detection
Terrain Relative Navigation
  Calculates absolute position by identifying features in the detected area and matching those features to known locations
  Laser pulse narrowly spread over a small area
  The central area of the detector array is Illuminated
  Maximum range is 20km
Relative Navigation
  Derives altitude from Time-of-Flight of active pixels
  Laser pulse is not spread
  A couple pixels in the center of the detector array are illuminated
  Maximum range is 50km

## Slide 6: Flash Lidar Software Requirements
Command and Control
  Control the Lidar Camera
  Control the Laser
  Control the Optics
Telemetry
  Range Images at 20Hz
  Altitude at 20Hz
  DEMs at 1Hz
  Hazard Maps at 1Hz
  Safe Sites at 1Hz
  Relative Motion at 20Hz
  Position at 1 Hz
Data Processing
  Generate DEMs
  Generate Hazard Maps
  Find Safe Locations
  Identify Features
  Track Features

## Slide 7: Software Flow
Mode
Acquire Range Image
Filter Range Image
Create DEM
Average Active Pixels
Create DEM
Calculate Relative Motion
Altitude
Relative Navigation
Terrain Relative Navigation
Hazard Detection
Hazard Avoidance
Match DEM to Database
Position
Calculate Position
Create Hazard Map
Identify Safe Sites
DEM
Range Images
Hazard Map
Safe Sites
Relative Motion

## Slide 8: Create DEM
Receive Range Image
First Image
Initialize State Vector
Update State Vector
Yes
No
Initialize
DEM
Update DEM
Last Image
State Vector
Point Spread Function
No
Yes
DEM
Problem: Current Space Flight Processors do not have the power to perform this operation in Real-Time

## Slide 9: GPUs in Space
NVIDIA Jetson TX2i based systems have shown promise as a space flight processor
  Launched missions using a TX2i
    The LOFTID re-entry vehicle from NASA Langley used 8 TX2i
    The La Jument CubeSat from Lockheed Martin and USC
    The ASTRA mission from NASA Stennis and Sidus Space
  Several more missions in development are planning on using a TX2i
  Multiple companies have begun selling TX2i systems designed for space
NVIDIA Jetson AGX Orin Industrial based systems will likely replace the TX2i in the near future
NVIDIA

## Slide 10: Software Layers
Software Modules
Software Framework
Application Libraries
Drivers
Operating System
Hardware Layer
NVIDIA Jetson TX2i
Jetson Linux (based on Ubuntu)
Jetpack SDK
CUDA
cuFFT
Custom Framework for GPU Applications
Create DEM
Range Filter
Identify Safe Sites
Calculate Motion
Scheduler
Create Hazard Map
Average Active Pixels
Lidar Interface
Commands
Telemetry

## Slide 11: Custom GPU Framework
C++17 based framework designed specifically for GPU processing
Modular Pipeline to work with typical CUDA data flows and manage CUDA memory
  Data Items are encapsulated CUDA buffers with metadata
  Pipes are thread-safe triple-buffers of Data Items
  Modules are threads with input and output Pipes
Lidar Interface
Range Filter
Create Dem
Create Hazard Map
Identify Safe Sites
Commands
Commands
Commands
Commands
Commands
Telemetry
Telemetry
Telemetry
Telemetry
Telemetry
Range Image
Digital Elevation Map
Filtered Range Image
Hazard Map

## Slide 12: Simulated Tests
Input Range
Image
DEM after
First image

## Slide 13: Simulated Test Results
DEM after
20 images
DEM after
First image

## Slide 14: Field Tests
Static Test
Drone Test
Gantry Test
Helicopter Test

## Slide 15: Field Test Results

## Slide 16: Future Work
Continue testing and refinement of algorithms
Build ETU as a payload on future lander missions
Investigate other computing platforms
  HPSC as a CPU approach
  Xilinx Kintex™ as an FPGA approach
  Xilinx Versal™ as a hybrid CPU, FPGA, AI Engine approach
AMD Versal
Trade names and trademarks are used in this report for identification only. Their usage does not constitute an official endorsement, either expressed or implied, by the National Aeronautics and Space Administration.