## Slide 1: Space Crop Production Gaps and Challenges
Gioia Massa
Exploration Research & Technology Programs
NASA, Kennedy Space Center

## Slide 2: Why grow plants in space?
Food
Psychological well being
ECLSS

## Slide 3
Ensure Food System Security on Long Duration Missions Beyond LEO
Near-Term Goal
Nutrient Supplementation of Prepackaged Food
Long-Term Goal
Caloric Replacement to Facilitate Earth Independence
NASA’s Space Crop Production Vision
For future, longer duration habitation on the Moon or Mars, Bioregenerative Life Support including Plants can be expanded to increase Mission Autonomy and Earth Independence
Near term missions will rely on Physico-Chemical Regenerative ECLSS and Stowed Food with Supplemental Fresh Food
Notes: Ralph
Ensure Food System Security on Long Duration Missions Beyond Low Earth Orbit (LEO)
Food and nutrition are the first line of defense for crew health and performance
Provide safe, nutritious and acceptable fresh food
Add variety to crew diet
Enhance morale
* Food security is the condition in which crew have continuous access to sufficient safe and nutritious food which meets both their dietary needs and food preferences in order to maintain peak health and performance.
Nutrient Supplementation of the Prepackaged Food System - Needed for: Deep Space Transport
Fresh produce supplements vitamins (B1, K, C) and bioactive compounds that degrade in the stored food system on multi-year exploration missions
“Pick-and-Eat” crops that require no processing and minimal preparation will provide variety, customization, and psychological appeal
Enable testing and demonstration of dependable crop production before reliance on system.
Limiting factors are vehicle resources mass, power, volume, water, air, crew time
Near Term Missions for NASA to Mars Will Rely on Physico-Chemical Regenerative ECLSS and Stowed with Supplemental Fresh Food
Caloric Replacement to Facilitate Earth Independence - Needed for: Long duration Surface missions on the Moon and Mars
  Reduce up-mass associated with pre-packaged food
In addition to “pick and eat” crops, include staple crops that require processing and preparation
Bioregenerative capability will be required for long duration surface missions
For future, longer duration habitation on Mars or the Moon, Bioregenerative Life Support Including Plants can be Expanded to Increase Mission Autonomy and Earth Independence

## Slide 4
Douglas et al., 2021, Sustaining Astronauts: Resource Limitations, Technology Needs, and Parallels between Spaceflight Food Systems and those on Earth, Sustainability
Notes: Figure https://www.mdpi.com/sustainability/sustainability-13-09424/article_deploy/html/images/sustainability-13-09424-g001.png

## Slide 5: Space Crop Production Challenges
LEO/Deep Space
Surface
Crop
Microgravity
Fluid movement
No convection
Water
Recycling
Radiation
Pressure
Micrometeorites
Dust & Regolith
Partial gravity
Productivity
Stress tolerance
Environmental optimization
Crop scheduling
Plant Size
High CO2
Food Safety & Microbiome
Nutrient output
Sustainability
Abiotic stresses
Vehicle resources
Crew time
Waste

## Slide 6: Current NASA Large Plant Research Capabilities On ISS
Notes: Veggie and the Advanced Plant Habitat

## Slide 7: Key Crop Plant Takeaways
Data indicate astronauts enjoy growing and eating plants in spaceflight
Crop yield is similar between ground and flight when plants are not stressed1
Some differences between ground and flight plant nutrient content, but these are not consistent between species or experiments 1, 2
  Influenced by crop type, harvest scenario, other environmental conditions (e.g., light, stress)
Microbial counts and compositions vary between flight and ground-grown plants1, 2
  Microbes typical of the space station environment are often associated with ISS-grown plants
  Human pathogens are rarely identified on space-grown plants and only below levels of concern to human health
Microbial communities vary between shoot and root tissues and but not as much between flight and ground 2
Plants adapt well to the space environment, and to date, space-grown crops are safe to eat, nutritious, and highly acceptable to astronauts 1,2
Bunchek et al., 2024, Pick-and-eat space crop production flight testing on the International Space Station, J. Plant Interact.
Khodadad et al., 2020, Microbiological and Nutritional Analysis of Lettuce Crops Grown on the International Space Station, Front. Plant Sci.

## Slide 8: Thank you!