## Slide 1: Robust Software Engineering at NASA Ames Research Center
Daniel Hulse (Ames Research Center)
Lukman Irshad (KBR)
Anastasia Mavridou (KBR)
Seydou Mbaye (Ames Research Center)
Irfan Sljivo (Wyle)
Hannah Walsh (Ames Research Center)
Notes: https://images.nasa.gov/details/PIA22109

## Slide 2: Presentation Outline
Part I: Robust Software Engineering
  Robust Software Engineering
Part II: Introduction to Tools
    AdvoCATE
    HADES
    FRET
    Proposed Workflow with Tools
  Part III: Troupe 2.0
Part IV: Application of Tools to Troupe 2.0
    Representation and Analysis in AdvoCATE
    Modeling and Analysis in HADES
    Requirements Specification and Analysis in FRET
Further Reading
Notes: https://images.nasa.gov/details/PIA24934

## Slide 3: Part I: Robust Software Engineering
Motivation, Past Work, V&V Approach, and Objectives

## Slide 4: RSE: Robust Software Engineering
The Robust Software Engineering team is part of the Intelligent Systems at NASA Ames.
We specialize in developing tools that catch problems early on in system design.
We develop tools that are designed to be intuitive and extensible

## Slide 5: RSE: From Design to Operations
Many of our tools utilize formal methods to functionally decompose the system and prove its properties
These properties can be captured as requirements
We can generate simulations and test cases for these requirements and prove the properties of the system
Concept of Operations
Requirements and Architecture
Detailed
Design
Implementation
Integration and test
Verification and Validation
Operations and Maintenance
Verification and Validation
Project Definition
Time
Test and Integration

## Slide 6: Part II: Introduction to Tools
AdvoCATE, HADES, FRET, and Proposed Workflow

## Slide 7: AdvoCATE: Assurance Case Automation Toolset
Capabilities​
  Hazard analysis and risk assessment
  Safety and assurance requirements capture
  Structured argument development
  Safety architecture development
  Traceability and consistency
  Evidence management and analytics via dashboards

## Slide 8: HADES: Hazard Analysis DESigner
Hazard Analysis Environment
Historic Knowledge Extraction via MIKA
Scenario-based Resilience Simulation via fmdtools
Graph-based System Modeling
Traceable Design Artefact Generation Environment
  Capabilities
  Scenario-based hazard analysis that accounts for all system elements (human, hardware, and software)
  Knowledge-assisted fault simulation capabilities with broad scenario coverage
  Parameterizable simulation (to study emergent failures even when hazards are not present)
  System-of-Systems simulations and fault combination evaluations
  Resilience studies and metrics
  Historic knowledge utilization for hazard identification and classification
  Safety requirement generation and validation
  Traceability with other system design artifacts
  Maintain design assurance artifacts dynamically
  Iterative testing, trade study setup, and mitigation validations
  HADES is currently under development, but most of the listed capabilities are included in the existing toolkits fmdtools and MIKA.
Hazard Tables
Safety Requirements
Safety Assurance Evidence
Safety Architectures

## Slide 9: MIKA: Manager for Intelligent Knowledge Access Used in HADES
Captures high level themes in large sets of documents
      Topic Modeling
Identifies documents relative to high level themes
      Semantic Search
Capabilities
Searches through large number of historical documents and updated reports to generate knowledge

## Slide 10: fmdtools: Fault Model Design Tools Used in HADES
Capabilities
Modelling of system architecture and behavior in consistent, composable, and parameterizable modelling paradigm, including:
  Functions, Components, and Human Actions
  Systems and Systems-of-Systems Architectures
Simulation of system behavior over scenarios of interest, including:
  Single and multiple-fault scenarios
  Wide ranges/sets of scenarios and system parameters
  Optimized cases, e.g., worst-case scenarios or most robust system parameters
Analysis of system resilience
      Visualization of behaviors and properties over time
      Scenario-based hazard/FMEA tables
      Visualization of system structure and scenario propagation
Mental Model of System and Hazards
Modelling
Simulation
Analysis
Analyst
Results
(e.g., Risk/Resilience Measures)
Modelling

## Slide 11: FRET: Formal Requirements Elicitation Tool
Capabilities​
Captures requirements in structured natural language with unambiguous semantics
  Explains formal semantics in various forms
  Formalizes requirements in a compositional (hence extensible) manner
  Analyzes consistency of requirements and provides feedback
  Generates test cases from requirements
  Connects with analysis tools:
      Model checkers
      Realizability analysis tools
      Runtime monitoring tools
​

## Slide 12: FRET: Formal Requirements Elicitation Tool
Autonomous systems bring new challenges: need to express uncertainty in requirements.
Plain English requirement:
Often ambiguous, not amenable to analysis
P>=1[((G ((! (((! auto_takeoff_mode) & (X
auto_takeoff_mode)))) | (X ((auto_takeoff_mode
& (X (! auto_takeoff_mode))) R (q_k =>
(P>0.99[((auto_takeoff_mode & (X (!
auto_takeoff_mode))) | ((X incursionDetected)
& (! (auto_takeoff_mode & (X (!
auto_takeoff_mode))))))])))))) & (auto_takeoff_mode
=> ((auto_takeoff_mode & (X (! auto_takeoff_mode)))
| ((auto_takeoff_mode & (X (! auto_takeoff_mode)))
R (q_k => (P>0.99[((auto_takeoff_mode
& (X (! auto_takeoff_mode))) | ((X
incursionDetected) & (! (auto_takeoff_mode & (X
(! auto_takeoff_mode))))))]))))))]
Probabilistic FRET: capture behavior of learning-enabled components using probabilistic requirements in a structured nature language
Automatic translation to PCTL* (uninterpretable to >99% of engineers according to RTX, US aviation industry)
(Assists with formalization and understanding of complex system requirements)

## Slide 13: Proposed Workflow with Tools
HADES
HADES
HADES
HADES
HADES

## Slide 14: Additional Tools: Testing and Runtime Verification
Inference Kernel for Open Static Analyzers (IKOS): Static analyzer for detecting runtime errors in C/C++.
AdaStress: Monte Carlo Simulations for optimized testing
CoPilot: Runtime monitors that validate the state of the system during execution

## Slide 15: Part III: Troupe 2.0
Representation and Analysis in AdvoCATE, Modeling and Analysis in HADES, and Requirements Specification and Analysis in FRET

## Slide 16: Troupe: Autonomous Micro Rover Swarm
Internal NASA Ames RSE project
Technology demonstrator and knowledge transfer
Aims at developing a fleet of rovers capable of autonomously mapping unknown terrain
  Including no-GPS zones such as caves

## Slide 17: Troupe: System Overview
Each rover runs the same core Flight System (cFS) application
  High-level cFS block diagram for a single Troupe rover
  Publish/subscribe architecture
  Messages are passed via shared memory on the core Flight Executive (cFE) software bus.
  Some applications are manually-coded others are code-generated using MATLAB/Simulink and an external code interface (ECI).

## Slide 18: Part IV: Application of Tools to Troupe 2.0
Representation and Analysis in AdvoCATE, Modeling and Analysis in HADES, and Requirements Specification and Analysis in FRET

## Slide 19: Representation and Analysis in AdvoCATE

## Slide 20: AdvoCATE: Physical and functional decomposition
Basis for hazard analysis
Includes failure mode and deviation specification

## Slide 21: AdvoCATE: Hazard Analysis and Safety Architecture
Hazard analysis goes through all the functional/physical components and the related conditions (failure modes/deviations), and identifies their effects
A safety architecture is automatically generated from the hazard log
  All the hazards/events (green boxes) connected with other events (causes/effects) and the applied mitigations (white/purple boxes)

## Slide 22: Modeling and Analysis in HADES: Complementing AdvoCATE Analysis

## Slide 23: System Modeling with HADES: Functional Model using Functional Reasoning Design Language (FRDL)
FRDL was developed to help specify hazard simulations in fmdtools
  Something that can be used to inform analysis prior to computer-based modelling activities
  Using FRDL means diagrams of system architectures will translate to fmdtools-based simulations
Replacement for Functional Decomposition/Function Block Diagrams typically used in FHA
  Goal: Language to inform analysis of fault/failure propagation (as much as possible)
  Key improvement: Better representation of causal propagation between functions, including shared variables (flows) and activations
  Key improvement: Provides means of annotating diagrams to better specify structure and behavior of functions

## Slide 24: System Modeling with HADES: Functional Model using Functional Reasoning Design Language (FRDL)
Function
Flow
MultiFlow
Connection Types
Shared Variables (Flows)
Behavioral Elements
Propagation
Reverse Propagation (r)
Aggregation)

## Slide 25: System Modeling with HADES: Functional Model using Functional Reasoning Design Language (FRDL)
Function
Flow
MultiFlow
Connection Types
Shared Variables (Flows)
Behavioral Elements
Propagation
Reverse Propagation (r)
Aggregation)
1: Loss of Obstacle
Detection
9: No Power
2: Incorrect Map
(None existent obstacle)
4: Crashes into
Obstacle
10: No Power
3: Incorrect Map
Communicated
8: No Power
5: Adverse/Undesired
Current Draw (locked wheels)
7: No Power supply
6: Damage or Fuse Blown

## Slide 26: Dataset for Use with HADES Knowledge Retrieval Capability: NASA Lessons Learned Information System (LLIS)
https://llis.nasa.gov​
Publicly available database of lessons learned at NASA​
Over 2000 lessons
For internal users, the database can be downloaded as a spreadsheet​
At right: Lesson 630

## Slide 27: Updating FHA with HADES Knowledge Retrieval Capability
Hazardous Activity | Hazard | Allocation | Conditions | Causes | Effects
HA2: Explore unknown area | E58-1: Loss of pose estimation | self_pose: Identifying own pose | no_own_pose: Self pose estimation loss | Inaccurate relative pose | E45-1: Rover goes off the planned path
 |  |  |  |  | E38-1: Path with an obstacle
HA2: Explore unknown area | E61-1: Loss of self mapping history | occupancy_map_building: Building the occupancy map | no_own_map: No map of own area | Loss of map retention | Loss/incorrect localization
HA2: Explore unknown area | E63-1: Loss of obstacle detection | occupancy_map_building: Building the occupancy map | obstacle_not_recognized: Obstacle not recognized | Invalid/no inputs due to loss of sensors, poor physical/software connection to the feed, software unable to initialize obstacles Loss of/incorrect localization | Path plans with obstacles can result in collision with obstacles resulting in loss of rover, Incomplete mission due to not reaching destination
HA2: Explore unknown area | E64-1: Non-existant obstacle detection | occupancy_map_building: Building the occupancy map | ghost_obstacle: Obstacle recognized where not supposed to | Loss of/Incorrect locatlization Invalid inputs due to physical/software connection interference , software initializes obstacles incorrectly | Path plans that are suboptimal resulting in rover traversing unwanted areas delaying or possibly compromising the mission. The mission may be compromised due loss of power because of the additional distance rover travels.
 | loss of mapping function | occupancy_map_building: Building the occupancy map | complete loss of mapping function | no inputs due to loss of sensor, poor physical/software connection to the feed, software unable to initialize obstacles Loss of power | Rover will get stuck inside the already mapped area may result in adverse energy use. Unable to complete the mission due to being stuck inside the already mapped area. In a dynamic environment, rover may collide with new obstacles on the return path due to being unable to detect them potentially resulting in the loss of the rover.
 | Delay in mapping | occupancy_map_building: Building the occupancy map | Delay in mapping | low energy supply poor computational resource allocation computational resource limitation latency in the sensor feed Poor parameter tuning | Delayed mission due to rover waiting for new maps. Incomplete mission due to additional energy used waiting for updated maps. Potential collision with obstacles due to delayed localization due to delayed mapping.
NEW CAUSE from LLIS: anomaly with memory from flight computer - rover lost ability to execute tasks requiring memory
NEW HAZARD from LLIS: loss of ability to anticipate harsh terrain, effects include damage to rover
NEW CAUSE from LLIS: anomaly with pose estimation - inaccurate relative pose

## Slide 28: Simulation: Function-based System Representation and Behavior Simulation
FRDL system model further simplified to ensure computational efficiency
  Communicate function which represents the communications with the ground control is represented as a parameter instead of the function, since it has no major behavioral effects on the rest of the system during a mission
  Navigate includes path planning and drive capabilities

## Slide 29: Simulation: Parameters
Parameters may be varied along with injected fault modes to create scenarios; they include
  Environment-related
    terrain size, resolution of the grid, max objects and object size
    Objects are placed randomly on the terrain in varying sizes
  Ground control-related
    Destination, acceptable buffer area from the destination, max rover speed
  Mission-related
    Mean and standard deviation of location and pose estimation error in the navigate function, mean and standard deviation of location and pose error in the sense function when there is a malfunction in sensing, safety buffer between rover and obstacles, maximum sensing delay
    Variations of the mission-related parameters can be analyzed to generate requirements

## Slide 30: Simulation: Example execution with the fault “no obstacle detection” in the Map function at t = 50
Initially, the rover detects the objects creating blind spots in the visible area
After the fault is injected, some objects are detected while others are not. Undetected objects have no blind spots.
Finally, the rover crashes into an obstacle at t=240 due to not detecting it.

## Slide 31: Simulation: Tracking the rover performance
We track the rovers’ safety and performance through a variety of metrics
  Mission status
  Number of explored obstacles
  Numbers of perceived obstacles
  Number of obstacles not detected
  Number of ghost obstacles detected
  Number of safety breaches

## Slide 32: Analysis: Planned
Response of the rover for individual and joint failure modes. For example, what is the response of the rover when there is no obstacle detection and sensing malfunction.
Variation of mission parameters to generate requirements: e.g., what is an ideal safety buffer, what is an acceptable location and pose estimation error for the navigation function
Variations in environment to define the rover operational envelope: e.g., can the rover perform safely in terrain with a high obstacle density?

## Slide 33: Requirements Specification and Analysis in FRET

## Slide 34: Specification, Understanding and Formalization: Requirements in FRETish
FRET uses a structured natural language, namely FRETish, which is based on 6 fields. Asterisk indicates mandatory fields.
Specification: FRETish text (structured natural language)
Understanding: Explanation of semantics in various formats. E.g.,
English description
Diagrammatic explanation
Formalization: Automatic translation to temporal logic formulas, which can be used for analysis.
Example TROUPE requirement in FRET

## Slide 35: Simulation: Interactive visualization of requirement semantics
Variable valuation that violates the requirement. Occupied does not become true within 2 seconds of the condition (F_leaderInCommRange & observed) being met.
Variable valuation that satisfies the requirement.

## Slide 36: Analysis: Consistency/Realizability Checking of Requirements
Identify conflicting requirements
Return counterexamples that help repair conflicting requirements

## Slide 37: Runtime monitoring: Connection with tools
Example of R2U2 monitor that was created using the formalized requirement exported by FRET:
FRET
R2U2 or Copilot/Ogma
Natural language
requirement
Formalized
requirement
Monitor app
FRET connects with different runtime monitoring tools such as NASA's R2U2 and Copilot/Ogma tools.
Here is a simplified workflow diagram:

## Slide 38: Further Reading
AdvoCATE
fmdtools
MIKA
FRET
https://ntrs.nasa.gov/api/citations/20220009664/downloads/AdvoCATE%20User%20Guide_1.4.pdf
https://github.com/nasa/fmdtools
https://github.com/nasa/mika
https://github.com/NASA-SW-VnV/fret