## Slide 1: Onboard Phase Retrieval for Habitable Worlds Observatory
Alden Jurling*,1, PhD. Kaitlyn Summey1, Der-You Kao2, PhD., and Thomas Zielinski1, PhD. *: alden.s.jurling@nasa.gov
Project Overview:
A key area of technology development for the Habitable Worlds Observatory (HWO) is telescope wavefront control capable of meeting the picometer-level telescope stability requirement.
We propose using phase retrieval in HWO imaging instruments and the light from out-of-field stars to measure the primary and secondary mirror alignment and enable closed-loop, onboard control or calibration of environmental disturbances. We have
Conducted parametric studies to determine the driving factors in phase retrieval performance
Established a flux budget and compared out-of-field instrument designs using realistic target stars and current Exploratory Design Concepts (EAC)
Developed a computing budget and proposed hardware for on-board computation
Compared parallel programming paradigms for phase retrieval
Real-Time Numerical Simulation Framework:
CPU: Xeon E5-2696v4 22-core
GPU: GTX 1080
Trades initial setup time for faster subsequent operations
~60x faster basis setup, ~200x faster fitting, ~300x faster projection, ~140x faster expansion operations than Phase Retrieval Metrology Software used during JWST Commissioning
Enables possibility of manipulating optical pupils at KHz rates (FP32) or hundreds of Hz (FP64)
Approx. Parallelized Basis Set Operations Times (ms) Simulated using M, N = 1024, 18 segments, and 36 segment and 20 global Zernikes |  |  |  |  | 
 |  | Setup | Fit | Project | Expand
CUDA SM60 | FP32 | 1510 | 3 | 3 | 1
 | FP64 | 1587 | 10 | 7 | 2
C++ OpenMP + Baselet | FP32 | 1333 | 7 | 5 | 4
 | FP64 | 1347 | 11 | 8 | 6
C++ OpenMP | FP32 | 351 | 33 | 27 | 37
 | FP64 | 381 | 30 | 35 | 57
Integration Time Simulations:
Method:
Use LUVOIR target list
Query 2Mass and Gaia catalogs to find 50 brightest point sources inside detector field of view
Calculate total flux
Calculate integration time to get required number of photons for 10 pm accuracy
Integration Times (minutes) |  |  |  |  |  | 
Percentage of Targets | EAC-1 |  |  | EAC-3 |  | 
 | HRI | GI | HRI+GI | HRI | GI | HRI+GI
25% | 14.2 | 9.1 | 4.2 | 21.1 | 3.1 | 2.3
50% | 63.6 | 16.1 | 11.5 | 78 | 8.6 | 7.4
75% | 268.8 | 77.7 | 33.1 | 282 | 30.3 | 18.9
95% |  | 487.4 | 195 |  | 172.6 | 121.2
Global, low order
Segment tip/tilt
Conclusion:
GI FOV largest impact on integration time for both EAC designs
A combined HRI + GI system is ideal
  Stars in J-band tended to be brighter
  NIR instrument performs better than VIS with equivalent FOV
*For 20% bandwidth
Computing Budget:
Phase retrieval parameters | 
Wavefront Zernikes | 
Amplitude Zernikes | 
Pupil size | 
Pad size | 
Image size | 
Oversampled pad size | 
Wavelength samples | 
Phase retrieval parameters | 
Wavefront Zernikes | 
Amplitude Zernikes | 
Pupil size | 
Pad size | 
Image size | 
Oversampled pad size | 
Wavelength samples | 
We investigated the floating-point operations (FPOs) and memory required for onboard phase retrieval
Algorithm Memory | 
Total: | 
Algorithm Memory | 
Total: | 
Assuming LO wavefront control and
695 M FPOs/iteration
45 MiB memory
,
,
, and
,
We would need:
Variable memory allocation | 
Total: | 
Variable memory allocation | 
Total: | 
Integration Times (minutes) |  | 
Percentage of Targets | EAC-1 | EAC-3
 | HRI+GI w/ 40% BW | 
75% | 8.4 | 1.74
95% | 47.4 | 11.1
GI A
GI B
HRI
CI
HRI
GI A
GI B
CI
EAC-1 Instrument FOV
EAC-3 Instrument FOV
Cumulative Sum of Integration Times for Segment PTT
Flux budget:
We evaluated phase retrieval performance using simulated, noisy PSFs with a range of total energies to estimate a flux budget for our integration time comparisons. The flux budget is based on requirements for measuring segment level piston tip and tilt.
EAC-1
EAC-3
Avg. RMS WFE Monte Carlo Results
To meet our sensing requirements for segment-level control, we need approximately
over the instrument’s field of view.
EAC-1 → nJ
EAC-3 → nJ
Background:
EAC Designs |  |  |  |  | 
 | HRI (NIR) |  | GI |  | 
 | EAC-1 | EAC-3 | EAC-1 | EAC-3 | 
FOV | 3x2 |  | 3x3 | 3x6 | arcmin
Pixel size | 10 |  | 10 | 5 | um
Wavelength | 800-2500 |  | 400-1000 |  | nm
Focal length | 120 | 160 | 93.8 | 149.3 | m
f/# | 15.6 | 18.7 | 15.6 | 18.7 | 
PM 3 DOF + SM 4 DOF
PM 5 DOF + SM 5 DOF
PM 5 DOF
In our parametric studies, we found that bandwidth was not a driving factor in phase retrieval accuracy.
If we increase the bandwidth and factor in the RMS relaxation for LO control, we get:
Proposed Hardware:
Gaisler GR765 with NOEL-V
6.95 seconds to compute 10 iterations per star
45 MB memory needed per star
  →Use RAM to overcome 4 MiB L2 cache limitation
Future Work:
Conduct trade studies for additional (and future) EAC designs
Integrate results from phase retrieval studies to simulate more realistic control outcomes
Developing RISC-V phase retrieval tools
We looked at the hexagonal segmented EAC-1 and keystone segmented EAC-3 designs.
We took into consideration the instrument FOV size and layouts to conduct our sky dependent studies.
For our out-of-field wavefront sensor studies, we compared the performance of segment-level piston, tip, and tilt of the primary mirror (PM) and global secondary mirror (SM) control for two EACs. Previous parametric studies showed that phase retrieval accuracy is not heavily influenced by things like bandwidth, wavelength, or number of stars, but an out-of-field system will be dependent on the stars available in the sky area around the target star.
We investigated “perfect” control over different degrees of freedom, and it shows that using a joint primary + secondary mirror control scheme gives promising performance.
HRI – High Resolution Instrument
GI – Guider Instrument
1: NASA GSFC
2: Genesis Engineering Solutions, Inc.