## Slide 1: Impingement Analysis Unreal Engine Implementation
Elijah Crouch (Amentum)
encrouch@ndc.nasa.gov
8/8/2025

## Slide 2: About Me
Hobbies
Playing Instruments
Playing/Making games
Tennis
Traveling
Background
Brigham Young University
Mechanical Engineering – Aerospace Emphasis
Graduating April 2027

## Slide 3: Impingement Visualization Development
Primary Objectives
1. Represent plume impingement on booster during separation
  Performant and Highly customizable decals
  Plume cutoff on collision
2. Surface Deformation to represent Plume Surface Interaction
  Both playback and real-time (Simulink co-simulation capability)
  Customizable shapes for more in-depth analysis
3. Elevation and slope shaders for hazard analysis

## Slide 4: Decals and Materials
Decals
Projects a material onto bodies within a localized area
Dynamic rotation, position, and size parameters
Materials
Rendering process that sends data to the graphics card to change the look of pixels.
Dynamics parameters such as color, emission, roughness, transparency, etc.

## Slide 5: Separation Impingement – Collision Detection and Application
Without Collision Detection
With Collision Detection
Trace a vector matching the position and rotation of each engine on the tanker as separation begins
Send the collision location to plume visuals to remove plumes past the collision
Place a decal on the hit location with the z axis and face normal aligned

## Slide 6: Modeling the Moon
The moon is rendered using a tool called Clip Map Unreal Terrain developed by JSC.
Converts DEMs to vertex height coordinates.
Applied to a lunar mean radius sphere mesh.
Uses clip mapping to render vertices in subsections called levels.
Subsequent levels have reduced vertex resolution.
Saves on VRAM and RAM.
Resolution is highest within center of camera view.
Updates with camera motion.
Multi-threaded to increase speed.

## Slide 7: Modeling Craters
CSV
Simulink
MathWorks Interface
Unreal Engine Data Table
Crater Shaping Plugin
Rendering
Input Source
API
Playback
Real-Time
Processing
Visualization

## Slide 8: Playback vs Real-time
Playback
Complete data available
Specified time can be selected for viewing
Unreal Engine sequencer compatible
Requires CSV data
Real-time
Speed of formation is visible
Simulink compatible
Active during simulation

## Slide 9: Playback Data Handling
Csv files are not natively supported.
Csv data must be converted to a data table which is an array of structs. Each struct contains one row of column data.
Format and Importing Notes
Data Tables must have unique entries in the first column.
The first column in a data table will not have a name. Every column after must have a name.
Edits to the data format must be reflected in the custom struct.

## Slide 10: Real-Time Simulink interface
As of MATLAB 2025a, a plugin is available that connects Unreal Engine and Simulink called MathWorks Interface.
Data sent as an array
Sent every time step
Same format as csv data
Data
Mux
Array
Write Message Block
Simulink
Unreal Engine
Sim3dGetFloat
Array
Height Map Modifier
Shared C++ memory space

## Slide 11: Crater Shaping
Equation Editing
Defaults to circular equation on the left
Blueprint or C++ editable
  Blueprint equation performs slower than C++ equation
  C++ is more robust
Calculation
Crater depth scales the equation
Blueprint available variables
  Vertex distance from center of crater
  Radius of crater
Crater Shape side views

## Slide 12: Elevation Map

## Slide 13: Slope Map
Green < 10° < Yellow < 15° < Red
Black = 0° White = 90°

## Slide 14: Questions?
Special thanks to Patrick Serafin (ESSCA), Peter McDonough (ESSCA), EV42, and the Amentum Intern team