## Slide 1: Advancements in Satellite-based Hyperspectral Microwave Sounding at NASA GSFC
Antonia Gambacorta1, Fabrizio Gambini1,2, Matt Fritts1, Berhanu Bulcha1, Alexander Kotsakis1,3, Narges Shahroudi1,3, Stephen Nicholls1,4, Patrick Stegmann1,3, Jordan Caraballo-Vega1,Victor Torres1, Priscilla Mohammed1.6, Jared Lucey1, Mark Stephen1
1. NASA Goddard Space Flight Center;
1.2 NASA Goddard Space Flight Center, University of Maryland Baltimore County, CRESST II
1.3 NASA Goddard Space Flight Center, University of Maryland College Park, ESSIC
1.4 NASA Goddard Space Flight Center, SSAI, Inc.
1.5 NASA Goddard Space Flight Center, SAIC, Inc.
1.6 NASA Goddard Space Flight Center, ASRC Federal System Solutions
Eumetsat Meeting, Lyon, France, September 19th, 2025

## Slide 2: Harnessing Improved Atmospheric Content in Hyperspectral Microwave Measurements
Total Precipitable Water
Total Cloud Liquid Water
Light Precipitation
Surface Temperature
Surface Emissivity
Surface Wind Vector
Sea Ice Concentration
Snow Depth
Snow Water Equivalent
Bare Surface Soil Moisture
Temperature
Surface Temperature
Precipitation
PBL Water Vapor
Surf. Emissivity
Hydrometeors
Water Vapor
Hydrometeors
Advanced Ultra-High Resolution Optical RAdiofrequency (AURORA) Pathfinder
Temperature

## Slide 3: MW Photonics Design
G-Band Rx
ASIC
EOM
SAWG
BPR
PD
Amplifies spectra.
Separates spectrum into
10 x 4 GHz sub-bands.
Sub-bands with minimal
structure are measured directly (Lo-Res Channel).
RF domain
RF domain
Optical domain
Baseband domain
(0 – 4 GHz)
Converts microwave spectrum to optical domain.
4 GHz
Optical domain
Hi-Res Channel
Sub-bands with structure
are mixed with a new
optical tone and digitized (Hi-Res Channels).
Lo-Res Channel
Lo-Res Channel
Captures MW spectrum.
Antenna
HyMPI is a modular design, with simultaneous 40 GHz coverage
Can be applied to multiple parts of the spectrum to obtain full, contiguous coverage of the MW thermal domain
Paired with ASICs - “PICASIC” - it enables full, contiguous, hyperspectral resolution coverage in entire Earth’s MW thermal domain
Gambini et al., 2024, https://ieeexplore.ieee.org/stamp/stamp.jsp?arnumber=10380670
US Patent 11852864
Title: “Serial Arrayed Waveguide Grating”​

## Slide 4: Serial Arrayed Waveguide Grating - SAWG
US Patent 11852864 – M. Stephen, “Serial Arrayed Waveguide Grating”
Gambini et al., 2024, An Ultra-Compact, Narrow-Bandwidth, and High-Density Channel Photonic Integrated Channelizer Based on Serial Arrayed Waveguide Grating Architecture, J. Lightwave Technol. 42, 2908-2916 (2024)
PIC microscope image
20 mm (0.8’’)
12.5 mm (0.5’’)

## Slide 5: SAWG system model
Optical and geometrical parameters define the frequency response of the filter:
  33 delay lines
  21 output channels
  2.5 GHz channel separation
  2.0 GHz channel 3dB bandwidth
  30 dB side-lobe suppression
Normalized intensity[dB]
[dB]
Example of SAWG Matlab model result

## Slide 6: The Advanced Ultra-high Resolution Optical and RAdiofrequency (AURORA) Pathfinder
~PBLH

## Slide 7: AURORA Pathfinder: harnessing PBL, Surface, Cloud information content in unexplored MW spectral domain
NEdT @ 1 GHz
NEdT @ 2.5 GHz
NEdT @ 4 GHz
US Standard
Midlat Summer
Midlat Winter
Arctic Winter
Frequency (GHz)
Frequency (GHz)
Frequency (GHz)
Delta BT(K)
10% Delta Water Vapor @ 850hPA
Midlat Sum: Surf. Emissivity Perturbation
Midlat Sum: CLW 10% Perturbation
Aurora Pathfinder = Sounder + Imager

## Slide 8: Applications: AURORA Pathfinder Will Enable Improved Sounding under Extreme Weather Measurements
Truth
ATMS
AURORA

## Slide 9: Applications: AURORA Pathfinder Will Enable New Discoveries in Temperature, Water vapor, Aerosol and Cloud Feedbacks
ATMS
AURORA v1
AURORA v2
AURORA v3
Gambacorta et al., IEEE TGRS, 2025 - In publication

## Slide 10
https://earth.gsfc.nasa.gov/climate/campaigns/WHyMSIE

## Slide 11: West-coast & Heartland Hyperspectral Microwave Sensor Intensive Experiment - WH2yMSIE
ER-2 |  | 
Instrument | Measurement Type | Spatial Scale
Conical Scanning Millimeter-wave Imaging Radiometer - Hyperspectral (CoSMIR-H) | Hyperspectral Microwave | 1 km
Microwave Barometric Radar and Sounder (MBARS) | Doppler Radar | 1-4 km
Cloud Radar System (CRS) | Doppler Radar | 300 m
Cloud Physics Lidar (CPL) | Backscatter Lidar | 125 m
Scanning High-resolution Interferometer Sounder (S-HIS) | Infrared | 2 km
National Airborne Sounder Testbed – Interferometer (NAST-I) | Infrared | 2.5 km
Advanced Microwave Precipitation Radiometer (AMPR) | Microwave | 0.64 – 2.78 km
MODIS/ASTER Airborne Simulator (MASTER) | Visible-Infrared | 50 m
Airborne Radio Occultation (ARO) | GPS Radio Occultation | ~125 km
G-III |  | 
High Altitude Lidar Observatory (HALO) | Differential Absorption Lidar | 6-12 km x 315 m
Aerosol Doppler Wind Lidar (AWP) | Doppler Lidar | ~ 2 km
Dropsondes | In Situ | ~ 20 km
Objectives
Demonstrate the capabilities of CoSMIR-H
Maximize sampling of ocean clear sky environments and under fly various POR satellites equipped with microwave instruments (ATMS, AMSU/MHS)
Capture a wide variety of atmospheric states that contribute to variability in PBL and surface emissivity over land (e.g. convective/non-convective)
Maximize validation opportunities and overflights of ground based PBL-focused networks (e.g. SGP, NCAR Boulder, G-III dropsondes)
Challenge the capability of the combined remote sensing payloads (ER-2 + G-III) by sampling baroclinic zones (T/q gradients) and cloudy environments (e.g. marine stratocumulus)

## Slide 12
WH2yMSIE Over Land Objectives and Ground-Based Support
Capture wide range a surface types to develop improved surface emissivity models critical for future PBL-relevant microwave retrievals of temperature and water vapor
Observe PBL dynamics over different surface types (dessert, grasslands, etc.) at different times of day to capture diurnal variability
Land Flight Overview
4 science flights
27 radiosondes
Clear sky
NOAA-21, EarthCare
WH2yMSIE Over Water Objectives and In Situ Validation Support
Maximize clear sky data points and under fly POR satellite instruments for future MW and IR cal/val comparisons
Observe a variety of marine PBL environments in clear and cloudy conditions
Ocean Flight Overview
6 science flights
40 dropsondes
Mix of clear and cloudy scenes
NOAA-21, Arctic Weather Satellite (AWS), EarthCare
WH2yMSIE Data Archive is located at https://www-air.larc.nasa.gov/