## Slide 1
Chintan Patel
Computational Fluid Dynamicist – ESSCA, Propulsion Fluid Dynamics Branch, NASA MSFC
November 25, 2025
Lana Asaad
Intern, Propulsion Fluid Dynamics Branch, NASA MSFC
Validation of Multi-species Two-phase Turbulent Flow CFD Model for Cryogenic Tank Pressurization
nasa.gov | Approved for public release.

## Slide 2
Background
Managing cryogens is a critical technology for NASA’s spaceflight missions
Cryogenic fluid management (CFM) challenges Long term propellant storage Pressure control for nominal operations Propellant transfer in microgravity Conditioning propellants with cryocoolers
NASA’s CFM Modeling Portfolio Develop, enhance and validate computational fluid dynamic (CFD)
Propulsion Fluid Dynamics Branch at NASA Marshall supports several projects with CFD analyses Human Landing System (HLS), Space Launch System (SLS), Commercial Lunar Payload Services (CLPS), etc.
Develop and validate Loci-Stream-VOF CFD solver to solve complex thermo-fluid and multi-physics problems for CFM Phenomena: self-pressurization, autogenous and non-condensable tank pressurization, tank depressurization, ullage collapse, tank filling with jets/sprays, cryocooler operations, etc.
Validation of MHTB Spray Bar Cooling with CFD with Eulerian-Lagrangian Particle Transport
Multi-purpose Hydrogen Test Bed (MHTB) Experiment[1]
[1] Hastings, L.J., Flachbart, R.H., Martin, J.J., Hedayat, A., Fazah, M., Lak, T., Nguyen, H., Bailey J.W., ‘Spray Bar Zero-Gravity Vent System for On-Orbit Liquid Hydrogen Storage”, NASA TM-212926, 2003

## Slide 3
Pressurization Experiments
DLR (German aerospace agency) and University of Bremen experiments
Insulated cylindrical tank of radius 0.148 m
Filled with liquid Nitrogen at initial pressure of 106 kPa
Pressurant gases: nitrogen or helium
Varied inlet pressurant temperatures across experiments
Primary comparison metric Pressurant mass requirement
Gas Probes
Wall Probe
Liquid Probes
Tank Pressure
[2] C. Ludwig, M.E. Dreyer, Investigations on thermodynamic phenomena of the active-pressurization process of a cryogenic propellant tank, Cryogenics, Volume 63, 2014, Pages 1-16
T17
Tank Height = 0.65 m
Fill Height = 0.445 m

## Slide 4
Modeling
Critical flow physics
  Interface turbulence transport (ITT)
  Phase change
ITT strongly influences propellant requirements, and consequently design of spaceflight missions
Time and length scales for ITT is orders of magnitude smaller than spaceflight
  Requires development and validation of computationally viable engineering model
Interface Turbulence Transport
Interface Thermal Transport and Temperature
Phase Change
Tank pressure prediction, Pressurant requirement, Propellant requirement, Active cooling requirements
[3] Chintan Patel. "Validation of Two Phase Flow Modeling Techniques in Loci-Stream Using Axial Jet Pressure Control and Autogenous Pressurization Experiments," AIAA 2025-1358. AIAA SCITECH 2025 Forum. January 2025
RANS – Reynold-average Navier Stokes
LES – Large Eddy Simulation
IDDES - Improved delayed detached eddy simulation
Pressure-based solver with mass, momentum, energy and species conservation
Physics Models
Two-phase model: Frozen interface
Turbulence model: IDDES (Hybrid RANS-LES)
Asymmetric interface turbulence transport model based on experimental and DNS evidence[3]
Phase change model: Hertz-Knudsen-Schrage (HKS)
Material Properties
NIST database
Nitrogen-Helium mass diffusivity from Chapman-Enskog theory
Axisymmetric simulations
Gas Phase
Liquid Phase
Wall-like Turbulence
Interface TKE is zero
Free-stream-like Turbulence
Interface TKE is extrapolated
Asymmetric Interface Turbulence Model
Phase Change Model

## Slide 5
Autogenous Pressurization
100-micron mesh resolution required for accurate resolution of the thermal gradients along with asymmetric interface turbulence transport modeling
Observed Dynamics from CFD Simulation – Vorticity, Velocity Magnitude, Turbulence Viscosity Ratio, and Temperature
Gas-Liquid Interface

## Slide 6
Autogenous Pressurization
Excellent agreement with test data error in predicting required pressurant mass (test had ±3.7% measurement accuracy)
  Temperatures across the tank as well as post-pressurization pressure drop are also well predicted
Pressure Change vs Time
Solution independent of spatial resolution, temporal resolution, accommodation factor of the phase change model, and inlet turbulence intensity
Temperature vs Time

## Slide 7
Non-condensable Pressurization
Faster pressurization with helium – computationally more challenging
Cascading rows of Rayleigh–Taylor instabilities due to low density helium displacing higher density nitrogen
  More complex vortical structures and more complex turbulent flow
Gas-Liquid Interface
Observed Dynamics from CFD Simulation – Helium mass fraction, Velocity Magnitude, Turbulence Viscosity Ratio, and Temperature

## Slide 8
Non-condensable Pressurization | Summary
Good agreement with pressurization data with error in pressurant mass prediction (test had ±2.5% measurement accuracy)
  Post-pressurization pressure drop prediction is unsatisfactory – resulting in 18.2% error in effective pressure increase
  Phase change model is suspected to be inadequate for condensation under quiescent flow with non-condensable present
Pressure Change vs Time
Solution independent of spatial resolution, temporal resolution, accommodation factor of the phase change model, and inlet turbulence intensity
Ullage Temperature vs Time
* Full time-series of the experiment data were not available. Based on engineering judgement, an appropriate range of inlet temperatures were chosen, and minimum error is indicated.
Temperature measurements are unavailable, but higher ullage temperature predicted by the CFD simulation are consistent with higher helium specific heat and faster tank pressurization rate
Experiment | Pressurant Requirement Error (%)
N200r* | 0.1
N400c* | 8.6
N200a* | 7.5
N200h* | 4.3
N300h | 4.0
He400c* | 4.9
He400h | 4.2
Excellent Pressurant Mass Prediction across Seven Tests

## Slide 9
Conclusion
Validated CFD model for autogenous and helium pressurization operation
  Careful interface turbulence transport modeling necessary for accurate predictions
  Post-pressurization pressure drop is well predicted for autogenous pressurization but is unsatisfactory for helium pressurization
Further Work
Identify and address root causes for unsatisfactory post-pressurization pressure drop
Validate with moving and morphing interfaces – more complex CFM operations
Successful validation across propellant tanks of all sizes, different cryogens, and varying CFM operations using the same modeling approach demonstrate wide model applicability for supporting NASA’s future spaceflight missions